## Slide 2: LIU for HL-LHC - Presentation on the LIU project with a summary of their RunI performance and projections for RunII (BCMS) with an outline of outstanding tests and improvements -
S. Gilardoni for the LIU project
Input from: H. Bartosik, G. Iadarola, Y. Papaphilippou, G. Rumolo, E. Shaposhnikova, G. Arduini, T. Argyropoulos, J. Bauche, T. Bohl, K. Cornelis, P. Costa Pinto, H. Damerau, R. de Maria, D. Manglunki, J. Esteban Müller, R. Garoby, B. Goddard, S. Hancock, W. Höfle, M. Meddahi, B. Mikulec, M. Taborelli, H. Timko, R. Wasef

## Slide 3: Luminosity and injectors performances
Maximum number of bunches depends on RF gymnastics (aka production scheme) chosen in PS plus number of PS injections in SPS*
* Once fixed the gaps for kicker rise times (PS, SPS, abort gap)
Minimum possible emittance deliverable is given by the Linac (L2 or L4)
Emittance conservation limited by Space-charge in PS and SPS
Maximum Intensity per bunch limited by longitudinal beam stability in PS and SPS and maximum RF power available in SPS
LIU goal: maximise number of protons circulating in the LHC while delivering sufficiently small emittances both @ LHC injection

## Slide 4: Catalogue of Possible production schemes - 25 ns
Schemes 25 ns | PSB – PS bunches | RF gym. in PS | RF gym. at injection | RF gym. at extraction | b/Train to SPS | SPS injections
3-spitting (standard scheme) | 4 + 2 | /3 ↗ /2 /2 |  |  | 72 | 4
BCMS | 4 + 4 | +2C/3↗/2 /2 |  |  |  | 
 |  |  |  |  | 48 | 5
BCS | 4 + 4 | C ↗ /2 /2 |  |  |  | 
 |  |  |  |  | 32 | 5
8b+4e | 4 + 2 | /2 ↗ /2 /2 |  |  |  | 
 |  |  |  |  | 48 | 5
/ Splitting C Batch Compression + Merging ↗Acceleration to 26 GeV/c

## Slide 5: How LIU performances are presented
Present situation
Achieved performance
HL - LHC
Non accessible beam parameters
RF limit* : PS or SPS
Space charge limits* in PSB/PS/SPS
*limits = preserve same beam quality as today

## Slide 6: Standard scheme (72 bunches / PS batch)
LIU upgrades on top of L4 connection
  SPS 200 MHz upgrade
  SPS e-cloud mitigation
  PSB-PS transfer at 2 GeV
Limitations standard scheme
  SPS: longitudinal instabilities + beam loading
  PSB: brightness
Performance reach
  2.0x1011p/b in 1.88μm (@ 450GeV)
  1.9x1011p/b in 2.26μm (in collision)
after connection
of Linac4

## Slide 7: BCMS scheme (48 bunches / PS batch)
LIU upgrades on top of the Linac4 connection
  SPS 200 MHz upgrade
  SPS e-cloud mitigation
  PSB-PS transfer at 2 GeV
Limitations BCMS scheme
  SPS: longitudinal instabilities + beam loading
  PS: space charge
  SPS: space charge
Performance reach
  2.0x1011p/b in 1.37μm (@450GeV)
  1.9x1011p/b in 1.65μm (in collision)

## Slide 8: LHC injectors upgrade Goals
“The LHC Injectors Upgrade should plan for delivering reliably to the LHC the beams required for reaching the goals of the HL-LHC. This includes LINAC4, the PS booster, the PS, the SPS, as well as the heavy ion chain…” (This is the mandate … Upgrade of Brightness)
+ determine possible improvements for high intensity beams.
PSB
SPS
PS
LHC /
HL-LHC
Output energy
160 MeV
1.4 GeV
26 GeV
450 GeV
7 TeV
Linac2
50 MeV
Proton flux / Beam power
Present
Linac4
PSB
PS
2.0 GeV
LIU (2019)

## Slide 9: Upgrade Timeline*
2012
2015
2016
2017
PSB-PS transfer 1.4 GeV  2 GeV
Linac 4 ready
PSB H- injection could be available
2013
2018
Chamonix 2012
Linac 4 connection
SPS aC coating, 200 MHz power upgrade completed
LS1 for injectors
LS2 for injectors
2019
Injectors commissioned to be ready for after LS3
2014
LS = Long Shutdown - No beam
* Pending RLIUP outcomes
LIU Project Baseline definition
Priority to LHC
Priority to Injectors Duration ~ 20 Months
Analysis of different limitations and parameters definition

## Slide 10: Project Organization Breakdown Structure
LIU-PSB coordination team
K.Hanke - MC
B.Mikulec – DMC
V.Raginel – SS
LIU- PS coordination team
S.Gilardoni – MC
H. Damerau– DMC
C. Y. Vallgren - SS
LIU-SPS coordination team
B.Goddard - MC
E.Shaposhnikova – DMC
G.Rumulo – SS
LIU-Project Safety coordination
A. Funken
Director of Accelerators and technology - Steve Myers
LIU Project team
Roland Garoby (Project Leader) - Malika Meddahi (Deputy) - Brennan Goddard (LIU-SPS machine coordinator) - Simone Gilardoni (LIU-PS machine coordinator) - Klaus Hanke (LIU-PSB machine coordinator) - Maurizio Vretenar (Linac4 Project Leader)- Anne Funken (Project Safety Officer)-Django Manglunki (LIU-Ion chain coordinator)
Linac4 Project
M.Vretenar - PL
A.Lombardi -DPL
LIU Administrative Support: Cécile Noels, Nadine Audrey. Project Support: Pierre Bonnal, Sylvain Weisz, Tadeusz Kurtyka - EVM coordinators: De Jonghe, Benoît Daudin
LIU- Ion coordination team
D. Manglunki – MC
B. Holzer – DMC
M. Bodendorfer - SS

## Slide 11: 2012 performance (@SPS extraction)
25 ns
Trains of 72 bunches to SPS
Used for the LHC scrubbing run in 2012
Trains of 48 bunches to SPS
Used for the LHC pilot physics run in 2012
Measurement points
Emittances deduced from combined wire-scans at end of SPS flat bottom (values cross-checked with LHC)
Error bars include spread from several measurements as well as systematic uncertainty (10%)
Intensity measured at SPS flat top after scraping

## Slide 12: 2012 performance (@SPS extraction)
25 ns
Projected lines derived from the measured brightness curve of the PSB translated into SPS flat top applying budgets (see table)
The traditional 25 ns beam suffers about 15% extra losses and/or emittance growth (slow losses at the SPS FB, PS space charge, electron cloud)
25 ns
 | Dex,y/ex0,y0 | DN/N0
PS | 5% | 5%
SPS | 10% | 10%

## Slide 13: Beams expected @ SPS extraction in 2014-15
 |  | Bunch intensity [1011 p/b] | Transv. Emittance** [1 σ norm, mm.mrad] | Bunches per batch (@ SPS inj.) | PSB rings | Harm. @PS inj.
Baseline for physics | 25 ns**** | 1.15 | 2.8 | 72 | 6 | 7
 | 25 ns BCMS | 1.15 | 1.4 | 48*** | 8 | 9
Eventually for startup | 50 ns | 1.65 | 1.7 | 36 | 6 | 7
 | 50 ns BCMS | 1.6 | 1.2 | 24 | 8 | 9
** Transverse Emittance= (εh+εv)/2 Beam are produced approx. round: linear coupling in PS used to avoid Head-tail instability
After LS1 it would be possible to have less round beams if needed.
*** Filling scheme with batches of 48 bunches exists giving a reduction of 8% in Luminosity compared to the same scheme with 72 bunches
**** Better performances measured during scrubbing run: 1.15 1011 p/b, 2.4-2.5 mm.mrad 1.4 1011 p/b produced but no emittance measurements available@SPS

## Slide 14: Possible performance improvements after LS1 ?
25 ns beam (both standard production and BCMS) already very close to the limits in injectors
  Intensity per bunch  10% from the limit due to the SPS constraints
  Brightness  At the limit for space charge in the PS
Higher intensity
  In 2012 SPS MD in which 1.35 x 1011 ppb were accelerated, but with degraded beam quality at 450 GeV/c (longitudinal instabilities, e-cloud ?)
  In any case, max 1.3 x 1011 ppb can be presently extracted from the SPS compatibly with RF power and longitudinal instabilities limitations
Higher brightness
  RF manipulations in the PS @2.5 GeV (instead of 1.4 GeV)
    Larger longitudinal emittance from the PSB
    Space charge alleviated by both longer bunches and larger momentum spread
  PSB control of longitudinal parameters along the cycle

## Slide 15: Potential improvement after LS1 (standard scheme – longer bunches PS-PSB transfer)
Present situation
Achieved performance
With new longitudinal parameters

## Slide 16: Potential improvement after LS1 (BCMS – longer bunches PS-PSB transfer)
Present situation
Achieved performance
With new longitudinal parameters

## Slide 17: Pure batch compression (BC) scheme
Alternative production scheme for 25 ns beams
Pure batch compression at 2.5 GeV (from h=9 to h=21)
Twice double splitting at FT
Trains of 32 bunches to the SPS
Extra-bright 25 ns beam
Trains of 32 bunches can relax the electron cloud issues in the LHC
About 13% lower # of bunches in the LHC
Production and transport of beams with sub-mm transverse emittance not yet demonstrated

## Slide 18: PSB @ 2 GeV : space-charge reduction at PS injection
PSB extraction energy upgrade needed
to reduce space-charge effects at PS injection 2 GeV upgrade requires
(only main elements cited) :
New main power supply (POPS-like)
Main Magnet cooling
New External dump
Main Magnet power distribution
New extraction elements
New transfer line elements
New external beam dump
New RF system
New 2 GeV PS injection elements
Finemet @ R4

## Slide 19: Challenges in the PS
Injection flat bottom:
Space charge  higher brightness with 2 GeV
Headtail instability  transverse FB
Acceleration/Bunch splittings
Longitudinal CBI  new damper
Transient beam loading  1 turn delay FB
Transition crossing  no limitation expected
Flat top:
Longitudinal CBI  new damper
Electron cloud  transverse FB
Transverse instabilities  transverse FB
Injection flat bottom:
Space charge  2 GeV injection upgrade
Headtail instability  transverse FB

## Slide 20: Longitudinal Coupled bunch instabilities
FB OFF
FB ON
Longitudinal CB instabilities appear after transition
With new dedicated longitudinal damper possible to reach more than 2.5e11 p/b at extraction.
Finemet cavity installed during LS1
Frequency : 0.5-5.5 MHz.
Peak voltage : up to 5 kV.
6-cells cavities.
Each cell with one gap and 2 Finemet® cores.
Each cell driven by two 2.5 kW solid-state amplifier.
Water cooled cavities and amplifiers.
PS cavities assembled

## Slide 21: SPS limitations overview
Along the whole cycle:
Electron cloud for 25 ns
Injection flat bottom:
Capture losses, incoherent losses
Space charge
TMCI
Ramp and flat top:
Longitudinal instability
Beam loading
RF power

## Slide 22: SPS 200 MHz travelling wave RF cavities
Total 200 MHz Power/cavity limit:
  Presently 0.7 MW (continuous mode)
  Around 1.05 MW for ½ ring in pulsed mode with new LLRF
  Limit reached already during acceleration
Beam loading: less voltage available for higher intensity!
Bunch length at extraction fixed by LHC acceptance
Upgrade:
  Rearrange 4 existing cavities into 6
    2x4+4x3 = 20 sections, with 2 spare sections
    gives also 20% less impedance
  2 additional new power plants with 1.6 MW each
Power/cavity (nominal intensity)
present power limit
Q20
Q26
t = const, LD+PWD
24+25
43+24
43+42
102
LD: Loss of Landau damp.
PWD: Potential well dist.
Z/n today
Pold = 1.05 MW
Pnew = 1.6 MW
RF voltage at transfer to LHC
Q20 optics

## Slide 23: 8b+4e scheme in the SPS
  Simulation
Ekin = 2.5 GeV
LD: Loss of Landau damp.
PWD: Potential well dist.
24+25
43+24
43+42
102
t = const, LD+PWD
Line density averaged over 0.3 ms (≈tfill/2) reduced by 2/3 at constant Nb
  50% more intensity per bunch for the same beam loading
No benefit for single-bunch instability effects
Nb ≈ 3 · 1011 ppb reachable assuming SPS impedance reduction by 50%
First beam tests after LS1 possible
4 bunches missing every 8 bunches  improvement for e-cloud
50% less bunches in LHC, but with significantly higher intensity

## Slide 24: e-cloud and scrubbing in the SPS
Strong limitation due to e-cloud in the past
  Instabilities at injection + incoherent effects
  Emittance blow-up along the batch
  High chromaticity needed for beam stability
  Pressure rise around the machine
Situation improved gradually due to scrubbing
  Secondary Electron Yield reduction by e-cloud itself
Scrubbing runs since 2002 → 2012 no beam degradation
  Performed at injection (~40 s cycle length)
  Typically limited by heating and/or outgassing
  ~1-2 weeks periods
SPS scrubbing history
2002
(14d)
2003
(8d)
2004
(10d)
2006
(5d)
2007
(7d)
2008
(2.5d)
2012
(5d)
2009
(1.5d)
Shutdown
400%
2000 (48 b. - 0.8x1011 p/b @inj.)
3.5 μm
2012 4x72 bunches (1.15x1011 p/b @inj.)

## Slide 25: Future: scrubbing or coating ?
New Scrubbing technique:
Injection of long bunches into SPS (with 25 ns spacing) Capturing each bunch in 2 neighboring 200 MHz buckets
Successfully tested in MDs at the end of 2012/13 run with 1.6x1011 p/doublet. New tests after LS2
Clear enhancement on e-cloud detectors compared to standard 25 ns beam measured
Thin a-C film a-C provides low SEY
Suppression of e-cloud in prototype chambers demonstrated with beam in SPS
4 SPS half cells (including quadrupoles) with a-C coating ready for the startup in 2014  further tests with beam after LS1
25 ns
5 ns
MBA
MBB
1.6x1011 p/doublet
1.6x1011 p/b
1.6x1011 p/b
1.6x1011 p/doublet
by mid 2015: decide if coating should be applied or scrubbing is sufficient

## Slide 26: High bandwidth transverse feedback (CERN/LARP)
High bandwidth (intra-bunch) feedback could help
  fight electron cloud instabilities
  improve beam quality during scrubbing  faster and more efficient machine scrubbing
  avoid running with high chromaticity settings  better beam lifetime and emittances
  stabilize the scrubbing beam (present damper cannot cope with “pi-mode” oscillations of doublets)
MD studies in 2012/2013 using a 200 MHz stripline pickup as kicker
  Feedback stabilizes the bunch  clearly works for dipole mode
Tune shift due to Beam loss
Instability
Feedback off
Feedback active
Instability
Fractional Tune
Turns (x1000)
Feedback switched OFF
Chromaticity ramped down
(below zero)
Fractional Tune
Turns (x1000)
Chromaticity ramped down
(below zero)
single bunch (1x1011 p/b)
Q26
Q26

## Slide 27: Ions Upgrades and studies
Linac 3: increase intensity
  10 Hz pulsing (included in consolidation - PIC)
  multiple charge acceleration (unsure of benefit for LEIR)
LEIR: Intensity limitation
  ~+40% needed for additional splitting, but cause presently unknown
PS: 50 ns splitting or batch compression near transition
  Tests of 2-bunch batch compression to 50 ns with Ar
  New cavity (Finemet)
  Transition-distortion optics for high energy splittings; imperfections?
SPS
  PFL on MKP + MSI-V septum for 100ns rise time injection / batch spacing
  New beam control allowing RF gymnastics for slip-stacking
  Are resulting imperfections after slip stacking acceptable by the LHC?
  Improvement of beam behaviour on flat bottom (RF noise…)

## Slide 28: Pb-Pb Summary: Peak luminosity & intensity (w.r.t. nominal) according to different schemes
Nominal
2011/2013
2015
Proposed
Baseline (100ns)
Slip stacking
Batch spacing in the SPS (ns)
Batch spacing in the SPS (ns)
Peak luminosity
Intensity/LHC ring
50ns batch compression in the PS

## Slide 29: Conclusions
The beam characteristics foreseen after implementation of all of LIU (25 ns, 2E11 p/b, 1.9 μm) are good enough for reaching the HL-LHC goal.
All LIU upgrades will be installed during LS2, including the L4 connection
Intermediate shutdowns will be used to minimize the duration and risks of LS2
Planning is an issue, particularly for the duration of LS2.
It will take ~3 years after the LIU hardware upgrades are installed to reach the promised beam characteristics, i.e., to be ready after LS3 for HL-LHC
The plan for upgrading the ion injectors is adequate for reaching the luminosity requested for ion physics.

## Slide 30
Back-up slides

## Slide 31: Assumptions for beam parameter estimation
- Scenario foreseen for the injectors:
  Brightness curve of Linac4 projected at PSB extraction
  all upgrade proposed for PSB/PS done (2 GeV + RF) + Linac4
  SPS: 200 MHz power upgrade, assumed e-cloud solved - possibly with aC coating of vacuum chambers
For beam quality preservation:
  Max Laslett tune shift in PS < |0.31|
  Max Laslett tune shift in SPS < |0.21|
  Max intensity in SPS@extraction with 200 MHz upgrade: 2.00 1011 p/b
Losses and emittance blow up:
  LHC: 20% Emittance blow up, 5% losses
  SPS: 10% Emittance blow up and losses
  PSB/PS: 5 % Emittance blow up and losses
  No blow-up or losses in transfer between machines

## Slide 32: 2012 performance with standard production scheme: summary table

## Slide 33: 2012 performance with BCMS scheme: summary table

## Slide 34: PSB 2 GeV extraction elements
PSB extraction bumpers  OK with present system
PSB extraction kickers  at the limit – to be measured which field can be reached in ferrites
PSB extraction septa: bus bars to be reinforced, magnets to be cooled in parallel to deal with increased RMS current
PSB recombination kickers  to be replaced

## Slide 35: Headtail instabilities
Headtail instabilities on injection flat bottom currently cured by introducing linear coupling
T-Damper/TFB 2012-2013 studies:
cured headtail at 1.4 GeV
power upgrade for 2 GeV
future chromaticity control needed to avoid high order modes
HT-Modes
Headtail instab. no T-damper
Headtail instab. with T-damper

## Slide 36: Scrubbing or coating? A possible strategy …
NO
a-C coating (during LS2)
2014
2015
Oct.
Nov.
Mar.
Jun.
YES
LIU-SPS Review: coating?
(after data analysis!)
Scrubbing qualification: No degradation for 2e11 p/b with 4x72 bunches and 6x48 bunches
Results from the 4 coated half cells
Simulations for higher brightness beams (from Linac4)
SCRUBBING RUN I (2 weeks)
beams: nominal intensity
Goal: recover the 2012 performance
Risk: mixed with machine start-up
SCRUBBING RUN II (2 weeks)
beams: 2e11 p/b, scrubbing beam, …
Scrubbing successful for high intensity?
Notes: Scrubbing run I: operational recovery
Scrubbing run II: for LIU

## Slide 37: LHC 25(50)ns alternative scheme in PS: BCMS
h = 9
h = 21
h = 9 10  1112  13  14  7  21
h = 21  42  84
+4 bunches
4 bunches
Production scheme: a) Double batch injection from PSB (4 + 4 bunches, 8 bunches for PS at h=9)
b) Up to 5 batches of 48 bunches each transferred to the SPS (240 bunches) Transverse emittance produced in the PSB, longitudinal in the PS
- Multiturn proton injection in PSB with shaving
RF gymnastics in PS@2.5 GeV/c:
  Batch compression
  Bunch merging
  Triple splitting
Acceleration
2 x Double splittings
  (1 Double splitting for 50 ns)
Bunch rotation
BCMS “Batch Compression, Merging and Splitting in PS”

## Slide 38: LHC 25ns alternative scheme in PS: BCS
h = 9
h = 21
h = 9 10  1112  13  14  7  21
h = 21  42  84
+4 bunches
4 bunches
Production scheme: a) Double batch injection from PSB (4 + 4 bunches, 8 bunches for PS at h=9)
b) Up to 5 batches of 32 bunches each transferred to the SPS (240 bunches) Transverse emittance produced in the PSB, longitudinal in the PS
- Multiturn proton injection in PSB with shaving
RF gymnastics in PS@2.5 GeV/c:
  Pure Batch compression
Acceleration
2 x Double splittings
  (1 Double splitting for 50 ns)
Bunch rotation
BCS “Batch Compression and Splitting in PS”
h = 9 → … → 21

## Slide 39: A simple overview of the main limitation for ε preservation: Evolution of space charge DQy across the injector chain
10.8 sec long flat bottom (FB) to allow for 4 injections
Limit set to 0.21
1.2 sec long flat bottom (FB) to allow for double batch injection
Limit set to 0.31
Large tune spreads
Determine brightness
Handled thanks to efficient resonance compensation, dynamic working point and rapid cycling
PSB cycle
(0.5 s)
PS cycle
(3.6 s)
PS FB
(1.2 s)
SPS FB
(10.8 s)

## Slide 40: Comparison of LIU and HL-LHC parameters

## Slide 41: Post-LS1 scenarios: summary

## Slide 42: e-cloud instabilities: simulations and T-damper
Damper/TFB tests proved that instability can be efficiently delayed
10 ms
-- Wall current monitor -- Sum -- Horizontal -- Vertical
Pycloud simulations for combined function magnets established to predict future operation
e-cloud observed for 25 ns beam production but no influence on beam quality
Transverse instability observed together with e-cloud if bunches shorter than nominal or kept in the machine for time longer than needed.
Shorter batches a la BCMS suffering less

## Slide 43: Issued analysed to preserve beam quality for HL-LHC
Possible production schemes
  3-splitting
  BCMS
Issues common for the two schemes:
  PSB
    Space charge → L4 connection
  PS
    Space charge → PSB@2 GeV
    Headtail instabilities → Transverse damper
    Transition crossing
    Longitudinal instabilities → Finemet cavity
    Electron cloud → Transverse damper
  SPS
    Space Charge → well matched to PS space charge
    Maximum available RF power → 200 MHz LL and HL upgrade
    Electron cloud → Wide-band damper – aC coating
L4 160 MeV (relaxed space charge)
H- injection

## Slide 44: Larger bunch intensity from SPS?
Baseline upgrade: shorter cavities and 21.6 MW RF power
Nb ≈ 2 · 1011 ppb without degradation, 2.5 · 1011 ppb for 10% longer bunches
RF voltage at transfer to LHC
To keep longitudinal stability (Landau damping + potential well dist.)
  Longitudinal emittance increases with intensity: 
  RF voltage requirement proportional to IRF
+0.51 · 1011
+0.29 · 1011
+0.18 · 1011
t = const, LD+PWD
24+25
43+24
43+42
102
LD: Loss of Landau damp.
PWD: Potential well dist.
Z/n today
Pold = 1.05 MW
Pnew = 1.6 MW
RF voltage at transfer to LHC
Q20 optics