## Slide 1: Pushing Luminosity of e+e- Colliders: the SuperKEKB project
Y. Funakoshi
KEK
Oct. 17 2013 6th TLEP workshop@CERN

## Slide 2: Concept of SuperKEKB

## Slide 3: KEKB B-Factory
Superconducting cavities (HER)
e-
e+
ARES copper cavities (LER)
8 GeV e- 3.5 GeV e+ Linac
e+ target
ARES copper cavities (HER)
Belle detector
KEKB B-Factory
TRISTAN tunnel
♦World-highest Peak Luminosity
    2.11 x 1034cm-2s-1
    Twice as high as design value
♦World-highest Integrated Luminosity
  Total: 1041fb-1 as of June 30th 2010
Crab cavities
1 for each ring
♦Crab crossing (f = 11 mrad)
♦Skew-sextupole magnets
The KEKB operation was terminated at the end of June 2010 for the upgrade toward SuperKEKB. Operation of SuperKEKB will start in Jan. 2015.

## Slide 4: SuperKEKB Luminosity Target
SuperKEKB
8x1035 cm-2s-1
2x1034 cm-2s-1
x40 !!
Notes: As you can see in this trend plot, the target luminosity of SuperKEKB is about 2 order higher than the current B factories.
But how can it be achieved?

## Slide 5: Luminosity of KEKB and SuperKEKB
 | KEKB Acieved |  | SuperKEKB Nano-Beam | 
 | LER | HER | LER | HER
Ibeam [A] | 1.6 | 1.2 | 3.6 | 2.6
βy* [mm] | 5.9 | 5.9 | 0.27 | 0.30
ξy | 0.09 | 0.12 | 0.088 | 0.081
Luminosity [cm-2 s-1] | 2.1 x 1034 |  | 8.0 x 1035 | 
Factor 2
Factor 20
Almost same
40 times higher

## Slide 6: Collision Scheme
d
Nano-Beam Scheme SuperKEKB
Half crossing angle: f
2 f = 83mrad
overlap region << bunch length
overlap region = bunch length
~ 6 mm
~ 300 μm
5-6 mm
10-12 mm
100-150 mm
6-7 mm
Hourglass requirement
Vertical beta function at IP can be squeezed to ~300μm.
Need small horizontal beam size at IP.
→ low emittance, small horizontal beta function at IP.
KEKB head-on (crab crossing)
No crab waist scheme has been assumed at SuperKEKB
P. Raimondi

## Slide 7: Machine Design Parameters
parameters |  | KEKB |  | SuperKEKB |  | units
 |  | LER | HER | LER | HER | 
Beam energy | Eb | 3.5 | 8 | 4 | 7.007 | GeV
Half crossing angle | φ | 11 |  | 41.5 |  | mrad
# of Bunches | N | 1584 |  | 2500 |  | 
Horizontal emittance | εx | 18 | 24 | 3.2 | 4.6 | nm
Emittance ratio | κ | 0.88 | 0.66 | 0.27 | 0.28 | %
Beta functions at IP | βx*/βy* | 1200/5.9 |  | 32/0.27 | 25/0.30 | mm
Beam currents | Ib | 1.64 | 1.19 | 3.6 | 2.6 | A
beam-beam param. | ξy | 0.129 | 0.090 | 0.088 | 0.081 | 
Bunch Length | sz | 6.0 | 6.0 | 6.0 | 5.0 | mm
Horizontal Beam Size | sx* | 150 | 150 | 10 | 11 | um
Vertical Beam Size | sy* | 0.94 |  | 0.048 | 0.062 | um
Luminosity | L | 2.1 x 1034 |  | 8 x 1035 |  | cm-2s-1

## Slide 8: What’s new at SuperKEKB
e- 7GeV 2.6 A
e+ 4GeV 3.6 A
Target: L = 8x1035/cm2/s
SuperKEKB
Colliding bunches
Damping ring
Low emittance gun
Positron source
New beam pipe
& bellows
Belle II
New IR
TiN-coated beam pipe with antechambers
Redesign the lattices of LER to squeeze the emittance
Add / modify RF systems for higher beam current
New positron target / capture section
New superconducting final focusing quads near the IP
Low emittance electrons to inject
Low emittance positrons to inject
Replace short dipoles with longer ones (LER)

## Slide 9: The construction works are in full swing at SuperKEKB. However, in this talk, instead of describing the construction status, I will focus on issues for SuperKEKB.

## Slide 10: Issues
IR design and dynamic aperture
Low emittance tuning
Magnet alignment strategy
Beam-beam related issues
IP orbit control
Beam loss and beam injection
Electron clouds
Detector beam background

## Slide 11: IR design and dynamic aperture
This is one of the key issues at SuperKEKB
  Success of SuperKEKB largely depends on how low values of IP beta-functions will be achieved with enough dynamic aperture.

## Slide 12
Y. Ohnishi

## Slide 13
Y. Ohnishi

## Slide 14
Y. Ohnishi

## Slide 15: Corrector coils
Dipole and skew dipole coils make a beam-line geometry and correct dispersions.
Skew quadrupole coils correct x-y couplings.
Sextupole and skew sextuple coils correct error field due to a misalignment of quadrupole coils. This error field affects the dynamic aperture significantly.
Octupole coils at QC1 and QC2 enlarge a transverse aperture.
HER cancel coils correct sextupole, octupole, decapole and dodecapole leakage field from QC1P in LER.

## Slide 16: Touschek Lifetime
Touschek lifetime depends on dynamic aperture.
Efforts to widen dynamic aperture
  Careful design of QCS magnets to minimize higher multipoles etc.
  Careful IR design: LCC, x-y coupling correction etc.
  Optimization of octupoles, ARC sextupoles, skew-sextupoles
w/o machine errors
Y. Ohnishi

## Slide 17: Low emittance tuning
The design vertical emittance of SuperKEKB is very small compared to those of existing colliders.
The low vertical emittances have been achieved in SR machines. However, low emittance tuning in colliders is much more difficult.
One of the key tuning issues at SuperKEKB will be low emittance tuning.

## Slide 18: Comparison of emittances of colliders
Existing colliders
Future colliders
From Beam Dynamics Newsletter No. 31
Courtesy of F. Zimmermann, H. Burkhardt and Q. Qin
LEP3
TLEP-H

## Slide 19
KEKB method of optics correction
SVD solver

## Slide 20
At SuperKEKB we will use skew-quad winding at sextuples instead of bumps.

## Slide 21
At SuperKEKB we will use skew-quad winding at sextuples instead of bumps.

## Slide 23: Simulation for SuperKEKB with machine errors
Simulation was done by H. Sugimoto in case of HER.
Assumed machine errors
Corrections
  Closed orbit, x-y coupling, beta-beat, dispersions (KEKB methods)
    SVD threshold = 10-2
 | sx = sy [mm] | sq [mrad] | DK/K
Normal Quad | 100 | 100 | 2.5 x 10-4
Sextu. | 100 | 100 | 2.5 x 10-4
Bend. | 0 | 100 | 0
QC1, QC2 | 100 | 0 | 0
BPM | 0 | 10 x 103 | 2mm (resolution)
Machine errors are created randomly with gaussian distributions.

## Slide 24: Results of simulation
Dynamic aperture after LET.
Vertical emittance distribution after LET
100 samples
No errors
H. Sugimoto

## Slide 25: Dynamic aperture with different types of errors
No errors
Rotation errors of quadruples seems most dangerous.
Each sextuple has a skew quadrupole corrector coil.
We may have to rethink tolerance of rotation errors of normal quadrupoles.
H. Sugimoto

## Slide 26: Magnet alignment strategy at SuperKEKB
The target positions of the initial alignment of SuperKEKB is a smoothed curve made from present (2013 )magnet positions (not on a plane).
The tolerance of magnets alignment around the target curve is the same as KEKB.
  Position error: 100 mm (1 s)
  Rotational error: 100 mrad (1 s)
    We have to rethink about this?
We will need special care for the alignment of the magnets around the local chromaticity correction.

## Slide 27: Effects of Tunnel deformation at SuperKEKB HER
Tunnel deformation observed at KEKB
- A large subsidence has been observed:
~ 2mm/year and still in progress.
- In the construction period of KEKB (1998), all magnets were aligned on the same plane.
Target (7.8pm)
Vertical emittance
-If the alignment error around the V-LCC (vertical local chromaticity correction) area is excluded, the vertical emittance can be preserved well below the target value with optics corrections.
- As for the alignment error of V-LCC, we will need a special care. This is a remaining problem.
A. Morita

## Slide 28: Beam-beam related issues
Beam lifetime shortening with beam-beam
Luminosity degradation
  The design luminosity was determined based on the strong-strong beam-beam simulation.
  Beam-beam + lattice nonlinearity and space charge effect

## Slide 29: LER Dynamic Aperture
beam-beam
aperture
lost
Y. Ohnishi

## Slide 30: HER Dynamic Aperture
beam-beam
aperture
lost
Y. Ohnishi

## Slide 31: Tune survey (LER)
H. Sugimoto

## Slide 32: LER Dynamic Aperture
crab waist (simple map at IP)
full
half
beam-beam
Y. Ohnishi
On-momentum
White > 1000turns
Black < 1 turn
w/ damping
w/o rad. Excitation w/ synchrotron motion

## Slide 33: Preliminary results on dynamic aperture study with sextupoles for crab waist
We have considered that the crab waist scheme can not be used at SuperKEKB due to the degradation of dynamic aperture. Now, we have started to study this scheme more seriously.
0%
50%
100%
50%
100%
before optimization
before optimization
with optimization
with optimization
H. Koiso
We are collaborating with people in BINP.

## Slide 34: SuperKEKB beam-beam simulation
K. Ohmi
Smaller (single beam ) vertical emittance gives higher luminosity.
Much lower vertical emittance than the design (about half) will be needed to achieve the design luminosity.
Strong-strong method (PIC)
For the long-rage force, the gaussian distribution was assumed.
 | LER | HER
ex [nm] | 3.2 | 4.6
ey [pm] | 8.64 | 11.5
k [%] | 0.27 | 0.25
SuperKEKB design
SuperKEKB design luminosity

## Slide 35: Strong-weak simulation (tune survey)
D. Zhou

## Slide 37
Crab waist seems to be effective to recover also the luminosity.
D. Zhou

## Slide 38: IP orbit control
The IP orbit control to maintain an optimum beam collision is more difficult than the KEKB case.
IP orbit is very sensitive to the vibration of QCS (QC1, QC2) magnets.
 | KEKB | SuperKEKB
ey | 150pm | ~8.6pm (LER)
by* | 5.9mm | 0.27mm(LER)
sy* | 940nm | 45nm

## Slide 39: QCSL vertical position oscillation (measurement) and orbit change (tracking) : SuperKEKB HER
Vertical orbit at IP
(simulation)
QCSL vertical position
(measurement)
-> QC1L (HER)
200nm -> ~4sy*
If the QC1L magnets of SuperKEKB vibrates with the same amplitude of the QCSL of the KEKB, the orbit change at IP amounts to 4sy*.

## Slide 40: Countermeasures
Reinforcement of supports for QCS magnets
Rely on the coherency of the oscillation of QC1P and QC1E (QC2P and QC1E).
Fast orbit feedback

## Slide 41: Orbit change at IP with 1mm offset of QCS magnets
 |  | K1 (/m) | Distancefrom IP [m] | bQ [m] | bIP[mm] | Dyy/2p | COD@IPfor 1mm Q-offset [mm] (New optics)
QC1L | LER | -1.717 | 0.912 | 2504.3 | 0.27 | 0.24995 | -0.706 (-0.7339)
 | HER | -1.142 | 1.390 | 5462.4 | 0.3 | 0.24997 | -0.731 (-0.7684)
QC1R | LER | -1.712 | 0.912 | 2567.7 | 0.27 | 0.24996 | -0.713 (-0.7362)
 | HER | -1.070 | 1.430 | 5592.6 | 0.3 | 0.24997 | -0.693 (-0.7299)
QC2L | LER | 0.84161 | 1.9099 | 962.2 | 0.27 | 0.25004 | 0.2145
 | HER | 0.65023 | 2.6799 | 1923.3 | 0.3 | 0.25030 | 0.2470
QC2R | LER | 0.83924 | 1.9760 | 924.6 | 0.27 | 0.25005 | 0.2097
 | HER | 0.55577 | 2.9449 | 1806.9 | 0.3 | 0.25004 | 0.2046
COD
If QCS magnets for both rings move coherently, orbit difference of the two beam becomes much smaller (1/10 ~ 1/20) than non-coherent case.
>
>
>
>
Old optics

## Slide 44: Orbit feedback at IP :Algorism
Beam-beam deflection (SLC, KEKB vertical)
Luminosity feedback (dithering)(PEP-II)
Beam size feedback (KEKB horizontal)
Dy at IP=
~5nm ~1/10sy*
BPM
IP
BPM
Dy at BPM= ~1.3mm
SupeKEKB case
y
Luminosity
When we shake the beam at around the peak of the luminosity, there appears twice of the frequency of the dithering frequency.
x
Beam size
sy (LER)
Luminosity
At KEKB before installation of crab cavities, the vertical beam of LER was used for the horizontal orbit feedback at IP.

## Slide 45: Rejection gain by fast orbit feedback
-17.8dB@30Hz
dB
Hz
H. Fukuma
~10dB@70Hz

## Slide 46: Electron cloud issues
The single bunch instability is main concern.
  Leads to increase in emittance
  Coupled bunch instabilities will be cured by feedback system.
Simulation and calculation by Ohmi, et al.
E [GeV] | = 4.0 |  |  |  | 
g | = 7828 | Nb | = 6.25E+10 |  | 
ns | = 0.026 | Qb[C] | = 1.4E-08 | (1.4 mA/bunch) | 
 |  | Sb [m] | = 1.2 | (4ns) | 
sz [m] | = 6.E-03 | l [C/m] | = 5.2E+12 | (Qb/2/sz) | 
c [m/s] | = 3.E+08 | s y [m] | = 2.E-05 |  | 
K | = 11 | s x [m] | = 2.E-04 |  | 
Q | = 7 |  |  |  | 
re [m] | = 2.80E-15 | we | = 5.46E+11 | K = we sz/c | 
b y [m] | = 25 | we sz/c | = 10.9 | Q = Min(Qnl, we sz/c) | 
L [m] | = 3016 |  |  | Qnl ~7 | 
K. Ohmi , KEK Preprint 2005-100 (2006)
  Here,
Target: 1E11
ρth [e-/m3] =1.59E11
Threshold of density
Y. Suetsugu

## Slide 47: Latest simulation result on the threshold value of instability
Simulation with PEHTS2 by D. Zhou and K. Ohmi
  With uniform beta functions and uniform electron cloud density along the ring, the threshold for electron cloud density is about 5.E11 m-3.
  With realistic beta functions and uniform electron cloud density along the ring, the threshold reduces to about 1.6E11 m-3.
  With realistic beta functions and estimated s-dependent electron cloud density along the ring, the threshold is about 5.E11 m-3.

## Slide 48: Countermeasures
For the upgrade of the vacuum system for SuperKEKB, the electron cloud is a key issue.
Drift section | Antechamber +Solenoid +TiN Coating
Q and Sx mag. | Antechamber +Solenoid +TiN Coating
Bend section | Antechamber +Groove+ TiN Coating
Wiggler section | Antechamber +Electrode (Cu)
Countermeasures are carefully chosen based on the various studies.
Y. Suetsugu

## Slide 49: Countermeasures for electron clouds
Drift section: Antechamber + TiN coating
Groove
Inside view
Electrode
Wiggler section:
Antechamber + Clearing electrode
Y. Suetsugu

## Slide 50: Expected electron density
ne after applying countermeasures: estimated from experiments (Red)
Compared with results of CLOUDLAND (Blue)
  dmax=1.2, Solenoid field=50G (ne=0), Antechamber; photoelectron yield =0.01 (1/10)
ne of approx. 1/5 of the target value is expected.
Target value for ne: ~1x1011
Condition | ne [m-3]
Circular Cu chamber [KEKB beam pipe] | 5.2E12
+Solenoid at Drift (1/50) | 4.7E11
+Antechamber (1/5)+TiN (3/5) | 5.7e10
+Electrode in Wiggler (1/100) | 3.5e10
+Groove in Bend (1/4) | 2.0E10
KEKB~3x1011
If the latest simulation result on the threshold is true, there is a margin of a factor 25!
Y. Suetsugu

## Slide 51: Beam lifetime
 | KEKB (design) |  | KEKB (operation) |  | SuperKEKB | 
 | LER | HER | LER | HER | LER | HER
Radiative Bhabha | 21.3h | 9.0h | 6.6h | 4.5h | 28min. | 20min.
Beam-gas | 45ha) | 45ha) |  |  | 24.5min.b) | 46min. b)
Touschek | 10h | - |  |  | 10min. | 10min.
Total | 5.9h | 7.4h | ~133min. | ~200min. | 6min. | 6min.
Beam current | 2.6A | 1.1A | 1.6A | 1.1A | 3.6A | 2.6A
Loss Rate | 0.12mA/s | 0.04mA/s | 0.23mA/s | 0.11mA/s | 10mA/s | 7.2mA/s
a) Bremsstrahlung
b) Coulomb scattering, sensitive to collimator setting
As for loss rate, beam loss accompanied with the beam injection should be added.

## Slide 53: Continuous injection
At SuperKEKB, the continuous injection (top-up injection) is indispensable, since the beam lifetime is very short.
  Max. 50 Hz (e- + e+)
  Azimuthal VETO (at KEKB not azimuthal 3.5msec after injection)
Before continuous injection
After continuous injection
Gain in integrated luminosity at KEKB: ~30%
8 hours
8 hours

## Slide 54: Beam background
At SuperKEKB with x40 larger Luminosity, beam background will also increase drastically.
  Touschek scattering
  Beam-gas scattering
  Synchrotron radiation
  Radiative Bhabha event: emitted g
  Radiative Bhabha event: spent e+/e-
  2-photon process event: e+e-e+e-e+e-
  etc…
e-
e+
e-
Beam-origin
Luminosity dependent
Notes: In this slide, I have listed up variety of possible beam background sources at SuperKEKB.
Among these background sources, so-called “Touschek scattering” will be the most difficult one to cope with, which I will explain in more detail in the following slides.

## Slide 55: Collimators
Horizontal collimators are effective to reduce Touschek BG in IR area
To reduce IR loss of beam-gas Coulomb BG, very narrow (~2mm half width) vertical collimator is required
TMC instability is an issue, low-impedance design of collimator head is important
Should withstand ~100GHz loss (tungsten)
Precise control of collimator width is important (otherwise IR loss rapidly increase)
Life time | Touschek | Beam-gas Coulomb | Rad. Bhabha
LER | 10 min. | 25 min | 28 min.
HER | 10 min. | 46 min. | 20 min.
IR loss ¦s¦<4m | Touschek | Beam-gas Coulomb | Rad. Bhabha
LER | 250 MHz | 90 MHz | 0.6GHz*
HER | 30 MHz | <10 MHz | 0.5GHz*
*Effective rate
Vertical collimator

## Slide 56: Tungsten shield inside QCS cryostat
QC2RP
QC2RE
QC1RP
QC1RE
Put as much tungsten as possible around the beam pipe
to stop showers generated by beam loss

## Slide 57: Impact on detector
Assuming design luminosity, BG impact on detector performance(occupancy, tracking/PID performance etc..) is tolerable.
Assuming 10 years operation at design luminosity, most of our detector components are safe for radiation damage/neutron flux.
  except for TOP PMT photocathode lifetime, which needs further x2 reduction.
Gammas in BGshower reach TOP quartz bar and generate electrons by Compton scattering and etc.. Those electrons emit Cerenkov photons and those photons reach PMT photocathode.
TOP: Time-of-Propagation counter, detect ring image Cerenkov radiation for particle ID

## Slide 58: Schedule

## Slide 59
Notes: The construction works for SuperKEKB is in full swing.

## Slide 60: SuperKEKB luminosity projection
Goal of Belle II/SuperKEKB
9 months/year
20 days/month
Commissioning starts
in early 2015.
Shutdown
for upgrade
Integrated luminosity
(ab-1)
Peak luminosity
(cm-2s-1)
Calendar Year

## Slide 61: Backup slides

## Slide 63
Skew-sextupoles

## Slide 79: RF Gun Development
Photo cathode : stability, longer life, efficiency
  At first LaB6, then Ir5Ce  5nC / bunch
Laser : higher power, pulse width control
  Nd:YAG medium, LD excitation  ~1.5mJ / 30ps / pulse at 266nm
  Polarization control for slant irradiation
  In parallel, fiber laser is under development
Cavity : better focusing field, higher gradient
  DAW (Disk and washer) type cavity
  Development of quasi-travelling-wave side-coupled cavity as well
Test stands
  RFgun at A-1 will be constructed this autumn for SuperKEKB
  RFgun at 3-2 was used to inject into PF with proper synchronization
  Long-period demonstration will be carried during this autumn
Ir5Ce
DAW
RF Gun for Low-emittance Electron Beam

## Slide 80: Comparison of emittances of colliders [cont’d]
Existing colliders
Future colliders
LEP3
TLEP-H

## Slide 81
R. Bartolini

## Slide 82: Difference between SR rings and colliders
IR
  Detector solenoid and its compensation
  Low beta insertion
  Local chromaticity correction
Size of rings
  In larger rings, orbit drift tends to be large.
    Accuracy of optics measurement with orbit drifts
Beam-beam interaction
  Beam-beam blowup
  Restriction on choice of working point

## Slide 83: Belle II Detector
electron (7GeV)
positron (4GeV)
KL and muon detector:
Resistive Plate Counter (barrel)
Scintillator + WLSF + MPPC (end-caps)
Particle Identification
Time-of-Propagation counter (barrel)
Prox. focusing Aerogel RICH (fwd)
Central Drift Chamber
He(50%):C2H6(50%), Small cells, long lever arm, fast electronics
EM Calorimeter:
CsI(Tl), waveform sampling (barrel)
Pure CsI + waveform sampling (end-caps)
Vertex Detector
2 layers DEPFET + 4 layers DSSD
Beryllium beam pipe
2cm diameter

## Slide 84
Model-A
R側
L側
25nm@20Hz
14nm@50Hz
Oscillation phases of QC1RP and QC1RE.

## Slide 85: f =24.75Hz (Model F)

## Slide 86: 24.75Hz (Model A)
The average luminosity is about 95.4% of the case w/o QCS vibration.

## Slide 87: IP machine parameters
 | KEKB |  | SuperKEKB | 
 | LER | HER | LER | HER
ex | 18nm | 24nm | 3.2 | 5.0
ey | 0.15nm | 0.15nm | 8.6pm | 13.5pm
k | 0.83 % | 0.62% | 0.27% | 0.25%
bx* | 120cm | 120cm | 32mm | 25mm
by* | 5.9mm | 5.9mm | 0.27mm | 0.31mm
sx* | 150mm | 150mm | 10mm | 11mm
sx’* | 120mrad | 120mrad | 450mrad | 320mrad
sy* | 0.94 mm | 0.94mm | 48nm | 56nm
sy’* | 0.16mrad | 0.16mrad | 0.18mrad | 0.22mrad
iBump horizontal offset |  | +/- 500mm |  | +/- 30mm?
iBump vertical offset |  | +/- 150mm |  | +/- 7.5mm?
iBump vertical angle |  | +/- 0.4mrad |  | +/- 0.4mrad?
~1/20
~1/4.5
~1/4

## Slide 88: Facilities
Storage and staging areas needed for magnet and vacuum components.
Need increased cooling water for klystrons and magnets:
  24 klystrons for ARES cavities, 8 klystrons for SCC
  Magnet cooling water needs double (4 plants -> 8)
Electricity:
88
KEKB/KEK total
Electricity Consumption: June-09
(Design option) | KEKB:MW | ΔMW | KEK:MW | ΔMW
Present(Average) | 45 |  | 64 | 
Nano Beam: June-09 | 70.7 | 24.3 | 96 | 32
Upgrade: Feb.-09 | 94.8 | 49.8 | 120 | 56
Super: ‘07-July | 102.6 | 57.6 | 128 | 64
Recent Design(Feb.-10): Add 2 ARES units--> +(3~4)MW
M. Ono

## Slide 89: Overall budget (original)
JFY2010 | JFY2011 | JFY2012 | JFY2013 | JFY2014 | Total
75.0 | 10.5 | 14.5 | 0 | 0 | 100.0
0 | 41.6 | 40.2 | 61.6 | 46.7 | 190.0
0 | 4.5 | 12.4 | 7.2 | 0 | 24.1
75.0 | 56.6 | 67.1 | 68.8 | 46.7 | 314.1
Supplied | Supplied | Supplied |  |  | 
JFY2010
JFY2011
JFY2012
JFY2013
JFY2014
JFY2015
JFY2016
Very Advanced Research SP (100 Oku-Yen)
Other budgets for construction (214 Oku-Yen)
Operation budget (continues - - - )
SuperKEKB commissioning
We are here
Budget
  Total construction budget is 314 Oku-Yen for Rings, Injector, and Belle-II.
  Most of the budget comes year-by-year based.
  Operation budget is expected in FY2014 and later.
VARSP
Others
Buildings
Total
Status
Unit: Oku-Yen (~1.1M$)

## Slide 90: Effect of mis-alignment of SX and Q
HER(Quad rotation)
  Coupling term: .0010816287630558967
  Dispersion term: 3.748599954860665e-05
HER(Sextu vertical misalignment)
  Coupling term: .044995709319378976
  Dispersion term: .0045765442050508375
Notes: （３）南アークはPSの建物の下を通っている。他は開削して埋め戻しているがここは添付資料にあるようについたてをつくって埋め戻している（添付資料の１頁目：IWAA2012山岡さんの発表より）。
トンネルの下にちゃんと埋め戻し土が入って行かなかったのではないか。