## Slide 1: CEPC Machine Optimization and Final Focus Design
Dou Wang, Jie Gao, Ming Xiao,
Sha Bai, Yiwei Wang, Feng Su
(IHEP)
16-18 October 2013, CERN. Geneva, Switzerland.
6th TLEP Workshop

## Slide 2: Outline
50 km CEPC optimized design
70 km CEPC optimized design
Primary results of final focus design

## Slide 3: 50 km Circular electron-positron Collider (CEPC) design

## Slide 4: Constraints from IP
Beam-beam parameter limit coming from beam emittance blow-up
Beam lifetime limit due to beamstrahlung
Extra energy spread due to beamstrahlung
Gao’s theory:
Valery Telnov’ theory

## Slide 5: luminosity of circular collider
Number of IPs
SR power

## Slide 6: Beam parameters calculation
Energy E0 | Circumference C0 | Goal luminosity L0 | IP number NIP | SR power /beam P0 | Bending radius  | aspect ratio r | Coupling  | Energy acceptance 
120GeV | 50 km | 161034 cm-2s-1 | 12 | 50 MW | 56.2 km | 200 | 0.005 | 5%12%
Input parameters

## Slide 7: Beam parameter scan-1

## Slide 8: Beam parameter scan-2

## Slide 9: Machine parameter choice
Less IP give higher luminosity
choose NIP=1
Larger bending radius give higher luminosity
choose =6.2 m （80% filling factor for bending dipoles）
Higher momentum acceptance give higher luminosity
How to choose ?
decided by RF parameters

## Slide 10: Constraints from RF system
Synchrotron radiation loss per turn
Synchrotron phase
Nature bunch length
Momentum acceptance
=6.2 m
=6.2 m

## Slide 11: Choice for RF technology
the maximum luminosity which we can obtain is decided by the RF technology (frequency). Higher RF frequency will give larger luminosity.
From the beam dynamics point of view, lower RF frequency is a better choice because the cavities with lower frequency have larger aperture and hence lower impendence which is a favor for the collective instabilities.
there are still technical difficulties to directly use ILC 1.3 GHz SC technology on storage rings, it’s better to choose the frequency lower than 1GHz. 700 MHz is a good candidate with better gradient and lower impedance.
the requirement of enlarging energy acceptance is translated to design a low momentum compaction lattice and also larger RF voltage will relax this tolerance and lose the difficulties of lattice design. So we need to make a reasonable choice for the total RF voltage while balancing the constraints from the RF frequency and momentum compaction.

## Slide 12: Optimization Parameter Design of CEPC
 | 350 MHz (LEP2-like) technology | 700 MHz technology |  | 1.3 GHz (LEP3-like) technology
Number of IPs | 1 | 1 | 2 | 1
Energy (GeV) | 120 | 120 | 120 | 120
Circumference (km) | 50 | 50 | 50 | 50
SR loss/turn (GeV) | 2.96 | 2.96 | 2.96 | 2.96
Ne/bunch (1012) | 1.61 | 0.79 | 1.12 | 0.33
Bunch number | 11 | 22 | 16 | 53
Beam current (mA) | 16.9 | 16.9 | 16.9 | 16.9
SR power /beam (MW) | 50 | 50 | 50 | 50
B0 (T) | 0.065 | 0.065 | 0.065 | 0.065
Bending radius (km) | 6.2 | 6.2 | 6.2 | 6.2
Momentum compaction (10-4) | 0.43 | 0.38 | 0.38 | 0.21
IP x/y (m) | 0.2/0.001 | 0.2/0.001 | 0.2/0.001 | 0.2/0.001
Emittance x/y (nm) | 29.7/0.15 | 14.6/0.073 | 29.1/0.15 | 6.1/0.03
Transverse IP (um) | 77/0.38 | 54/0.27 | 76/0.38 | 35/0.17
x/IP | 0.103 | 0.103 | 0.073 | 0.103
y/IP | 0.103 | 0.103 | 0.073 | 0.103
VRF (GV) | 4.1 | 6 | 6 | 9.3
f RF (MHz) | 350 | 704 | 704 | 1304
z (mm) | 4.6 | 2.2 | 2.2 | 0.95
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.13
Energy acceptance (%) | 3.5 | 5 | 5 | 7.7
BS (10-4) | 9.7 | 13.8 | 13.8 | 21.3
n | 0.86 | 0.6 | 0.6 | 0.39
BS (10-4) | 4.3 | 4.3 | 4.3 | 4.3
Life time due to beamstrahlung (minute) | 30 | 30 | 30 | 30
F (hour glass) | 0.49 | 0.68 | 0.68 | 0.87
Lmax/IP (1034cm-2s-1) | 2.2 | 3.1 | 2.2 | 4.0

## Slide 13: Linear lattice design
60 FODO cells in arc
16-fold symmetry
SC cavities and other cryogenic system are inserted in 14 linear sections.
Dispersion suppressor

## Slide 14: Lower power design of CEPC
 | Baseline | Low power design |  | 
Number of IPs | 1 | 1 | 1 | 1
Energy (GeV) | 120 | 120 | 120 | 120
Circumference (km) | 50 | 50 | 50 | 50
SR loss/turn (GeV) | 2.96 | 2.96 | 2.96 | 2.96
Ne/bunch (1012) | 0.79 | 0.38 | 0.33 | 0.28
Bunch number | 22 | 23 | 21 | 19
Beam current (mA) | 16.9 | 8.45 | 6.76 | 5.07
SR power /beam (MW) | 50 | 25 | 20 | 15
B0 (T) | 0.065 | 0.065 | 0.065 | 0.065
Bending radius (km) | 6.2 | 6.2 | 6.2 | 6.2
Momentum compaction (10-4) | 0.38 | 0.38 | 0.38 | 0.38
IP x/y (m) | 0.2/0.001 | 0.071/0.00048 | 0.056/0.00042 | 0.041/0.00035
Emittance x/y (nm) | 14.6/0.073 | 9.5/0.035 | 9.1/0.031 | 8.9/0.026
Transverse IP (um) | 54/0.27 | 25.9/0.13 | 22.7/0.11 | 19.2/0.096
x/IP | 0.103 | 0.076 | 0.069 | 0.06
y/IP | 0.103 | 0.103 | 0.103 | 0.103
VRF (GV) | 6 | 6 | 6 | 6
f RF (MHz) | 704 | 704 | 704 | 704
z (mm) | 2.2 | 2.2 | 2.2 | 2.2
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.13
Energy acceptance (%) | 5 | 5 | 5 | 5
BS (10-4) | 13.8 | 13.8 | 13.8 | 13.8
n | 0.6 | 0.6 | 0.6 | 0.6
BS (10-4) | 4.3 | 4.3 | 4.3 | 4.3
Life time due to beamstrahlung (minute) | 30 | 30 | 30 | 30
F (hour glass) | 0.68 | 0.48 | 0.45 | 0.41
Lmax/IP (1034cm-2s-1) | 3.1 | 2.31 | 1.97 | 1.58
AC power for RF source/two beam (MW) | 286 | 143 | 114 | 86

## Slide 15: CEPC low power scheme with recovered luminosity
 | Baseline – 50 MW | Low power design – 25 MW |  | 
Aspect ratio (coupling factor) | ~200 | ~200 | ~550 | ~1200
Number of IPs | 1 | 1 | 1 | 1
Energy (GeV) | 120 | 120 | 120 | 120
Circumference (km) | 50 | 50 | 50 | 50
SR loss/turn (GeV) | 2.96 | 2.96 | 2.96 | 2.96
Ne/bunch (1012) | 0.79 | 0.38 | 0.51 | 0.079
Bunch number | 22 | 23 | 17 | 111
Beam current (mA) | 16.9 | 8.45 | 8.45 | 8.45
SR power /beam (MW) | 50 | 25 | 25 | 25
B0 (T) | 0.065 | 0.065 | 0.065 | 0.065
Bending radius (km) | 6.2 | 6.2 | 6.2 | 6.2
Momentum compaction (10-4) | 0.38 | 0.38 | 0.38 | 0.38
IP x/y (m) | 0.2/0.001 | 0.071/0.00048 | 0.13/0.00024 | 0.11/0.0001
Emittance x/y (nm) | 14.6/0.073 | 9.5/0.035 | 9.4/0.017 | 9.4/0.0073
Transverse IP (um) | 54/0.27 | 25.9/0.13 | 34.9/0.063 | 32.4/0.027
x/IP | 0.103 | 0.076 | 0.103 | 0.016
y/IP | 0.103 | 0.103 | 0.103 | 0.103
VRF (GV) | 6 | 6 | 6 | 6
f RF (MHz) | 704 | 704 | 704 | 704
z (mm) | 2.2 | 2.2 | 2.2 | 2.2
Energy spread (%) | 0.13 | 0.13 | 0.13 | 0.13
Energy acceptance (%) | 5 | 5 | 5 | 5
BS (10-4) | 13.8 | 13.8 | 13.8 | 13.8
n | 0.6 | 0.6 | 0.6 | 0.6
BS (10-4) | 4.3 | 4.3 | 4.3 | 4.3
Life time due to beamstrahlung (minute) | 30 | 30 | 30 | 30
F (hour glass) | 0.68 | 0.48 | 0.32 | 0.18
Lmax/IP (1034cm-2s-1) | 3.1 | 2.31 | 3.1 | 4.1
AC power /two beam (MW) * | 286 | 143 | 143 | 143
Technology Maturity |  |  |  | 

## Slide 16: Parameter comparison with exist machine
Parameters | PEP-X | ESRF | SSRF | Swiss Light Source | Diamond | PETRA III Positron Machine | NSLS-II | Spear-III | TLS | TPS | NSRL | CEPC-25MW |  | 
 |  |  |  |  |  |  |  |  |  |  |  | βIP x/y (m) |  | 
 |  |  |  |  |  |  |  |  |  |  |  | 0.071/0.00048 | 0.13/0.00024 | 0.11/0.0001
E(GeV) | 4.5 | 6.03 | 3.5 | 2.4 | 3 | 6.0 | 3 | 3 | 1.5 | 3 | 0.8 | 120 | 120 | 120
Circumference(m) | 2199.32 | 844 | 432 | 288 | 561.6 | 2304 | 620 | 234.126 | 120 | 518.4 |  | 50 | 50 | 50
Emittance(nm-rad) | 0.094 | 4/0.025 | 3.9 | 4.8 | 2.74/0.0274 | 1/0.01 | 1.5/0.008 | 18.6 | 25.5(nature) | 1.7(nature) |  | 9.5/0.035 | 9.4/0.017 | 9.4/0.0073
γ (E/m0c2) | 8806.26 | 11800.39 | 6849.32 | 4696.67 | 5870.84 | 11741.68 | 5870.84 | 5870.84 | 2935.42 | 5870.84 | 1565.56 | 234833.66 | 234833.66 | 234833.66
Normalized Emittance (nm-rad) | 827.79 | 47201.56/295.01 | 26712.348 | 22544.03 | 16086.10/ 160.86 | 11741.68/ 117.42 | 8806.26/ 46.97 | 109197.62 | 74853.21 | 9980.43 |  | 2230919.77/ 8219.18 | 2207436.39/ 3992.17 | 2207436.39/1714.29
κ(Coupling Factor) |  | 160 |  |  | 100 | 100 | 187.5 |  |  |  |  | 271.43 | 552.94 | 1287.67
Momentum compaction factor(E-4) | 0.472 |  |  | 7 | 1.7 | 12 | 3.7 | 11.3 | 67.8 | 2.0 |  | 0.38 | 0.38 | 0.38
Energy loss per turn(keV) | 3270 |  |  | 512 | 1250 | 20.9 | 286.4 | 912 | 128 | 853 |  | 2960000 | 2960000 | 2960000
Energy spead(%) | 0.112 |  |  | 0.09 |  | 0.1 | 0.094 | 0.097 | 0.0756 |  |  | 0.13 | 0.13 | 0.13
Beam current(mA) |  | 200 | 300--500 | 400 | 300(500) |  |  |  |  |  |  | 8.45 | 8.45 | 8.45
Beam life time (h) |  |  | >10 | <10 | >10(20) |  |  |  |  |  |  | 0.5 | 0.5 | 0.5

## Slide 17
70 km Circular electron-positron Collider (CEPC) design

## Slide 18: Beam parameter scan -1
L0
L0
L0
L0

## Slide 19: Beam parameter scan -2
L0
L0
L0

## Slide 20: RF parameter scan for 70km CEPC

## Slide 21: Lattice design for 70km CEPC
60 FODO ARC cell
Dispersion suppressor
Parameters from lattice design:
=8.56 km
x=9.5 nm
p=4.710-5

## Slide 22: Optimized machine parameters for 70km CEPC
 | Baseline design |  | Low power design | 
Number of IPs | 1 | 2 | 1 | 2
Energy (GeV) | 120 | 120 | 120 | 120
Circumference (km) | 70 | 70 | 70 | 70
SR loss/turn (GeV) | 2.14 |  | 2.14 | 
Ne/bunch (1012) | 0.87 | 1.23 | 0.44 | 0.61
Bunch number | 39 | 28 | 39 | 28
Beam current (mA) | 23.3 | 23.3 | 11.7 | 11.7
SR power /beam (MW) | 50 |  | 25 | 
B0 (T) | 0.047 |  | 0.047 | 
Bending radius (km) | 8.56 |  | 8.56 | 
Momentum compaction (10-5) | 4.7 |  | 4.7 | 
IP x/y (m) | 0.4/0.001 | 0.79/0.001 | 0.1/0.0005 | 0.2/0.0005
Emittance x/y (nm) | 9.5/0.094 | 9.5/0.19 | 9.5/0.047 | 9.5/0.094
Transverse IP (um) | 61.6/0.31 | 86.6/0.43 | 30.8/0.15 | 43.3/0.22
x/IP | 0.175 | 0.245 | 0.087 | 0.123
y/IP | 0.088 | 0.062 | 0.088 | 0.062
VRF (GV) | 5.8 |  | 5.8 | 
f RF (MHz) | 709 |  | 709 | 
z (mm) | 2.5 |  | 2.5 | 
Energy spread (%) | 0.11 |  | 0.11 | 
Energy acceptance (%) | 4.4 |  | 4.4 | 
BS (10-4) | 12.2 | 12.2 | 12.2 | 12.2
n | 0.58 | 0.58 | 0.58 | 0.58
BS (10-4) | 3.7 | 3.7 | 3.7 | 3.7
Life time due to beamstrahlung (minute) | 30 | 30 | 30 | 30
F (hour glass) | 0.65 |  | 0.47 | 
Lmax/IP (1034cm-2s-1) | 3.5 | 2.5 | 2.5 | 1.8
AC power for RF source/two beam (MW) | 286 |  | 143 | 

## Slide 23: 3. Primary results of final focus design
Thanks to Sha Bai and Yiwei Wang in our group!

## Slide 24: Local compact FFS design L*=1.5m

## Slide 25: IP parameters (25MW, 1.5m)
IP parameters
  BETX := 0.071;
  ALFX := 0;
  BETY := 0.00048;
  ALFY := 0;
  DX := 0;
  DPX := -0.00795452718;
  BLENG := 2.2E-3; !bunch length (m)
  ESPRD := 1.3E-3; !energy spread (1)
  EMITX := 9.5E-9;
  EMITY := 0.035E-9;
  D0->L = 1.5;
From Sha Bai (baisha@ihep.ac.cn)

## Slide 26: Refit IP to QF1
Fit five variables :
  QD0 length
  QF1 length
  Pole-tip strength of QD0
  Pole-tip strength of QF1
  Distance between QD0&QF1
From Sha Bai (baisha@ihep.ac.cn)

## Slide 27: Linear lattice
fit B1, B2 and B5 to obtain Dx=0 and Dpx=0 at exit of B5
reverse the system, refit QMs to match β and α.
From Sha Bai (baisha@ihep.ac.cn)

## Slide 28: Chromaticity
natural chromaticity decreased (compared with L*=3.5m)
From Sha Bai (baisha@ihep.ac.cn)

## Slide 29: Reduce the length of Bend
We are trying to reduce the length of the bends as the beam energy of CEPC is lower than the 500GeV ILC.
From Sha Bai (baisha@ihep.ac.cn)

## Slide 30: Local non-compact FFS design

## Slide 31: Procedure & Method
The CEPC design parameters :
two cases of βy=1mm and βy=0.35mm.
FFADA program
Matching section, CCS, Final Doublet.
Non-interlaced sextupoles
From Sha Bai (baisha@ihep.ac.cn)

## Slide 32: IP βy=1mm
at IP:
bx=0.2 m
by=1 mm
L*=3.5 m
From Sha Bai (baisha@ihep.ac.cn)

## Slide 33: Beta Function at IP vs momentum
Good region of ±0.4% in Dp/p is necessary for the core in beam distribution.
From Sha Bai (baisha@ihep.ac.cn)

## Slide 34: IP lowβy=0.35mm
at IP:
bx=0.041 m
by=0.35 mm
L*=3.5 m
From Sha Bai (baisha@ihep.ac.cn)

## Slide 35: Beta Function at IP vs momentum
Optical bandwidth needs optimization.
From Sha Bai (baisha@ihep.ac.cn)

## Slide 36: Summary
A general method of how to make an optimized parameter design of a circular e+e- Higgs Factory was given.
Based on beam parameters scan and RF parameters scan, a set of optimized parameter designs for 50 km Circular e-e+ Collider (CEPC) with different RF frequency was proposed.
In order to reduce the total AC power, we decrease the SR power from 50 MW (baseline design) to 25 MW even to 15 MW (low power design) .
Luminosity: 3.12.3 1034 cm-2s-1
Recover the luminosity to the baseline design (3.1 1034 cm-2s-1) by the low power scheme. But we undertake the challenge of technology (ultra-low * and ultra-flat beam).
There are two FFS Design considerations: the local-compact FFS Desgin which we tried to reduce the L* to reduce the chromatic aberrations and local non-compact FFS Desgin which using the non interleaved sextupoles to reduce the third order "kick".
70km CEPC optimized design was done, including normal and low power scheme.

## Slide 37: References
J. Gao, “emittance growth and beam lifetime limitations due to beam-beam effects in e+e- storage rings”, Nucl. Instr. and methods A533（2004）p. 270-274.
V. Telnov, “Restriction on the energy and luminosity of e+e- storage rings due to beamstrahlung”, arXiv:1203.6563v, 29 March 2012.
V. Telnov, “Limitation on the luminosity of e+e- storage rings due to beamstrahlung”, HF2012, November 15, 2012.
Dou Wang, Jie Gao et al., “Optimization parameter design of a circular e+e- Higgs factory”, Chinese Physics C Vol. 37, No. 9 (2013).
Dou Wang, Ming Xiao,Jie Gao, “CEPC low power design”, IHEP-AC-LC-Note2013-015, 7 Aug. 2013.
Dou Wang, Ming Xiao, Jie Gao, “CEPC low power scheme with ultra-low betay”, IHEP-AC-LC-Note2013-020, 9 Sep. 2013.
Dou Wang, Ming Xiao, Jie Gao, “CEPC low power scheme with recovered luminosity”, IHEP-AC-LC-Note2013-022, 16 Sep. 2013.
Dou Wang, Ming Xiao, Jie Gao, “70 km CEPC optimized design”, IHEP-AC-LC-Note2013-018, 23 Aug. 2013.

## Slide 38
Thank you!