## Slide 1: Comments on CLIC Phase Stability
D. Schulte

## Slide 2: CLIC Layout at 3 TeV
Drive Beam Generation Complex
Main Beam Generation Complex
140 ms train length - 24  24 sub-pulses
4.2 A - 2.4 GeV – 60 cm between bunches
240 ns
24 pulses – 101 A – 2.5 cm between bunches
240 ns
5.8 ms
Drive beam time structure - initial
Drive beam time structure - final

## Slide 3: Main Beam to Main Beam Phase Error
Most important jitter source is BC2 RF -> need phase alignment over 50km (<0.6° for 1% luminosity loss, 42μm, 140fs)
Equivalent to 0.4° over 25km (assuming central clock is master)

## Slide 4: Drive Beam Phase Tolerance
Main to drive beam timing error
14μm (0.2°, 50fs) coherent error along the whole main linac
40μm (0.6°, 150fs) if jitter changes from from decelerator sector to decelerator sector

## Slide 5: Drive Beam Requirements
Emittance εx,y ≤ 150μm
Transverse jitter ≤ 0.3σ
Current stability 0.75 10-3
Phase stability 0.2° @ 12GHz
Bunch length stability 1%
RF power stability 0.2%
RF phase stability 0.05°
Phase stability 2.5° @ 12GHz
0.2° @ 1GHz

## Slide 6: Main Beam Phase Reference
Compare and correct drive beam phase with respect to outgoing main beam

## Slide 7: External Phase Reference
Compare a correct drive beam phase with respect to external reference system

## Slide 8: External Phase Reference II
Pulse-to-pulse feedback adjusts the setpoints for the feed forward

## Slide 9: External Reference System
Chain of reference lines
  Random walk error propagation along the line
  Additional local extraction error
  DESY demonstrated 3μm over ~800m (RF to RF)
Require σ≤3μm phase drift per 900m segment
  Main beam to main beam error ~7σ=21μm
  Relevant main to drive beam offset ~3-5σ=9-15μm (larger RF phase at the end of the linac)
  Direct optical-to-optical transition might be better

## Slide 10: Main Hardware Components
RF systems
  Measurements of errors
  Modelling of errors
  Improvements
Feedbacks/feedforwards
  Lattice designs
  Component design (phase monitor, kickers amplifiers)
  Component and beam tests
Timing reference system
  Local system shown in EUROTeV
  Coupled clock system to be developed

## Slide 11: Activities
Past activities
  Development of local phase reference
Ongoing activities
  Beam phase jitter measurements in CTF3
  Klystron phase jitter measurements at different locations
  Modelling of expected modulator jitter
  Feedforward test in CTF3
    Phase monitors
    Fast kickers and amplifiers
    Beam test
  Development of phase stabilisation concept, beam dynamics studies
Foreseen activities
  Distributed phase reference system

## Slide 12: CLIC Test Facility (CTF3)
High current, full
beam-loading operation
Operation of isochronous lines and rings
Bunch phase coding
Beam recombination and current multiplication by RF deflectors
12 GHz power generation by drive beam deceleration
High-gradient two-beam acceleration
4 A, 1.4us
120 MeV
30 A, 140 ns
120 MeV
30 A, 140 ns
60 MeV

## Slide 13: Reserve

## Slide 14: RF Plan
CTC-RF (E. Jensen)
  Task3: DB LLRF design
    Design of LLRF system for DB with optimization for phase and amplitude stability; Designs, measurements at other plants, modelization tools 2011-2016
  Will this be enough to cover other LL RF stability issues?
RF-DESIGN (A.Grudiev, I. Syratchev)
  Task 5: Design of X-band crab cavity RF system
    Design of crab cavity and the corresponding high power RF system 2012-2016
  Does this cover crab cavity low level RF?

## Slide 15: Lattice Design/Beam Physics Plans
CD-DR Damping (Yannis Papaphilippou)
  Task 2: Correction techniques
    Determine dynamic tolerances and requirements for the feedback; report 2011-2016
  Should make sure this contains phase stability
CD-RTML (Andrea Latina)
  Main beam jitter sources
  Bunch compressors (with RF)
  Main beam feedback/feedforward implementation
CD-DRV (Bernard Jeanneret)
  Drive beam jitter sources
  Bunch compressors
  Drive beam feedback/feedforward implementation
CD-BDS (Rogelio Tomas)
  Crab cavity phasing
  Integration with RF studies?

## Slide 16: Timing Reference Plans
CTC-CO (M. Draper)
  Task1: Timing reference, timing distribution and 10 fs synchronization
    Review of specifications, design of fine-timing system, first practical demonstration
    Specifications, Designs, Lab set-up of master-clock and distribution system
    Timing reference for CTF3?
    Provide models for integrated studies 2012-2014
  Are both timing system options covered?

## Slide 17: Test Plan (and Components)
CTF3-002 Drive Beam phase feed-forward and feedbacks (P. Skowronski)
  Task 1: Drive Beam phase monitors
    Understand sources of drive beam phase jitter
    Used in feedbacks and feed-forward test
    Drive Beam phase monitor prototype, phase monitor small series (2-3), electronics and acquisition; Monitor proto 2011 – 4Q, Monitor series: 2013 – 2Q
  Task 2: Feed-forward kickers
    Two strip-line kickers; 2012 – 4Q
  Task 3: Feed-forward pulsers
    Fast amplifiers for the two kickers
    Fast electronics; 2013 – 4Q ?
  Task 4: Infrastructure and operation
    Cabling, infrastructure, controls, operational support; distributed 2012-2016

## Slide 18: Integration Plans
WP: CD-LUMI, Feedback Design (DS)
  Task 1: Determination of feedback layout
    Integrate area feedback systems into one coherent set of feedback systems; Baseline feedback layout 2011-2016
  Task 2: Controller design
    Develop, adjust and optimise controller for performance, cost and risk; 2011-2016
  Task 6: Phase and amplitude stability
    Objective: Develop an integrated concept to mitigate drive and main beam phase and amplitude errors Description: Determine the impact of hardware on beam phase and amplitude stability In collaboration with hardware experts identify critical hardware and required R&D
    Identify and follow relevant beam tests
    Design feedback and feed-forward systems
    Optimise beam line design for stability

## Slide 19: Instrumentation Plans
CTC-BDI: (T. Lefevre)
  Task 3b: Longitudinal Emittance measurements
    Development of 20fs time resolution longitudinal profile monitor using EO techniques. Prototype of each monitor End 2014
    Development and test of cheap high resolution bunch length monitor based on Coherent Diffraction Radiation Prototype of each monitor End 2016
  Only bunch length but not phase covered in BDI
  Energy measurements to be checked

## Slide 20: Main Cause of Beam Phase Jitter
RF errors and bunch compression

## Slide 21: Main Timing Tolerances
Main beam to main beam timing error
  40μm (0.6°, 150fs) [=20μm shift of collision point]
Main to drive beam timing error
  14μm (0.2°, 50fs) coherent error along the whole main linac
  40μm (0.6°, 150fs) if jitter changes from from decelerator sector to decelerator sector
Crab cavity to crab cavity timing error
  0.8μm (0.01°, 3fs)
Each tolerance leads to 1% luminosity
loss, so would like even better values

## Slide 22: Main Beam Tolerances
 | MB ref. | Ext. ref.
Energy jitter from damping ring | 2x10-4 | 4x10-4
Phase jitter from damping ring | 0.2° | 0.35°
Phase error of BC1 RF @4GHz | 0.08° | 0.14°
Gradient error booster linac | 1x10-3 | 1x10-3
Phase error of BC2 RF @ 12GHz | 0.2° | 0.2°
Could gain a factor if main beam is used as a reference if we use a collision waist feedforward