## Slide 1: Construction of and experience with a 2.4 x 1 m² micromegas chambers
Givi Sekhniaidze
On behalf of the Micromegas community

## Slide 2: Outlook
Mechanical issues
Electrical issues
First results
Conclusions and future plans

## Slide 3
Exploded view of the drift/ro panels
FR4 skin
Honeycomb
Al frame
Drift/RO PCB

## Slide 4
Drift panel frame
Mesh frame support
External frame
Gas manifold
Honeycomb
Mesh frame
Gas In/Out

## Slide 5
Drift panel preparation
On the 2.8 x 2.8 m² granite table was placed thin plastic mesh for pressure distribution
Covered with 175 μm thick mylar foil with ø3 mm holes
The FR4 skins were placed on the mylar and sucked

## Slide 6
Drift panel preparation – honeycomb
On the skin surface has been applied expansive glue (PB250/SD5604)
The honeycomb pieces were placed on the skin

## Slide 7
X 12
Vacuum
Clarinet gas
PCB
Vacuum
Expansive glue
Vacuum
Precise shim
Skin
Drift panel preparation – stiff-back

## Slide 8
25x50 mm cross-bars – 1.2 m
50x80 mm long bars – 2.5 m
Glued with Araldite 2011
4-5 sucking heads per bar
Drift panel preparation – stiff-back

## Slide 9
Drift panel preparation – Mesh frame
Mesh
Cyanoacrylate
Araldite 2011
Drift PCB

## Slide 10
4.9 mm thick Aluminum frame mounted on the panel
Mesh stretched and glued on the frame
3 special inserts for drift/read-out panel interconnection
Drift panel preparation – Mesh

## Slide 11
Read-out panel
0.5 mm thick FR4 external skin
10 mm thick Aluminum honeycomb
External Aluminum frames

## Slide 12
Mechanical issues – Read-out panel
Pillars
Shortcuts between
resistive strips

## Slide 13
Chamber assembling
Drift panel
APV25 board
Read-out panel
5 mm spacer

## Slide 14
Chamber assembling

## Slide 15
M3 screw
O-ring
Pillars
Insert
Mesh
Drift panel
Read-out panel
Chamber assembling – interconnection

## Slide 16
Drift panel preparation – Inserts

## Slide 17
Electrical issues
L2/L3 chamber – all read-out parts are working well
L2 chamber – one read-out board had a problem: short between a resistive strip and read out strip below; the read out strip was identified and disconnected from connector, problem disappeared
Initially there was a current on the drift electrode and it was identified as a leak on the O-ring surface – HV connection was insulated with kapton tape and problem disappeared
Typical current between resistive strips and mesh 0 -20 nA
HV up to 580 V the sparks are not observed

## Slide 18
Preliminary results
Summary plot from
Event browser
Single event
Shower event

## Slide 19: TQF1 Resistive Strips Layout
1
2
3
4
Resistive strips aligned with the read out strips
1
2
Resistive strips shifted by a half pitch, w.r.t. the readout strips
3
Resistive strips rotated by -2°, w.r.t. the read out strips , crossing every cm
4
Resistive strips rotated by 1°, w.r.t. the read out strips , crossing every
2cm

## Slide 20
Desy Setup for TQF1 studies
Tmm3
Tmm2
10
2
2
5
5
Tmm3
T3
10
2
2
5
5
T8
200
100
200
0 mm
20
202
301
321
597.5
Tmm2
TQF1
T2
T3
T8
Tmm5
Tmm6
46.0
46.0
222
517.5
Al
Al
Al
Al
Tmm5
10
2
2
5
5
Tmm6
TQF!
10
2
2
5
5
T2
Not acquired
Fully acquired 3X and 3Y APV each
Electron Beam
Notes: Digressione sull’unificazione di elettricita’ e magnetismo nell’elettromagnetismo
Maxwell
Weinberg premio nobel per “unificazione” elettrodebole

## Slide 21: Beam Spot from Tmm2
HV Distribution Side
1
2
3
4

## Slide 22: Resolution
σ = 76.8 µm
Residual from the “Standard” corner
Residual using also TQF1
Residual without TQF1
Standard Corner | Half pitch Shift | 2° rotation | 1° rotation
76.8 µm | 82 µm | 86 µm | 81.2 µm

## Slide 23
Future plans – L2/L3 chambers
L2/L3 chambers – gas leak reparation work in progress, we’re trying to use another type of the O-rings (bigger diameter, rectangular shape, …)
L3 chamber – we have to open chamber to understand the problems with one of the read-out PCB
L3 chamber – more precise scan of the surface to understand the behavior of the interconnection places

## Slide 24
Full-wedge small sector quadruplet
  Eta and stereo doublet
Drift gap spacers: 5 mm
Total thickness: 70–80 mm
Gas distribution
Mesh?
Future plans – Full wedge chambers

## Slide 25
All panels of equal thickness: 11-12 mm
Standard Al profiles of t=10 mm as frames with special angular inserts
  Skins = 0.5 mm (FR4)
  Foam panel of t=10 mm plastic mesh of t=100-200µm glue Araldite AY-103/AH-991
Future plans – Full wedge chambers

## Slide 26
Future plans – Full wedge chambers
We got the space with 4 x 2.5 m² table (153-R-030)
Stiff-back structure has been glued, preparation work in progress
FR4 skins are prepared

## Slide 27
Conclusions
We have constructed a 1 x 2.4 m² Micromegas chambers with 0.45 mm strip pitch and 4096 read-out channels, the worldwide largest MicroMegas chambers so far
The drift and read-out panels were made from four PCBs glued to a stiffener without dead space
Separate (floating) single mesh covering the full area.
The L2 chamber is working smoothly and shows reasonably uniform response over the full detector area
No signal reduction over the 1m strip length has been observed
A second 1 x 2.4 m² has been constructed (where a few of the shortcomings of the first one have been fixed); it is working smoothly as well and is now under study
The space, flat table, materials, man-power are ready for the full-wedge mechanical prototype production