## Slide 1: Introduction to Trigger/DAQ challenges at CERN
Niko Neufeld, CERN/PH
Many stimulating, fun discussions with my T-DAQ friends in ALICE, ATLAS, CMS and LHCb, and with a lot of smart people in CERN/IT (openlab) and industry are gratefully acknowledged

## Slide 2: The LHC Experiments today
ALICE – “A Large Ion Collider Experiment”
  Size: 26 m long, 16 m wide, 16m high; weight: 10000 t
  35 countries, 118 Institutes
  Material costs: 110 MCHF
ATLAS – “A Toroidal LHC ApparatuS”
  Size: 4 6m long, 25 m wide, 25 m high; weight: 7000 t
  38 countries, 174 institutes
  Material costs: 540 MCHF
CMS – “Compact Muon Solenoid”
  Size: 22 m long, 15 m wide, 15 m high; weight: 12500 t
  40 countries, 172 institutes
  Material costs: 500 MCHF
LHCb – “LHC beauty” (b-quark is called “beauty” or “bottom” quark)
  Size: 21 m long, 13 m wide, 10 m high; weight: 5600 t
  15 countries, 52 Institutes
  Material costs: 75 MCHF
Regular upgrades … first 2013/14 (Long Shutdown 1)
1 CHF ~ 1 USD

## Slide 3: What do Events Look Like?
Notes: Upper left ATLAS look along beampipe .. Inner part are tracks … green bars represent energy measured in ECAL … “trees” – energy in HCA: … leaving at right: Myon
Upper right: CMS: bars represent energy dumped in calorimeters.
Bottom left: hits and tracks in LHCb
Bottom right ALICE: tracks in a heavy ion collision

## Slide 4: The needle in the hay-stack: pp Collisions at 14 TeV at 1034 cm-2s-1
(pp) = 70 mb --> >7 x 108 /s (!)
In ATLAS and CMS* 20 – 30 min bias events overlap
HZZ Z mm H 4 muons: the cleanest (“golden”) signature
And this
(not the H though…)
repeats every 25 ns…
*)LHCb @4x1033 cm-2-1 isn’t much nicer and in Alice (PbPb) is even more busy

## Slide 5: Data Rates
Particle beams cross every 25 ns (40 MHz)
  Up to 25 particle collisions per beam crossing
  Up to 109 collisions per second
Basically 2 event filter/trigger levels
  Data processing starts at readout
  Reducing 109 p-p collisions per second to O(1000)
Raw data to be stored permanently: >15 PB/year
 | Incoming data rate | Outgoing data rate | Reduction factor
Level1 Trigger (custom hardware) | 40000000 s-1 | 10^5 – 10^6 s-1 | 400-10,000
High Level Trigger (software on server farms) | 2000-1000000 s-1 | 1000 -10000 s-1 | 10-2000
Physics Process | Events/s
Inelastic p-p scattering | 108
b | 106
W → eυ ; W → µυ ; W → τυ | 20
Z → ee ; Z → µµ ; Z → ττ | 2
t | 1
Higgs boson (all; mH = 120GeV) | 0.04
Higgs boson (simple signatures) | 0.0003
Black Hole (certain properties) | 0.0001

## Slide 6: LHC planning
Long Shutdown 2 (LS2)
CMS & ATLAS track-trigger
ALICE continuous read-out
LHCb 40 MHz read-out
CMS: Myrinet  InfiniBand / Ethernet
ATLAS: Merge L2 and EventCollection infrastructures

## Slide 7: Future DAQs in numbers
 | Event-size [kB] | Rate of events into HLT [kHz] | HLT bandwidth [Gb/s] | Year [CE]
ALICE | 20000 | 50 | 8000 | 2019
ATLAS | 4000 | 200 | 6400 | 2022
CMS | 2000 | 200 | 3200 | 2022
LHCb | 100 | 40000 | 32000 | 2019
It’s a good time to do DAQ
CMS and ATLAS numbers are growing as we speak…
40000 kHz == collision rate  LHCb abandons Level 1 for an all-software trigger

## Slide 8: Challenge #1 The first level trigger

## Slide 9: Level 1 Trigger
The Level 1 Trigger is implemented in hardware: FPGAs and ASICs  difficult / expensive to upgrade or change, maintenance by experts only
Decision time: ~ a small number of microseconds
It uses simple, hardware-friendly signatures  looses interesting collisions
Each sub-detector has its own solution, only the uplink is standardized 

## Slide 10: A Track-Trigger at 40 MHz 2020++
Goals:
  Resolve up to 200÷250 collisions per bunch crossing
  Maintain occupancy at the few % level
  Maintain overall L1 rate within 100 KHz
  Keep latency within ~ 6 μs (ECAL pipeline 256 samples = 6.4 μs)
      The current limit is the Tracker
L1 tracking trigger data combined with calorimeter & muon trigger data
    With finer granularity than presently employed.
Physics objects made from tracking, calorimeter & muon trigger data transmitted to Global Trigger.
Intro to Trigger/DAQ challenges at CERN - N. Neufeld

## Slide 11: Level 1 challenge
Can we do this in software?
Maybe in GPGPUs / XeonPhis  studies ongoing in the NA62 experiment
We need low and – ideally – deterministic latency
Need an efficient interface to detector-hardware: CPU/FPGA hybrid?
Or forget about the whole L1 thing altogether and do everything in HLT  requires a lot of fast, low-power, low-cost links, did anybody say Si-photonics?

## Slide 12: Challenge #2 Data Acquisition

## Slide 13: Data Acquisition (generic example)
GBT: custom radiation- hard link from the detector 3.2 Gbit/s
DAQ (“event-building”) links – some LAN (10/40/100 GbE / InfiniBand)
Links into compute-units: typically 10 Gbit/s (because filtering is currently compute-limited)
Detector
DAQ network
100 m rock
Readout Units
Compute Units
Every Readout Unit has a piece of the collision data
All pieces must be brought together into a single compute unit
The Compute Unit runs the software filtering (High Level Trigger – HLT)
10000 x
~ 1000 x
~ 3000 x

## Slide 14: Key Figures – Example LHCb
Minimum required bandwidth: > 32 TBit/s
Number of 100 Gbit/s links: > 320
Number of compute units: > 4000
Event size: 100 kB
Number of events per seconds: 10 – 40 Millions per second
Number of events retained for permanent storage: 20k – 30k per second
  storage allows to “defer” the decision at the cost of disks and tapes

## Slide 15: Design principles
Minimize number of expensive “core” network ports
Use the most efficient technology for a given connection
  different technologies should be able to co-exist (e.g. fast for building, slow for end-node)
  keep distances short
Exploit the economy of scale  try to do what everybody does (but smarter )

## Slide 16: The evolution of NICs
Chart: Gbit/s
| 2008.0 | 2012.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0
Ethernet | 10 | 40 | 40 | 40 | 40 | 100 | 100
InfiniBand x4 | 32 | 54 | 54 | 100 | 100 | 100 | 100
PCIe x8 | 32 | 64 | 64 | 64 | 64 | 128 | 128
PCIe Gen4
expected
Chelsio T5 (40 GbE
and Intel 40 GbE
expected
Mellanox FDR
Mellanox 40 GbE NIC
PCIe Gen3
available
EDR (100 Gb/s) HCA
expected
100 GbE NIC
expected

## Slide 17: A realistic DAQ / HLT for LHC
10 GBaseT
100 Gb/s
bi-directional
These 2 not necessarily the same technology

## Slide 18: Keep an eye on the fringe
There is always the temptation to remove the switch altogether  merge fabric and network
Modern versions of an old idea (token-ring, SCI)
  PCIe based (for example VirtualShare Ronniee a 2D torus based on PCIe, creates a large 64 bit shared memory space over PCIe)
  IBM blue-gene interconnect (11 x 16 Gb/s links integrated on chip – build a 5N torus)
Notes: Mention Billi, get some info on Blue-gene interconnect, check cray

## Slide 19: DAQ challenge
Transport multiple Terabit/s reliably and cost-effectively
Integrate the network closely and efficiently with compute resources (be they classical CPU or “many-core”)
Multiple network technologies should seamlessly co-exist in the same integrated fabric (“the right link for the right task”)

## Slide 20: Challenge #3 High Level Trigger

## Slide 21: High Level Trigger: Key Figures
Existing code base: 5 MLOC of mostly C++
Almost all algorithms are single-threaded (only few exceptions)
Currently processing time on a X5650 per event: several 10 ms / process (hyper-thread)
Currently between 100k and 1 million events per second are filtered online in each of the 4 experiments

## Slide 22: Online Trigger Farms at the end of Run 1
 | ALICE | ATLAS | CMS | LHCb
# cores (+ hyperthreading) | 2700 | 17000 | 13200 | 15500
# servers (mainboards) | ~ 500 | ~ 2000 | ~ 1300 | 1574
total available cooling power [ kW] | ~ 500 | ~ 820 | 800 | 525
total available rack-space (Us) | ~ 2000 | 2400 | ~ 3600 | 2200
CPU type(s) | AMD Opteron, Intel 54xx, Intel 56xx, Nvidia GPU | Intel 54xx, Intel 56xx | Intel 54xx, Intel 56xx Intel E5-2670 | Intel 5450, Intel 5650, AMD 6220
Massive upgrades foreseen for Run 2

## Slide 23: HLT needs for the future: 2018+
 | Event-size [kB] | Rate of events into HLT [kHz] | HLT bandwidth [Gb/s] | Year [CE]
ALICE | 20000 | 50 | 8000 | 2019
ATLAS | 4000 | 200 | 6400 | 2022
CMS | 2000 | 200 | 3200 | 2022
LHCb | 100 | 40000 | 32000 | 2019
Up a factor 10 to 40 from current rates - with much more complex events

## Slide 24: Coprocessors and all that
Many core co-processors (Xeon/Phi, GPGPUs) are currently very much in fashion in the HPC world
  Lots of interest in HEP, but few successful applications so far: ALICE, NA62
It might be that it will be most efficient to include them directly in the event-building network (i.e. receive data directly on the GPGPU/XeonPhi rather than passing through the main CPU)– this is supported today using IB by both Intel and Nvidial
The “co-processor” could become an independent unit on he network  this will clearly require very high-speed network interfaces (>>100 Gb/s to make sense over PCIe Gen3)

## Slide 25: High Level Trigger compared to HPC
Like HPC:
  full ownership of the entire installation  can choose architecture and hardware components
  single “client” / “customer”
  have a high-bandwidth interconnect
Unlike HPC:
  many independent small tasks which execute quickly  no need for check-pointing (fast storage)  no need for low latency
  data driven, i.e. when the LHC is not running (70% of the time) the farm is idle  interesting ways around this (deferal, “offline usage)
  facility is very long-lived, growing incrementally

## Slide 26: High Level Trigger challenge
Make the code-base ready for multi/many-core (this is not Online specific!)
Optimize the High Level Trigger farms in terms of cost, power, cooling
Find the best architecture integrating “standard servers”, many-core systems and a high-bandwidth network

## Slide 27: Summary
LHC “online” computing needs to acquire move and process huge amounts of data in real-time
Level 1 trigger challenge: replace custom by industry-standard hardware; move more data with less power
Data acquisition challenge: very high bandwidth, low-overhead networks, tightly integrated with computing resources
High Level Trigger challenge: make most out of the CPU power (parallelisation), find the most power- and cost-efficient way to provide as much computing power as possible for extracting the most interesting physics

## Slide 28: More material

## Slide 29: Challenge 4: I/O on x86 servers

## Slide 30: The evolution of PCs
PCs used to be relatively modest I/O performers (compared to FPGAs), this has radically changed with PCIe Gen3
Xeon processor line has now 40 PCIe Gen3 lanes / socket
Dual-socket system has a theoretical throughput of 1.2 Tbit/s(!)
  Tests suggest that we can get quite close to the theoretical limit (using RDMA at least)
This is driven by the need for fast interfaces for co-processors (GPGPUs, XeonPhi)
For us (even in LHCb) CPU will be the bottle-neck in the server - not the LAN interconnect – 10 Gb/s by far sufficient

## Slide 31: Keep distances short
Multi-lane optics (Ethernet SR4, SR10, InfiniBand QDR) over multi-mode fibres are limited to 100 (OM3) to 150 (OM4) meters
Cable assemblies (“direct-attach) cables are either
  passive (“copper”, “twinax”), very cheap and rather short (max. 4 to 5 m), or
  active – still cheaper than discreet optics , but as they use the same components internally they have similar range limitations
For comparison: price-ratio of 40G QSFP+ copper cable assembly, 40G QSFP+ active cable, 2 x QSFP+ SR4 optics + fibre (30 m) = 1 : 8 : 10

## Slide 32: The evolution of lane-speed
All modern interconnects are multiple serial: (x something SR)
Another aspect of “Moore’s” law is the increase of serialiser speed
Higher speed reduces number of lanes (fibres)
Cheaper interconnects also require availability of cheap optics (VCSEL, Silicon-Photonics)
VCSEL currently runs better over MMF (OM3, OM4 for 10 Gb/s and above)  per meter these fibres are more expensive than SMF
Current lane-speed 10 Gb/s (same as 8 Gb/s, 14 Gb/s)
Next lane-speed (coming soon and already available on high-end FPGAs) is 25 Gb/s (same as 16 Gb/s)  should be safely established by 2017 (a hint for GBT v3 ?)

## Slide 33: Classical fat-core event-builder
About 1600 core ports