## Slide 2: LIU: Exploring alternative ideas
H. Damerau
Review of LHC & Injector Upgrade Plans Workshop (RLIUP)
30 October 2013
Acknowledgements: G. Arduini, T. Argyropoulos, M. Benedikt, T. Bohl, C. Carli, S. Gilardoni, B. Goddard, W. Herr, W. Höfle, B. Mikulec, E. Montesinos, G. Rumolo, L. Sermeus, H. Timkó, R. Tomas, R. Wasef and many others
Contributions from: H. Bartosik, R. Garoby, S. Hancock, Y. Papaphilippou, E. Shaposhnikova

## Slide 3
Overview
Introduction
Alternative schemes in the Pre-injectors
  Manipulation schemes in the PS
  Additional improvements
  Special case for limited upgrades
Alternative schemes in the SPS
  RF power considerations
  Transverse improvements
Summary

## Slide 4
Introduction: baseline upgrade plan
Linac2, 1.4 GeV, 3-split
Linac4, 2.0 GeV, 3-split
Increase brightness from Linac with PS Booster Linac2  Linac4
Reduce space charge in the PS PSB/PS transfer energy 1.4 GeV  2 GeV
Increase intensity per bunch in SPS RF upgrade 4.2  7.6 MW, 4  6 cav.
Achieved
LIU: after upgrades
HL-LHC request
 | 25 ns | 50 ns
Splitting ratio PS ejection/injection | 12 | 6
Batch length from PS | 72 | 36
Are there alternatives?

## Slide 5
Overview of upgrade options
Linac4
PSB
PS
SPS
Basic choices
Additional benefit/margin
2.0 GeV at PSBPS transfer
SPS RF upgrade: 43+24
Baseline Beam studies before LS1 Beam studies possible after LS1 Needs hardware
Faster recombination kickers PSB-PS (with 1.4 GeV)
Double-batch or h=5 single-batch injection
3-split, BCMS, BCS or PBC (pure batch comp.)
8b+4e together with 3-split or BCMS
Resonance compensation
Special injection optics
Long. flat or hollow bunches
Split tunes optics
Special injection optics
28 GeV at PSSPS transfer
+5 %
+? %
+15 %
+25 %
+? %
+? %
+? %
Vertical painting Linac4
+25 %
Long. flat or hollow bunches
More RF power plants: 42+43 or 102
Relaxed el with 200 MHz in LHC
Basic choices + alternatives

## Slide 6
Assumptions
Basic assumptions for performance evaluation:
 | Parameter | 
L4+PSB | Transverse emittances halved compared to Linac2 | ~0.6 mm/1012
PS | Beam loss | 5%
 | Transverse emittance growth | 5%
 | Tolerable space charge tune shift, DQy | -0.31
 | Maximum bunch length at injection | Recomb. kickers
SPS | Beam loss | 10%
 | Transverse emittance growth | 10%
 | Tolerable space charge tune shift, DQy | -0.21
 | Baseline intensity per bunch after RF upgrade | 2.0·1011 ppb
All parameters only valid for 25 ns bunch spacing
For comparison, performances are given at extraction from SPS
Caution: most considerations over-simplified

## Slide 7
Overview
Introduction
Alternative schemes in the Pre-injectors
  Manipulation schemes in the PS
  Additional improvements
  Special case for limited upgrades
Alternative schemes in the SPS
  RF power considerations
  Transverse improvements
Summary

## Slide 8
Batch compression, merging, splitting
Ekin = 2.5 GeV
  Measurement
Effectively reduce PSB brightness by smaller splitting factor in PS
Successfully made operational in 2012, baseline for 25 ns after LS1
HL-LHC request
Bunches split by 6 in PS: batches of 48 bunches, 6% less bunches in LHC
Perfectly matches PS (2 GeV) and SPS space charge limits
Brightness reach beyond with HL-LHC request for 25 ns beam

## Slide 9
Pure batch compression
Extreme case of no bunch splitting at low energy at all
Bunches split by 4 in PS: batches of 32 bunches, 13% less bunches in LHC
Can be tested after LS1 controls upgrade of PS LLRF
Pushes SPS to space charge limitation!
  Simulation
Ekin = 2.5 GeV

## Slide 10
4 bunches missing every 8 bunches  improvement for e-cloud
50% less bunches in LHC, but with significantly higher intensity
To be tested with beam after LS1
8b+4e bunch pattern schemes
Replace h = 7  21 triple split by direct double split, leaving empty bucket
In combination with BCMS beams, merging and triple split suppressed
Bunch pattern 6(8b+4e) or 4(8b+4e)
  Simulation
Ekin = 2.5 GeV
  Simulation
Ekin = 2.5 GeV

## Slide 11
Overview
Introduction
Alternative schemes in the Pre-injectors
  Manipulation schemes in the PS
  Additional improvements
  Special case for limited upgrades
Alternative schemes in the SPS
  RF power considerations
  Transverse improvements
Summary

## Slide 12
Space charge reduction, longitudinal
Flat-bunches
  Double harmonic RF or hollow bunch distribution
  Space charge reduction by up to 25%
Longer bunches
  Bunch length at PSB-PS transfer limited by switching time between PSB rings
  Reducing switching time: 105 ns  65 ns (1.4 GeV), 110 ns  70 ns (2 GeV)
Reduce DQsc at PS flat-bottom, potential brightness about 15%
Technically challenging even for transfer at 1.4 GeV
No interest after upgrade of to 2.0 GeV
4+2 injection into h = 7
4+4 injection into h = 9

## Slide 13
Space charge reduction, transverse
  Compensation of resonances (Qx/y=0.21/0.24)
    Closest resonance 4Qy = 1 difficult as excited by space charge
    Compensation of 2Qx + Qy = 1 and 3Qy = 1 lines during studies in 2013
  Special optics with vertical dispersion
    Introduce vertical dispersion to maximize beam size and reduce DQsc
    Optics becomes very irregular, needs simulations and beam studies
    Evaluate potential benefit with first beam studies after LS1
Regular optics, zero Dy
Irregular optics, non-zero Dy
Requires hardware upgrades
Present configuration

## Slide 14
Overview
Introduction
Alternative schemes in the Pre-injectors
  Manipulation schemes in the PS
  Additional improvements
  Special case for limited upgrades
Alternative schemes in the SPS
  RF power considerations
  Transverse improvements
Summary

## Slide 15
Single-batch injection with Linac4
Combination of Linac4 with 1.4 GeV PSBPS transfer energy unfavorable
  Linac4 + PSB can deliver brightness far beyond PS space charge limit
Transfer 4 long bunches from PSB to h = 5 in PS, then h = 5  10  20  21
Linac4, 1.4 GeV, 3-split
Double-batch transfer
Rematches Linac4 + PSB and PS in terms of space charge
Bunches split by 16 in PS: batches of 64 bunches, 3% less bunches in LHC
Needs additional RF cavity at h = 5 or renovated cavities in PS
Single-batch transfer
Linac4, 1.4 GeV, h = 5 inj.

## Slide 16
Overview
Introduction
Alternative schemes in the Pre-injectors
  Manipulation schemes in the PS
  Additional improvements
  Special case for limited upgrades
Alternative schemes in the SPS
  RF power considerations
  Transverse improvements
Summary

## Slide 17
Maximum intensity from SPS
24+25
43+24
43+42
102
Fixed bunch length required at SPS  LHC transfer
Available RF voltage decreases with beam intensity
Pulse amplifiers at frev for more power during beam passage (new LLRF)
Effective RF power 0.7 MW  ~1.05 MW
Pnow = 0.7 MW
Pold = 1.05 MW
Pnew = 1.6 MW
RF voltage at transfer to LHC (25ns)
Q20 optics

## Slide 18
Baseline upgrade: shorter cavities and 21.6 MW RF power
Nb ≈ 2 · 1011 ppb without degradation, 2.5 · 1011 ppb for 10% longer bunches
Even shorter cavities and more RF power?
Larger bunch intensity from SPS?
t = const, LD+PWD
24+25
43+24
43+42
102
LD: Loss of Landau damp.
PWD: Potential well dist.
Z/n today
Pold = 1.05 MW
Pnew = 1.6 MW
RF voltage at transfer to LHC
RF voltage at transfer to LHC
To keep longitudinal stability (Landau damping + potential well dist.)
  Longitudinal emittance increases with intensity: 
  RF voltage requirement proportional to IRF
+0.51 · 1011
+0.29 · 1011
+0.18 · 1011
Q20 optics

## Slide 19
8b+4e scheme in the SPS
LD: Loss of Landau damp.
PWD: Potential well dist.
24+25
43+24
43+42
102
t = const, LD+PWD
Line density averaged over 0.3 ms (≈tfill/2) reduced by 2/3 at constant Nb
  50% more intensity per bunch for the same beam loading
No benefit for single-bunch instability effects
Nb ≈ 3 · 1011 ppb reachable assuming SPS impedance reduction by 50%
First beam tests after LS1 possible
Bunch pattern from PS
Triple splitting: 6(8b+4e)
BCMS –like manipulation: 4(8b+4e)

## Slide 20
200 MHz in LHC
t = const, LD+PWD
VRF for 3 MV at 200 MHz in LHC
24+25
43+24
43+42
102
t = const, LD+PWD
VRF for 3 MV at 200 MHz in LHC
24+25
43+24
43+42
102
Injecting with 200 MHz RF in LHC relaxes emittance constraint:
  el = 1.0…1.5 eVs, depending on whether transfer to 400 MHz RF
  No single-bunch stability issues at SPS flat-bottom
el ~ 1 eVs at SPS  LHC transfer
Combined with 8b+4e scheme
Larger el in SPS associated with 200 MHz LHC helps on SPS flat-top
Power limitations for longitudinal emittance during acceleration?

## Slide 21
25 ns acceleration limit with 43+24 cavities 2.3 · 1011 ppb
Limit with 8b+4e scheme (density in PS) 3.0 · 1011 ppb
Power Requirements during Acceleration
Present configuration
Nb = 1.2 · 1011 ppb
Nb = 2.3 · 1011 ppb
Nb = 3.2 · 1011 ppb
43+24 cavities (baseline upgrade)
43+42 cavities (extended upgrade)
Small el imposed during first part of acceleration (present magnetic cycle)
200 MHz in LHC or 8b+4e scheme only beneficial with SPS RF upgrade
P [MW]
P [MW]
P [MW]
AB [eVs]
AB [eVs]
AB [eVs]
AB required could be even higher
estimated

## Slide 22
Overview
Introduction
Alternative schemes in the Pre-injectors
  Manipulation schemes in the PS
  Additional improvements
  Special cases for limited upgrades
Alternative schemes in the SPS
  RF power considerations
  Transverse improvements
Summary

## Slide 23
Reducing space charge in the SPS
  Increase extraction energy from PS
    Transfer LHC-type beams at 28 GeV instead of 26 GeV
    Immediate space charge tune shift reduction by 15%
    Combinable with any scheme at SPS space charge limit
Less possibilities and margin than in PS
  Split tunes optics, Qh = 20 and Qv = 26
    Gain from simulations 5% with respect to Qh,v = 20
    Beneficial for injection of 28 GeV beam
  Irregular optics with non-zero vertical dispersion
    Important changes to cabling and supply of skew quadrupoles
DQsc/Nb [1011 ppb]
ex/y [mm]
[…] the maximum energy was increased to 28 GeV.

## Slide 24
Overview
Introduction
Alternative schemes in the Pre-injectors
  Manipulation schemes in the PS
  Additional improvements
  Special cases for limited upgrades
Alternative schemes in the SPS
  RF power considerations
  Transverse improvements
Summary

## Slide 25
Preliminary summary and remarks
No magic alternative to Linac4 + 2.0 GeV + SPS RF upgrade
Large number of schemes to increase intensity and brightness from injectors
  Linac4+PSB+PS may push SPS to space charge limit
Longitudinally larger bunches in SPS possible together with RF upgrade
Limited reach of brute-force approach for even more RF power
Interesting alternatives can be studied in injectors after LS1
  PSB: Hollow bunches
  PS: Flat or hollow bunches, special flat-bottom optics, pure batch compression, 8b+4e schemes, higher PS-SPS transfer energy
  SPS: split tunes optics, higher intensity with slightly longer bunches
Combinations of alternatives keep flexibility of injector complex to react to requests from LHC: short-, micro-, 8b+4e-batches

## Slide 26
THANK YOU FOR YOUR ATTENTION!

## Slide 27
PSB
Small upgrades beyond baseline:
Vertical painting at PSB injection from Linac4
  More flexibility in controlling transverse distribution
Reduction of horizontal tune by one unit to increase dispersion
Optimization of resonance compensation
  Potentially higher brightness (study will be pursued anyway)
Discarded options:
Replacement of PSB magnets for energy above 2 GeV
  Present main magnets potentially useable up to ~2.2 GeV (M. Giovannozzi) (http://indico.cern.ch/getFile.py/access?contribId=34&sessionId=7&resId=1&materialId=paper&confId=67839)
  New magnets expensive and require excessive shutdown for installation
Significantly fast cycling  Rapid cycling synchrotron (K. Hanke et al., 2011) (https://edms.cern.ch/file/1154705/1.2/PBU-1154705-10-20.pdf)
  Decision not to pursue PSB replacement by RCS

## Slide 28
PS
Discarded options:
Direct H--injection from SPL-like like prolongation of Linac4 into PS
  Requires down-graded SPL, transfer line and new injection system 40 MHz PS2-like acceleration system for LHC-type beams, but incompatible with other physics users (C. Carli, Chamonix 2010)
  (http://indico.cern.ch/getFile.py/access?contribId=36&sessionId=7&resId=2&materialId=paper&confId=67839)
20 ns bunch spacing from the PS (and possibly 10 ns)
  Interesting as RF frequencies in all machines become integer multiples
  Requires 50/100 MHz (h = 105/210) cavities for bunch rotation in PS
  Possible production scheme 8b/h9  16b/h18  32b/h36  32b/h35  96b/h105 requires even more RF system
  40 ns bunch spacing practically impossible

## Slide 29
SPS
Discarded options:
Slip-stacking in the SPS (T. Argyropoulos, E. Shaposhnikova, LIU brainstorming) (http://indico.cern.ch/getFile.py/access?contribId=16&sessionId=1&resId=1&materialId=slides&confId=138437)
  Many issues: beam loading, too large longitudinal emittance, etc.
Low frequency cavities (e.g. 80 MHz, 120 MHz) in the SPS to capture longer bunches: less space charge, better stability in PS due to larger el
  Introduces important beam stability issues in the SPS (E. Shaposhnikova) (http://paf-spsu.web.cern.ch/paf-spsu/meetings/2011/m14-04/Low_frequency_RF_Heiko.pptx)
400 MHz cavities for bunch compression and Landau damping in the SPS
  Originally foreseen for bunch compression (D. Boussard, Th. Bohl) (Part. Acc. 58, 1997, pp. 237-240 and SL/Note 93-47, http://cds.cern.ch/record/703346/files/CM-P00064463.pdf)
  Issues with beam loading would require non-integer harmonic number acceleration
Bunch splitting on flat-top against e-cloud on flat-bottom; merging for higher intensity
  Empty buckets between bunches would require re-bucketing to lower harmonic RF system, which is excluded for stability reasons

## Slide 30: New PS Injector: SPL
Geometry (just to fix ideas) for 2.5 GeV:
  Length of SPL ~300m (in addition to Linac4, extrap. from sLHC Proj. Rep. 0015)
  ~500 m transfer line
PS Injection
  New H- charge exchange injection to be constructed
  Flexibility to generate suitable PS bunch structures (SPL chopper, painting?)
  Close to East Hall ejection
Simplified PS RF system with ~40MHz possible for LHC protons only (see PS2 scheme)
75 m

## Slide 31
Space charge reduction, longitudinal
  Flat-bunches in double-harmonic RF system
    Requires two RF systems
    Transfer between accelerators difficult
  Bunch distributions with depleted core, flat profile
    Only single harmonic RF system needed
    Little complexity in downstream chain
    Even survives distribution conserving RF manipulations, e.g. pair splitting
  Measurement, 2001
  PSB, Ekin = 1.4 GeV
Reduce DQsc at PS flat-bottom, potential brightness gain up to 25%
Last studies in 2001; simulations preparing new beam studies ongoing

## Slide 32: Compensation of the 2Qx+Qy = 19 in the PS
Scan direction
Scan direction
  A. Huschauer, R. Wasef

## Slide 33: Compensation of 3Qy = 19 in the PS
Scan direction
Scan direction
A. Huschauer