## Slide 1
Integrated performance of the LHC at 25 ns
without and with LINAC4
J. Wenninger
G. Arduini, G. Rumolo, V. Kain, A. Apollonio, A. Gorzawski

## Slide 2: 25 ns @ SPS
Beam type | Scenario | Nbunch [1011] | e* [mm] | Limit
BCMS | Achieved | 1.15 | 1.39 | --
BCMS | No upgrade | 1.3 | 1.28 | PS/SPS
BCMS+L4 | Linac 4 | 1.3 | 1.28 | PS/SPS
Standard | Achieved | 1.2 | 2.6 | --
Standard | No upgrade | 1.3 | 2.44 | SPS
Standard+L4 | Linac 4 | 1.3 | 1.65 | SPS
Only standard beam gains with Linac4.
Limits after LS1:
  Brightness in the PS (BCMS),
  RF in the SPS (all).
See presentation by G. Rumolo

## Slide 3: 25 ns @ LHC collisions
Beam type | Nbunch [1011] | e* [mm] | k | b* [cm] | ½ Xing angle [mrad]
BCMS (+L4) | 1.25 | 1.65 | 2590 | 40 / 50 | 150 / 140
Standard | 1.25 | 2.9 | 2740 | 50 | 190
Standard+L4 | 1.25 | 2.0 | 2740 | 40 / 50 | 150 / 140
Nbunch and e* : values for LHC collisions.
From SPS extraction to LHC collision:
  Assumed emittance blow up of 15% on top of IBS - optimistic wrt 2012 (~ 30% observed),
    E-cloud-driven and additional 2012-like blow up under control,
  Transmission of 96% (~ 2012 values).
Crossing angles: deduced from an analysis by R. Bruce.
Filling scheme variations may affect k at the level of ~5%.

## Slide 4: Pile-up & luminosity limits
A maximum average pile-up of 45 events per crossing is used as upper limit (given as rough guideline for 2015).
  Based on a visible cross-section of 85 mb @ 6.5 TeV.
  For simplicity it is assumed that we can also level at a pile-up of 45.
The cooling of the triplet sets a limit to the maximum achievable luminosity of ~1.75 ×1034 cm-2s-1 ±10-20%.
  We will have to explore the limit in 2015+.
  Further reduction of limit due to e-could heat load?
  A study will be launched to analyze all possible limitations in the triplet (starting with the limiting heat-exchanger).
L. Tavian
@ Evian 2012

## Slide 5: Intensity & brightness limitations
The intensity/brightness may be limited by instabilities.
  25 ns up to 1.3E11 ppb just at the edge?
  Stabilized by head-on beam-beam if needed, but implies more complicated operation.
Other possible limitations to intensity:
  heating,
  e-cloud,
  UFOs.
  - more experience must be collected in 2015+.

## Slide 6: UFOs
Extrapolation from 2012 to 7 TeV: ~100 beam dumps from UFOs
UFO rate depends on bunch spacing, stronger with 25 ns.
  But: fast conditioning observed over a few fills in 2012 – there is hope !
We have to expect serious deconditioning after LS1.
Current status of quench test analysis (LBOC meeting 22.10): we may have extra margin (x 2) at 4 TeV for UFO timescales. To be confirmed.
Clear picture only after 2015.
T. Baer

## Slide 7: E-cloud in 2012
Scrubbing
  Demonstrated to be efficient at 450 GeV
  It lowers e-cloud in dipoles, less evident in quadrupoles (due to a significantly lower threshold SEY)
Despite 2-beam-50 ns operation in triplet for ~ 2 years (high electron dose), e-cloud still present in triplets.
  SEY ~1.2-1.3 – deduced from heat-load & simulations.
Significant increase of heat load (~ factor 4) in arcs during ramp.
  From e-cloud in the dipoles. No change in quadrupoles.
  Does not decrease over time at flattop (no scrubbing at flattop ?)
  Underlying mechanism to be understood
G. Rumolo at al

## Slide 8: E-cloud for 2015
Available cooling power in the arcs (~ 250 W / ½ cell) will possibly limit (initial) operation at 6.5 TeV.
  Limitations in SAMs will be lifted during LS1.
Projection of CURRENT situation to 2015: limitation to  ½ number of bunches at 25 ns (~1400).
Idea to enhance scrubbing at 450 GeV to remove e-cloud in the dipoles “completely” with dedicated scrubbing beam.
  Use doublet beam : 5 – 20 ns or 2.5 – 22.5 ns spacing
  Implications and issues (BI, RF, ADT) under investigation. Report at the next LHC Beam Operation Committee (5th November).
25ns
25ns
25ns
5 or 2.5 ns

## Slide 9: Run length & overheads
A run length of 160 days (high int pp) per year is assumed.
Periods of reduced luminosity are embedded in our runs. Such periods include:
  Initial intensity ramp up – few weeks. Likely to improve every year up to an incompressible minimum.
  Ramp up after technical stops: ~ 2 days.
b* leveling setup may be required (and learning curves).
  Important to train asap – LHCb !
And one should not forget all the special runs like high-beta, LHCf etc that eat up additional few % of the proton runs.
>> this reduces the integrated luminosity by 5-10%

## Slide 10: Availability in 2012
The 2012 run can be split into 3 blocks.
    On a per-physics-fill basis we had:
Stable beams
Faults
Turn-around =
the ‘rest’
6.1 hours
4.8 hours
5.5 hours
 36% stable beams fraction / physics efficiency
The blue turn-around box also accounts for
    Test cycles (Q/Q’ measurements, FB tests, loss maps, high beta setup…) and lost cycles.
    ‘Short’ tests that were inserted in a standard cycles.
    A certain number of pre-cycles.
    Etc…
    Minimal / best turn-around time ~ 2.2 hours.
This will always be required !

## Slide 11: Failure breakdown
Ordered by 2012 top-10
Cryo + injectors account for ~1/3 of fault time in 2012.
  Typical SPS efficiency:85 ± 5%.
A. Macpherson

## Slide 12: Physics Efficiency of LHC & LEP
LEP1
LEP2
LEP1 reached physics efficiencies > 50% (1992-1994).
  Simpler machine, long fills.
  LEP2 had short(er) fills – similar to LHC.
With one exception, best LHC weeks achieved ~45% physics efficiency. Do it more often...
2011
2012

## Slide 13: Availability Modeling - future
Our current accounting of faults & ‘turn-around’ is rather coarse.
There is an ongoing effort between AWG (Availability WG) and OP to improve the modeling and information on the different phases.
Aim to build a tool that combines
    Cycle information (beam modes, intensity, energy),
    Post-mortem information
    Fault information,
    Etc
    … to provide a better model for faults and for ‘the rest’.
Work in progress

## Slide 14: Availability assumption
What we know:
    The cycle length increases by ~20 minutes.
Baseline assumption for performance:
    Everything remains the same except for cycle length,
    Assume that in ‘Turn-around’ there are ~2 cycles  40 minutes,
Stable beams
Faults
Turn-around =
the ‘rest’
6.1 hours
4.8 hours
6.2 hours
 35% stable beams fraction
Many uncertainties  assumptions optimistic for 2015? No point in speculating too much.
Baseline for analysis: stable beams efficiency of 35%.

## Slide 15: Luminosity model
A simple luminosity model is used for 6.5 TeV, based on 2012 observations during collisions.
Ingredients:
  Burn-off (s = 105 mb),
  Single beam lifetimes,
  Emittance growth.
Cross-checked with:
  Simple analytic approach (simple closed formula) for exponential fill length distribution and constant averaged luminosity lifetime (CERN-ATS-Note-2013-033 PERF).
  Monte-Carlo approach (A. Apollonio).
Model dependence of predictions can be > 10%

## Slide 16: Intensity lifetime
2012 beam intensity lifetimes:
  t  25-40 hours in collision (includes burn-off)
  Before collision tricky to obtain due to large influence of tails in the squeeze.
   assume 60 hours average intensity lifetime without burn-off.
Time in stable beams [h]
Lifetime [h]
2012 average
A. Gorzawski

## Slide 17: Emittance growth
A. Gorzawski
Significant ‘effective’ emittance growth is observed in collision (from luminosity evolution) at 3.5/4 TeV.
  Origin of growth not understood. IBS is not sufficient, need an extra 20 h emittance growth time ( G. Arduini).
  Growth was steeper in 2011.
  2012 evolution is used to model the luminosity at 6.5 TeV, corrected for radiation damping.
2011: e2  e02 + 0.59 t
2011: b* 1 m
2012 : after MO polarity switch

## Slide 18: Luminosity lifetimes 2012
2012 run experience @ 4 TeV:
  t  6-8 hours – first hour,
  t  12-15 hours – after 8 hours.
M. Hostettler, G. Papotti
Luminosity lifetime from burn-off @ 2×1034 cm-2s-1 + 6.5 TeV :
  t  12 hours.
Reproduced by the model

## Slide 19: Fill length
An exponential fill length distribution is used for the performance figures quoted in the next slides.
2011
2012
Fill lengths in 2011 and 2012  exponentials.
  ~30% of the fills are dumped by OP.

## Slide 20: Distributions
Effect of the fill length distribution:
  Exponential (truncated @ 20 hours), flat, delta – mean length 6.5 h in all cases.
Distribution | Rel. Int. L
Exponential | 1
Flat | ~1.1
Delta | ~1.2
Depends on lifetime assumptions
Distribution for 2012 is a mixture of:
  Exponential – faults (~2/3),
  Flat + smeared delta from OP dumps (1/3).
+5-10% wrt exponential

## Slide 21: BCMS example
 | Nbunch [1011] | e*l [mm] | k | b* [cm] | ½ Xing [mrad]
BCMS (w/wo L4) | 1.25 | 1.65 | 2590 | 40 | 150
Leveling ~2.5 hours
Model | Int L/fill (pb-1)
Exp (6.5 h) | 259
Flat (6.5 h) | 283
Dump (6.5 h) | 306

## Slide 22: Optimum fill length – BCMS example
35%
40%
45%
50%
The 6.5 hours dump time is not too far from the optimum ~ 8-10 h.
-- Turnaround = 6h
-- Turnaround = 8h
-- Turnaround = 10h
-- Turnaround = 15h

## Slide 23: Comparison – exponential model
Beam | b* (m) | Leveled L (1034 cm-2s-1) | Peak L (1034 cm-2s-1) | Leveling time (h)
Standard L4 | 0.4 | 1.65 | 2.1 | ~1.6
BCMS | 0.4 | 1.54 | 2.2 | ~2.5
Standard L4 | 0.5 | 1.65 | 1.9 | ~0.7
BCMS | 0.5 | 1.54 | 2.0 | ~1.6
Standard | 0.5 | 1.65 | 1.2 | --
48-53 fb-1/year
BCMS & standard are very close in performance.
Leveled L ~at the triplet limit, peak lumi BCMS / L4 above limit.
With 2011 emittance model, values increase ~2%.
Add 5-10% to account for mixed fill length distribution

## Slide 24: BCMS example – no leveling
 | Nbunch [1011] | e*l [mm] | k | b* [cm] | ½ Xing [mrad]
BCMS (w/wo L4) | 1.25 | 1.65 | 2590 | 40 | 150
Initial L lifetime ~5 h
10-15 h L lifetime ~14 h

## Slide 25: Performance – no leveling
  Modest gain of a few fb-1 due to short leveling time & low(er) initial lifetime.
  BCMS and Standard+L4 have again similar performance, but higher pile-up with BCMS.
  Peak pile-up ~66 for BCMS and b* = 0.4 m.
50-55 fb-1/year

## Slide 26: Monte-Carlo Model
  Monte-Carlo model by A. Apollonio, developed for HL-LHC, to model luminosity (simplified), failures and turn-around. Applied to 25 ns operation post-LS1:
    30% fills dumped by operation,
    6.2 hours of turn-around,
    Fault time modeled by 4 LogNormal distributions.
  Results are consistent in the range of ~45 fb-1.
  The increased impact of UFOs (~100 dumps/year) can lower the integrated luminosity by 15% for the current BLM thresholds.

## Slide 27: Summary (1)
The expected integrated luminosity per year for 25 ns is in the range of 45-55 fb-1 for a 2012-like efficiency.
    For 5 ½ years of operation until LS3  250-300 fb-1.
    Before L4 : use BCMS – with L4: use standard beam.
    Unknowns on limitations, emittance, efficiency – 10% level effects – situation will be clearer end 2015.
    Peak luminosity close to / above expected triplet limitation !!!!
With L4 the standard 25 ns beams and the BCMS beams have very similar performance.
  Bonus for standard 25 ns: lower pile-up (~10%).
  The emittances that are eventually achieved may make the difference – easier for standard (larger e) ?

## Slide 28: Summary (2)
To be sure to reach/exceed 300 fb-1 by LS3 we should aim to improve the average physics efficiency of the LHC from ~35% to at least 40%.
    Concerted long term effort !
    Could reduce peak L / pile-up and compensate with efficiency if we get too close to detector damage.
To reach luminosities of 2.5 1034 cm-2s-1 as quoted in reference figures b* needs to be pushed further, emittances lowered etc.

## Slide 30: High-Luminosity LHC and Availability
Fault time distributions in 2012 (4 logn):
A. Apollonio

## Slide 31: SPS efficiency (fixed target)
SPS
?
Shutdown

## Slide 32: Summary: β*-reach
50 ns, 2.5 um | beta* crossing (cm) | beta* separation (cm) | Half crossing angle (urad) | BB sep (sigma)
mm scaled, no BPM | 47 | 49 | 129 | 9.3
mm scaled, BPM | 39 | 39 | 141 | 9.3
2 sig retraction, no BPM | 42 | 43 | 136 | 9.3
2 sig retraction, BPM | 35 | 33 | 150 | 9.3
50 ns, 1.6 um | beta* crossing (cm) | beta* separation (cm) | Half crossing angle (urad) | BB sep (sigma)
mm scaled, no BPM | 43 | 49 | 108 | 9.3
mm scaled, BPM | 35 | 39 | 119 | 9.3
2 sig retraction, no BPM | 38 | 43 | 115 | 9.3
2 sig retraction, BPM | 31 | 33 | 127 | 9.3
25 ns, 3.75 um | beta* crossing (cm) | beta* separation (cm) | Half crossing angle (urad) | BB sep (sigma)
mm scaled, no BPM | 60 | 49 | 180 | 12
mm scaled, BPM | 52 | 39 | 194 | 12
2 sig retraction, no BPM | 55 | 43 | 189 | 12
2 sig retraction, BPM | 46 | 33 | 205 | 12
25 ns, 1.9 um | beta* crossing (cm) | beta* separation (cm) | Half crossing angle (urad) | BB sep (sigma)
mm scaled, no BPM | 49 | 49 | 141 | 12
mm scaled, BPM | 42 | 39 | 154 | 12
2 sig retraction, no BPM | 45 | 43 | 149 | 12
2 sig retraction, BPM | 37 | 33 | 163 | 12
Updates after MD?

## Slide 33: Summary: β*-reach in crossing plane