## Slide 1
Update on LHC observations in LSS and simulation studies
C. Octavio Domínguez
22 July 2013 - e- cloud meeting
Thanks to
G. Iadarola, G. Rumolo and F. Zimmermann

## Slide 2
Outline
Pressure rise observations with 25 and 50 ns beams
Bunch intensity thresholds for 50 ns
Behavior during pre-ramp and energy ramp
Interpretation using PyECLOUD simulations
Conclusions
22 July 2013 - e- cloud meeting

## Slide 3
Outline
Pressure rise observations with 25 and 50 ns beams
Bunch intensity thresholds for 50 ns
Behavior during pre-ramp and energy ramp
Interpretation using PyECLOUD simulations
Conclusions
22 July 2013 - e- cloud meeting

## Slide 4
DP with 25 and 50 ns
Pressure rises were the first ECE observed in the LHC with 150 and 75 ns
Beam 1
Beam 2
No pressure increase
Pressure increase
150 ns - 450 GeV
G. Bregliozzi
22 July 2013 - e- cloud meeting

## Slide 5
Pressure rises were the first ECE observed in the LHC with 150 and 75 ns
I focused on pressure gauges located in warm-warm transitions (VGI type):
They are more accurate than other types of gauge in the machine
They are all located in the same type of module (with simple geometry)
Ø 80 mm
StSt – Cu coated
DP with 25 and 50 ns
22 July 2013 - e- cloud meeting

## Slide 6
Pressure rises were the first ECE observed in the LHC with 150 and 75 ns
I focused on pressure gauges located in warm-warm transitions (VGI type):
They are more accurate than other types of gauge in the machine
They are all located in the same type of module (with simple geometry)
These modules are located between two 7 m NEG-coated beam pipes
> 7 m NEG coating
> 7 m NEG coating
There are 173 gauges of this type around the ring (easier comparison and extrapolation)
SEY estimated by the vacuum colleagues: ~ 1.6 – 1.9 [1]
DP with 25 and 50 ns
22 July 2013 - e- cloud meeting
There are few exceptions where one side is shorter
I’ll focus here on beam 1 (68 guages), although conclusions are equivalent for both beams.

## Slide 7
DP with 25 and 50 ns
22 July 2013 - e- cloud meeting
I base my observations on 50 ns on 6 fills:
  2124: 19 September 2011 (before MDs with 25 ns)
  2240: 22 October 2011 (between 14 October MD and 24
  October MD)
  2261: 27 October 2011 (after 25 ns MDs)
  Nb≈1.37e11 ppb for all three
  2736: 16 June 2012 (Nb≈1.47e11 ppb)
  3000: 24 August 2012 (Nb≈1.52e11 ppb)
  3286: 14 November 2012 (Nb≈1.65e11 ppb)
  Three random long physics fills during 2012 operation
  I’ll show some observations of 25 ns for the 24/10/11 MD

## Slide 8
DP with 25 and 50 ns - Injection
22 July 2013 - e- cloud meeting
Quite stable sz
DP after 2nd injection
Sector 1-2
Fill 2124
DP after 8th injection
Too close to the cryocell.
More difficult comparison.
I discarded it.

## Slide 9
DP with 25 and 50 ns - Injection
22 July 2013 - e- cloud meeting
Sector 1-2
Small DP after 10th injection
No visible DP
We observe different behaviors  Different conditioning states?
Fill 2124

## Slide 10
DP with 25 and 50 ns - Injection
22 July 2013 - e- cloud meeting
Sector 1-2
Fill 2240
DP after 5th injection
No DP for the rest of the gauges
There is a visible conditioning effect after the MD on 14 October with 25 ns

## Slide 11
DP with 25 and 50 ns - Injection
22 July 2013 - e- cloud meeting
Sector 1-2
MD 24 October 2011 – 25 ns
With 25 ns we observe DP in all the gauges

## Slide 12
DP with 25 and 50 ns - Injection
22 July 2013 - e- cloud meeting
Sector 1-2
Fill 2261
No e-cloud related DP observed in any of the gauges  Clear improvement after conditioning

## Slide 13
DP with 25 and 50 ns - Injection
22 July 2013 - e- cloud meeting
Sector 1-2
Fill 2736
DP after 5th injection
Nb≈1.47∙1011 ppb, but looking at the thresholds it seems that some deconditioning took place in gauge VGI.137.7R1.B

## Slide 14
DP with 25 and 50 ns - Injection
22 July 2013 - e- cloud meeting
Sector 1-2
Fill 3000
DP after 4th injection
DP after last injection
Nb≈1.52∙1011 ppb, DPFill3000> DPFill2736  some deconditioning without 25 ns beams?

## Slide 15
DP with 25 and 50 ns - Injection
22 July 2013 - e- cloud meeting
Nb≈1.65∙1011 ppb. It has a higher threshold. All gauges must be below this threshold
Sector 1-2
Fill 3286

## Slide 16
DP with 25 and 50 ns - Injection
22 July 2013 - e- cloud meeting
Sector 2-3
Fill 2124
Similar behavior as in sector 1-2

## Slide 17
DP with 25 and 50 ns - Injection
22 July 2013 - e- cloud meeting
Sector 2-3
Fill 2240
Similar behavior as in sector 1-2 (some conditioning observed after MD with 25 ns)

## Slide 18
MD 24 October 2011 – 25 ns
DP with 25 and 50 ns - Injection
22 July 2013 - e- cloud meeting
Sector 2-3
Again, with 25 ns we observe DP in all the gauges

## Slide 19
DP with 25 and 50 ns - Injection
22 July 2013 - e- cloud meeting
Sector 2-3
Fill 2261
Again, conditioning observed after MDs with 25 ns.
Not enough to condition gauge VGI.697.5L3.B below the 50 ns threshold

## Slide 20
DP with 25 and 50 ns - Injection
22 July 2013 - e- cloud meeting
Sector 2-3
Fill 2736
DP after 8th injection
Gauge VGI.697.5L3.B looks better conditioned than before!

## Slide 21
DP with 25 and 50 ns - Injection
22 July 2013 - e- cloud meeting
Sector 2-3
Fill 3000
Nb≈1.52∙1011 ppb, DPFill3000> DPFill2736  some deconditioning without 25 ns beams?

## Slide 22
DP with 25 and 50 ns - Injection
22 July 2013 - e- cloud meeting
Nb≈1.65∙1011 ppb. It has a higher threshold. Still some DP visible for VGI.697.5L3.B
Sector 2-3
Fill 3286

## Slide 23
DP with 25 and 50 ns - Injection
22 July 2013 - e- cloud meeting
After the 25ns MDs, there are two gauges still showing large DP
Sector 3-4
Fill 2261

## Slide 24
DP with 25 and 50 ns - Injection
22 July 2013 - e- cloud meeting
Nb≈1.65∙1011 ppb. It has a higher threshold, but still some gauges show DP
Sector 3-4
Fill 3286

## Slide 25
DP with 25 and 50 ns - Injection
22 July 2013 - e- cloud meeting
Sector 6-7
Fill 2124
Almost all gauges show DP before the 25 ns MDs

## Slide 26
DP with 25 and 50 ns - Injection
22 July 2013 - e- cloud meeting
Sector 6-7
Fill 2261
No visible DP after the 25 ns MDs  Enhanced conditioning in
sector 6-7?

## Slide 27
Outline
Pressure rise observations with 25 and 50 ns beams
Bunch intensity thresholds for 50 ns
Behavior during pre-ramp and energy ramp
Interpretation using PyECLOUD simulations
Conclusions
22 July 2013 - e- cloud meeting

## Slide 28
50 ns – Nb threshold
22 July 2013 - e- cloud meeting
Maximum activity for Nb=1.3-1.4
Thresholds around dmax ≈ 1.45 – 1.55
450 GeV

## Slide 29
50 ns - Thresholds
22 July 2013 - e- cloud meeting
450 GeV
dmax = 1.55
dmax,thres < 1.55

## Slide 30
50 ns - Thresholds
22 July 2013 - e- cloud meeting
450 GeV
dmax = 1.50
dmax,thres < 1.50 for Nb=1.3-1.4
dmax,thres ≈ 1.50 for Nb=1.0,1.15, 1.5 and 1.6

## Slide 31
50 ns - Thresholds
22 July 2013 - e- cloud meeting
450 GeV
dmax = 1.45
dmax,thres ≈ 1.45 for Nb=1.3-1.4

## Slide 32
50 ns – Nb threshold
22 July 2013 - e- cloud meeting
Maximum activity for Nb=1.3-1.4
Thresholds around dmax ≈ 1.45 – 1.55
4 TeV
N.B: The PY* has been reduced by a factor 10 to better assess de multipactig threshold

## Slide 33
50 ns - Thresholds
22 July 2013 - e- cloud meeting
Nb (∙1011 ppb) | dmax,thres (450 GeV) | dmax,thres (4 TeV)
1.0 | 1.50 | 1.50
1.15 | 1.50 | 1.45
1.3 | 1.45 | 1.45
1.4 | 1.45 | 1.45
1.5 | 1.50 | 1.45
1.6 | 1.50 | 1.50
emax=230 eV
sz,450 GeV= 10 cm
sz,4 TeV= 9.5 cm
ex= 2.4 mm
ey= 2.9 mm
Ø = 80 mm
The maximum e-cloud activity occurs at Nb = 1.3-1.4 ∙1011 ppb.
Why DPFill3000> DPFill2736 in most gauges  some deconditioning without 25 ns beams?
Thresholds are quite similar for all bunch populations.
Despite a stronger activity at 4 TeV (photoelectrons), threshold values are very similar at both energies

## Slide 34
Outline
Pressure rise observations with 25 and 50 ns beams
Bunch intensity thresholds for 50 ns
Behavior during pre-ramp and energy ramp
Interpretation using PyECLOUD simulations
Conclusions
22 July 2013 - e- cloud meeting

## Slide 35
Pre-ramp and ramp
22 July 2013 - e- cloud meeting
Sector 1-2
Fill 2261
In this example, none of the gauges exhibit DP during injection and all detect some DP during the ramp (at about 2.4 TeV)

## Slide 36
Pre-ramp and ramp
22 July 2013 - e- cloud meeting
Sector 2-3
Fill 2124
Not all gauges show a response to the ramp (especially the most active at injection)!
No clear response to the ramp
“Funny” DP behavior before the ramp

## Slide 37
Pre-ramp and ramp
22 July 2013 - e- cloud meeting
Gauge VGI.804.4R6.B in sector 6-7
Fill 2261
No e-cloud signs during injection and suddenly, before the ramp, there is an important DP
Good example of the “funny” prototype pre-ramp DP

## Slide 38
Pre-ramp and ramp
22 July 2013 - e- cloud meeting
Gauge VGI.141.6L4.B in sector 3-4
Fill 2124
“funny” pre-ramp behavior
P follows sz (usual behavior for many guages)

## Slide 39
22 July 2013 - e- cloud meeting
Sector 6-7
Fill 2124
No effect during the energy ramp! (only a bit for gauge VGI.172.7L7.B)
Pre-ramp and ramp

## Slide 40
Pre-ramp and ramp
22 July 2013 - e- cloud meeting
Sector 6-7
Fill 2261

## Slide 41
Pre-ramp and ramp
22 July 2013 - e- cloud meeting
Sector 6-7
Fill 2736
For this fill there is a DP with the ramp in gauges that never showed it
The DP during the ramp occurs earlier than “usual” (≈1.5 TeV)

## Slide 42
Pre-ramp and ramp
22 July 2013 - e- cloud meeting
Are these effects really generated by e-cloud?
Very different responses for different gauges
Very different responses for different fills (same gauges)
Different starting points (form 1.2 TeV to 2.9 TeV)
Thresholds at 450 GeV and 4 TeV are very similar
Alternative explanations
Photodesortion: does it present a threshold effect? Maybe:
  The SR monitor switches at about 1.5-2 TeV from ondulator to D3 [2,3]
Heating?
Orbit excursions?
Losses in collimators?

## Slide 43
Outline
Pressure rise observations with 25 and 50 ns beams
Bunch intensity thresholds for 50 ns
Behavior during pre-ramp and energy ramp
Interpretation using PyECLOUD simulations
Conclusions
22 July 2013 - e- cloud meeting

## Slide 44
Benchmarking
22 July 2013 - e- cloud meeting
First 50 ns MDs in November 2010:
  Exploration of e-cloud effects with train length
12+12
12+24
12+36

## Slide 45
Benchmarking
22 July 2013 - e- cloud meeting
First 50 ns MDs in November 2010:
  Exploration of e-cloud effects with train length
  Exploration of e-cloud effects with bunch intensity
0.6x1011 p/bunch
0.8x1011 p/bunch
1.1x1011 p/bunch

## Slide 46
Benchmarking
22 July 2013 - e- cloud meeting
First 50 ns MDs in November 2010:
  Exploration of e-cloud effects with train length
  Exploration of e-cloud effects with bunch intensity
  Exploration of e-cloud effects with the spacing between trains
38.85 ms
28.85 ms
8.85 ms
1.35 ms
1.85 ms
1 ms

## Slide 47
Benchmarking
22 July 2013 - e- cloud meeting
Following the methodology explained in [4], we get for gauge VGI.141.6L4.B:

## Slide 48
Benchmarking
22 July 2013 - e- cloud meeting
6ms
4ms
2ms
2.125 ms
Scrubbing run in April 2011 with 50 ns
With constant spacing between trains we would expect a linear behavior

## Slide 49
Benchmarking
22 July 2013 - e- cloud meeting
We observe a transient before the linear behavior is achieved
10/4/2011
19/5/2011

## Slide 50
Benchmarking
22 July 2013 - e- cloud meeting
We observe a transient before the linear behavior is achieved
This behavior cannot be fully reproduced by simulations:

## Slide 51
Benchmarking
22 July 2013 - e- cloud meeting
We observe a transient before the linear behavior is achieved
This behavior cannot be fully reproduced by simulations:

## Slide 52
Benchmarking
22 July 2013 - e- cloud meeting
The exact behavior for the first trains is not well reproduced by the simulations, whereas the linear dependence after some trains disregarding the concrete dmax and R values used is well reproduced.
Lower values of R give a better agreement for the shape presented by the first trains (change of slope). High values of R always exhibit a linear behavior from the first trains.
In the linear part, flux ratio lines for the benchmarking are expected to be ideally equal since there is not enough information to infer the reflectivity (due to a constant train spacing and the linear increases).
We observe a transient before the linear behavior is achieved
This behavior cannot be fully reproduced by simulations:

## Slide 53
Benchmarking
22 July 2013 - e- cloud meeting
Following the methodology explained in [4], we get for gauge VGI.141.6L4.B:

## Slide 54
Benchmarking
22 July 2013 - e- cloud meeting
10 April 2011
19 May 2011
(RESULTS WITH ECLOUD)
Clear conditioning effect
Following the methodology explained in [4], we get for gauge VGI.141.6L4.B:

## Slide 55
Benchmarking
22 July 2013 - e- cloud meeting
Following the methodology explained in [4], we get for gauge VGPB.2.5L3.B:
25 October 2011
(RESULTS WITH ECLOUD)

## Slide 56
Benchmarking
22 July 2013 - e- cloud meeting
Gauge VGPB.2.5L3.B
27 October 2011 – Physics fill 2261

## Slide 57
Outline
Pressure rise observations with 25 and 50 ns beams
Bunch intensity thresholds for 50 ns
Behavior during pre-ramp and energy ramp
Interpretation using PyECLOUD simulations
Conclusions
22 July 2013 - e- cloud meeting

## Slide 58
Conclusions
22 July 2013 - e- cloud meeting
Different gauges in the warm-warm straight sections show different behaviors
Conditioning effects seem to be stronger for some gauges
Thresholds are between 1.45 and 1.5 for Nb=1.0-1.6∙1011 ppb
Thresholds at 450 GeV and 4 TeV are very similar
There are some behaviors during pre-ramp and ramp that are not explained yet and cannot be reproduce with simulations
Benchmarking simulated flux and measured pressure can help monitoring the evolution of dmax and can explain some vacuum observations due to e-cloud

## Slide 59
22 July 2013 - e- cloud meeting
THANK YOU
FOR YOUR ATTENTION

## Slide 60
References
22 July 2013 - e- cloud meeting
[1] M. Facchini, R. Jung, R. Maccaferri, D. Tommasini and W. Venturini Delsolaro,
“The 5 T Superconducting Undulator for the LHC Synchrotron Radiation Profile Monitor,” EPAC-2004-WEPKF017.
[2] T. Lefevre, E. Bravin, G. Burtin, A. Guerrero, A. Jeff, A. Rabiller, F. Roncarolo and A. Fisher, “First Beam Measurements with the LHC Synchrotron Light Monitors,” Conf. Proc. C 100523 , IPAC’10, Kyoto, 2010, MOPE057.
[3] O. Dominguez and F. Zimmermann, “Benchmarking electron-cloud simulations and pressure measurements at the LHC,” CERN-2013-002, pp. 79-83.