## Slide 1: Summary of parameters for upgrade scenarios (PIC/US1/US2)
R. De Maria, G. Arduini, O. Brüning with input from: H. Bartosik, R. Bruce, S. Fartoukh, M. Fitterer, S. Gilardoni, M. Giovanozzi, M. Lamont, A. MacPherson, S. Redaelli, G. Rumolo and LIU/HL-LHC teams

## Slide 2: Best beam parameters from LIU (SPS extraction) - BCMS
 | Nbunch SPS ext [1011] | e*SPS-ext [mm] | Bunch population limit reached | Brightness limit reached
2015 (=Achieved in 2012) | 1.15 | 1.39 | none | none
No Upgrades (> 2016) | 1.31) | 1.28 | SPS | PS
Only LINAC 4 | 1.31) | 1.28 | SPS | PS
PIC | 1.31) | 1.28 | SPS | PS
US1 | 1.452) | 0.91 | SPS | PS/SPS
US1 with full SPS RF upgrade/no 2 GeV PSB upgrade | 2.03) | 2.18 | SPS | PS
US2-LIU | 2.03) | 1.37 | SPS | PS/SPS
US2-HL-LHC | 2.324) | 2.08 | SPS | No
from S. Gilardoni, G. Rumolo and LIU team
All schemes are based on BCMS scheme (maximum 240 (=5x48 from PS) bunches per SPS extraction)
Bunch population limited SPS RF low level/RF power
Bunch population limited SPS RF power (assuming low-level upgrade for US1)
Bunch population limited by SPS RF power (new limit after upgrade for US2) and longitudinal impedance. Could be increased (10-15%?) after further impedance reduction campaign. Still under investigation.
Would be feasible possibly with additional impedance reduction campaign in SPS
In all cases limited in bunch population!

## Slide 3: Best beam parameters in the LHC in collision (BCMS)
 | Nbunch LHC coll [1011] | e*LHC-coll [mm]
2015 (=Achieved in 2012) | 1.09 | 1.9
No Upgrades (>= 2016) | 1.24 | 1.54
Only LINAC 4 | 1.24 | 1.54
PIC | 1.24 | 1.54
US1 | 1.38 | 1.09
US1 with full SPS RF upgrade/no 2 GeV PSB upgrade | 1.90 | 2.62
US2-LIU | 1.90 | 1.64
US2-HL-LHC | 2.2 | 2.5
Assumed 5% losses from injection to start collision
Assumed 20% emittance blow-up from injection to collision

## Slide 4: Filling patterns with BCMS and max of 5 PS train per SPS extraction
 | KB1/B2 | kIP1/IP5 | kIP2 | kIP8
Filling 1 | 2508 | 2508 | 2108 | 2204
Filling 2 | 2508 | 2472 | 2087 | 2240
Filling 3 | 2508 | 2428 | 2061 | 2284
Filling 4 | 2508 | 2384 | 2035 | 2328
Filling 5 | 2652 | 2652 | 1839 | 1859
Abort Gap Keeper at 276 bunches
Max. 5 PS train/SPS extraction (=240 bunches)
No isolated bunches to ATLAS and CMS
12 bunches intermediate injection
Over injection over pilot
B. Gorini
Any preference from beam dynamics point of view  Beam-beam team
Any counter proposal?
Selected for the rest of the presentation

## Slide 5: Best beam parameters from LIU (SPS extraction) - Standard
from S. Gilardoni, G. Rumolo and LIU team
All schemes are based on standard scheme (maximum 288 (4x72 from PS) bunches per SPS extraction)
Bunch population limited SPS RF low level/RF power
Bunch population limited SPS RF power (assuming low-level upgrade for US1)
Bunch population limited by SPS RF power (new limit after upgrade for US2) and longitudinal impedance. Could be increased (10-15%?) after further impedance reduction campaign. Still under investigation.
Would be feasible possibly with additional impedance reduction campaign in SPS
 | Nbunch SPS ext [1011] | e*SPS-ext [mm] | Bunch population limit reached | Brightness limit reached
2015 (=Achieved in 2012) | 1.20 | 2.6 | none | none
No Upgrades (> 2016) | 1.31) | 2.44 | SPS | No
Only LINAC 4 | 1.31) | 1.65 | SPS | PS
PIC | 1.31) | 1.65 | SPS | PS
US1 | 1.452) | 1.37 | SPS | No
US1 with full SPS RF upgrade/no 2 GeV PSB upgrade | 2.03) | 2.85 | SPS | PS
US2-LIU | 2.03) | 1.88 | SPS | No
US2-HL-LHC | 2.324) | 2.08 | SPS | No

## Slide 6: Best beam parameters in the LHC in collision (Standard)
 | Nbunch LHC coll [1011] | e*LHC-coll [mm]
2015 (=Achieved in 2012) | 1.14 | 3.12
No Upgrades (>= 2016) | 1.24 | 2.93
Only LINAC 4 | 1.24 | 1.98
PIC | 1.24 | 1.98
US1 | 1.38 | 1.64
US1 with full SPS RF upgrade/no 2 GeV PSB upgrade | 1.90 | 3.42
US2-LIU | 1.90 | 2.26
US2-HL-LHC | 2.20 | 2.50
Assumed 5% losses from injection to start collision
Assumed 20% emittance blow-up from injection to collision
Tentatively the extrapolation of the (rather democratic) filling pattern from the 50 ns one used in 2012 should give 2760 bunches in total with 2760 colliding pairs in IP1/5 and 2548 colliding pairs in IP8. Asked Benedetto to verify.

## Slide 7: Integrated luminosity targets
 | No PIC Only gain in reduced SD | PIC | US1 | US2
Integrated luminosity by 2021/2035 | 300 | 300/1000 | 300/2000 | 300/3000
Number of years of operation after 2021 | >10 (shorter SD) | >10 (shorter SD?) | 10 | 10
Goal luminosity/year | 30-50 | 70 | 170 | 270
Assumptions:
  Luminosity in 2015=30 fb-1
  300 fb-1 by 2021. 400 would imply producing 340 fb-1 in the period 2016-2020 (< 5 years as there will be certainly a Shut-down)  >70 fb-1/year. Unrealistic if pile-up limited at 40
  2012 performance >23fb-1 in 2012 with peak luminosity of 7.7x1033 cm-2s-1 and average weekly luminosity of 0.72 fb-1. Expect 1.7x1034 cm-2s-1 from simple scaling (4 to 6.5 TeV, 50 to 25 ns, 1.6x1011 p/bunch to 1.15 x1011 p/bunch, 2.5 to 1.9 mm). This should give 40 fb-1 if scaled for 160 days of operation (vs. 200.5 in 2012). To be confirmed taking into account lifetimes, possible reduction in b*, etc.

## Slide 8: Operational parameters assumed so far
2012 data | 
Scheduled Physics Time for p-p luminosity production/year (Tphys) [days] | 200.5
Average Turn-Around Time (Taround-ave) [h] (faults subtracted) | 5.5
Minimum Turn-Around Time (Taround-min) [h] | 2.35
Average Fill length Tfill[h] | 5.96
Record Peak Luminosity (Lpeak) [1034 cm-2s-1] | 0.7695
Integrated Luminosity (Lint) [fb-1] | 23.269
Hübner Factor (=(Lint*1039)/(Lpeak*Tphys*24*3600)) | 0.175
Stable Beam Time Fraction [%] | 36.5
Fills that made it to physics (Nfill) | 295
Availability for successful fills = Nfill*(Taround-min+Tfill)/Tphys*100 [%] | 50
HL-LHC Assumptions | 
Scheduled Physics Time for p-p luminosity production/year (Tphys) [days] | 160
Minimum Turn-Around Time [h] | 3
Average Fill length [h] | 6
Hübner Factor | 0.2
Availability for successful fills – goal [%] | 50

## Slide 9: Beam/Machine parameters
Momentum [TeV/c] | 6.5
Max. Number of bunches/colliding pairs IP1/5 | 2508 (2592)
Total RF Voltage | 16
eL*[eV.s] at start of fill | 2.5
Bunch length (4 s)[ns]/ (r.m.s.) [cm] | 1/7.5
“Visible” cross-section IP1-5-8 [mb] for pile-up estimation | 851)
Likely 70-75 for LHCb at 6.5 TeV (R. Jacobsson)
Likely 4.5 for LHCb assuming the visible cross section above (R. Jacobsson)
Feasible?
Pile-up limit IP1 | 140
Pile-up limit IP5 | 140
Pile-up limit IP8 | 62)
Luminosity limit IP2 [1034 cm-2 s-1] | 0.0023)
Pile-up Density can be an issue here
Need limits from experiments!

## Slide 10: Beta* optimizations
Assuming ATS scheme (see S. Fartoukh – SLHC PR49 and Chamonix 2011) not only for chromatic aberrations but also because it minimize matching section aperture requirements.
Without crab cavities it is not optimal beta*<40cm (-> flat optics)
40/20 in reach if assuming 6.5TeV (strength limits in arc sextupoles and Q5 in IR6).
MS in Q10 gives 20% smaller beta* (or 20% arc beta blowup).
For 40/10, 30/7.5, 15/15 needs of matching section upgrade
Cleaning compatible with aperture at 12 sigma (with mech. tolerances and 3mm closed orbit and no impedance issues). New TCT needed for protecting D2-Q4, Q5. (R. Bruce, S. Redaelli).

## Slide 11: Aperture estimates for PIC layouts
M. Fitterer
Beta*<20cm needs MS in Q10 and new Q5 IR6

## Slide 12: Example flat beam optimization

## Slide 13: Assumed HW changes - PIC (c/o Lucio, Paolo)
IR (Interaction Region)
  New TAS, 60 mm
  New IT, D1, 150 mm aperture in P1 and P5
  New Correctors for IR (MCBX and HO): 150 mm
  Need for IR cryoplants? Not sure given larger aperture IT/D1  Laurent. Larger availability?
  New powering of IR magnets with EPC and DFBs on surface + SC links
  New powering with SC links at P7 (RR)
  New Cryoplant P4 for SCRF  down-time reduction (e.g. winter stop)
No other changes to the matching section:
  radiation issues due to the larger aperture of the triplet?

## Slide 14: Assumed HW changes - PIC (c/o Lucio, Paolo)
Collimators (all with buttons)
  Might need replacement due to change of jaw material properties (resistivity) and mechanical
  Replacement of secondaries with Molybdenum-Graphite jaws with Molybdenum coating for impedance reduction. Necessary for impedance at this stage?
  Possibly additional TCTs to protect D2, Q4, Q5 from async. dumps (R. Bruce, S. Redaelli)
Experiments capable of digesting pile-up of up to 140 after 2021
No BBLR  12 sigma beam-beam separation

## Slide 15: PIC (Machine availability to obtain 70 fb-1/year)
Flat optics (see S. Fartoukh – SLHC PR49 and Chamonix 2011) 40/20 cm
Nb=1.24x1011 (Limited by SPS RF) - BCMS
Minimum required availability for successful fills= 33%
 “Easy” to reach luminosity goal
Minimum emittance achievable in collision
Colour scale ranging between 30 and 50%

## Slide 16: PIC (Machine availability to obtain 70 fb-1/year)
Round optics 30/30 cm (see for ex. SLHC v2.0 see S. Fartoukh Chamonix 2010)
Nb=1.24x1011 (Limited by SPS RF) - BCMS
Minimum required availability for successful fills= 40%
 “Easy” to reach luminosity goal
Minimum emittance achievable in collision
Colour scale ranging between 30 and 50%

## Slide 17: PIC (Machine availability to obtain 70 fb-1/year)
Flat optics (see S. Fartoukh – SLHC PR49 and Chamonix 2011) 40/20 cm
Nb=1.24x1011 (Limited by SPS RF) - Standard
Minimum required availability for successful fills= 35%
 “Still Easy” to reach luminosity goal. Could be of interest
if additive sources of blow-up in the LHC are important
Minimum emittance achievable in collision
Colour scale ranging between 30 and 50%

## Slide 18: PIC (Machine availability to obtain 70 fb-1/year)
Round optics 30/30 cm (see for ex. SLHC v2.0 see S. Fartoukh Chamonix 2010)
Nb=1.24x1011 (Limited by SPS RF) – Standard
Minimum required availability for successful fills= 42%
 “Still Easy” to reach luminosity goal. Could be of interest
if additive sources of blow-up in the LHC are important
Minimum emittance achievable in collision
Colour scale ranging between 30 and 50%

## Slide 19: PIC Scenarios for consideration (for aperture, collimation, electron-cloud, beam-beam, impedance, cryo power estimates, etc,)
Nb LHC [1011] | e*coll [mm] | B-B Sep [s] | Min b* (xing/sep) [cm] | Xing angle [mrad] | Lpeak [1034 cm-2s-1] | Llev [1034 cm-2s-1] | tlumi [hours] | Levelling time [hours] | Machine eff. 6 h fills [%] | Machine eff. opt. fill length | Opt. Fill length [hours]
1.24 | 1.541) | 12 | 30/30 | 328 | 2.9 | - | 6.7 | - | 40.2 | 40.1 | 5.5
1.24 | 1.541) | 12 | 40/20 | 285 | 3.6 | - | 5.8 | - | 33.9 | 33.6 | 5.1
1.24 | 1.982) | 12 | 30/30 | 372 | 2.5 |  | 9.3 |  | 42.0 | 41.9 | 6.6
1.24 | 1.982) | 12 | 40/20 | 323 | 3.1 |  | 8.1 |  | 35.0 | 35.0 | 6.1
BCMS scheme (2508 colliding pairs in IP1/5)
Standard PS production scheme (2760 colliding pairs in IP1/5)
30/30 should not pose aperture problems
Issues for 40/20 optics:
  Need new TAN? Movable?
  Compatible with collimation/protection?
  Other aperture bottlenecks in the matching section? Need replacement/movement of other equipment?
  Radiation issues in the matching section due to larger aperture triplets

## Slide 20: PIC Summary
PIC goal can be met and exceeded if detector upgrade to 140 pile-up limit both for 30/30 and 40/20 optics (the latter might have some implications for aperture to be verified)
Standard PS production scheme not so attractive although it could be an option in case additive sources of emittance blow-up dominate

## Slide 21: Assumed HW changes – US1 on top of PIC (c/o Lucio, Paolo)
IR (Interaction Region)
  Need for IR cryoplants? Not sure given larger aperture IT/D1  Laurent. Larger availability?
Changes to the matching section/dispersion suppressors:
  BBLR (DC) to reach 10 sigma separation (design and effectiveness to be proven)
  TAN replacement due to larger than nominal luminosity (peak and integrated)? Will MS be still protected and kept far from radiation damage limit?
  Q5 in IR6 (strength limit at 6.6TeV, is it an issue?)
  MS at Q10 might be useful to push beta* further with few rotation of beam screen (to be verified) .
  SC links to remove EPC and DFB of MS: do we need it for US1?
Collimators (all with buttons)
  Replacement of secondaries with Molybdenum-Graphite jaws with Molybdenum coating for impedance reduction. Particularly interesting if the injector intensity limit could be lifted ( SPS power upgrade). Needed?
  Dispersion suppression collimation?
  Additional TCTs to protect D2-Q4 and Q5 (S. Redaelli, R. Bruce)

## Slide 22: US1 (Machine availability to obtain 170 fb-1/year)
Round optics 20/20 cm Nb=1.38x1011 (Limited by SPS RF)
Minimum required availability for successful fills= 61%
 No way to reach luminosity goal
.
Minimum emittance achievable in collision

## Slide 23: US1 (Machine availability to obtain 170 fb-1/year)
Flat optics 40/10 cm (should be best option for flat optics - Stephane)
Nb=1.38x1011 (Limited by SPS RF) - BCMS
Minimum required availability for successful fills = 49%
Short fill length due to IBS for small emittance
 Marginal to reach luminosity goal
Colour scale ranging between 40 and 50%

## Slide 24: US1 (Machine availability to obtain 170 fb-1/year)
Flat optics 40/10 cm (should be best option for flat optics, needs MS in Q10 and new Q5 in IR6- Stephane)
Nb=1.38x1011 (Limited by SPS RF) - Standard
Minimum required availability for successful fills = 47%
Short fill length due to IBS for small emittance
 Feasible to reach luminosity goal
Colour scale ranging between 40 and 50%

## Slide 25: US1 (Machine availability to obtain 170 fb-1/year)
Flat optics 40/10 cm (should be best option for flat optics, needs MS in Q10 and new Q5 in IR6- Stephane)
Nb=1.9x1011 (assuming SPS RF power upgrade and no PSB 2 GeV energy upgrade) - BCMS
Minimum required availability for successful fills = 41%
Longer fills (but still reasonable)
“Easy” to reach luminosity goal
Colour scale ranging between 40 and 50%

## Slide 26: US1 (Machine availability to obtain 170 fb-1/year)
Flat optics 40/20 cm (should be achievable with PIC - Stephane)
Nb=1.9x1011 (assuming SPS RF power upgrade and no PSB 2 GeV energy upgrade) - BCMS
Minimum required availability for successful fills = 49%
Longer fills
Marginal
Colour scale ranging between 40 and 50%

## Slide 27: From Stephane
Optimum LLBB Wire position is 10 beam-sigma! -> compensation of all resonance driving term.
  operating with small emittance beam options implies a close positioning of the wires that might be incompatible with the collimation system hierarchy! (TCTs are at 12sigma 3.5um, S. Redaelli)
  desire for operating with ‘large’ emittance beam parameters!

## Slide 28: US1 Scenarios for consideration (for aperture, collimation, electron-cloud, beam-beam, impedance, cryo power estimates, etc,)
Nb LHC [1011] | e*coll [mm] | B-B Sep [s] | Min b* (xing/sep) [cm] | Xing angle [mrad] | Lpeak [1034 cm-2s-1] | Llev [1034 cm-2s-1] | tlumi [hours] | Levelling time [hours] | Machine eff. 6 h fills [%] | Machine eff. opt. fill length | Opt. Fill length [hours]
1.38 | 1.641) | 10 | 40/10 | 253 | 6.9 | 5.1 | 5.3 | 1.6 | 47.4 | 47.1 | 5.1
1.9 | 2.622) | 10 | 40/10 | 320 | 7.4 | 4.6 | 8 | 3.7 | 41.8 | 41.4 | 7.2
1.9 | 2.622) | 10 | 40/20 | 310 | 5.4 | 4.6 | 8 | 1.2 | 49.4 | 49.4 | 6.2
Standard PS production scheme (2760 colliding pairs in IP1/5)
BCMS scheme (2508 colliding pairs in IP1/5)
Conceivable to anticipate SPS RF power upgrade with higher priority with respect to PSB energy upgrade?
40/20 does not pose additional questions as compared to PIC. Minimalistic solution on which we could build
Question marks for 40/10 optics:
  Would be interesting to explore benefits of a movable TAN
  Compatible with collimation/protection?
  Other aperture bottlenecks in the matching section? Need replacement/movement of other equipment?
  Need stronger Q5 in point 6?
  Need Sextupole at Q10?
  Rotation of beam screens?

## Slide 29: Summary (US1)
Small emittance beams from SPS imply low luminosity lifetime (IBS) and short fill length (<6 hours). Small emittance not so attractive…
Flat beam options can satisfy marginally the US1 goal with LIU-US1 parameters
Standard filling scheme can provide some margin there (larger emittance)
Flat beam options with BBLR can satisfy comfortably the US1 goal with the high intensity/larger emittance beam option that could be obtained with the SPS RF upgrade and would not require the PSB energy upgrade
  40/10 cm would allow to achieve the luminosity goal comfortably while the 40/20 cm option is marginal but this could be a minimalistic approach and possible phase on which building US2 scenario
The aperture bottleneck in the matching section are by order of descending criticality TAN/Q5/D2/Q4.
We should then definitely identify the minimum beta* reach for PIC (Triplet plus TAN)and evaluate how a movable TAN can optimize the performance reach for PIC, US1 and US2.

## Slide 30: US2 Scenarios
Target Integrated luminosity 3000 fb-1 in 2035. 270 fb-1 per year
Full upgrade package with crab cavities and high bunch intensity.
If pile-up limited, performance dominated by leveling time (10h with 2760 bunches needed to reach 50%). Crucial is the number of bunches.
If pile-up density limited, higher leveled luminosity possible (see S. Fartoukh coordination meeting) and significant improvement

## Slide 31: US2 round beam scenarios
Nb LHC [1011] | e*coll [mm] | B-B Sep [s] | Min b* (xing/sep) [cm] | Xing angle [mrad] | Lpeak [1034 cm-2s-1] | Llev [1034 cm-2s-1] | tlumi [hours] | Levelling time [hours] | Machine eff. 6 h fills [%] | Machine eff. opt. fill length | Opt. Fill length [hours]
2.2 | 2.51) | 12 | 15/15 | 590 | 20 | 5.1 | 8.2 | 11.2 | 57.3 | 47.3 | 13
2.2 | 2.52) | 12 | 15/15 | 590 | 18 | 4.6 | 8.2 | 11.2 | 63 | 52.4 | 13
1.9 | 2.261) | 12 | 14.5/14.5 | 570 | 17 | 5.1 | 7.3 | 8.7 | 57.3 | 50 | 10.7
1.9 | 2.013) | 12 | 14/14 | 546 | 19 | 4.9? | 6.7 | 9.1 | 59.4 | 51.5 | 10.8
1.9 | 1.652) | 12 | 13.5/13.5 | 505 | 22 | 4.6 | 5.7 | 8.9 | 63 | 55 | 10.5
1.9 | 1.652) | 12 | 13.5/13.5 | 505 | 22 | 6.64) | 4.6 | 5.6 | 44 | 43 | 7.4
Standard PS production scheme (2760 colliding pairs in IP1/5)
BCMS scheme (2508 colliding pairs in IP1/5)
H9 scheme (64 bunches for in SPS batches, filling scheme to be defined guessing 2660
Pille –up at 200 kissing scheme (see S. Fartoukh coordination meeting)
Using pp cross section 85 mb for pile –up and burn-off, assuming no closed orbit tolerances for the triplets
Open questions:
E-cloud effects on high intensity beams
Leveling efficiency (or about 1um orbit control at IP)
Crab cavities integration
Change to pile-up density limit and higher leveled luminosity?
TAN design (flat beams seem to mitigate the issues)
D2 field quality
Beam-beam aspect: crossing angle scaling, pacman effects for flat beams, DA
Magnet types for Q5 in IR1, IR5, IR6

## Slide 32: Validation
For the above scenarios the following aspects need to be further checked:
  Collimation settings and apertures
  Strength/ orbit and optics correction limitations
  Impedance
  Energy deposition
  Electron cloud effects
  Beam-beam aspects
  Cryogenics limits

## Slide 33
Reserve

## Slide 34: Approximations
IBS lifetime from scaling from nominal values
Luminosity lifetime obtained by considering the superimposition of exponential decays with time constants calculated for:
  Burn-off
  IBS longitudinal and horizontal emittance lifetime
  Radiation damping not considered yet
For the time being burn-off calculation based on inelastic cross-section (likely optimistic). Could be better to consider total cross section (at least include elastics and diffractives down to a certain angle/momentum deviation)

## Slide 35: US1 (Machine availability to obtain 170 fb-1/year)
Flat optics 30/10 cm Nb=1.38x1011 (Limited by SPS RF) - BCMS
Minimum required machine efficiency= 49%
Short fill length due to IBS for small emittance
 Marginal to reach luminosity goal
Colour scale ranging between 40 and 50%

## Slide 36: Break-down of Turn-Around (2012)
Phase | Duration [min]
Ramp down/pre-cycle | 45
Pre-injection checks and preparation | 15
Checks with set-up beam | 15
Nominal injection sequence | 20 (=2*12 injections*48.8s)
Ramp preparation | 5
Ramp | 13
Squeeze/Adjust | 20
Total | 133
A. Macpherson, M. Lamont

## Slide 37: Break-down of Turn-Around (HL-LHC)
Phase | Duration [min]
Ramp down/pre-cycle | 60
Pre-injection checks and preparation | 15
Checks with set-up beam | 15
Nominal injection sequence | 20 (=2*12 injections*48.8s)
Ramp preparation | 5
Ramp | 25
Squeeze/Adjust | 40
Total | 180
M. Lamont