## Slide 1: Summary of parameters for upgrade scenarios (PIC/US1/US2)
G. Arduini, O. Brüning, R. De Maria with input from: H. Bartosik, R. Bruce, S. Fartoukh, M. Fitterer, S. Gilardoni, M. Giovanozzi, M. Lamont, A. MacPherson, S. Redaelli, G. Rumolo and LIU/HL-LHC teams

## Slide 2: Hardware changes: PIC
  PIC
  Experiment compatible with 140 pileup-ev crossing
  New TAS, 60 mm, IT, D1, 150 mm, correctors
  New collimators with buttons, new materials for robustness and impedance, new TCTs in IR1-5 for D2-Q5 for cleaning and protection
  Arc sextupoles (MS) at 600A
  SC links in IR15, QRL
  New powering with SC links at P7 (RR)
  New Cryoplant P4 for SCRF
  Cryoplants in P1,5?
  Beam pipes and Y chamber between D1 and TAN?

## Slide 3: Hardware changes US1, US2
  US1
  All what it is in PIC
  BBLR in IR1 and IR5 located where effective
  US2
  All what it is in US1
  new matching section (D2, TAN, Q4, Q5) in IR1-5 with line shielding
  Stronger Q5 IR6
  Sextupoles in Q10 in Sectors 12,45,56,81
  Crab cavities
  800MHz?
  e-lens ?

## Slide 4: Assumed injector upgrades / feedback for LIU
PIC:
  LINAC4 and 160 MeV PS Booster injection
  LLRF SPS upgrade allowing pulsing the RF
US1:
  In order to achieve the target luminosity we would need (although not planned, presently) in addition:
    SPS RF upgrade (power and LLRF) to increase bunch population
    No PSB energy upgrade would be strictly required at this stage

## Slide 5: Assumed injector upgrades / feedback for LIU
US2:
  In addition to upgrades proposed for US1:
    PSB energy upgrade
    Further bunch population increase to 2.2x1011 p/bunch (further impedance reduction in SPS?)
  In all cases considered we assumed >2500 bunches per beam (2508 for BCMS and 2760 for standard production schemes)

## Slide 6: Scenarios for consideration with 140 pile-up limit (6.5 TeV)
 | Nb inj [1011] | e*inj [mm] | Nb coll [1011] | e*coll [mm] | B-B Sep [s] | Min b* (xing/sep) [cm] | Xing angle [mrad] | Lpeak [1034 cm-2s-1] | Llev [1034 cm-2s-1] | tlumi [h] | Lev. time [h] | Machine eff. 6 h fills [%] | Machine eff. opt. fill length [%] | Opt. Fill length [h] | Avg. Peak-pile-up density [ev./mm] | Target int. Lumi [fb-1/year]
PIC | 1.45 | 1.45 | 1.38 | 1.81) | 12 | 40/20 | 308 | 3.8 | - | 5.5 | - | 32.9 | 32.5 | 4.9 | 1.32 | 70
PIC | 1.45 | 1.85 | 1.38 | 2.222) | 12 | 40/20 | 342 | 3.4 | - | 7.3 | - | 32.8 | 32.8 | 5.8 | 1.06 | 70
US1 | 2.0 | 2.18 | 1.9 | 2.621) | 104) | 40/20 | 310 | 5.4 | 4.6 | 7.0 | 1.1 | 51.7 | 51.7 | 5.7 | 1.47 | 170
US2 | 2.32 | 2.08 | 2.2 | 2.52) | 12 | 15/15 | 5903) | 206) | 5.1 | 6.9 | 9.4 | 57.3 | 49.3 | 11.2 | 1.16 | 270
US2 | 2.32 | 2.08 | 2.2 | 2.52) | 104) | 30/7.5 | 3483) | 18.86) | 5.1 | 6.9 | 9.0 | 57.3 | 49.8 | 10.8 | <1.245) | 270
Using total bunch length of 1 ns and 2760 bunches where not specified differently.
Average pile-up density calculated but not included in the optimization.
BCMS scheme (2508 colliding pairs in IP1/5)
Standard PS production scheme (2760 colliding pairs in IP1/5)
Crab cavities used
BBLR used (parameters to be matched)
Crab kissing scheme could be used to reduce and the average peak pile-up density (S. Fartoukh)
Crab cavity RF curvature not included

## Slide 7: Scenarios for consideration with 140 pile-up limit (7 TeV)
 | Nb inj [1011] | e*inj [mm] | Nb coll [1011] | e*coll [mm] | B-B Sep [s] | Min b* (xing/sep) [cm] | Xing angle [mrad] | Lpeak [1034 cm-2s-1] | Llev [1034 cm-2s-1] | tlumi [h] | Lev. time [h] | Machine eff. 6 h fills [%] | Machine eff. opt. fill length [%] | Opt. Fill length [h] | Avg. Peak-pile-up density [ev./mm] | Target int. Lumi [fb-1/year]
PIC | 1.45 | 1.45 | 1.38 | 1.81) | 12 | 40/20 | 296 | 4.1 | - | 5.5 | - | 30.4 | 30.0 | 4.9 | 1.42 | 70
PIC | 1.45 | 1.85 | 1.38 | 2.222) | 12 | 40/20 | 330 | 3.7 | - | 7.3 | - | 30.4 | 30.4 | 5.8 | 1.15 | 70
US1 | 2.0 | 2.18 | 1.9 | 2.621) | 104) | 40/20 | 298 | 5.8 | 4.6 | 7.3 | 1.7 | 48.2 | 48.2 | 6.1 | 1.47 | 170
US2 | 2.32 | 2.08 | 2.2 | 2.52) | 12 | 15/15 | 5703) | 21.56) | 5.1 | 7.4 | 10.6 | 57.3 | 48.2 | 10.6 | 1.16 | 270
US2 | 2.32 | 2.08 | 2.2 | 2.52) | 104) | 30/7.5 | 3353) | 20.26) | 5.1 | 7.4 | 10.1 | 57.3 | 48.6 | 11.9 | <1.245) | 270
Using total bunch length of 1 ns and 2760 bunches where not specified differently.
Average pile-up density calculated but not included in the optimization.
BCMS scheme (2508 colliding pairs in IP1/5)
Standard PS production scheme (2760 colliding pairs in IP1/5)
Crab cavities used
BBLR used (parameters to be matched)
Crab kissing scheme could be used to reduce and the average peak pile-up density (S. Fartoukh)
Crab cavity RF curvature not included

## Slide 8: IBS (Rogelio, Octavio)
IBS at injection and during the ramp/squeeze (Rogelio, Octavio):
  Check longitudinal/RF parameters with Elena, Philippe
    Longitudinal parameters after capture
    Longitudinal blow-up at injection/during ramp
    RF voltage during the ramp. Can we limit the voltage to 10 MV?
  Provide table with emittances in collision with IBS only

## Slide 9: Aperture, Optics (Riccardo, Roderik)
Are the assumed parameters compatible with protection at 12 sigma? If not by how much we have to re-scale apertures?
Are the proposed optics compatible with the assumed upgrades? If not what are the modifications required?

## Slide 10: Energy deposition and radiation (Helmut, Luigi, Francesco)
Are the considered scenarios compatible with energy deposition and radiation limits in the various stages?
E.g.: can we run with larger triplets and no modifications to the matching section for PIC?
Do we need to modify the TAN for US1? Is a movable TAN a possible solution for US1 and US2?

## Slide 11: Transverse beam stability and heating (Elias, Benoit, Nicolas)
Are the above schemes compatible with transverse stability taking into account the collimator settings (assuming present jaw materials) presented by Roderik at the WP2 meeting on 13/9 and assuming operation up to 7 TeV?
At which stage do we need to have Molybdenum-Graphite jaws with Molybdenum coating for impedance reduction?
Is the octupole strength sufficient for all cases up to 7 TeV?
When heating is becoming an issue for the present hardware?

## Slide 12: Beam-beam (Sasha, Tatiana)
Is there any scheme among those proposed for BCMS (see next slide) that could pose problems for beam-beam effects?
What is the required beam-beam separation for flat optics and no BBLR? What is the dependence on intensity?
BBLR position vs emittance, flat beam crossing angle with BBLR. Is it compatible with collimation?

## Slide 13: Filling patterns with BCMS and max of 5 PS train per SPS extraction
 | KB1/B2 | kIP1/IP5 | kIP2 | kIP8
Filling 1 | 2508 | 2508 | 2108 | 2204
Filling 2 | 2508 | 2472 | 2087 | 2240
Filling 3 | 2508 | 2428 | 2061 | 2284
Filling 4 | 2508 | 2384 | 2035 | 2328
Filling 5 | 2652 | 2652 | 1839 | 1859
Abort Gap Keeper at 276 bunches
Max. 5 PS train/SPS extraction (=240 bunches)
No isolated bunches to ATLAS and CMS
12 bunches intermediate injection
Over injection over pilot
B. Gorini
Any preference from beam dynamics point of view  Beam-beam team
Any counter proposal?
Selected for the rest of the presentation

## Slide 14: Electron cloud effects (Elias, Giovanni2)
What are the heat loads that we can expect after scrubbing for the considered scenarios? And during scrubbing?
What is the required SEY to achieve in the triplets to avoid electron cloud build-up?
What are the electron cloud effects that we can expect after scrubbing during the various phases?
Countermeasures?

## Slide 15: Longitudinal parameters (Elena)
Are the above parameters consistent with longitudinal stability
What are the possible RF and longitudinal parameters at injection, after capture, during the ramp and at flat-top?
In which phases are we going to have controlled longitudinal blow-up? To which values?

## Slide 16
Reserve

## Slide 17: Beam/Machine parameters
Momentum [TeV/c] | 6.5 / 7
Max. Number of bunches/colliding pairs IP1/5 | 2508 or 2760
Total RF Voltage | 16
eL*[eV.s] at start of fill | 2.5
Bunch length (4 s)[ns]/ (r.m.s.) [cm] | 1/7.5
“Visible” cross-section IP1-5-8 [mb] for pile-up estimation | 851)
Likely 70-75 for LHCb at 6.5 TeV (R. Jacobsson)
Likely 4.5 for LHCb assuming the visible cross section above (R. Jacobsson)
Feasible?
Pile-up limit IP1 | 140
Pile-up limit IP5 | 140
Pile-up limit IP8 | 62)
Luminosity limit IP2 [1034 cm-2 s-1] | 0.0023)
Pile-up Density can be an issue here
Need limits from experiments!

## Slide 18: Aperture estimates for PIC layouts
M. Fitterer
Beta*<20cm needs MS in Q10 and new Q5 IR6

## Slide 19: Integrated luminosity targets
 | No PIC Only gain in reduced SD | PIC | US1 | US2
Integrated luminosity by end 2021/ end 2035 | 300 | 300/1000 | 300/2000 | 300/3000
Number of years of operation after 2021 | >10 (shorter SD) | >10 (shorter SD?) | 10 | 10
Goal luminosity/year | 40-60 | 70 | 170 | 270
Assumptions:
  Luminosity in 2015=30 fb-1
  310 fb-1 by the end of 2021. See M. Lamont 6th HL-LHC Coordination Group meeting 26.07.13.