## Slide 1: Beam Diagnostics PIC-US1-US2
Rhodri Jones (BE/BI)
3rd RLIUP Preparation meeting
11th September 2013

## Slide 2: Introduction
Current BI Work units
  Cryogenic BLMs for the Triplet
  BLM - Radiation Hard Electronics (IR3 / IR7 / LSS)
  Fast Wire Scanners
  New BPMs Q1 to Q5
  Luminosity Monitors
  Diagnostics for Crab Cavities
  Upgrade to Synchrotron Light Monitor
  General R&D (students & fellows)
  Halo Diagnostics
  Beam Gas Vertex Detector
  Second Undulator Per Beam
  Long Range Beam-Beam Compensator
Started
Started under LIU

## Slide 3: PIC #1
Cryogenic BLMs (1.7 MCHF)
  Current configuration in LSS not suitable for HL-LHC
    Cannot distinguishing dangerous losses from collision debris
  Radiation detectors being developed for cryogenic environment
    Placed inside cryostat of the new triplet magnets
    Dose measured more accurately represents correspond dose deposited in the coils
    Allows system to be used to for quench or damage prevention
Radiation Hard Electronics - IR3/IR7/LSS (0.6 MCHF)
  Quench levels for 7TeV close to noise level of the acquisition system
    Mainly due to long cables from detectors to front-end electronics
  Development started to implement this electronics in a radiation hard Application Specific Integrated Circuit (ASIC) to remove this limitation
New BPMs Q1 to Q5 (1.2 MCHF)
  New design required for new triplet layout
  Linked to any change in triplet

## Slide 4: PIC #2
Fast Wire Scanners (0.6 MCHF)
  Would allow average emittance measurement of every batch at injection
    Currently limited to first 2 batches injected
  Prototype for LS2 & full installation for LS3
Upgrade to Synchrotron Light Monitor (0.4 MCHF)
  Interlocked abort gap monitor
  Prototype for LS2 full installation LS3
New Wideband Pick-ups for Instability Monitoring (0.2 MCHF)
  Prototyping phase for crab cavity diagnostics
Long Range Beam-Beam Compensator Prototype (1 MCHF)
  On-going with installation foreseen between LS1 and LS2
Beam Gas Vertex Detector – BGV (200kCHF proto + Final)
  Prototype underway for installation during/after LS1
  Full system would significantly enhance emittance measurement capabilities

## Slide 5: US1
Luminosity Monitors (0.8 MCHF)
  New design required for new TAN Layout
  Linked to any change in TAN
Long Range Beam-Beam Compensator (4 MCHF)
  Design, production & installation of final system
  US1 or US2?
    Needs input from ABP
Halo Diagnostics (0.5 MCHF)
  Required for Long Range Beam-Beam Compensator & Hollow e-Beam Lens

## Slide 6: US2
Diagnostics for Crab Cavities (1.2 MCHF)
  Additional wideband pick-ups in the LSS
  Streak Camera diagnostic system
Upgrade to Synchrotron Light Monitor (0.8 MCHF)
  Linked to streak camera installation
    New light extraction system
    New optical dark room in UA43/47

## Slide 7: Summary
PIC (6.7 MCHF + BGV)
  Cryogenic BLMs for the Triplet & Radiation Hard Electronics (IR3 / IR7 / LSS)
  New BPMs Q1 to Q5
  Fast Wire Scanners
  Beam Gas Vertex Detector
  Upgrade to Synchrotron Light Monitor (Abort Gap diagnostics)
  BBLR Prototype
  R&D (students & fellows)
US1 (6.3 MCHF)
  Luminosity Monitors
  Long Range Beam-Beam Compensator (US1 or US2? – needs input from ABP)
  Halo Diagnostics
  R&D (students & fellows)
US2 (3 MCHF)
  Diagnostics for Crab Cavities (Assuming these are US2)
  Upgrade to Synchrotron Light Monitor (New optical hutch linked to crab cavity diagnostics)
  R&D (students & fellows)
Second Undulator Per Beam (1.7 MCHF)
  Not thought to be required – maybe for the SPS!
  Only required for measurement of single ion bunches at injection