## Slide 1: Parameters given by LIU for US1 and US2
1
Oliver Brüning BE-ABP CERN
Following discussions with Simone Gilardoni, Gianluigi Arduini, Stephane Fartoukh, Steffano Redaelli and John Jowett
2nd RLIUP Preparation meeting 14th August 2013

## Slide 2: Simone’s Table:
BCBMS  2592 bunches for trains of 48 bunches
following presentation by John Jowett @ LIU Technical meeting
and Christian Carli’s Chamonix 2011 presentations
Second but last Line refers to SPS LLRF upgrade
Last line refers to SPS upgrade with RF Power upgrade [ca. 25MCHF]

## Slide 3: General HL-LHC Assumptions for US1:
-New triplet magnets (PIC) -> smaller then nominal beta* reach
-No new magnets or movements in the matching section (we still need confirmation for minimum b* reach for round and flat beam operation)
-No Crab Cavities for US1
-Long Range Beam-Beam wire compensators at a position of ca. 10 sigma resulting in a required beam separation of 10 sigma (question was raised why we assume LRBB wires for US1 but not for US2).
-160 days of operation for physics production; -Beam energy = 6.5 TeV
-25ns scheme using BCMS -> 2593 bunches
-5% intensity loss from SPS extraction to LHC collisions
-Cases #a: 20% emittance blow-up from SPS extraction to LHC collisions (the question was raised if this is a realistic assumption for small emittance beams)
-Cases #b: emittances between 1.8 and 2 micrometer (between 50% and 75% blow up from SPS extraction to LHC collisions using Simone's table)

## Slide 4: Small Emittance Beams for US1: Case 1a
-US1 round beams; SPS with new LLRF system but without the RF power upgrade
-N at collisions = 1.37 10^11ppb
-n = 2593 (BCMS)
-emittance = 1.25 micrometer (20% blow-up wrt SPS extraction)
-round beams with beta* = 0.2m
-bean separation of 10sigma -> crossing angle of 300 microrad
-IBS growth rates of ca. 7h horizontally and 14h longitudinally (scaled)
-Peak Luminosity = 5.7 10^34 cm^-2s^-1
-leveling time of 0.6 h; Lumi decay time = 5 h; Turnaround time = 3 hours
-Total fill length (leveling + decay + turnaround) = 8.6h
-Integrated Lumi per fill = 0.68 fb-1; Lumi per year for perfect operation = 302fb-1
-Required efficiency for achieving 160fb^-1 per year = 53%
-Yearly integrated luminosity for a Hubner factor of 0.2 and using the peak luminosity = 158fb^-1
==> Case 1a can not reach the US1 goals & challenging from the IBS point of view.

## Slide 5: Small Emittance Beams for US1: Case 2a
-US1 round beams; SPS with new LLRF system but without the RF power upgrade
-N at collisions = 1.37 10^11ppb
-n = 2593 (BCMS)
-emittance = 1.25 micrometer (20% blow-up wrt SPS extraction)
-flat beams with beta* = 0.3m / 0.1m
-bean separation of 10sigma -> crossing angle of 245 microrad
-IBS growth rates of ca. 7h horizontally and 14h longitudinally (scaled)
-Peak Luminosity = 8.8 10^34 cm^-2s^-1
-leveling time of 2.4 h; Lumi decay time = 5 h; Turnaround time = 3 hours
-Total fill length (leveling + decay + turnaround) = 10.4h
-Integrated Lumi per fill =1 fb-1; Lumi per year for perfect operation = 369fb-1
-Required efficiency for achieving 160fb^-1 per year = 43%
-Yearly integrated luminosity for a Hubner factor of 0.2 and using the peak luminosity = 123fb^-1
==> Case 2a could reach the US1 goals but challenging from the IBS point of view.

## Slide 6: Small Emittance Beams for US1: Case 1b
-US1 flat beams; SPS with new LLRF system but without the RF power upgrade
-N at collisions = 1.37 10^11ppb
-n = 2593 (BCMS)
-emittance = 1.8 micrometer (73% blow-up wrt SPS extraction)
-round beams with beta* = 0.2m
-bean separation of 10sigma -> crossing angle of 360 microrad
-IBS growth rates of ca. 13h horizontally and 22h longitudinally (scaled)
-Peak Luminosity = 4 10^34 cm^-2s^-1
-No leveling; Lumi decay time = 5 h; Turnaround time = 3 hours
-Total fill length (leveling + decay + turnaround) = 8h
-Integrated Lumi per fill =0.45 fb-1; Lumi per year for perfect operation = 215fb-1
-Required efficiency for achieving 160fb^-1 per year = 74%
-Yearly integrated luminosity for a Hubner factor of 0.2 and using the peak luminosity = 110fb^-1
==> Case 1b can not reach the US1 goals but OK from the IBS point of view.

## Slide 7: Small Emittance Beams for US1: Case 2b
-US1 round beams; SPS with new LLRF system but without the RF power upgrade
-N at collisions = 1.37 10^11ppb
-n = 2593 (BCMS)
-emittance = 1.8 micrometer (73% blow-up wrt SPS extraction)
-flat beams with beta* = 0.3m / 0.1m
-bean separation of 10sigma -> crossing angle of 295 microrad
-IBS growth rates of ca. 13h horizontally and 22h longitudinally (scaled)
-Peak Luminosity = 6.7 10^34 cm^-2s^-1
-leveling time of 0.9 h; Lumi decay time = 4 h; Turnaround time = 3 hours
-Total fill length (leveling + decay + turnaround) = 7.9h
-Integrated Lumi per fill =0.66 fb-1; Lumi per year for perfect operation = 319fb-1
-Required efficiency for achieving 160fb^-1 per year = 50%
-Yearly integrated luminosity for a Hubner factor of 0.2 and using the peak luminosity = 168fb^-1
==> Case 2b could reach the US1 goals & OK from the IBS point of view.

## Slide 8: Discussions with Stephane:
-Best option for flat beam ratio of 10cm / 40cm
-Flat beam ration of 20cm / 40cm should be compatible with PIC
-The aperture bottleneck in the matching section are by order of descending criticality TAN/Q5/D2/Q4.
 We should then definitely use this at a starting point and then look at
what needs to be changed in the MS to reach 37cm/10cm