LIU-PS Meeting 59 (6 August 2013)
Ecloud simulations of PS chambers
G. Iadarola, S. Rioja Fuentelsaz, G. Rumolo
Many thanks to:
O. Berrig, S. Gilardoni, G. Sterbini, C. Yin Vallgren

---
Ecloud simulations of PS chambers
- Outline
  - 0.- Introduction
  - 1.- Combined function magnets of the PS
  - 2.- Magnetic field along the PS
  - 3.- Chambers for the magnets
  - 4.- E-cloud thresholds for a pattern train
  - 5.- Energy loss per metre due to e-cloud
  - 6.- Stable phase shift

---
0.- Local view e-cloud
Thanks to the new e-cloud monitor we are going to be able to see what really happens in the presence of a magnetic field
E-cloud monitors:
SS84 (drift section) (CHAMBER st)
SS98 (drift section) (CHAMBER st)
MU98 (ext_op) (R, foc) (CHAMBER st)
[ ] “Comparison of Enamel and Stainless Steel Electron Cloud Clearing Electrodes Tested in the CERN Proton Synchrotron”
[ ] "Electron cloud detection and characterization in the CERN Proton Synchrotron”

---
0.- Integrated view e-cloud
40 Mhz RF cavities
SS77 and SS78
Only one is used
(the other one: spare)
What the beam sees is an integrated effect (and not a local one) of the ecloud. We want to relate the energy losses with the shift of the stable phase.
An idea to have an integrated view of the ecloud along the CERN PS is measuring the stable phase shift of the proton bunches (through the 40Mhz RF system)
[ ] “The PS complex as proton pre-injector for the LHC: design and implementation report”

---
1.- Combined function magnets of the PS
Each half unit is made of 5 blocks.
Each half unit is a focusing or defocusing depending on the shape of the edge of yoke.
If the proton beam was going outside (+u_z) (clockwise, then these were “inside units”):
> OPEN --> Hor defocusing
> CLOSED --> Hor focusing
There are 100 magnet units:
> R: 35 of the 100 magnets
> S: 15 of the 100 magnets
> T: 35 of the 100 magnets
> U: 15 of the 100 magnets

---
1.- Combined function magnets of the PS
BLOCK interior_open -->	defocusing part of T & U units
BLOCK interior_closed ->	focusing part of T & U units
BLOCK exterior_open -->	focusing part of R & S units
BLOCK exterior_closed ->	defocusing part of the R & S units

---
2.- Magnetic field along the PS
>Sense of rotation:	CLOCKWISE;
>External ring:
Quadrupole field
Hor Foc (blue)
Hor Def (red)
>Next ring:
The 4 types of main	magnets
(R red,S cyan,
T blue,U green)
>Next ring:
Straight sections
(Drift sections,
more magnets,
RF system...)
Courtesy of G. Sterbini

---
3.- Chambers for the magnets
>Total length of PS:
2*pi*100m = 628m
>Total length of main magnets:
100*4.94m = 494m
>It's the 78.6%
>Total length of straight sec:
(every 4 short: 1long)
80*1.05+
+20*2.45=
=133m
>It's the 21.2%
Courtesy of G. Sterbini

---
3.- Chambers for the magnets
> STANDARD:	68 in the 100 magnets
So 54% in length of the PS
38 outside (R & S) and 30 inside (T&U)
> SP. EXT:	16 in the 100 magnets
So 13% in length of the PS
8 outside (R & S) and 8 inside (T&U)
> SP. INT:	6 in the 100 magnets
So 5% in length of the PS
3 outside (R & S) and 3 inside (T&U)
The +u_z axis is going outside the paper, so does the proton beam (clockwise sense of rotation). Then the centre of the machine would be on the left of the paper.

---
3.- Chambers for the magnets
   These were the most common chambers for the main magnets, the remaining 10 magnet chambers form less than the 8% in length of the accelerator. They are:
   MU14, MU15, MU16, MU41, MU42, MU43, MU56,	MU57, MU60, MU62.

---
3.- Chambers for the magnets
TEN SECTORS OF THE CERN-PS
>External ring:
The 4 types of main magnets
(R red,S cyan,
T blue,U green)
>Internal ring:
The most common chambers for	the magnets
(“st” yellow,
“sp.ext” magenta,
“sp.int” orange)

---
3.- Chambers for the magnets
> FOUR STANDARD:
Very similar behaviour for the four magnetic fields. This is why here we only present one kind of magnetic field (focusing part of outside units - R & S -)
> FOUR SP. EXT:
Up to now we have not simulated this chamber.
> FOUR SP. INT:
We only have simulated one magnetic field for this chamber.

---
4.- E-cloud thresholds for a pattern train
- The e-cloud thresholds depend on several parameters, including:
  - Pattern train (72bunches + 12 empty buckets)
  - Chamber shape
  - Magnetic field
- We have done simulations for:
  - Chamber ST. (4 magnets)(R,S,T,U)
  - Chamber ST. (drift section)(SS98)
    Chamber SP.INT. (focusing part of T & U)(MU57)

---
4.- E-cloud thresholds for a pattern train
We are only interested in the last 6 ms of the cycle (i.e. after the last splitting), when we have 72 bunches and 12 empty buckets. Note that 1 turn is 100*pi*2 metres and takes 2.1 microseconds.

---
4.- E-cloud thresholds for a pattern train
To make a reference to the multipacting effect (avalanche) we define the thresholds as a max density of 1e+07 e/m. Bellow this value the ecloud grows linearly, and above this value it grows exponentially reaching densities several orders of magnitude higher.

---
4.- E-cloud thresholds for a pattern train
If SEY=1.6 we would see multipacting effect in the last 2ms (4sigma=12ns) of the cycle.

---
4.- E-cloud thresholds for a pattern train
If SEY=1.6 we would see multipacting effect in the last 2ms (4sigma=12ns) of the cycle.

---
4.- E-cloud thresholds for a pattern train
If SEY=1.6 we would see multipacting effect after the last splitting (6 last miliseconds of the cycle). This case is a drift section (no mag field)

---
4.- E-cloud thresholds for a pattern train
When a magnetic field is present on the chamber, the multipacting thresholds are almost independent on the bunch intensity.

---
4.- E-cloud thresholds for a pattern train
When a magnetic field is present on the chamber, the multipacting thresholds are almost independent on the bunch intensity.

---
4.- E-cloud thresholds for a pattern train
In the case of a drift section, the thresholds decrease with the bunch intensity.

---
5.- Energy loss per metre due to e-cloud
An idea to have an integrated view of the ecloud along the CERN PS is through the 40Mhz RF system
The V_rf voltages in this graph are the “peak” values (and not the “rms” values)

---
5.- Energy loss per metre due to e-cloud

---
5.- Energy loss per metre due to e-cloud
Example for lhc25 nominal beams. Evolution of ecloud with respect to the time.

---
5.- Energy loss per metre due to e-cloud
Example for lhc25 nominal beams. Bunch by bunch proton energy losses in 1 turn (at flat top)

---
6.- Stable phase shift
For each bunch, the step in energy in each passage through the accelerating station is given by:
Even when we are not accelerating the bunches (we are at the flat top energy) we are going to see an stable phase shift.

---
6.- Stable phase shift
Example for lhc25 nominal beams. Bunch by bunch stable phase shift in 1 turn (at flat top)

---
6.- Stable phase shift
As we have not finished all the simulations,
we take the worst scenario (least ecloud signal)
(least stable phase shift)
REAL ACCELERATOR	SIMPLIFIED ACCELERATOR
4 magnetic fields on main magnets	Only one kind of magnetic field (“ext op”)
Straight Sections with also magnetic fields	No SS (more ecloud when are DRIFT SECT)
At least 4 kinds of chambers	Only one kind of chamber(“st”)
494m of MU's and 133m of SS's	628 m of hor focusing part of R&S units

---
As we are taking the worst scenario (because when a magnetic field is present, the multipacting thresholds are higher and then the ecloud signal is lower) we are going to predict downward the phase stable shift.
RANGE OF INTENSITIES
1.0e+11 ppb
1.3e+11 ppb => nominal lhc25 beams
1.9e+11 ppb
2.6e+11 ppb => HL-LHC beams
From a benchmarking on SS98 we think that SEY is next to 1.6 on CERN-PS
[ ] “Comparison between electron cloud build-up measurements and simulations at the CERN PS”

---
6.- Stable phase shift
If SEY=1.6 we would not see an stable phase shift until the last 2ms (4sigma=12ns) of the cycle.

---
6.- Stable phase shift
If SEY=1.6 we would not see an stable phase shift until the last 380 microseconds (4sigma<11ns) of the cycle.

---
6.- Stable phase shift
If SEY=1.6 we would not see an stable phase shift until the last 380 microseconds (4sigma<11ns) of the cycle.

---
6.- Stable phase shift
If SEY=1.6 we would not see an stable phase shift until the last 380 microseconds (4sigma<11ns) of the cycle.

---
Conclusions
Except for an intensity of 1.0e+11 ppb we would see an stable phase shift (around 0.5 degrees) for the last 380 microseconds of the cycle.
But this was a downward prediction because we supposed than all the machine was made of main magnets (only one field simulated) and there is more ecloud signal in the drift sections (i.e. in some straight sections)

---
Future work
When we will finish all the simulations
SIMPLIFIED ACCELERATOR	REAL ACCELERATOR
Only one kind of magnetic field (“ext op”)	4 magnetic fields on main magnets
No SS (more ecloud when are DRIFT SECT)	Straight Sections with also magnetic fields
Only one kind of chamber(“st”)	At least 4 kinds of chambers
628 m of hor focusing part of R&S units	494m of MU's and 133m of SS's

---
BUCKUP SLIDES

---
3.- Chambers for the magnets
Injection and Extraction only possible through inside Magnet Units (T or U) or Straight Sections
>MU41...MU43
  (injection p from Linac II--> booster)
>SS74 (injection e- to LEP)
>SS92 (injection e+ to LEP)
>MU56...MU63
  (slow extraction to East Hall)
  (magnetic septum SS57)
  (magnetic septum SS61)
  (bumpers SS53, SS59, SS61, SS67)
  (extractor septum SS61)
>MU22...MU25
  (slow extraction to East Hall)
  (electrostatic septum SS23)
  (bumpers SS19, SS27)
[ ] “Fifty years of the CERN Proton Synchrotron: Volume 1” Chapter “Beam extraction”

---
3.- Chambers for the magnets
Injection and Extraction only possible through inside Magnet Units (T or U) or Straight Sections
>MU22...MU25
  (CT extraction to SPS)
  (bumper SS21)
  (quadrupole -deflector- Q25)
>MU26..MU33
  (injection ions from Linac III--> LEIR)
  (CT extraction to SPS)
  (electrostatic septum SS31)
>MU6...MU7
  (CT extraction to SPS)
  (quadrupole -deflector- Q5))
  (bumper SS9)
>MU14...MU19
  (CT extraction to SPS)
  (magnetic septum SS16)
  (extractor septum SS16)
[ ] “A modulated fast bump for the CPS Continuous Transfer” 1977