## Slide 1: CTF3 in 2007 Optics Measurements
1
Caterina Biscari, Yu-Chiu Chao, Roberto Corsini, Anne Dabrowski, Steffen Doebert, Andrea Ghigo, Seyd Hamed Shaker, Piotr Skowroński, Frank Tecker
CLIC Meeting
CERN 29 February 2008

## Slide 2: 2007 Run
Planned for 22 weeks
  Excluding PETS only running
Very uneasy run due to
  Large number of hardware failures
    For most of the time mal behaving gun
      Periods of large current variation from shot to shot, sudden jumps of the average current, large current change along the pulse
    Total 6 weeks of down-time
      The run extended for additional 4 weeks because of that
      3 vacuum leaks
      2 klystrons out due to failures of parts we didn’t have in spare
      Gun cathode exchanged
      And many, many, many more!
  Instability induced by the wake in the Combiner Ring RF deflectors
  Bugs in the machine
    Swapped cables between devices
  Bugs in the online model
    Wrong calibration factors for some magnets

## Slide 3: Achievements
We have achieved the main goal: the recombination
  To reduce the effect of the instability cut a gap within the trains with the extraction kicker

## Slide 4: Achievements
Finally we have understood what prevented the beam from staying in the Combiner Ring for more than 2 turns: Instability
current
Vpos
Hpos

## Slide 5: It is not fast ion instability
29 Feb 2008
CLIC Meeting, CERN
5
RF deflector in DL set up to kick out every second bunch from the train
    Same charge per bunch
    Twice smaller current
    Twice bigger spacing between bunches
If it is fast ion instability then the frequency should change
  It is not
3GHz
1.5GHz

## Slide 6: The Optics Studies
All along the Run 2 we were performing the machine measurements
  Dispersion
  Tunes
  Response Matrix
  Combiner Ring Length
  Bunch length
They allowed us to discover many discrepancies in the machine and in the model
  Of course, that is why we do them

## Slide 7: Nominal Optics Linac
7
We measure what comes out of the buncher and rematch linac to regular optics

## Slide 8: Nominal Optics CT Line
20 Jan 2008
CTF3 Collaboration Meeting, CERN
8
Optics in the Stretcher Chicane is adjusted to the required R56

## Slide 9: TL1 and CR optics
The optics in the Combiner Ring is adjusted to
  The beam energy
  Wiggler current
In TL1 the isochronous optics is matched to the CR optics

## Slide 10: Quad Scans
We measure beam parameters with quad scans
  Measure beam profile for different settings of the upstream quad(s)
  Beam size depends quadratically with quad strength
  Parabola parameters are linked to the Twiss parameters just before the quad

## Slide 11: Quad Scans
We can do quad scans at few locations
  Girder 4 of the Linac
  Girder 10 of the Linac
  Girder 4 of CT line
  Beginning of TL1 in CTS
  After injection in Combiner Ring
    Sending the beam to the screen in CRM
      Tricky since dipole can not be demagnetized
Routinely the beam parameters are measured at 2 and 3 or 4 during beam setup

## Slide 12: Emittances
We have made a lot of quad scans during the last year, however, we never performed detailed study of the emittances
  The data points we have are taken
    With completely different conditions
    Sometimes with wrongly calibrated screens
    Almost never at a couple of locations the same day

## Slide 13: Dispersion
Dispersion is measured in two ways
  By observing the orbit change while setting all elements strengths proportionally higher or lower
    The lattice becomes mismatched to the beam energy
    Specialized MatLAB script doing the job
      Read the current setting of the magnets
      Get the reference orbit over several shots
      Scale all the elements in the specified range about desired value(s)
      Get the orbit over several shots
      Return to the original setting
      Prepare the input for MADX and run the model
      Plot the measured and the model dispersions together
  Measuring the position jitter from pulse to pulse
    RMS of a pickup position reading is proportional to the dispersion
    The pattern is normalized so the dispersion in the Stretcher chicane agrees with the model
      It is well controlled there
    It is much less precise method comparing to the former one, however, it allows to monitor dispersion on-line
      Facilitates the beam setup

## Slide 14: Dispersion in the CT line
Measured dispersion in the Stretcher Chicane does not agree with the model
  Discrepancy tracked to the quadrupole CT.QFE 0250
  Fudge factor 0.86 applied in the model
Measured and corrected model dispersion

## Slide 15: Dispersion in TL1 and CR
Dispersions agrees with the model within the error-bars
CR
TL1
TL1

## Slide 16: Response Matrix
Register the orbit position in all BPMs
Change setting of one (or more) corrector
Look into orbit position change (difference)
Compare with the model predicted change
If they do not agree, the model does not describe the machine correctly
  It is easy to localize the region where the error occures
    Between the element the discrepancy occurs first and the previous one or two
  Even if there are more errors we still can find them
    If the kick is applied after the first error the pattern should agree
The measurements were automatized with a MatLAB script

## Slide 17: The Response Matrix Study
The measurements made during Run 1 traced us to
  Wrong calibration of the J type quads about 6%
  A few correctors with wrong polarities
The first data
Problem in the wiggler area
Corrected J type

## Slide 18: The new wiggler model
Caterina Biscari has prepared detailed wiggler model based on the magnetic measurements of the device
  It describes more correctly the wiggler vertical focusing
  Still there is not understood discrepancy in horizontal
  Need more detailed measurements for different wiggler currents
    The most importantly with wiggler off

## Slide 19: Discrepancy in 2nd short section
Increasing 820-880 doublet by 15% gives good agreement between the data and the model
CR.QFJ0880
CR.QFJ0820

## Slide 20: Tunes
We measure tunes doing FFT of a pickup analog signal
  Using a scope
Measure distance between the main frequency peak frev and the second highest fQ Q = N ± (frev- fQ)/frev N is an integer that is obtained as the number of the orbit oscillations around the ring
To distinguish the sign observe how frev- fQ changes while changing a quad strength

## Slide 21: Combiner Ring Tunes
The measured tunes does not agree with the model
  What only confirms the observations from the response matrix measurements

## Slide 22: Measurement of the ring length
BPR: RF Phase Monitor
Gives sum of the beam induced signal and internal frequency (3GHz)
If beam has also 3GHz it measures phase offset between the two signals
Simulated signal
Combination factor 4
Combination factor 4 with + 5 error
1st turn
2nd turn
3rd turn
4th turn

## Slide 23: BPR measurement
Short pulse for many turns
FFT of the BPR signal gives the ring length
  frev gives total ring length LR= (N – 1/CF) lRF
  Df gives fractional part of ring length 1/CF lRF
Df = (A - B) / 2
A
B
Suppressed revolution frequency
fREV =(A + B) / 2
BPR signal
FFT

## Slide 24: BPR measurement: frev
21 Jan 2008
Measure for different values of the wiggler current
A
fREV =(A + B) / 2
Theoretical fREV
B
fREV =(A + B) / 2
Theoretical fREV
Measured LR = c b / fREV
Theoretical LR = (848 - 0.225) lRF
LR = (849 - 0.225) lRF

## Slide 25: BPR measurement: Df
expected
measured
Measured Lfrac = - 1/CF lRF
CF 5, - 1/5 lRF
CF 4, - 1/4 lRF
Expected ring length for nominal wiggler current
About 1.5 mm
C. Biscari

## Slide 26: Bunch length
Chart: 
| -16 | -13 | -10 | -8 | -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8 | 10 | 13 | 16
RF Deflector Phase(degree) | 0.1838 | 0.27796 | 0.57229 | 0.78388 | 1.9911 | 1.2326 | 9.5546 | 31.6704 | 33.9312 | 61.7052 | 68.2023 | 64.6791 | 40.0269 | 35.2117 | 26.293
 | 5.5732e-06 | 0.00031711 | 0.010194 | 0.075042 | 0.4286 | 1.8992 | 6.5296 | 17.4169 | 36.0443 | 57.8737 | 72.095 | 69.6801 | 52.2506 | 21.0815 | 4.8052
Intensity
Bunch length(mm)
Klystron 13 Phase(degree)
RF Deflector Phase(degree)
lb= 2.68±0.60 mm
The bunch length achieved by measuring the intensity of a thin band at middle of screen for each RF deflector phase and fitting a Gaussian distribution. The standard deviation of this chart is related to bunch length by c/f constant. c is speed of light and f=1.5 GHz is frequency of RFD. The errors are large due to the beam jitter but is good for first measurement by this method

## Slide 27: Conclusions
The optics tests are indispensable for
  A good control over the machine
  Fishing out all the machine and the model errors
The measurements we did helped to solve a number of problems and show that there are still more
We were not given a chance to perform enough measurements up to now and to gather enough high quality data for offline analysis
  Instability of the machine
  A bounty of hardware failures
  The instability in Combiner Ring
During the beginning of the next run we plan a campaign for systematic optics measurements which would hopefully let us find all the remaining optics errors

## Slide 28: Conclusions - Online Tools
Already during the last run we developed set of software tools that allow to test quickly the optics and compare immediately the results with the model
  Dispersion measurements
    Magnet scaling
    Using position jitter from shot to shot
      Online dispersion monitoring
  Response Matrix measurements
We need set of more robust tools
  Which would speed up the measurements and analysis
  They are currently under development

## Slide 29: Outlook- New Tools
Quad scans
  Precise fit is obtained only if the shape around the parabola minimum is measured
    Often, it is difficult to find a good range for quad strengths
    In consequence we do not do them sufficiently often because it takes too much time
      Currently it is at least one hour exercise
  We want to make a new tool which would find a range itself and eventually obtain Twiss parameters in a range of quads

## Slide 30: Outlook- New Tools
“Orthogonal” response matrix
    In preparation by Chao (JefLAB)
    Complete & even coverage of phase space what would help to isolate the sources of errors
    See Chao’s talk from CTF3 technical meeting in January for more details
BPMs
Correctors
X
X’
X
X’
M
Global transfer matrix determination
Orbits on both ends determined on equal footing  Rigorous error analysis
Orthogonal phase space coverage
Large signal-to-noise ratio
Symplectification
Diagonally reflected scan pattern to combat pulse-to-pulse jitter, and increase signal amplitude.

## Slide 31: Outlook- New Tools
Codes for measurement automatization of
  Bunch length with RF deflector – Hamed
  Bunch length with RF pick-up – Anne
  Energy and energy spread with the new segmented dump – Anne
Code for Combiner Ring orbit correction – Caterina and Simona