## Slide 1: LHC Operation: Past and Future – part 1
After a successful first running period, LHC is now well into a two year shutdown for extensive consolidation. A pedagogical overview of the machine, its operating principles, its systems and underlying accelerator physics is presented. Performance past and future is discussed. (These lectures will be presented in three parts.)
Mike Lamont with acknowledgements to all the people whose material I’ve used
(including Ralph Assmann, Luca Bottura, Heiko Damerau, Bernhard Holzer, Rende Steerenberg, Ralph Steinhagen, Jorg Wenninger...)
Chris Henschke

## Slide 2: Contents
Base
  Magnets, cryogenics, QPS
  Optics etc.
  Beam (injectors, LHC)
  Crossing angles, squeeze…
  RF, Instrumentation
Pulling it together
  The nominal cycle
  Machine protection
Performance
  Past performance
  Limitations
  LS1
  The future and beyond

## Slide 3
Beam dumps
RF
Collimation
Collimation
1720 Power converters
> 9000 magnetic elements
7568 Quench detection systems
1088 Beam position monitors
~4000 Beam loss monitors
150 tonnes Helium, ~90 tonnes at 1.9 K
140 MJ stored beam energy in 2012
450 MJ magnetic energy per sector at 4 TeV
LHC: big, cold, high energy
Injection B2
Injection B1

## Slide 4
2008
2009
2010
2011
LHC Timeline
September 10, 2008
First beams around
September 19, 2008
Disaster Accidental release of 600 MJ stored in one sector of LHC dipole magnets
August 2008
First injection test
August, 2011
2.3e33, 2.6 fb-1
1380 bunches
October 14 2010
1e32
248 bunches
November 2010
Ions
March 30, 2010
First collisions at 3.5 TeV
1380
June 28 2011
1380 bunches
November 29, 2009
Beam back
2012
18 June, 2012
6.6 fb-1
to ATLAS & CMS
6 June, 2012
6.8e33
4 July, 2012

## Slide 5: LHC – principles & reality
High energy
High bunch intensity
Many bunches
Small beam size
Superhuman operations team
LEP tunnel defines the bending radius
Superconducting magnet technology
1.9 K cryogenics
Bending radius & achievable field strength -> 7 TeV/c
Two beam pipes - 2 in 1 magnet design
Separated function - strong focusing
Luminosity insertions
Injectors
High energy
High luminosity
High availability

## Slide 6: Superconductivity
To produce the high magnetic fields we need very high currents…
Make use of the remarkable properties of He II
Superfluid helium:
  Very high thermal conductivity (3000 time high grade copper)
  Very low coefficient of viscosity… can penetrate tiny cracks, deep inside the magnet coils to absorb any generated heat.
  Very high heat capacity…stablizes small transient temperature fluctuations
How many Bose-Einstein condensates are there in the LHC?

## Slide 7
Video 1’44’’

## Slide 8: Phase diagram of Helium

## Slide 9: Cooling magnets with superfluid helium

## Slide 10: Operation prerequisite 1: 90 tonnes He II
Cryogenics system availability in 2012: 93.7%

## Slide 11: The superconductor
Strand
Filament
Cable
Used 1200 tonnes/7600 km of cable
Niobium-titanium Rutherford cable

## Slide 12: Critical surface of niobium-titanium
Niobium-titanium NbTi is the standard ‘work horse’ of the superconducting magnet business
Picture shows the critical surface, which is the boundary between superconductivity and normal resistivity
Superconductivity prevails everywhere below the surface, resistance everywhere above it
Field (Tesla)
Temperature (K)
Current density (kA.mm-2)
Notes: All superconducting accelerators built so far have used niobium titanium.

## Slide 13: Main components – dipole magnets
I
I
I
B

## Slide 14
Number of dipoles 1232
Dipole field at 450 GeV 0.535 T
Dipole field at 7 TeV 8.33 T
Bending radius 2803.95 m
Main Dipole Length 14.3 m
Horizontal force component per quadrant (nominal field) 1.7 MN/m
Force tends to “open” the magnet, hence the Austenitic steel collars

## Slide 15
1984
September 19, 2008
90
91
97
95
96
94
92
93
98
99
05
03
04
02
00
01
06
07
10
08
09
April 2008
Last dipole down
First set of twin 1 m prototypes
Over 9 T
SSC cancelled
June 2007 First sector cold
2002 String 2
November 2006
1232 delivered
Main contracts signed
1994 project approved by council (1-in-2)
June 1994 first full scale prototype dipole
ECFA-CERN workshop

## Slide 16
During magnet test campaign, the 7 MJ stored in one magnet were released into one spot of the coil (inter-turn short)
P. Pugnat
Quench protection: if not fast and reliable…
Energy stored in the magnets: quench

## Slide 17: Quench - discharge of the energy
Magnet 1
Magnet 2
Power Converter
Magnet 154
Magnet i
Protection of the magnet after a quench:
The quench is detected by measuring the voltage increase over coil.
The energy is distributed in the magnet by forced quenching using quench heaters.
The current in the quenched magnet decays in < 200 ms.
The current flows through the bypass diode (triggered by the voltage increase over the magnet).
The current of all other magnets is discharged into the dump resistors.
Discharge resistor

## Slide 19: Vacuum
Beam vacuum ~10-10 mbar (~3 million molecules/cm3)
Cold
  Pumping is insured by cold surfaces for all gases except helium. To avoid subsequent desorption, low initial pressures are required before cool-down, and this is ensured by turbo molecular pumps etc.
Warm
  NEG provides most of the pumping capacity, with additional ion pumps for the noble gases which are not pumped by the NEG

## Slide 20: OPTICS
Recall: a quadrupole magnet will focus in plane and de-focus in the other.
Convention: a “focusing” quadrupole focuses in the horizontal plane

## Slide 21: Alternate gradient focusing
(and similarly for the vertical plane y)
The general linear magnet lattice can be parameterized by a ‘varying spring constant’, K=K(s).
K(s) describes the distribution of focusing strength along the lattice and is periodic.
This is Hill’s equation.
s
x

## Slide 22: Betatron oscillations
The solution to Hill’s equation.
Amplitude term
Oscillatory term
s
x
A and 0 are constants, which depend on the initial conditions.
(s) = the amplitude modulation due to the changing focusing strength.
(s) = the phase advance, which also depends on focusing strength.
The amplitude and phase advance are both modulated by the beam envelope function, b.

## Slide 23:  function
β(s) maybe interpreted as the local wavelength of the oscillation (divided by 2π)
Put the assumed solution into Hill’s equation and turn the handle…
define the envelopes in x and y of all the particle trajectories (all f0) with amplitude value A.
depend not only on the local focusing, Kx,y(s0), but also on the focusing strength Kx,y(s) around an entire period of the lattice.

## Slide 24
Question: what will happen, if the particle performs a second turn ?
x
... or a third one or ... 1010 turns
0
s
Bernhard Holzer

## Slide 25: Amplitude modulation

## Slide 26: FODO cell
MB lattice dipole MQ lattice quadrupole
MSCB lattice sextupole+orbit corrector MO lattice octupole
MQT trim quadrupole MQS skew trim quadrupole
MCDO spool-piece decapole-octupole MCS spool-piece sextupole
beta_y
beta_x

## Slide 27: For real
Video 1’22’’

## Slide 28: Betatron oscillations
Typical beam position monitor does not resolve individual particles.
However, if the beam is deviated from the ideal trajectory it will oscillate due to the (de)-focusing fields of the accelerator.
NB: single pass

## Slide 29: Injection test – 5 years ago

## Slide 30: Tune
TUNE:
  number of betatron oscillations a particle makes in one turn of the ring
  Horizontal QH = 64.31
  Vertical QV = 59.32
Non-integer part is relevant for beam stability
Has to be controlled very carefully
Because like any other oscillator it can get into resonance…
LHC revolution frequency: 11.3 kHz

## Slide 32: TRANSVERSE ACCELERATOR COORDINATES
We are discussing the paraxial (small deflection angles => linear), uncoupled (x & y independent) transverse motion of on-momentum particles around the design trajectory/orbit for a magnet lattice:
s = coordinate along design orbit
s
x’
x
(and similarly for y view)

## Slide 33: Phase Space
1
x
s
2
3
1
2
3
4
4
x
x’
1
2
3
4
x

## Slide 34: Phase space
Sit at a focusing quadrupole (for example) and plot the phase space coordinates of a single particle, it will describe an ellipse:
x’ [rad]
x [mm]
t1
t4
t5
t2
t3
t6

## Slide 35: Phase space
x
x’
x
x’
x
x’
As we move around the ring the ellipse changes orientation BUT the area remains the same

## Slide 36: Emittance
Linear motion → beam ellipse in 2-d-space
Ellipse area in (x,x’) plane:
Define emittance by a contour confining some fraction of particles depending on distribution (typically Gaussian)
Units: mm.mrad (but you will see microns)
Imagine sitting at one location and plotting x,x’ of all particles
Or tracking one particle over many turns

## Slide 37: Emittance
x’
x

x
Area of phase space ellipse = 

## Slide 38: Normalized emittance
Geometric emittance {x,x’} shrinks naturally as we go up in energy
Important – it’s energy independent and can be used across the accelerator complex and will show up later in a useful formulation of luminosity
Normalized emittance | 2.5 mm.mrad
Emittance 450 GeV | 5.2 nm.rad
Emittance 7000 GeV | 0.34 nm.rad
Beta [m] | Sigma 450 GeV [micron] | Sigma 7 TeV [micron]
180 | 967 | 246
30 | 395 | 100
4000 | 4566 | 1158
0.6 | 56 | 14
NB: relativistic β and ϒ!

## Slide 39: LHC beam envelope
1 sigma envelope – 68.3% of particles assuming a Gaussian distribution
4 TeV
εn=2.5 and 3.75 microns
mm
IP5

## Slide 40: Phase space
Simulation showing the chaotic effect of the beam–beam interaction
Phase space trajectories near the septum of a compact synchrotron during low extraction

## Slide 41: Magnet - basic arsenal
Dipole; constant field:
Quad; linear variation:
Sext.: quadratic variation:
x
By
By
x
x
By

## Slide 42: Dispersion
Closed orbit for p < p0
Closed orbit for p=p0
Closed orbit for p > p0

## Slide 43: Dispersion at LHC
HORIZONTAL
VERTICAL
Between an arc and the straight section there is the so-called dispersion suppressor that brings the dispersion function to zero in the straight section in a controlled way.
Beam size affected

## Slide 44: Chromaticity
A particle with a higher momentum than nominal will be deviated less in the quadrupole and will have a lower betatron tune
A particle with a lower momentum than nominal will be deviated more in the quadrupole and will have a higher betatron tune
 spread in the tunes
due to spread in momentum
Rende Steerenberg

## Slide 45: Chromaticity
And we have dispersion…
x

## Slide 46: Chromaticity correction
Fx
QF
QF
QF
QD
QD
SF
SF
SF
SD
SD
with sextupoles

## Slide 48: LHC Injector Cycling
PSB
PS
SPS
Time
= Field in main magnets
= Proton beam intensity (current)
= Beam transfer
1.2 seconds
To LHC clock-wise or counter clock-wise
450 GeV
26 GeV
1.4 GeV

## Slide 49
Triple splitting after 2nd injection
Split in four at flat top energy
26 GeV/c
1.4 GeV
2nd injection
The LHC 25 ns cycle in the PS
→ Each bunch from the Booster divided by 12 → 6 × 3 × 2 × 2 = 72
h = 7
Eject 72 bunches
(sketched)
Inject 4+2 bunches
gtr
h = 84
h = 21

## Slide 50
LHC bunch structure - 2012
1 SPS batch
(144 bunches)
26.7 km 1380 bunches
Abort gap
1 PS batch
(36 bunches)
50 ns bunch spacing
Maximum bunch intensity 1.7 x 1011 protons per bunch

## Slide 51: From the control room

## Slide 52: A bunch
Number of protons | Up to 1.7 x 1011 so far
Transverse beam size (1 sigma) at IP5 | 18.8 microns (4 TeV, β* = 60 cm.)
Transverse beam size (1 sigma) in arc | .97/.4 mm (450 GeV 2012)
Bunch length (4 sigma) | 1.25 ns (37.5 cm) in 2012
Momentum spread (1 sigma) | 1.129 x 10-4 i.e. ± 0.8 GeV 7 TeV (design report)

## Slide 53: Interaction region
D2

## Slide 54: In the long straight section
Video 1’57’’

## Slide 55: Crossing angle
work with a crossing angle to avoid parasitic collisions.
generates additional tune shift
requires larger triplet magnet aperture
breaks symmetry between x,y planes
odd order resonances are exited
couples longitudinal and transverse motion
breaks the bunch symmetry
lowers available luminosity

## Slide 56: Crossing and Separation Bumps
Collapse the separation bump (vertical in CMS) after the squeeze to bring the beams into collision
Crossing angle bump (Horizontal in CMS)
110 m
CMS

## Slide 57: In practice
HORIZONTAL
VERTICAL
+/- 6 mm at 450 GeV

## Slide 58: Squeeze in ATLAS
Image courtesy John Jowett
βmax ~4.5 km
β* = 60 cm
x´
x
NB: round beams at IP

## Slide 59: Beam - Squeeze
Small beam in the IP  big beams in the inner triplets  reduced aperture
Therefore inject & ramp with bigger beam sizes at IP.

## Slide 60: Squeeze
Going to use quadrupoles both sides of a given IP all the way out to the arc to control the optics during the squeeze.
Current in the inner triplets doesn’t actually change very much during the squeeze – but the beam size does.
IP1
TRIPLET
SEPARATION
DIPOLES
Dispersion suppressor
Long straight section

## Slide 61: Triplet
Video 58’’

## Slide 62: Program…
Today
  Dipoles, cryogenics, QPS
  Optics and basic beam parameters
  Beam configuration
  Interaction region layout
  Crossing angle and separation bumps
  Squeeze
Tomorrow
  Getting operational
  Without doing any damage (machine protection)