## Slide 1: LHC operations past and future: part 2
RF – briefly
Instrumentation – even more briefly
The nominal cycle
  Injection
  Ramp
  Squeeze
Machine protection
  Beam interlock system
  Beam dump
  Collimation
Plus 3 visits to the tunnel
Mike Lamont with acknowledgements to all the people whose material I’ve used
(including Ralph Assmann, Luca Bottura, Heiko Damerau, Bernhard Holzer, Rende Steerenberg, Ralph Steinhagen, Jorg Wenninger...)

## Slide 2: Radio Frequency
Briefly!
Bunch the beams (longitudinal focussing)
Accelerate particles during the ramp

## Slide 3
S34
S45
B2
B1
194 mm
420 mm
ADT
Q5
Q6
Q7
ACS
ACS
ACS
ACS
D3
D4
2 x four cavity cryo module per beam
400 MHz
16 MV/beam (7 TeV design)
Nb on Cu cavities @4.5 K
Beam pipe diam.=300 mm

## Slide 5
Courtesy Andy Butterworth

## Slide 6
Courtesy Andy Butterworth

## Slide 7
E
t (or )
V
Synchronous particle
RF Bucket
Bunch
t (or )
Lower energy particles – bent more – shorter revolution time
Higher energy particles – bent less – longer revolution time

## Slide 8: The motion in the bucket (2)
E
t (or )
V
Rende Steerenberg

## Slide 9: The motion in the bucket (3)
E
t (or )
V

## Slide 10: The motion in the bucket (4)
E
t (or )
V

## Slide 11: The motion in the bucket (5)
E
t (or )
V

## Slide 12: The motion in the bucket (6)
E
t (or )
V

## Slide 13: The motion in the bucket (7)
E
t (or )
V

## Slide 14: The motion in the bucket (8)
E
t (or )
V

## Slide 15: The motion in the bucket (9)
E
t (or )
V
Phase focussing - important!!!
Synchrotron oscillations
(In the LHC when dp/dt=0, the stable phase is 180 degrees. During the ramp it reaches 176.5 degrees)

## Slide 16
Synchrotron light
Beam Position Monitors
Beam loss monitors
Base-Band-Tune (BBQ)
Beam Instrumentation – our eyes
Wire scanner
Longitudinal density monitor

## Slide 17: The LHC BPM system
1088 button and coupler monitors – 2176 position readings.
Excellent availability
Typical orbits
±7 mm

## Slide 18: Beam loss monitors
Around 4000 ionization chambers protect the LHC superconducting magnets against quenches and damage from beam loss.
The system has been designed with high safety standard (SIL3) and is an essential component of the LHC Machine Protection System.
  Smallest loss integration interval is 40 microsecond ~½ LHC turn.
  The BLM system will dump if a SINGLE monitor goes above threshold.
A large fraction of the BLMs are installed on super-conducting magnets with dump thresholds set to some fraction of the estimated quench level loss.

## Slide 20: Operational cycle
Beam dump
Ramp down/precycle
Injection
Ramp
Squeeze
Collide
Stable beams
Ramp down | 35 mins
Injection | ~30 mins
Ramp | 12 mins
Squeeze | 15 mins
Collide | 5 mins
Stable beams | 0 – 30 hours
Turn around from stable beams to stable beams - 2 to 3 hours on a good day

## Slide 21: Nominal cycle
Globally the machine state is fairly well described by machine mode/beam mode combination

## Slide 22: Sequencer tasks
  Task by task breakdown of everything that needs to be done to drive LHC through the nominal operational cycle – semi-automatic

## Slide 23: Precycle/rampdown
Aim: reproducible magnetic machine
Coming back from access
  Full pre-cycle of all magnetic circuits
After stable beams
  Ramp-down/precycle combination

## Slide 24: Transfer & injection
1 km
Transfer line
LHC
SPS
6911 m
450 GeV / 400 GeV
CNGS Target
IR8
Switching magnet
Fast extraction kicker
Injection kicker
Transfer line
Injection kicker
IR2
Fast extraction kicker
2012: 144 bunches of 1.7e11 ppb - 1.8 MJ
HiRadMat
One SPS batch: 2.2 km long (7 microseconds)

## Slide 25: Reasons to be careful
During an SPS extraction test in 2005…
The beam was a 450 GeV full LHC injection batch of 3.4 1013 p+ in 288 bunches [2.5 MJ]

## Slide 26: End of TI2
Video 2’29’’

## Slide 27: Injection
Require from the injection kickers:
< 1ms rise time (gap between SPS injections),
<3 ms fall time (abort gap),
8 ms flat-top length (1 SPS batch)

## Slide 28: Layout (point 8)
5 septum magnets
(MSI)
4 injector kickers
(MKI)
TCDD absorber
TDI collimator

## Slide 29: Septa and beyond
Video – 2’26’’

## Slide 30
Injection kickers
Fast resonant charging systems (RCS) are used to charge the PFNs within 1 ms to 60 kV
PFN - pulse forming network

## Slide 31
Injection of beam from SPS

## Slide 32: Filling
LHC makes requests to the Central Beam and Cycle Manager (CBCM) which takes care of sorting things out in the injectors
  Ring, number of batches, bucket number
Injection process controlled semi-automatically by injection sequencer

## Slide 33: Injection – general
Transfer lines steering
RF: phasing, synchronization
Beam Quality Check in SPS
  Bucket, bunch length…
Injection Quality Check in LHC
  inhibits further injection if issues
Worry a lot about losses and beam quality

## Slide 34: Injection Quality Checks
Beam loss

## Slide 35: Injection Quality Checks
Trajectory

## Slide 36
LHC Capture Transients
Phase Loop Error: Beam PU-Cav Sum
Synchro Loop Error: VCXO-Freq Prgm
Inj Phase Error 35 deg/45 deg
Cavity field “jumps” on the beam in ~ 10 turns
Phase loop is fast: “jumps” the RF on the beam at injection
Synchro loop is slow. No reaction in first 100 turns. Slope gives frequency (energy) error at injection
-30 deg in 60 turns -> -15 Hz @ 400 MHz
Dp/p ~ 10-4
Synchro loop brings RF (and beam) back to Freq Prgm reference
Very slow (seconds) time constant. Boosts DC gain to minimize thermal drifts
-15 deg in 80 turns -> -6 Hz @ 400 MHz
Philippe Baudrenghien

## Slide 37: Emittance measurement
Wire scanners

## Slide 38: Prepare ramp
Load power converters (1700+)
Load collimators
Load RF
Load transverse feedback
Get orbit and tune feedback on
Send timing event
Get a cup of coffee

## Slide 40: Ramp
450 GeV – 4000 GeV
  13 minutes
  Parabolic – exponential – linear – parabolic to minimize effects of snapback and duration
  Snapback correction for b2, b3, b5 calculated just before ramp start and incorporated into settings
injection
pre-injection
I  t2
I  et
I  t

## Slide 41: Persistent currents
DB
+Jc
-Jc
MDC
Field change DB
Eddy currents Jc with t=  persistent
Diamagnetic moment at each filament: MDCJc*Dfil
This really messes with the field quality of the main dipoles. Large field errors, in particular, sextupole, are introduced.
Exacerbated by the fact the effects are dynamic…

## Slide 42: Decay and Snap-back
snap-back
decay
LHC operation cycle
Luca Bottura

## Slide 43: Increasing the momentum
Momentum follows magnet field variation due to RF phase focussing:
inject beam into ring at B0 with momentum p0 = qRB0
increase B-field → B + ΔB
bending radius shrinks
path becomes shorter by 2πΔR
particles arrive earlier by Δt = (2πΔR)/βc
RF cavity: U(Δt) = U0 sin(ωΔt + φ) > 0
Acceleration by Δp = βqU(Δt)
⇒ self-synchronization of p(t) with B(t)

## Slide 44
Chart: Current [A]
Tracking between the three main circuits of sector 78
2ppm
Phenomenal performance from the power converters
Courtesy Freddy Bordry & Dave Nisbet
Main bend power converters: tracking error between sector 12 & 23 in ramp to 1.1 TeV

## Slide 45: Ramp - collimators
Jaw positions in ramp

## Slide 46: Losses per bunch in ramp

## Slide 47
Reduction of beam size at interaction points
(beams still separated)

## Slide 48: Squeeze 2012
From 11-10-11-10 to 0.6-3.0-0.6-3.0 m
Collisions tunes (.31/.32)
Orbit feedback - obligatory
Worry about:
  tune, chromaticity, coupling, orbit, optics corrections
  beam loss and instabilities… (tight collimator settings)
Activity kicks off on beam 1 – end of squeeze
Sustained beam loss both beams – finally dumping on collimator temperature interlock

## Slide 49: Squeeze in practice
Beta* - 11 m ATLAS, CMS; 10 m in ALICE, LHCb
Time in seconds
Beta* - 0.6 m ATLAS, CMS; 3 m in ALICE, LHCb
Matched optics
Current during the squeeze in a few quads at point 1

## Slide 50
Luminosity
Beam intensity

## Slide 51
Beam based feedbacks
Courtesy Ralph Steinhagen

## Slide 52: Orbit feedback
Orbit-Feedback is the largest and most complex LHC feedback:
  1088 BPMs → 2176+ readings @ 25 Hz from 68 front-end computers
  530 correction dipole magnets/plane, distributed over ~50 front-end computers
Total >3500 devices involved
Mandatory in ramp and squeeze
Stability in ramp and squeeze of ~ 50 micron rms or better

## Slide 53: Tune feedback in ramp
Courtesy Ralph Steinhagen
Without
With

## Slide 54: The transverse damper in general
The transverse damper is a feedback system: it measures the bunch oscillations and damps them by fast electrostatic kickers
OFF
ON
Turn number
Injection oscillations
Transverse position
Courtesy Wolfgang Hofle & Daniel Valuch

## Slide 55: ADT as seen from the CCC
Daniel Valuch: Transverse damper system, Evian 2012

## Slide 56: ADT as really seen from the CCC
ON
OFF
WHY ISN’T IT WORKING?
Phone Wolfgang or Daniel

## Slide 57: Transverse feedback

## Slide 58: Operations’ 7 pillars of wisdom
Availability
Reproducibility
Control
Instrumentation
Optimization and stability
Understanding
Safety systems
Given an impeccably debugged, optically good machine with an excellent magnet model, operations then rely on:

## Slide 59: Machine protection
~3.6 GJ of energy stored in the main dipoles
140 MJ stored in each beam ~21 kg of TNT.
4 TeV with 1380 bunches – 2012

## Slide 60: Beam Interlock system
UPS
Timing
Software Interlocks
LHC
Beam
Interlock
System
Powering
Interlock
System
BLMs aperture
BPMs for Beam Dump
LHC Experiments
Collimators / Absorbers
NC Magnet Interlocks
Vacuum System
RF + Damper
Beam Energy
Tracking
Access Safety
System
Quench
Protection
Power Converters
Discharge
Switches
dI/dt beam current
Beam Dumping
System
AUG
DCCT Dipole
Current 1
DCCT Dipole
Current 2
RF turn clock
Cryogenics
Beam Dump
Trigger
Beam Current
Monitors
Current
BLMs arc
BPMs for dx/dt + dy/dt
dI/dt magnet current
Energy
SPS Extraction
Interlocks
Injection
Kickers
Safe LHC
Parameters
Energy
essential
circuits
auxiliary
circuits
Screens
SafeBeam
Flag
Energy
TL collimators
Software Interlocks
Operators
Over 10’000 signals enter the beam interlock system (BIS). The BIS will trigger a beam dump if any input signals a fault.

## Slide 61: Beam Interlock System (BIS)
The communications from one point to another is carried out over four dedicated fibre optic channels. A clockwise and anticlockwise link exists for each beam to be interlocked by the Beam Interlock System. This means that the request for a Beam Dump always takes the shortest path from one BIC to LBDS.
Ben Todd

## Slide 62: LHC beam dump
MKD (14x)
MSD (3x5)
MSDA
MSDC
TDE
MKB
MKBH (4x)
MKBV (6x)
Q5R
Q4R
Q4L
Q5L
TCDS
TCDQ
Beam 2
Beam 1

## Slide 63: Beam dump system – point 6
Video 2’10”

## Slide 64: Abort Gap
dump trigger
3.0 ms
particle-free
abort gap
Extraction kicker MKD deflection
LHC
Beam

## Slide 65: Asynchronous Beam Dump
TCSG
TCDQ = 6 m long CFC* one-sided collimator TCSG = 1 m long CFC* two-sided collimator
TCDQ + TCSG to protect downstream superconducting magnets (Q4)
*CFC = carbon fibre compound
Estimated occurrence : at least once per year, 1 events up to now!

## Slide 68: Pedagogical collimation 1
Primary
Secondary
Dump Protection
Tertiary
+Triplet
Tertiary
+Triplet
Dump Kicker
“The hierarchy”
Closed orbit
Ralph Assmann
Collimation is set up with multi-stage logic for cleaning and protection
Let’s look in normalized phase space, talking in nominal sigmas:

## Slide 69: Pedagogical collimation II
Collimation is set up with multi-stage logic for cleaning and protection
Let’s look in normalized phase space, talking in nominal sigmas:
Primary
Secondary
Dump Protection
Tertiary
+Triplet
Tertiary
+Triplet
Dump Kicker
Primary beam and primary halo

## Slide 70: Pedagogical collimation III
Collimation is set up with multi-stage logic for cleaning and protection
Let’s look in normalized phase space, talking in nominal sigmas:
Primary
Secondary
Dump Protection
Tertiary
+Triplet
Tertiary
+Triplet
Dump Kicker
Beam dump envelope

## Slide 71: Pedagogical collimation IV
Collimation is set up with multi-stage logic for cleaning and protection
Let’s look in normalized phase space, talking in nominal sigmas:
Primary
Secondary
Dump Protection
Tertiary
+Triplet
Tertiary
+Triplet
Dump Kicker
Beam dump envelope
ROBUST
Not robust
Not robust
… but efficient …

## Slide 72: Pedagogical collimation V
Collimation is set up with multi-stage logic for cleaning and protection
Let’s look in normalized phase space, talking in nominal sigmas:
Primary
Secondary
Dump Protection
Tertiary
+Triplet
Tertiary
+Triplet
Dump Kicker
Beam dump envelope
ROBUST
Not robust
Not robust
… but efficient …
MARGIN

## Slide 73: Collimator hierarchy
The hierarchy must be respected at all times.
The collimators and protection devices are positioned with respect to the closed orbit
Therefore the closed orbit must be in tolerance at all times.
This includes the ramp and squeeze.
  Orbit feedback becomes mandatory
  Interlocks on orbit position become mandatory

## Slide 74: Collimation/reproducibility
.
Orbit at Primary collimator (TCP) in ramp
ORBIT FEEDBACK
2011-2012: only ONE full alignment in IR3/IR7
J. Wenninger
IR7 collimators – beam 1
Orbit at primary

## Slide 75: Collimation
Generate higher loss rates: excite beam with transverse dampers
Betatron
Off-momentum
Dump
TCTs
TCTs
TCTs
TCTs
Beam 1
Legend:
Collimators
Cold losses
Warm losses
0.00001
0.000001
Routine collimation of 140 MJ beams without a single quench from stored beam
Stefano Redaelli

## Slide 76: RESERVE

## Slide 77: Correcting the closed orbit
Represent beam position by M-dimensional vector
Represent the corrector kicks by an N-dimensional vector
M is the number of BPMs and N is the number of correctors.
Now
Where A is the linear response matrix (N x M) which describes the relation between corrector kicks and beam position changes at the BPMs.
Aij corresponds to the orbit change at the ith monitor due to a kick from the jth corrector

## Slide 78: Orbit correction
Just need to invert this
Poorly positioned correctors, errors in measurements means the matrix is often ill conditioned
Variety of methods MICADO, SVD designed to deal with this problem
e.g. minimising
A lot of options and facilities provided on-line at the LHC by YASP

## Slide 79: The extraction process
V
2.4 mrad
0.06 mrad
Q4
Kickers (H)
Septum (V)
LHC orbit
H
0.33 mrad
LHC orbit
From the kickers require:
<3 ms extraction kicker rise time (abort gap),
>89 ms extraction kicker flat-top length (full LHC turn)