## Slide 1: Simulation of GEM-CSC Integrated Trigger: Status and Plans
US CMS EMU Workshop 2013-10-01
Vadim Khotilovich, Texas A&M University
for GEM DPG group

## Slide 2: Outline
What is implemented in CMSSW simulation now
  Integrated local GE1/1-ME1/b trigger (ILT) with simple Df, Dh, and DBX matching in the emulator
Plans for GEM-CSC trigger simulation
  Integrated local GEM-CSC trigger
  GEM-CSCTF trigger path
  Use of GEM in HLT
Note: the current task list spreadsheet is available in indico

## Slide 3: Current ILT Implementation
Input to ILT
  Proto LCTs from ME1/b
    ALCTs and CLCTs that are matched, but not yet sorted
  GEM trigger pad digis (OR of 4-strips)
Current ILT algo:
  Implemented as a simple method of the TMB emulator in CMSSW
  For each proto-LCT it attempts to find GEM pads matching within certain Dh and DBX and have min|Df| within some range
    Df and Dh are deltas between global f’s and h’s of GEM pad and LCT position at key layer
  Final result is either:
    Throwing away ME1/b LCTs with 1.64<|h| that don’t have a matching GEM within specified limits Df, Dh, and DBX
    Don’t throw any stubs away, but store information about Df in a CSCCorrelatedDigi‘s data member
      currently a float number that is used in further studies

## Slide 4: How to use it
The custom simulation workflow described in https://twiki.cern.ch/twiki/bin/view/MPGD/GemSimulationsInstructionsCMSSW
  Sven is working on integrating it into the cmsDriver in one of the SLHC cmssw releases, so that production of official samples with GEMs would be possible
Currently available samples https://twiki.cern.ch/twiki/bin/view/MPGD/GEMSimulationsGeometrySamples
  Note: we have a fairly large (60M) minbias sample for pileup studies with 6 partitions GEM geometry

## Slide 5: Integrated Local GEM-CSC Trigger Plans
Changes in data formats
  What optimal set of additional GEM-related information we need to add to the existing CSC trigger stub data?
  I will talk about it in another session today
Algorithm development
  Factorized models (GEM is integrated at LCT level)
  Integrated models (GEM is integrated into CLCT reco)
  Integration into CSCTF

## Slide 6: ILT Plans: Factorized Models
(“Factorized”: GEM is integrated after CLCT was reconstructed)
Df and Dh matching tuning, defining a discrete Df scale
  Closely tied to the new TMB output raw data format definition
Using GEM to aid with ghost resolution
Tuning of LCT timing using the times of ALCT, CLCT and GEM
Redundancy against failure: look into a possibility of using a good GEM coincidence as a substitute for a missing ALCT or CLCT
  Work out a realistic an detailed GEM-CSC matching algorithm for OTMB firmware
  It is very important to implement a realistic electronics test-bed for hands-on experimentation with firmware algorithms

## Slide 7: ILT Plans: Integrated Models – Improving CLCT efficiency with GEM
(GEM is integrated during CLCT reconstruction)
CLCTs are usually the largest contributor to the inefficiency
With GEMs, we effectively would have 8 layers instead of 6
  4-out-of-8 trigger integrated patterns finding should be more efficient then the 4-out-of-6 CSC only
Pre-requisite study: enumeration and sorting of remaining sources of ineffciency
1st simple study:
  Lower the 4-out-of-6 CLCT trigger stub requirement to 3-out-of-6 (same as pre-triggers) in the CSC emulator configuration
Further studies would require rather serious CLCT emulator code changes
  If we want true 4-out-of-8 trigger pattern, we need to be able to build a stub from any combination of 4 CSC+GEM layers
  TODO: would need to brainstorm about options for combined patterns and efficient matching

## Slide 8: ILT Plans: Integration into CSCTF
CSCTF would need to be able to access GEM-related information in ME11 stubs and act on it
  Data format for ME11 stubs would be different
  Hopefully, there would be no need for ghost resolution combinatorics for GEM-matched stubs
  GEM-matched stub would carry GEM-CSC delta-phi information that would be very useful for pt assignment
    Need to determine realistic options to make use of it

## Slide 9: Plans for the GEM-CSCTF Path
Need to define the GEM input to CSCTF
  Simple case: use perfect GEM superchamber coincidence pads (would need to keep the inefficiency in mind)
  More complex: less perfect coincidence trigger pads with possibly some sort of quality value dependent on how close are two pads in phi, eta, or BX
Algorithm development and optimization
  TODO: Some sort of a baby-steps algorithm would be needed first
Would need to think about possible changes in CSCTF raw data formats

## Slide 10: Plans for GEM use in HLT
While the HLT is under the trigger territory, this is more related to RECO then to anything that we have discussed earlier
  Framework for usage of GEMs in muon RECO would be a prerequisite
Possible opportunities for profit:
  L2: reducing soft muons rate before tracking kicks in
  L2.5: Use bending angle with pixel vertices and pixel hits to improve resolution
  L3: better redundancy and efficiency using GEM offline tools

## Slide 11: Summary
The basic simulation implementation of an integrated local GEM-CSC trigger for ME1/1 exists in CMSSW and produces encouraging results
Still, there are many areas that need work
  to make the simulation more realistic
  to fully take advantage of information from GEM detectors

## Slide 12: Backup

## Slide 13: ILT Plans: Delta phi and eta matching
We already did basic studies of Df and Dh matching
  Possible improvements could come from incorporation the dependencies of Df and/or Dh on h
  Need to define more rigorously the discrete Df thresholds scale
    Possible criteria: scale’s bins occupancies should be close to uniform
    A parametrization of Df threshold dependent on efficiency, pt threshold, and eta could be very helpful to easily build various equal-occupancy scales of various granularity
Need to keep in mind the constraints from how much extra information we can keep in raw TMB data format
  We would store as much info as possible, but the resources are scarce
  That will take some time to converge

## Slide 14: ILT Plans: Ghost Resolution
Ghost resolution is needed only if a chamber has 2 CLCTs and 2 ALCTs in a single BX and they match into 2 LCTs in different strips and wire-groups
GEMs would be very helpful for that
  Would be a simple improvement to the algorithm that we currently have
Things to study:
  Probability to have ghost stubs in a chamber that has LCTs
    how it depends on luminosity, is it a non-linear dependency?
    How much GEMs help to decrease it? Does the number of eta partitions matter?
  Does ghosting seriously affect efficiency or rates?
    Select events in high PU + signal sample that don’t have ghosts in a chamber and look at LCT efficiency, compare it to the normal case
    In high PU rate samples: select events with CSCTF tracks that have stubs in ME1/b chambers that don’t have ghosts and compare the trigger rate to the normal case
    Does ghost resolution with GEMs help with rates?
  For muon-jet physics-like studies could also generate muon gun samples with multiple close muons
It would be really nice if we could have an option to disable the CSCTF’s ghost combinatorics for ME1/b

## Slide 15: ILT Plans: Tuning of LCT Timing
It should be possible to improve stub timing resolution using GEM information
BX of LCT is defined by ALCT
  Wiregroups have very good time resolution (3-4 ns?) but not perfect
Time resolution of time-coincident GEM pads in two layers would provide a very precise BX ID
  Single GEM has ~5-7 ns resolution, but two GEM pads coincident in a superchamber would be much more precise
To try first:
  if we get perfect superchamber-coincidence GEM pads, assign GEM’s time as integrated stub’s BX
  How often would it change stub BX? Would it improve rate or efficiency?
Next: more complex “voting” algorithm
  “Majority” vote with some weights between ALCT, CLCT and GEM

## Slide 16: GEM as Redundancy for ME11 Failures
Look into possibilities of using GEM pad coincidences as substitutes for missing either ALCT or CLCT stubs to build an LCT
  A good quality GEM coincidence pad (2 layers with the same BX and pad#) would provide very precise timing and, likely, good protection against neutron BG
    The distance between two GEM layers is ~4.5 cm which is at least 2x larger then between CSC layers – less chance of 2-layer coincidence from neutron BG
  Keep an eye on the rate
For this task it is important to have a mature neutron BG simulation for GEM

## Slide 17: ILT Plans: Integrated Models – Improving CLCT efficiency with GEM
CLCTs are usually the largest contributor to the inefficiency
With GEMs, we effectively would have 8 layers instead of 6
  4-out-of-8 trigger patterns finding should be more efficient then the 4-out-of-6
Pre-requisite study: enumeration and sorting of remaining sources of ineffciency
  Identify the inefficiencies of the different stages in PU+signal sample
1st simple study:
  Lower the 4-out-of-6 CLCT trigger stub requirement to 3-out-of-6 (same as pre-triggers) in the CSC emulator configuration
    Stubs matched to GEM would effectively have at least 4-out-of-8 layers
    How much would that improve the CLCT efficiency in high PU? What about the final LCT efficiency?
    How much would it increase the rate?

## Slide 18: ILT Plans: Integrated Models – Improving CLCT efficiency with GEM
2nd study would require rather serious CLCT emulator code changes
  If we want true 4-out-of-8 trigger pattern, we need to be able to build a stub from any combination of 4 CSC+GEM layers
  That would require some substantial change for how we do the pattern matching
    A naïve approach of creating 2-layer CLCTs first and then matching them to GEM would very likely not work: the GEM matching takes time and the FPGA would most likely not able to do it fast enough
  TODO: need to brainstorm about creating combined patterns and the efficient matching