Studies for Phase-II Muon Detector
(|η| = 2.4-4.0) – Plans
Emanuela Barberis David Nash Daniele Trocino
Northeastern University
Muon Upgrade Meeting

---
Summary (I)
- The lower portion of the new muon station would extend offline muon reconstruction coverage to a region between |η| = 2.4 and |η| = 4.0
  - for now, simply emulated as a flat surface
    at |z| = 560 cm, covering |η| = 2.4-4.0
  - 2D hits only (could be extended to segments)

---
Summary (II)
- Here we will describe the first plans we have made and discussed with Slava (thanks again!), exploiting the material and tools available now or in reasonable time scale as well as give an overview our results so far
  - particle-gun muon samples with FastSim, including an extended Pixel detector and a pileup
    scenario ”à la Summer12”
    - first sample available (20 GeV muon gun),
      produced by A. Levin (thanks!)
- Clearly, this is just the beginning. We will need also
  - larger pile-up, as expected in Phase-II
  - more realistic physics signals
  - realistic QCD backgrounds to study rates of hadronic
    punchthrough, decays-in-flight, etc.
      → full simulation may be necessary

---
Simulating Material Effects
- In absence of full or fast simulation of the extended muon detector, the effect of the material
  can be studied via propagation
- Propagate the generated-track initial state and covariance matrix (null at IP) to a surface
  at z = 560 cm, using the SteppingHelixPropagator
  - after the propagation, the covariance matrix will include the uncertainty from material
    effects only (multiple scattering, energy-loss fluctuations, bremsstrahlung, etc.)
Use the position error on the muon detector surface to smear the propagated position and “emulate” a sim-hit
General strategy:
longitudinal view
transversal view
y
“sim-hit”
“sim-hit”
Δ(rφ)
gen track
Δr
rec-hit
rec-hit
reco pixel
track
IP
IP
x
560 cm
z
r = (x2 + y2)½

---
Use of the Extended Muon Detector
The new muon detector can be used for two different purposes
As a simple “muon tagger”, to identify the muon track, without using the muon hits to improve the track fit
  - Very similar to the current “tracker-muon” reconstruction
  - Need to define criteria to associate the muon hit (or segment) to the correct pixel track
  - Performance is deteriorated by the abundant expected pile-up
To add an extra point to the muon track fit
  - This can improve the momentum resolution, especially at high pT, thanks to the larger lever arm
  - Need to determine
    - pT range in which the muon detector can contribute significantly

---
Muon Identification: Matching Windows
- Need to determine matching windows in r and rφ to associate the muon hit to the corresponding reco pixel track
- Propagate the generated particle to z = 560 cm (only B field and average energy loss) → PGEN
- Produce the “simulated hit” (multiple scattering, etc) → PSIM
  - Smear PGEN according to its position error to emulate PSIM
- Propagate the reconstructed pixel track → PREC
  - From the outermost pixel hit
Muon matching window
(only material effects)
   ΔM = PSIM – PGEN
Pixel matching window
(pixel detector performance)
   ΔP = PREC – PGEN
Total matching window
(full performance)
ΔMP = ΔM – ΔP
“sim-hit”
PSIM
ΔM
PGEN
ΔMP
ΔP
gen particle
PREC
reco pixel
track
IP
Outer Hit
560 cm
z
r = (x2 + y2)½

---
Muon Matching Window ΔM
ΔM is affected only by material effects (in part. multiple scattering)
r coordinate
rφ coordinate
mean, RMS
mean, RMS
The matching window can be chosen e.g. as a 95 / 99% probability region (2 / 3 × RMS)

---
Pixel Matching Window ΔP
ΔP is affected only by the resolution of the reconstructed pixel tracks
rφ coordinate
r coordinate
mean, RMS
mean, RMS
The matching window can be chosen e.g. as a 95 / 99% probability region (2 / 3 × RMS)

---
Total Matching Window ΔMP
ΔMP combines material and pixel detector effects
rφ coordinate
r coordinate
mean, RMS
mean, RMS
The matching window can be chosen e.g. as a 95 / 99% probability region (2 / 3 × RMS)

---
Summary: ΔM , ΔP , ΔMP
ΔMP is dominated by ΔP except for the low |η| region
We also add, for comparison, the position error of the propagated reco track
(not initialized to null) at the surface
r coordinate
rφ coordinate
The matching window can be chosen e.g. as a 95 / 99% probability region (2 / 3 × RMS)

---
Muon Identification: Pile-Up
- Determine windows Δr, Δ(rφ) to match the muon hit to the pixel track e.g. with 95/99% probability
- Determine the mismatch rate due to the pile-up, i.e. how often a random pile-up (reco) track rather than the reco muon track is wrongly associated to the simulated muon hit
  This can be done by:
  - propagating all pile-up tracks and checking how often they end up inside the matching window, closer to the simulated muon hit than the reco muon track
  - using the expected average density of pile-up tracks d2N/dηdφ and the matching area (some quick estimates from Alexei on the following slide)
Simulated sim hit
pileup tracks
Reco muon track
560 cm
z
r = (x2 + y2)½

---
Some quick estimates (-Alexei)
- The matching window is about Dh x Df = 0.002 (pT=5, for higher pT it’s smaller)
- Total area of the detector: Dh x Df = 2x2xp = 12
- Scenario A (event vertex is known):
  - About 0.25 pixel tracks and about 100 muon hits per BX
    - Crudely, an average number of accidental matches with pT>5 GeV: N~ 0.25 tracks*100 muon hits / 6000 windows ~ 0.004 fake muons per BX
- Scenario B (event vertex is not known):
  - The number has to be multiplied by NPU
    - For PU=200, N~0.8 fake muons/BX for pT=5 GeV
    - For pT>10 GeV N~0.08 fakes
- Further studies will be done, of course, these are just crude initial estimates

---
Muon Fit
Determine the momentum range where the muon chamber can improve significantly the resolution of the track fit
  - propagate both the generated and reconstructed tracks to the muon surface
    - the reco'ed track can be propagated from the outermost tracker layer
  - evaluate the displacements ΔG and ΔR w.r.t. a straight line (in part. in φ projection)
  - the comparison of ΔG and ΔR indicates where we can gain by using the muon information
    - at high pT, the reconstruction resolution gets worse and ΔR broadens w.r.t. ΔG
PLINEAR
ΔG
y
Low pT
ΔR
PGEN
|Δ|
PREC
High pT
x
|Δ|

---
ΔG vs ΔR
rφ coordinate distance from straight line
rφ coordinate RMS
Dr(prop. track, straight line)
Note that at this high h, pT=20 GeV corresponds to p~100-400 GeV

---
Summary and Plans
- We have conducted initial studies with our first samples, which were received:
  - Matching windows (to simulated sim hits, and w.r.t. straight line)
  - Some initial tests with pileup studies (although the pileup scenarios were minimal with respect to what we'd need)
- Local Sample Production:
  - Working now to reproduce results with the 20 GeV muon gun sample we received (did not receive the corresponding config file)
  - Planning to produce a range of pT values
- Pileup studies
  - Produce our full pileup scenario
  - Likewise pT dependent

---
BACKUP

---
Scatter plots corresponding to slide 12
r coordinate
rφ coordinate