## Slide 1: DCFEB
Firmware Updates

## Slide 2: Future Firmware Features
Auto loading constants:
  Initializes firmware registers and DAC settings after hard reset from constants stored in the PROM.
Ring buffer to replace FIFO:
  For L1A separated by less than 400nS.
Possible TMB communication enhancments:
  Encoded BC0 for synchronization monitoring
SEU Mitigation:
  Soft Error Mitigation in FPGA configuration memory.
  ECC for data in stored in BlockRAMs.
  Triple voting critical logic.

## Slide 3: Ring Buffer
Currently in firmware: Pipeline to FIFO
Pipeline
FIFO
L1A
Ring Buffer upgrade: Pipeline to Memory, write address to FIFO, handles event overlap
Pipeline
L1A
Event n
Event n+1
Address FIFO
Write Addr
Data Transmission
Data Transmission
Read Addr

## Slide 4: SEM Controller
Xilinx Virtex 6 has built-in feature for Soft Error Mitigation
  Continuously reads configuration memory and checks each frame for errors.
  If single bit errors exist, it corrects the error and re-writes the frame.
But the built in feature has known issues.
  Experts suggest using the SEM Controller IP core.
The SEM Controller:
  Utilizes the built-in feature to do continuous readback and CRC checking
  Handles correcting single bit errors
  Has port for injecting errors for testing

## Slide 5: SEM Controller
Taken from Xilinx document PG036

## Slide 6: SEM Controller
Taken from Xilinx document PG036

## Slide 7: SEM Controller
Expected sequence of events:
  Goto Idle state
  Inject error
  Error recognized by Frame_ECC_Virtex6 primative
  Goto Observation state
  Error detected
  Goes to Correction state
  Writes corrected frame through ICAP_Virtex 6 primitive
  Passes through classification state
  Back to Observation state.
What we see:
  In Correction state, “uncorrectable” bit set and goes back to Idle.