## Slide 1: GEM Design Plans
Jason Gilmore
TAMU Workshop
1 Oct 2013

## Slide 2: The CMS GEM project : Global Requirements on Electronics
GEM detectors
Triggering
Tracking
Provide full granularity tracking data on receipt of a L1A
  Full resolution not available before L1A ?
Be compatible with CMS trigger upgrade possibilities
  LV1A latency < 20us
  LV1A rate < 1MHz Poisson
Provide Trigger & Tracking data from all GE1/1 GEM Chambers
Provide “Fast OR” trigger information with granularity of 2 or 4 channels to send locally to CSC TMB.
Timing resolution <8ns.
Design optimized for GEM detectors
  Use CERN common Projects where possible (GBTs & Versatile Link)

## Slide 3: GEM Front-End Electronics Geometry
GEMs are logically divided by columns in phi and partitions in eta
  Each region is 128 strips wide
  Read out with a VFAT3 chip
3 columns
6, 8, 10 partitions
VFAT3 chips
GEM hit location encoding:
  Column (2 bits)
  Partition (3-4 bits)
  Trigger Pad ID (5-6 bits)
Total: 10-12 bits (most likely 10 bits)
GEM data to OTMB over 2 fiber links:
  96 bits/BX using DCFEB fiber protocol
  Encode up to 9 GEM pad hits
  Negligible probability to have more than 9 hits in a GEM chamber

## Slide 4: VFAT3 Front-End Chip Separated Trigger & Tacking (STT)
Fixed Latency trigger path: “S” bits
Tracking path,
After L1A
This is the favorite architecture for CMS

## Slide 5: Trig Unit
Synchronous to LHC Bx, Reduced granularity to 2 or 4 strips
Example 1: (1 bit per 2 channels)
Trigger granularity = 2 strips,
Frequency = 320Mbps
send 64 bits per Bx
7/8 bit encoding ?
10 slvds O/Ps = 70 bits / bx
1 bit for clock tick (sync)
5 bits spare
(Example 1.2): (1 bit per 4 channels)
Trigger granularity = 4 strips,
Frequency = 320Mbps
send 32 bits per Bx
7/8 bit encoding ?
5 slvds O/Ps = 35 bits / bx
1 bit for clock tick (sync)
2 bits spare
Both require Data Concentrator ASIC or FPGA to :
Gather Trigger signals from 24 VFAT3s
Encode addresses of hits to include chip location
Transmit to dedicated trigger GBT or optical Tx
Example 2: Encode (7 bits) + next ch
Trigger granularity = 1 strip,
Max 8 hit channel addresses + neighbor
Frequency = 320Mbps
No 7/8 bit encoding
8 slvds O/Ps = 80 bits / bx
1 slvds O/P for clock sync
Example 2.2: Encode (6 bits) + next ch
Trigger granularity = 2 strips,
Max 8 hit channel addresses + neighbor
Frequency = 320Mbps
7/8 bit encoding
8 slvds O/Ps = 80 bits / bx
1 slvds O/P for clock sync
Channel address hit
Neighbor hit
1 bit per hit
1)
2)
(Can incur losses)
(lossless)

## Slide 6: Separated Trigger & Tracking Plan [Fixed Latency Trigger ASIC (FPGA)]
Trig data
(encoded S-bits)
TMB
uTCA
Concentrator & Encoding: FPGA
24*DataOut
@ 320Mbps
“S” signals @ 320Mbps
Bandwidth = 3.2Gbps
24 VFAT3 (STTP version)
TRIGGER PATH
Fixed Latency Trigger
If granularity = 2 strips > 1536 addresses (11 bit address)
If granularity = 4 strips > 768 addresses (10 bit address)
Aim : Keep complexity of concentrator chip low
GBT
GBT
GBT
GBT
Data PATH
Full granularity
(non zero suppressed)
1GBT for 8 VFATs
VFAT3
STT

## Slide 7: CMS GEM Electronics Overview
GBT readout
Direct e-link communication between front-ends and GBT
No Separate path for trigger.
Trigger path to external systems at uTCA level.
Optical path to uTCA relies n GBT ASIC development

## Slide 8: CMS GEM Electronics System Development
VFAT3 under design
Hybrid development underway
GEM_PCB (CERN)
Development underway
Opto hybrid (ULB):
Hardware design started
Using CERN common Projects
(GBTs & Versatile Link)
& collaboration with TAMU & TAMUQ
GLIBs
Common CERN development
AMC13 from Boston Uni.
uTCA
CMS standard for upgrades
Development (ULB)
Interface to CMS
CAEN power supplies
Initial prototype : Using VFAT2 + Opto hybrid (without GBT) + uTCA
Final prototype : VFAT3 + Opto hybrid with GBT + uTCA
……. Under development
……. Foreseen for 2016

## Slide 9: Prototype Development Plan
30x30
Full size prototype
To evaluate GEB (GEM Electronic Board), VFAT hybrid, cooling mechanics.
VFAT2
Erni to Erni
Turbo
VFAT2
Opto hybrid
uTCA
VFAT2
Opto hybrid
VFAT3
Opto hybrid 2
VFAT3 + Final Optohybrid with FPGA + GBT
uTCA
TMB
uTCA
TMB
uTCA
TMB
Optional step : Small uTCA setup, allows opto hybrid, uTCA and DAQ software development
Full size setup, allows opto hybrid, uTCA, DAQ software and link to CSC TMB
Optional step : If GBT project is delayed
Final setup with VFAT3 and GBT
VFAT2
uTCA
ULB: Software communication to VFAT2 through uTCA
3rd q 14
3rd q 15
2nd q 13
3rd q 13
4th q 13
3rd q 15