ArcPic simulations
results updates
13/8/2013
Kyrre Sjøbæk

---
Outline
- New analysis
  - Cathode field
  - Electric field
  - Particle impacts
  - Currents
- Plasma oscillations during breakdown
  - Convergence check for superparticle ratio
- Heat spike sputtering
Most data here presented via “standard” run, as usual
However some data has been produced at lower superparticle ratio (~5 vs. ~21 => better statistics)

---
New cathode field analysis
- Plotting the field on the cathode as a function of time
- Clearly see the strong increase in field when ignition happens
- Pre-breakdown field sign flipping due to space charge also visible
- Radius of high field region
  ~= 0.4 µm = injection radius...
- When breakdown occurs, precursor + “overshoot”
- Some post-breakdown oscillation visible

---
New electric field analysis
- Plotting the field in the volume
- Field patterns surprisingly complicated!
No field!
Just before breakdown
Just after breakdown
Field emission
dt = 0.01 ns

---
New electric field analysis
R- and Z-fields also complex
(Zoomed in)

---
New electric field analysis

---
Particle impacts
- Energy spectrum shows lower peak than found in 1D
- Consistent with sheath voltage
  ≈> 50 V

---
Particle impacts
Also interesting: Correlations with time, impact radius, and energy

---
Currents
- Slow oscillation during breakdown clearly visible
- Noisy electron emission,
  especially before breakdown
- Some particles escape through side wall, but this is far from the plasma => system large enough
Smooth

---
Plasma oscillations
during breakdown
- Visible on previous plots
- Frequency 30 GHz
- Also visible in field- and
  particle plots
- Weaker when increasing the superparticle ratio, but
  frequency constant
Nsp = 5.3
Nsp = 21
Nsp = 10.6

---
Heat spike sputtering
- Old model:
  If ion current* > 107 A** in ANY cell, emit 1000 Cu superparticles and no Yamamura-Tawara sputtering
- New model:
  If Cu current* > threshold T,
  emit Cu with yield Y in addition to Yamamura-Tawara sputtering (Y<= 20)
- In new model, threshold checked for circular areas with increasing r
- If average current within any such area > T => heatspike
- Heatspike radius = radius of largest area fulfilling condition
- Scanning T and Y
- If T or Y too high => runaway
- If T or Y too low, no effect
*) Only count particles with energy > 23.383 eV
**) 107 A = 6.24*1025 ions/cm2/s

---
Heat spike sputtering
NOT caused by heat spikes
(but sometimes causing)

---
Heat spike sputtering