## Slide 1
Lars V. Jørgensen, BE-OP
ELENA Review – Oct. 14, 2013
The ELENA Electron Cooler - Requirements and
Magnet System

## Slide 2: The Need for Electron Cooling
Electron cooling essential in ELENA to counter emittance blow-up caused by the deceleration process.
To prepare bunches with sufficiently low emittance for extraction to the experiments via the electrostatic extraction lines.
Cooling needed at 2 momenta: 35 MeV/c and 13.7 MeV/c.
Expected emittances prior
to cooling:
@ 35 Mev/c:
ε ~ 50 π mm mrad
(Δp/p) = ± 2 × 10-3
Needed emittances at extraction:
ε ≤ ~ 3 π mm mrad
(Δp/p) ≤ ± 1 × 10-3

## Slide 3: General requirements
Must be very compact!
Must fit in Section 4 incl. solenoid compensators and correctors.
~ 2 meters available for the electron cooler.
Space constraints also necessitate 90°bends on relatively small radius (25 cm)
E-cooler length

## Slide 4: Further requirements
Operate at very low electron energies (down to 55 eV).
Operate at very low magnetic field to minimize disturbance to circulating low energy antiprotons – we have chosen 100 Gauss in the cooler.
Have extremely good vacuum.
Adiabatic expansion to reduce transverse temperatures.
Very good field quality – especially in the cooler solenoid (B˔/Bǁ < 5 × 10-4 ).
Orbit correctors and solenoid compensators.

## Slide 5: Electron Cooler parameters
Momentum (MeV/c) | 35 | 13.7
β | 0.037 | 0.015
Electron beam energy (eV) | 355 | 55
Electron current (mA) | 5 | 2
Electron beam density (m-3) | 1.38 x 1012 | 1.41 x 1012
Bgun (G) | 1000 | 
Bdrift (G) | 100 | 
Expansion factor | 10 | 
Cathode radius (mm) | 8 | 
Electron beam radius (mm) | 25 | 
Twiss parameters (m) | βh=2.103, βv=2.186, D=1.498 | 
Flange-to-flange length (mm) | 1930 | 
Drift solenoid length (mm) | 1000 | 

## Slide 6: Kyoto connection
- requirements lead us to look for inspiration at the very compact and relatively low energy e-cooler built by Toshiba Corp. for the S-LSR ring in Kyoto.
S-LSR electron cooler | 
Magnetic field uniformity in drift solenoid | 5×10-4
Electron beam energy (keV) | 1-5
Electron current (mA) | 50-400
Gun perveance (µP) | 2.2
Bgun (G) | 1500
Bdrift (G) | 500
Expansion factor | 3
Cathode radius (mm) | 15
Electron beam radius (mm) | 25
Twiss parameters | βh=1.7, βv=2.4
Bending radius (mm) | 250
Drift solenoid length (mm) | 800

## Slide 7: The magnet system
Magnetic system components
Main cooler solenoid
Gun solenoid
Collector solenoid
Expansion solenoid
Reverse coil at collector
2 x Toroid section consisting of
9 racetrack coils each
Various corrector coils to
ensure good field quality
Orbit correctors
Solenoid compensators

## Slide 8: Correction coils
Double Helmholtz transverse correctors for the 3 main solenoids – to correct for stray fields and other remnant static fields
End winding correctors on 3 main solenoids – in case it is needed!
Main Y correctors at the end of the cooler solenoid – crucial to extend the good field region
Several (up to 8) small Y correctors inside the cooler solenoid – for fine tuning the good field region
Coils inside the toroid section to steer the electrons – if needed
Toroid kick orbit correctors just outside the toroids – to cancel out the kick to the antiprotons from the toroids
Solenoid compensators further out – to cancel out the horizontal-vertical coupling induced by the solenoid field

## Slide 9: The whole package
The whole system will be shielded to attain better field quality and to exclude stray fields - ~ 1 Gauss in the area of the AD where it will be installed.
The electron cooler will be mounted horizontally for ease of maintenance.

## Slide 10: Orbit correctors
Two types of orbit correctors have been studied:
Kyoto-style
Standard
Kyoto-style is more compact
Standard is based on an existing LINAC4 design and offers the possibility of a local bump (steering in both directions)

## Slide 11: Axial field - electrons
Chart: Distance from center of drift magnet [cm]
Chart: Distance from center of drift magnet [cm]
Chart: Distance from center of drift magnet [cm]
Axial field without correction
Conclusion: The expansion coil has a significant influence on the axial field in the drift solenoid.

## Slide 12: Transverse field - electrons
Transverse field without correction
Conclusion: Moving the expansion coil further away makes the field at the center of the drift solenoid flatter and much easier to correct.
Chart: Distance from center of drift magnet [cm]
Chart: Distance from center of drift magnet [cm]
Chart: Distance from center of drift magnet [cm]

## Slide 13: Orbit correctors
Chart: Distance from center of drift solenoid [cm]

## Slide 14: Axial field - antiprotons
Chart: Distance from center of drift solenoid [cm]
Chart: Distance from center of drift solenoid [cm]
Final field incl. all transverse and orbit correctors

## Slide 15: The good field region
Chart: Distance from center of drift solenoid [cm]
Standard: B˔/B║ < ±3 × 10-4 for 63 cm
77 A/cm2 in orbit correctors 14 A/cm2 in US transverse corrector 7 A/cm2 in DS transverse corrector
Kyoto: B˔/B║ < ±5 × 10-4 for 65 cm
32 A/cm2 in orbit correctors 14 A/cm2 in US transverse corrector 7 A/cm2 in DS transverse corrector

## Slide 16: Orbit correctors and bumps
The standard orbit correctors take up more space – and we would have to go to a different design to be able to make a sizeable local bump – but luckily we have a little space left over!