## Slide 1: ELENA Vacuum System R. Kersevan, TE-VSC-IVM
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN

## Slide 2
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Agenda
Machine physics vacuum requirements
Materials, requirements
Expected gas loads and pumping speeds
Lattice Design and Integration Issues
Vacuum Sectoring and Pumping
Conclusions

## Slide 3
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Machine physics vacuum requirements
This translates into an average pressure at the lower limit of Ultra-High Vacuum Range:
Paverage < 3.0E-12 Torr ( < 4E-12 mbar) N2-equiv.!!
C. Carli, this review.

## Slide 4
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Materials
Requirements:
Availability, Cost
Known Cleaning Procedures
Low Magnetic Permeability
Weldability
Low Outgassing Rate
Capable to Sustain Bake-Out up to 250 ºC
Reliable Sealing Techniques
Requirements 1 through 7 identify 316 LN Stainless-Steel as the Material of Choice, With ConFLat Flanges to be Used Anywhere Possible

## Slide 5
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Expected Gas Loads and Pumping Speeds
The (very) initial estimate of the expected gas load and pumping scheme/requirements dates to this meeting…
(presentation by P. Chiggiato, TE-VSC-IVM)
Today’s Update:
Estimated total geometric area of vacuum chamber: ~10 m2
Estimated total outgassing rate at 1.0E-12 Torr*l/s/cm2:
1~5E-7 Torr*l/s

## Slide 6
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
… and also sufficient space for bellows, gate valves, etc… : GREAT!
The initial lattice seemed to leave sufficient space for installing lumped pumps in each straight section (plus,eventually,one pump on each dipole)…
Lattice Design and Integration Issues

## Slide 7
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
… but once all machine/diagnostic components have been designed, the space for pumps has been reduced by a lot…
X
X
Lattice Design and Integration Issues

## Slide 8
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Lattice Design and Integration Issues: Ring

## Slide 9
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Details of injection septum/kicker tank and magnet
Lattice Design and Integration Issues: Sector 1 (case study)
2x Coaxial BPMs
Injection Septum Tank w/ Kicker

## Slide 10
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Lattice Design and Integration Issues: Sector 1
Details of injection septum/kicker tank and magnet
Latest Version

## Slide 11
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Lattice Design and Integration Issues: Sector 1
Details of injection septum/kicker tank and magnet
Bad conductance to 500 l/s Ion-Pump (plate under magnet)
1000 l/s NEXTorr pump added
NEG-coating of Tank MANDATORY
Average Pressure Along Section is at the Limit the 3E-12 Torr Specification

## Slide 12
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Lattice Design and Integration Issues: Sector 1
Details of injection septum/kicker tank and magnet

## Slide 13
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Lattice Design and Integration Issues: Sector 2
Details of Coaxial BPMs
NEG-coating of ALL surfaces inside BPMs MANDATORY
Bellows convolutions contribute significantly to outgassing (larger surface per unit length), will be coated too

## Slide 14
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Vacuum Sectoring
Sector
Gate Valves
(GV)
Lattice Design and Integration Issues
Outcome: unevenly long vacuum sectors

## Slide 15
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Expected Gas Loads and Pumping Speeds
Vacuum Sectors
Vacuum Sectoring and Pumping

## Slide 16
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Expected Gas Loads and Pumping Speeds
Pumps
NEXTorr
(NEG pump with integrated Ion-pump)
Or
Ion-Pumps
2x
Vacuum Sectoring and Pumping
16 Bellows in the straight sections
+ 6x2 on Dipoles

## Slide 17
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Vacuum Sectoring and Pumping
“NEXTorr D300” integrated NEG/Ion-pump (SAES Getters, Milan)
ELENA will employ either D1000 or D2000 models (i.e. 1000 or 2000 l/s @H2) on dipoles, and D300 on cylindrical chambers except on injection and extraction elements, cavities, where higher gas loads and localized pressure bumps may be expected. Ion-Pumps will be installed there.
Note how the pumping speed of the ion-pump (StarCell,Agilent) decreases with the pressure, while the speed for the NEG-pump is pressure independent

## Slide 18
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Vacuum Sectoring and Pumping
Zero Pumping Speed on Sect.1 Straight Section Pump: 5% increase of <P> at Sect.1
Switch-off or malfunction of SS1 NEG/Ion-Pump means ~ 5% pressure rise DPH2 at Sect.1, i.e. DPH2< 1% over complete ring.

## Slide 19
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Conclusions:
The design of the vacuum system of the ELENA ring is being finalised.
All major integration issues (but 1, refer to 7 below) have been solved
The material chosen for the vacuum chambers is 316 LN stainless-steel
Conical ConFlat flanges (PS-type geometry) with collar are implemented everywhere except on gate valves, cavities, and injection/extraction devices. This saves us some space,longitudinally, as they do not need to have available the length of the screws
NEG-coating will be applied as much as possible
Extensive numerical modeling of the pressure distributions show that the pressure specification compatible with the operation of the machine will be met (Paverage < 3.0E-12 Torr)
Only notable vacuum issue not solved yet is the reduction of H2 gas leaking out of the H+/- commissioning source (see talk by T.Eriksson on Tue 15/10). A dedicated differential pumping system is under study.

## Slide 20
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Conclusions (cont.):
The ELENA transfer lines (TL) to the experiments will be made using as much as possible a repetitive modular design (not discussed here, see W.Bartmann’s presentation)
Optimization of the pumping speed of the fast switching electrostatic elements has been initiated. Preliminary calculations show that pressures in the low 1.0E-10 Torr should be easily reached
Pumping of the TLs will either be obtained via ion-pumps of NEG-pumps. NEG-coatings only if extremely low pressure will be needed bu experiments (TBD)
The fabrication of the modified AD extraction line (“Line 7000”) has been started
Tests on thin-film heating devices will be done shortly
Modifications/re-cabling of the control cabinets for vacuum controllers is underway (within LS1 program)
The e-cooler design and integration has not been done yet (other than identifying the available space in Sector 4). See G. Tranquille’s presentation for further details.
Thanks for your attention! 

## Slide 21
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Bonus:
ATRAP ES Switchyard, With Lenses and Beam Diagnostic Device

## Slide 22
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Bonus:
Cross-section of the chamber through the plane of the orbit

## Slide 23
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Bonus:
Pressure Profile, With and Without NEG-Coating on Tanks, Item on Previous Page

## Slide 24
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Bonus:
Area yet to be defined in detail…

## Slide 25
R. Kersevan, “ELENA Vacuum System”, - ELENA Project Review, Oct14-15, 2013, CERN
Bonus:
Differential Pumping Concept for H-/+ Commissioning Injector