## Slide 1: ECFA Workshop: Calorimetry PG
Francesco Lanni – ATLAS BNL
Marcello Mannelli – CMS CERN
Alberto Valero (ATLAS), Arno Straessner (ATLAS)
David Barney (CMS), Pawel de Barbaro (CMS)
David Silvermyr (ALICE), Frederic Machefert (LHCb)

## Slide 2: Proposed Agenda
30’ Introduction and Overview of Physics Goals and Calorimeter Requirements
  Marcello
30’ Calorimeter Electronics: Longevity issues and/or new requirements and resulting upgrades
  Arno Straessner
45’ Calorimeter Detectors: Longevity issues and/or new requirements and resulting upgrades
  Pawel de Barbaro
15’ Summary and Conclusions
  Francesco

## Slide 3: Summary of Input to Report I
Providing highest possible granularity & resolution Calorimeter information for the L1 Trigger is a common goal for both ATLAS and CMS
  Requires Major Calorimeter Electronics Upgrades
Key enabling technologies are
  High speed optical data links, with manageable power
  High performance back-end systems (uTCA, ATCA)
Other system aspects are also concerned, eg Power System
  Bulk supplies in counting room and/or cavern
  On –Detector DC-DC conversion, etc

## Slide 4: Summary of Input to Report II
For the calorimeters themselves, the major upgrades concern the CMS End-Caps
  The ATLAS End-Cap LAr calorimeters are intrinsically radiation hard
    The FCAL may suffer due to the high instantaneous rates, and may need to be replaced
    The HEC cold electronics may need to be replaced, necessitating opening of the cryostat
  The LHCb ECAL may require substituting some of the modules closest to the beam, for which existing spares may suffice
  ALICE is considering the possible addition of a Forward Calorimeter, after LS2

## Slide 5: Summary of Input to Report III
For the calorimeters themselves, the major upgrades concern the CMS End-Caps
  The performance of the CMS EndCap ECAL and HCAL would substantially degrade at HL-LHC, and both must be replaced
A targeted R&D program is underway to meet the challenges of replacing the CMS End-Cap calorimeters
Different options are under study

## Slide 6: Summary of Input to Report IV
Option I
  Replace the present homogenous Crystal ECAL with a radiation tolerant Crystal sampling calorimeter
  Replace the present Plastic Scintillator sampling HCAL with a radiation tolerant Plastic Scintillator sampling calorimeter
Option II (Integrated approach)
  Particle Flow / Imaging Gas Sampling Calorimeter
  Dual Read Out, Cerenkov/Scintillator Sampling Calorimeter

## Slide 7: Status and Plans
Outlines of the Electronics and Calorimeter presentations for the ECFA calorimeter session exist, and are linked to the Twiki
  Have discussed with Magnus and Philippe to ensure consistency & manage overlaps with Electronics session
The plan is to finish collecting the necessary material by Sept 6, and have preliminary drafts of the presentations by Sept 13
  Most of the material if available, some plots may still require approval
Meet to Review talks (Electronics & Detectors): Sept 17
Meet to Review input to Summary document: Sept 19
Final Rehearsal of ALL the talks: Sept 23

## Slide 8: Backup

## Slide 9: Abstracts
Introduction and Overview:
Physics goals and calorimeter requirements
We discuss how the HL-LHC luminosity target and Phase II physics goals drive the Calorimeter performance requirements of the LHC experiments, and motivate the program of Upgrades being developed to address these. The need to provide more detailed information to the L1 Trigger at 40MHz, in order to maintain the necessary physics acceptance, imposes new requirements on the calorimeter electronic systems. The extremely high levels of integrated luminosity and radiation damage, on top of the very high occupancy resulting from the increased instantaneous luminosity, place stringent demands on the calorimeter systems and detectors. Together, these require a substantial program of upgrades in order to maintain functionality throughout the HL-LHC, and fully exploit its physics potential.

## Slide 10: Abstracts
Calorimeter Detectors: Longevity issues and/or new requirements and resulting upgrades
Although the instantaneous and integrated luminosity in HL-LHC will be far higher than the LHC detectors were originally designed for, the Barrel calorimeters of the four experiments are expected to continue to perform well throughout the Phase II program. The conditions for the End-Cap calorimeters are far more challenging and whilst some detectors will require relatively modest changes, others require far more substantial upgrades.
We present the results of longevity and performance studies for the calorimeter systems of the four main LHC experiments and outline the upgrade options under consideration. We include a discussion of the R&D required to make the final technology choices for the upgraded detectors.

## Slide 11: Abstracts
Calorimeter Electronics: Longevity issues and/or new requirements and resulting upgrades
Operations during the HL-LHC era will impose challenges on the calorimeter electronics both for the main readout and the trigger systems. Aging, radiation tolerance limits and new requirements from the trigger result in the need for substantial upgrades of the calorimeter electronics. We review the evolution of the readout architecture, the strategies and the technical developments in the front-end and back-end electronics as pursued by the calorimeter groups in the four LHC experiments, both emphasizing common aspects as well as pointing out issues specific to a given experiment.

## Slide 12: Abstracts
Summary and Conclusions
We summarize the challenges and the required developments to the calorimeter systems of the LHC experiments, for operation at HL-LHC. While the different technologies adopted for the existing calorimeter systems have a specific impact on the upgrade plans of each experiment, common requirements and strategies can nonetheless be identified, suggesting possible synergies for the developments in either detector, readout and trigger electronics. A few examples are analyzed. A possible roadmap is outlined together with required resources, for example in terms of R&D infrastructures and technology transfer among collaborations.