## Slide 1
Electron cloud build-up in the inner triplets (IP1-5)
G. Iadarola, G. Rumolo
Electron cloud meeting – 10/09/2013
Many thanks to:
H. Bartosik, N. Mounet, B. Salvant, L.Tavian, R. Tomas, C. Zannini

## Slide 2
Outline
  Introduction
  Simulating the inner triplets in PyECLOUD
  Simulation results
  Machine observations (heat load)
  Some considerations on e- - beam interaction
  Endoscopy observations

## Slide 3
Outline
  Introduction
  Simulating the inner triplets in PyECLOUD
  Simulation results
  Machine observations (heat load)
  Some considerations on e- - beam interaction
  Endoscopy observations

## Slide 4
Machine layout and optics near IP1
  Common beam pipe
  Separated beam pipes
  Separated beam pipes
  IP1
  IP1, 4 TeV, β* = 0.6 m

## Slide 5
B2L1
A2L1
3L1
1L1
Machine layout and optics near IP1
  IP1, 4 TeV, β* = 0.6 m
  IP1
1R1
A2R1
B2R1
3R1

## Slide 6
B2L1
A2L1
3L1
1L1
Machine layout and optics near IP1
  IP1, 4 TeV, β* = 0.6 m
  IP1
1R1
A2R1
B2R1
3R1

## Slide 7
  IP1, 4 TeV, β* = 0.6 m
B2L1
A2L1
3L1
1L1
Machine layout and optics near IP1
  IP1
1R1
A2R1
B2R1
3R1

## Slide 8
  IP1, 4 TeV, β* = 0.6 m
B2L1
A2L1
3L1
1L1
Machine layout and optics near IP1
  IP1
1R1
A2R1
B2R1
3R1

## Slide 9
  IP1, 4 TeV, β* = 0.6 m
B2L1
A2L1
3L1
1L1
Machine layout and optics near IP1
  IP1
1R1
A2R1
B2R1
3R1

## Slide 10
Machine layout and optics near IP1
  IP1, 4 TeV, β* = 0.6 m
  IP1
1R1
A2R1
B2R1
3R1

## Slide 11
Machine layout and optics near IP1
  IP1, 4 TeV, β* = 0.6 m
  IP1
1R1
A2R1
B2R1
3R1

## Slide 12
Machine layout and optics near IP1
  IP1, 4 TeV, β* = 0.6 m
  IP1
1R1
A2R1
B2R1
3R1

## Slide 13
Machine layout and optics near IP1
  IP1, 4 TeV, β* = 0.6 m
  IP1
1R1
A2R1
B2R1
3R1

## Slide 14
IP1 vs. IP5
  IP1, 4 TeV, β* = 0.6 m
  IP5, 4 TeV, β* = 0.6 m
  Crossing angle in the V plane
  Crossing angle in the H plane
  Due to symmetry considerations it is sufficient to study only one of the inner triplets

## Slide 15
IP1 vs. IP5
  Due to symmetry considerations it is sufficient to study only one of the inner triplets
B1
B2
B2
B1
B2
B1
B2
B1

## Slide 16
The longitudinal direction
  The delay between two following bunch passages changes along the machine elements
  Locations of long range encounters spaced by half the bunch spacing
7.5 m
Beam 2
Beam 1
  IP1
  25 ns spac.

## Slide 17
The longitudinal direction
  The delay between two following bunch passages changes along the machine elements
  Locations of long range encounters spaced by half the bunch spacing
7.5 m
Beam 2
Beam 1
  IP1
  25 ns spac.

## Slide 18
The longitudinal direction
  The delay between two following bunch passages changes along the machine elements
  Locations of long range encounters spaced by half the bunch spacing
7.5 m
Beam 2
Beam 1
  IP1
  25 ns spac.

## Slide 19
The longitudinal direction
  The delay between two following bunch passages changes along the machine elements
  Locations of long range encounters spaced by half the bunch spacing
7.5 m
Beam 2
Beam 1
  IP1
  25 ns spac.

## Slide 20
The longitudinal direction
  The delay between two following bunch passages changes along the machine elements
  Locations of long range encounters spaced by half the bunch spacing
7.5 m
Beam 2
Beam 1
  IP1
  25 ns spac.

## Slide 21
The longitudinal direction
  The delay between two following bunch passages changes along the machine elements
  Locations of long range encounters spaced by half the bunch spacing
7.5 m
Beam 2
Beam 1
  IP1
  25 ns spac.

## Slide 22
The longitudinal direction
  The delay between two following bunch passages changes along the machine elements
  Locations of long range encounters spaced by half the bunch spacing
7.5 m
Beam 2
Beam 1
  IP1
  25 ns spac.

## Slide 23
The longitudinal direction
  The delay between two following bunch passages changes along the machine elements
  Locations of long range encounters spaced by half the bunch spacing
7.5 m
Beam 2
Beam 1
  IP1
  25 ns spac.

## Slide 24
The longitudinal direction
  The delay between two following bunch passages changes along the machine elements
  Locations of long range encounters spaced by half the bunch spacing
7.5 m
Beam 2
Beam 1
  IP1
  25 ns spac.

## Slide 25
The longitudinal direction
  The delay between two following bunch passages changes along the machine elements
  Locations of long range encounters spaced by half the bunch spacing
7.5 m
Beam 2
Beam 1
  IP1
  25 ns spac.

## Slide 26
The longitudinal direction
  The delay between two following bunch passages changes along the machine elements
  Locations of long range encounters spaced by half the bunch spacing
7.5 m
Beam 2
Beam 1
  IP1
  25 ns spac.

## Slide 27
The longitudinal direction
  The delay between two following bunch passages changes along the machine elements
  Locations of long range encounters spaced by half the bunch spacing
7.5 m
Beam 2
Beam 1
  IP1
  25 ns spac.

## Slide 28
The longitudinal direction
  The delay between two following bunch passages changes along the machine elements
  Locations of long range encounters spaced by half the bunch spacing
15 m
Beam 2
Beam 1
  IP1
  50 ns spac.

## Slide 29
Outline
  Introduction
  Simulating the inner triplets in PyECLOUD
  Simulation results
  Machine observations (heat load)
  Some considerations on e- - beam interaction
  Endoscopy observations

## Slide 30
PyECLOUD simulations for the inner triplets
  A quite challenging simulation scenario:
  Two beams with:
    Different transverse position (off center)
    Different transverse shape
    Arbitrarily delayed with respect to each other (no real bunch spacing)

## Slide 31
PyECLOUD simulations for the inner triplets
  A quite challenging simulation scenario:
  Two beams with:
    Different transverse position (off center)
    Different transverse shape
    Arbitrarily delayed with respect to each other (no real bunch spacing)
  Quadrupolar magnetic field
  Non elliptical chamber

## Slide 32
PyECLOUD simulations for the inner triplets
  A quite challenging simulation scenario:
  Two beams with:
    Different transverse position (off center)
    Different transverse shape
    Arbitrarily delayed with respect to each other (no real bunch spacing)
  Quadrupolar magnetic field
  Non elliptical chamber
Required the introduction of new features in PyECLOUD

## Slide 33
PyECLOUD simulations for the inner triplets
  A quite challenging simulation scenario:
  Two beams with:
    Different transverse position (off center)
    Different transverse shape
    Arbitrarily delayed with respect to each other (no real bunch spacing)
  Quadrupolar magnetic field
  Non elliptical chamber
Required the introduction of new features in PyECLOUD
  Beam properties (delay, position, size) changing along the structure:
  Simulated 10 slices per magnet
  SEY = 1.0, 1.1, … , 2.0
  50 ns and 25 ns

## Slide 34
PyECLOUD simulations for the inner triplets
  A quite challenging simulation scenario:
  Two beams with:
    Different transverse position (off center)
    Different transverse shape
    Arbitrarily delayed with respect to each other (no real bunch spacing)
  Quadrupolar magnetic field
  Non elliptical chamber
Required the introduction of new features in PyECLOUD
  Beam properties (delay, position, size) changing along the structure:
  Simulated 10 slices per magnet
  SEY = 1.0, 1.1, … , 2.0
  50 ns and 25 ns
~1000 simulations,
~48 h for two bunch trains,
~120 GB of sim. data

## Slide 35
# SIMULATION PARAMETERS
machine_param_file='machine_parameters.input'
secondary_emission_parameters_file='secondary_emission_parameters.input'
beam_parameters_file='beam1.beam'
secondary_beams_file_list = ['beam2.beam']
logfile_path = './logfile.txt'
progress_path = './progress.txt'
Dt=25e-12 #s (no effect if long. profile is imported from file)
t_end=1e-9; #s (no effect if long. profile is imported from file)
lam_th=1.e2 #e-/m
Dx_hist=1.e-3 #m
r_center=2.e-3 #m
Dt_En_hist = 25e-9 #s
Nbin_En_hist= 100
En_hist_max= 1000. #eV
...
  simulation_parameters.input
  Features available in PyECLOUD 3.06 or later:
  Optional input to specify secondary beam parameter files
PyECLOUD simulations for the inner triplets

## Slide 36
# SIMULATION PARAMETERS
machine_param_file='machine_parameters.input'
secondary_emission_parameters_file='secondary_emission_parameters.input'
beam_parameters_file='beam1.beam'
secondary_beams_file_list = ['beam2.beam']
logfile_path = './logfile.txt'
progress_path = './progress.txt'
Dt=25e-12 #s (no effect if long. profile is imported from file)
t_end=1e-9; #s (no effect if long. profile is imported from file)
lam_th=1.e2 #e-/m
Dx_hist=1.e-3 #m
r_center=2.e-3 #m
Dt_En_hist = 25e-9 #s
Nbin_En_hist= 100
En_hist_max= 1000. #eV
...
  simulation_parameters.input
  Features available in PyECLOUD 3.06 or later:
  Optional input to specify secondary beam parameter files
  The main beam file is the one that gives timings during the simulations (steps, spacings for macroparticle cleaning and regeneration, length of the simulation  add empty buckets if other beam is longer!)
PyECLOUD simulations for the inner triplets

## Slide 37
# BEAM PARAMETERS
energy_eV= 4000e9 #eV
nemittx = 2.4e-6
nemitty = 2.4e-6 #m
betafx = 9.454233e+02
betafy = 9.595226e+02
x_beam_pos = 5.915084e-11
y_beam_pos = -3.478057e-03
beam_field_file =-1
Dh_beam_field=0.5e-4
#save_beam_field_file_as = 'beam1field.mat'
b_spac = 50e-9
fact_beam = 1.65e+11
flag_bunched_beam = 1 # 1: bunched beam 0:load profile from file
# to be filled in case of bunched beam
sigmaz = 0.097 #1.3ns
t_offs = 2.5e-9 + 2.*2.389798e+01/299792458.
filling_pattern_file = 2*(4*(36*[1.]+4*[0.])+15*[0.])
  beam2.beam
  Features available in PyECLOUD 3.06 or later:
  Beam size and position can be defined for each beam
PyECLOUD simulations for the inner triplets

## Slide 38
# BEAM PARAMETERS
energy_eV= 4000e9 #eV
nemittx = 2.4e-6
nemitty = 2.4e-6 #m
betafx = 9.454233e+02
betafy = 9.595226e+02
x_beam_pos = 5.915084e-11
y_beam_pos = -3.478057e-03
beam_field_file =-1
Dh_beam_field=0.5e-4
save_beam_field_file_as = 'beam1field.mat'
b_spac = 50e-9
fact_beam = 1.65e+11
flag_bunched_beam = 1 # 1: bunched beam 0:load profile from file
# to be filled in case of bunched beam
sigmaz = 0.097 #1.3ns
t_offs = 2.5e-9 + 2.*2.389798e+01/299792458.
filling_pattern_file = 2*(4*(36*[1.]+4*[0.])+15*[0.])
  beam2.beam
  Features available in PyECLOUD 3.06 or later:
  The electric field of the beam can be calculated using the embedded Poisson solver
PyECLOUD simulations for the inner triplets

## Slide 39
# BEAM PARAMETERS
energy_eV= 4000e9 #eV
nemittx = 2.4e-6
nemitty = 2.4e-6 #m
betafx = 9.454233e+02
betafy = 9.595226e+02
x_beam_pos = 5.915084e-11
y_beam_pos = -3.478057e-03
beam_field_file =-1
Dh_beam_field=0.5e-4
save_beam_field_file_as = 'beam1field.mat'
b_spac = 50e-9
fact_beam = 1.65e+11
flag_bunched_beam = 1 # 1: bunched beam 0:load profile from file
# to be filled in case of bunched beam
sigmaz = 0.097 #1.3ns
t_offs = 2.5e-9 + 2.*2.389798e+01/299792458.
filling_pattern_file = 2*(4*(36*[1.]+4*[0.])+15*[0.])
  beam2.beam
  Features available in PyECLOUD 3.06 or later:
  The electric field of the beam can be calculated using the embedded Poisson solver
  Beam field can be dumped to file:
PyECLOUD simulations for the inner triplets

## Slide 40
# BEAM PARAMETERS
energy_eV= 4000e9 #eV
nemittx = 2.4e-6
nemitty = 2.4e-6 #m
betafx = 9.454233e+02
betafy = 9.595226e+02
x_beam_pos = 5.915084e-11
y_beam_pos = -3.478057e-03
beam_field_file =-1
Dh_beam_field=0.5e-4
save_beam_field_file_as = 'beam1field.mat'
b_spac = 50e-9
fact_beam = 1.65e+11
flag_bunched_beam = 1 # 1: bunched beam 0:load profile from file
# to be filled in case of bunched beam
sigmaz = 0.097 #1.3ns
t_offs = 2.5e-9 + 2.*2.389798e+01/299792458.
filling_pattern_file = 2*(4*(36*[1.]+4*[0.])+15*[0.])
  beam2.beam
  Features available in PyECLOUD 3.06 or later:
  The electric field of the beam can be calculated using the embedded Poisson solver
  Crosschecked by taking the divergence
PyECLOUD simulations for the inner triplets

## Slide 41
# BEAM PARAMETERS
energy_eV= 4000e9 #eV
nemittx = 2.4e-6
nemitty = 2.4e-6 #m
betafx = 9.454233e+02
betafy = 9.595226e+02
x_beam_pos = 5.915084e-11
y_beam_pos = -3.478057e-03
beam_field_file =-1
Dh_beam_field=0.5e-4
save_beam_field_file_as = 'beam1field.mat'
b_spac = 50e-9
fact_beam = 1.65e+11
flag_bunched_beam = 1 # 1: bunched beam 0:load profile from file
# to be filled in case of bunched beam
sigmaz = 0.097 #1.3ns
t_offs = 2.5e-9 + 2.*2.389798e+01/299792458.
filling_pattern_file = 2*(4*(36*[1.]+4*[0.])+15*[0.])
  beam2.beam
  Features available in PyECLOUD 3.06 or later:
  The electric field of the beam can be calculated using the embedded Poisson solver
  Crosschecked by taking the divergence
  Warning: the beam region must be sampled correctly!
PyECLOUD simulations for the inner triplets

## Slide 42
# BEAM PARAMETERS
energy_eV= 4000e9 #eV
nemittx = 2.4e-6
nemitty = 2.4e-6 #m
betafx = 9.454233e+02
betafy = 9.595226e+02
x_beam_pos = 5.915084e-11
y_beam_pos = -3.478057e-03
beam_field_file =-1
Dh_beam_field=0.5e-4
save_beam_field_file_as = 'beam1field.mat'
b_spac = 50e-9
fact_beam = 1.65e+11
flag_bunched_beam = 1 # 1: bunched beam 0:load profile from file
# to be filled in case of bunched beam
sigmaz = 0.097 #1.3ns
t_offs = 2.5e-9 + 2.*2.389798e+01/299792458.
filling_pattern_file = 2*(4*(36*[1.]+4*[0.])+15*[0.])
  beam2.beam
  Features available in PyECLOUD 3.06 or later:
  An arbitrary delay can be added to the beam longitudinal profile
PyECLOUD simulations for the inner triplets

## Slide 43
# BEAM PARAMETERS
energy_eV= 4000e9 #eV
nemittx = 2.4e-6
nemitty = 2.4e-6 #m
betafx = 9.454233e+02
betafy = 9.595226e+02
x_beam_pos = 5.915084e-11
y_beam_pos = -3.478057e-03
beam_field_file =-1
Dh_beam_field=0.5e-4
save_beam_field_file_as = 'beam1field.mat'
b_spac = 50e-9
fact_beam = 1.65e+11
flag_bunched_beam = 1 # 1: bunched beam 0:load profile from file
# to be filled in case of bunched beam
sigmaz = 0.097 #1.3ns
t_offs = 2.5e-9 + 2.*2.389798e+01/299792458.
filling_pattern_file = 2*(4*(36*[1.]+4*[0.])+15*[0.])
  beam2.beam
  Features available in PyECLOUD 3.06 or later:
  Compact form for filling pattern (usual load from file still available)
PyECLOUD simulations for the inner triplets

## Slide 44
# SIMULATION PARAMETERS
machine_param_file='machine_parameters.input'
secondary_emission_parameters_file='secondary_emission_parameters.input'
beam_parameters_file='beam1.beam'
secondary_beams_file_list = ['beam2.beam']
logfile_path = './logfile.txt'
progress_path = './progress.txt'
Dt=25e-12 #s (no effect if long. profile is imported from file)
t_end=1e-9; #s (no effect if long. profile is imported from file)
...
el_density_probes = [\
{'x' : 5.915084e-11, 'y': -3.478057e-03, 'r_obs': 1e-3},
{'x' : -1.128269e-10, 'y': 3.452395e-03, 'r_obs': 1e-3}]
  beam2.beam
  Features available in PyECLOUD 3.06 or later:
  Arbitrarily define electron density probes
PyECLOUD simulations for the inner triplets

## Slide 45
  Moreover:
  Synchrotron radiation seeding with uniform distribution needed to be implemented
  Macroparticle cleaning/regeneration thresholds had to be optimized in order to cope with very fast buildup
  Field lines parallel to the chamber’s wall found to create some problem to the backtracking algorithm (code resorting to “fallback” algorithm, less accurate but more robust)
PyECLOUD simulations for the inner triplets

## Slide 46
Outline
  Introduction
  Simulating the inner triplets in PyECLOUD
  Simulation results
  Machine observations (heat load)
  Some considerations on e- - beam interaction
  Endoscopy observations

## Slide 47
Simulated scenarios
8
72
8
72
72
8
72
  25 ns beam – 1.15 x 1011 ppb
38
8
72
8
72
72
8
72
38
4
36
4
36
36
4
36
  50 ns beam – 1.65 x 1011 ppb
19
4
36
4
36
36
4
36
19
  Other beam parameters:
  Beam energy: 4 TeV
  Transverse emittance: 2.4 μm
  Bunch length: 1.3 ns
  Optics with β* = 0.6 m

## Slide 48
  Few snapshots of the electron distribution (see also beam2_50ns_pass0.avi)
Beam 1
A look to the EC buildup

## Slide 49
  The presence of two beams enhances the multipacting efficiency, especially far enough from the locations of the long range encounters
A look to the EC buildup

## Slide 50
  The presence of two beams enhances the multipacting efficiency, especially far enough from the locations of the long range encounters
A look to the EC buildup

## Slide 51
  The presence of two beams enhances the multipacting efficiency, especially far enough from the locations of the long range encounters
A look to the EC buildup

## Slide 52
  Similar behavior for 50 ns spacing
A look to the EC buildup

## Slide 53
Heat load density along the triplet - 50 ns
  Locations of long range encounters
  Remarks:
  EC much weaker close to long range encounters
  Modules with the same beam screen behave very similarly
1R1
A2R1
B2R1
3R1

## Slide 54
Heat load density along the triplet - 50 ns
1R1
A2R1
B2R1
3R1
  Remarks:
  EC much weaker close to long range encounters
  Modules with the same beam screen behave very similarly
  The presence of the two beams leads to an important lowering of the multipacting threshold w.r.t. the single beam case (dashed)

## Slide 55
Heat load density along the triplet - 50 ns
1R1
A2R1
B2R1
3R1
  Remarks:
  EC much weaker close to long range encounters
  Modules with the same beam screen behave very similarly
  The presence of the two beams leads to an important lowering of the multipacting threshold w.r.t. the single beam case (dashed)

## Slide 56
Heat load density along the triplet - 50 ns
1R1
A2R1
B2R1
3R1
  Remarks:
  EC much weaker close to long range encounters
  Modules with the same beam screen behave very similarly
  The presence of the two beams leads to an important lowering of the multipacting threshold w.r.t. the single beam case (dashed)

## Slide 57
Heat load density along the triplet - 50 ns
1R1
A2R1
B2R1
3R1
  Remarks:
  EC much weaker close to long range encounters
  Modules with the same beam screen behave very similarly
  The presence of the two beams leads to an important lowering of the multipacting threshold w.r.t. the single beam case (dashed)

## Slide 58
Heat load density along the triplet - 25 ns
  Locations of long range encounters
  Remarks:
  EC much weaker close to long range encounters
  Modules with the same beam screen behave very similarly
1R1
A2R1
B2R1
3R1

## Slide 59
Heat load density along the triplet - 25 ns
1R1
A2R1
B2R1
3R1
  Remarks:
  EC much weaker close to long range encounters
  Modules with the same beam screen behave very similarly
  As in the other quardupoles in the LHC, the multipacting threshold is already quite low even for a single beam with 25 ns spacing

## Slide 60
Heat load density along the triplet - 25 ns
1R1
A2R1
B2R1
3R1
  Remarks:
  EC much weaker close to long range encounters
  Modules with the same beam screen behave very similarly
  The presence of the two beams leads to an important lowering of the multipacting threshold w.r.t. the single beam case (dashed)

## Slide 61
Heat load density along the triplet - 25 ns
1R1
A2R1
B2R1
3R1
  Remarks:
  EC much weaker close to long range encounters
  Modules with the same beam screen behave very similarly
  The presence of the two beams leads to an important lowering of the multipacting threshold w.r.t. the single beam case (dashed)

## Slide 62
Heat load density along the triplet - 25 ns
1R1
A2R1
B2R1
3R1
  Remarks:
  EC much weaker close to long range encounters
  Modules with the same beam screen behave very similarly
  The presence of the two beams leads to an important lowering of the multipacting threshold w.r.t. the single beam case (dashed)

## Slide 63
Average heat load density – 50 ns vs. 25 ns
  Remarks:
    Above threshold values are very similar  enhancement from hybrid spacings much stronger on the 50 ns than on 25 ns

## Slide 64
Average heat load density – 50 ns vs. 25 ns
  Remarks:
    Above threshold values are very similar  enhancement from hybrid spacings much stronger on the 50 ns than on 25 ns
  For each triplet we get:

## Slide 65
Outline
  Introduction
  Simulating the inner triplets in PyECLOUD
  Simulation results
  Machine observations (heat load)
  Some considerations on e- - beam interaction
  Endoscopy observations

## Slide 66
Machine observations – 50 ns
Data provided by L. Tavian
  No big change during ramp and squeeze

## Slide 67
Machine observations – 50 ns
  No big change during ramp and squeeze
Data provided by L. Tavian

## Slide 68
Machine observations – 50 ns
  No big change during ramp and squeeze
Data provided by L. Tavian

## Slide 69
Machine observations – 50 ns
  No big change during ramp and squeeze

## Slide 70
Machine observations – 50 ns
  Heat load much higher than in two-aperture qaudrupoles
Data provided by L. Tavian

## Slide 71
Machine observations – 25 ns (450 GeV)

## Slide 72
Machine observations – 25 ns (450 GeV)
  Heat load very similar to two-aperture qaudrupoles

## Slide 73
Machine observations – 25 ns (4 TeV)
  No big change during ramp and squeeze

## Slide 74
Machine observations – 25 ns (4 TeV)
  No big change during ramp and squeeze

## Slide 75
Comparison against simulations
Fill 3429
Fill 3286
Fill 3405
50 ns, 4 TeV
25 ns, 450 GeV
25 ns, 4 TeV
  1.2 < SEYmax < 1.3
  is compatible with the observations

## Slide 76
Crosscheck with single beam MDs
  For the estimated SEY value we do not expect nor observe EC in the triplets with only one beam with 50 ns spacing circulating in the LHC

## Slide 77
Crosscheck with single beam MDs
  For the estimated SEY value we do not expect nor observe EC in the triplets with only one beam with 50 ns spacing circulating in the LHC

## Slide 78
Outline
  Introduction
  Simulating the inner triplets in PyECLOUD
  Simulation results
  Machine observations (heat load)
  Some considerations on e- - beam interaction
  Endoscopy observations

## Slide 79
e- density at the two beam locations
  We are interested to the electron density “seen” by the beam. Therefore we compute the following weighted average density:
  In the transverse plane, the electron density is averaged over a circle of 1 mm radius

## Slide 80
e- density at the two beam locations – 50 ns
  IP1
1R1
A2R1
B2R1
3R1
  Strongly dependent on the beam position with respect to the e- stripes
Beam 1
1R1
A2R1
B2R1
3R1

## Slide 81
e- density at the two beam locations – 50 ns
  IP1
1R1
A2R1
B2R1
3R1
  Strongly dependent on the beam position with respect to the e- stripes
Beam 2
1R1
A2R1
B2R1
3R1

## Slide 82
A closer look to a particular section
  The field at the beam location is determined by the whole distribution (not only by the local density)

## Slide 83
A closer look to a particular section
  The field at the beam location is determined by the whole distribution (not only by the local density)

## Slide 84
Outline
  Introduction
  Simulating the inner triplets in PyECLOUD
  Simulation results
  Machine observations (heat load)
  Some considerations on e- - beam interaction
  Endoscopy observations

## Slide 85
A picture from an SPS endoscopy
  Dark stripes in SPS quadrupoles seem to confirm the e- distribution we get in simulations
  A recent endoscopy of the LHC triplets does not show this kind of signs  are we sure the graphitization process still works in the LHC temperature/B field/vaccum conditions?!

## Slide 86
Thanks for your attention!

## Slide 87
e- density at the two beam locations – summary

## Slide 88
e- density at the two beam locations – summary
  Average along the triplet

## Slide 89
e- density at the two beam locations – summary
  Average between the two beams