ArcPIC status
Kyrre N. Sjøbæk
26/8/2013
(update 2/9/2013)

---
Outline
- PIC & field emission
  - See separate presentation
- Heatspike yield & threshold
- Field movie
- Particle weight scan
- Evaporation scan
- Model refinements
- Other stuff

---
Heatspike yield & threshold
- Ran the new model (“NewHS-modelC”) many times to find the minimum yield and heatspike threshold sufficient for a “runaway” breakdown
- Results on next slide:
  - Number = time in ns until “breakaway” from
    zero-heatspike ion number curve
  - Red:	Rapid runaway
  - Yellow:	Runaway but was able to follow for some time
  - Green:	No significant difference from no-heatspike
    curve

---
	Threshold [particles / cm² / s]
Yield		1.0E+25	2.0E+25	3.0E+25	4.0E+25	5.0E+25	5.5E+25	6.0E+25	7.0E+25
	1		0.570	inf
	5		0.570	0.603	inf
	10				0.666	inf
	15					inf
	25				0.598	0.720
	50			0.575		0.630	inf	inf
	75					inf
	85					inf
	90					0.655
	95					0.589
	100	0.480	0.500	0.574		0.587		0.630	inf
	250	0.486
	500	0.485
	850	0.480	0.490	0.571		0.572		0.577	inf
	1000
	1500					inf

---
Heatspike yield & threshold: all runs

---
Heatspike yield & threshold: all runs

---
Heatspike threshold =
1e25 ions/cm²/s

---
Heatspike threshold =
2e25 ions/cm²/s

---
Heatspike threshold =
3e25 ions/cm²/s

---
Heatspike threshold =
4e25 ions/cm²/s

---
Heatspike threshold =
5e25 ions/cm²/s

---
Heatspike threshold =
5.5e25 ions/cm²/s

---
Heatspike threshold =
6e25 ions/cm²/s

---
Heatspike threshold =
7e25 ions/cm²/s

---
Heatspike yield & threshold: conclusions
- Most impactors have low energy
  =>Y < 1
- Increasing neutral population necessary for neutral population growth
- Some is provided by evaporation
  (Lotta's expanding run from last year)
- Heatspike, even with Y=1
  (given low-enough threshold),
  provides enough neutrals
Average Y = 0.58
YASUNORI YAMAMURA* and HIRO TAWARA:
ENERGY DEPENDENCE OF ION-INDUCED SPUTTERING YIELDS FROM MONATOMIC SOLIDS AT NORMAL INCIDENCE

---
Field movie

---
Particle weight scan
- Ran simulations with different particle weights
- Nsp = n_ref*Ldb^3/Ndb
  - Ndb = 1500 (standard)
    -> Nsp = 21.35
  - Ndb = 3000
    -> Nsp = 10.67
  - Ndb = 6000
    -> Nsp = 5.34

---
Particle weight scan
Ndb = 1500
Ndb = 3000
Ndb = 6000
- Convergence seems OK
- Have to confirm that slow-pulsing frequency is the same

---
Evaporation scan
- Tried to change neutral evaporation ratio from 0.015 to 0.010 and 0.005*
- 0.010 also broke down, but it took longer
  - Heatspikes OFF
- 0.005 didn't break down
  - New model

---
Model refinements
- Flat surface emission:
  - May start as Remission OR Remission_theor
  - Separate evaporation ratio
  - Evaporation located at flat surface, not at tip
  - Uniform injection
- More output - separately specify
  - emitted_flat
  - emitted_SEY
  - emitted_evap
  - emitted_sputter_cat
  - emitted_sputter_ano
  - emitted_heatspike
Need to understand why I don't reproduce old results exactly in the beginning (no flat surface interaction)

---
Other stuff
- Helsingfors/Helsinki summer student Miika Haataja
  - Field emission + space charge benchmark
  - Neutrals-in-gap without evaporation
  - Presented work Monday 26/8
  - Will produce report this week
- Increased current after breakdown may be due to SEY, not flat emission
  - SEY for low energy ions < 0.5...
Harddrives “humongous1”
and “humongous2” (2x 2 TB)
for local scratch space
(USB drives are cheap, local, and unbureaucratic..)