Error on field from PIC scheme
and its effect on field emission
Kyrre Ness Sjøbæk
15/8/2013-20/8/2013
(+ update on time step 26/8)

---
Outline
- Field from a test particle at (z,r)
  observed at (0,0)
  - Analytical
  - PIC
- PIC field versus analytical field
- Effect on field emission in ArcPIC2D

---
Field from test particle on tip: analytical (1)
r
- Due to coordinate system,
  particles appears as
  infinitely thin circles with radius r
  at height z above surface
- Surface is perfectly conducting,
  so the boundary condition
  may be approximated by placing an identical but oppositely charged
  ring at -z
- We are interested in the field from a negative test particle
  located at (r,z) when observed
  at the emitter position (0,0)
Emitter position
Negative
“particle”
z
Image
charge
Electric
field lines
Conducting surface

---
Field from test particle on tip: analytical (2)
- This field may be calculated by summing up the field from infinitivly many charges dq distributed along the ring
- The single-particle field observed at position (x,y,z) from a particle located at (0,0,0) is given as:
- When swapping observation and test charge position, the sign of E is reversed
- The field from one particle on the emitter is then given as:
vec E = int {dq over k_e} {-hat R} over R^2 ~ = ~ newline int_0^{2%pi} {Q ` d%theta} over {k_e 2%pi} left(- {z hat z} over R^3 + {hat x cos %theta + hat y sin %theta} over R^3 right) ~ = ~ newline {-Q z hat z} over {k_e R^3} ~ = ~ {N_{sp} e z hat z} over {k_e R^3}
vec E = q over k_e hat R over R^2
where
k_e = 4 %pi %epsilon_0
hat R = vec R over R
and the unit vector
where
and
R = sqrt{x^2 + y^2 + z^2} = sqrt{r^2 + z^2}
Q = int dq = - N_{sp} e
where
and
vec R = r hat r(%theta) + z hat z = r (cos(%theta) hat x + sin(%theta) hat y) + z hat z newline `= x hat x + y hat y + z hat z
e is the electron charge, Nsp the superparticle ratio

---
Field from test particle on tip: analytical (3)
- We have two perfectly conducting surfaces, so both requires an image charge
- The image charges are then mirrored on the other surface
- This leads to a series expansion of the field
Z_{-i} = -i*D + left lbrace matrix { D-z # i ~ ital odd ## z # i ~ ital even } right rbrace
Z_{+i} = i*D + left lbrace matrix { D-z # i ~ ital odd ## z # i ~ ital even } right rbrace
E_z = E_z (z_0) + sum_{o=1}^infty left ( E_z (z_{+i}) + E_z (z_{-i}) right )
0
z
D
2D
3D
-D
-2D
Order 0
Order 1
Order 2
Order 1
Order 2
Z0 = Z
Z-1 = -Z
Z1 = 2d-Z
Z2 = 2d+Z
Z-1 = 2d-Z

---
Field from test particle on tip: analytical (4)
- What is not taken into account in the analytical model is the r-boundary found in the simulation
- In the simulation, this is represented by a Neuman boundary condition at
  r = Rmax = nr :
- In an analytical model, this can often be represented by a same-sign image charge
- I was not able to come up with a “mirror” charge distribution for this case
- Thus the analytic and numerical results differ at big r
- I am most interested in field at small r (big r fields anyway small)
+
+
{partial %varphi} over {partial r} = 0 Rightarrow E_r = 0

---
Field from test particle on tip: analytical (5)
- The resulting field is shown on the right
  - Black line marks
    usual system size 12 µm
- Parameters:
  - Nsp = 21.35
  - Sum order = 25
  - D = 20 µm
- Note negative field
  at large radius
  - Happens due to image charge field – positive images with z>D, negative with z<0
  - Not important at small r

---
Field from test particle on tip: PIC (1)
- In PIC:
  - The charge is first interpolated onto the grid points
  - Poissons equation solved on the grid points => potential
  - Field calculated by derivative of potential on grid points
  - Field interpolated to observer position
- This leads to underestimation of field and other inaccuracies at short range
- OK for plasma bulk
  (given that dz << typical length scale)
- Problematic at emitter
  - Relevant space-charge shielding charges very close
  - There may be effects of being at r=0 which is simultaneously a Neuman boundary and Dirichlet boundary
- Also, field close to r=dr is disturbed by Neuman boundary condition

---
Field from test particle on tip: PIC (2)
Near emitter
(dashed lines = grid)
Whole volume
Boundary effects
Flipped sign!
Under-estimated
PIC
Analytical

---
PIC field versus analytical field (1)
- See that it matches reasonably well far away
  - Boundary effects are visible, and large relative errors
  - These fields are however *absolutely* small
    (when observed from the emitter)

---
PIC field versus analytical field (2)
- Mitigation of boundary effect possible by extending the grid (assuming the arc has the same size)
- However this carries the penalty of slowing down the field solver (matrix size ~ (nr*nz)^2)

---
PIC field versus analytical field (3)
- Field very wrong close to emitter
  - This is where the recently emitted electrons are found...
  - Too-low field => overestimation of emission
    - These extra charges then leads to extra-much space charge -> emission quench
    - This again results in the observed pulsing during space-charge limited Fowler-Nordheim cold field emission

---
Effect on field emission in ArcPIC2D (1)
Direct field
- I implemented a test emission model class in ArcPIC using the analytical expression to calculate the tip field
  - Only image charge at -z
    taken into account
  - No neutrals etc
  - Inter-electron and external field forces handled by PIC
- Still some instability
  due to field ~1/z^2
  - Sometimes evaluated
    with a “close” particle
  - Looks better
  - Less “structured” pulses
PIC field

---
Effect on field emission in ArcPIC2D (2)
Due to first-step overshoot
- Field emission current reduced significantly
- More random oscillations
- TODO:
  - Expand test model to include neutrals & ions
  - Run breakdown simulation w/ this model

---
Appendix

---
Pulsing is NOT caused by statistics
... but as expected, the higher-Ndb runs are less noisy

---
Pulsing NOT caused by time step
- See that current well converged in dt
- Increasing dt leads to cycle “emission -> acceleration -> emission”, increasing the average current
- Small dt leads to only 0-1 electrons emitted per time step
- Grid convergence may be more interesting
  - Analytic result is basically an infinite grid,
    but still noisy (not single frequency tough)