## Slide 1
Two Beam Module
Thermo-mechanical tests
30.07.2014
Elena Daskalaki
Alex Vamvakas
Athanasios Zelios

## Slide 2
Tasks summary
Hardware
Add and re-organize temperature sensors
Add, connect and calibrate flow meters
Add real-time power sensors
Software
Update/modify LabVIEW
Tests
Water only tests
PID tuning
Transients
Preparation for next module

## Slide 3
Hardware
Vacuum tank
  Add two thermocouples inside (total: 2)
Calibration of new RTD sensors using high precision calibration bath
PETS
  Reorganize sensors (put all on copper)
  Put sensor inside each PETS (total: 2)
Girders
  Add three sensors at each girder (total: 6)
Cradles
  Add sensor on cradles close to the girder displacement sensors (total: 4)
Temperature sensors

## Slide 4
Hardware
Add one flow meter at each cooling channel
Test flow meters based on the highly accurate Siemens MASS 6000
Flow meters
Real-time power measurement
Current sensor to measure the current of the AS and PETS heaters
Calculation of heaters’ power in real-time

## Slide 5
Update software to increase usability
Add new components (sensors, flow meters, power measurement)
Alarms
Real-time statistics (min, max, steady-state)
Automation of inputs (heaters’ power, water flow)
Interface to host two or more modules
Software
LabVIEW

## Slide 6
Test all flow meters range and accuracy
Choose the best flow meter for SAS and PETS
Tests
Water tests
Thermal/thermo-mechanical tests
Finalize PID for the control of flow rate
Verify real-time power measurement
Study the module’s transients

## Slide 7
Transients
To find the time constant of each component as a function of:
Power applied
Water flow
Component mass
Ambient conditions
Aim

## Slide 8
Mode | Component | Power (W) | Water flow (m3/h) | Ambient temperature (oC)
1 | SAS | 410 | 0.04 | 20
 | PETS | 220 | 0.01 | 
2 | SAS | 820 | 0.068 | 30
 | PETS | 440 | 0.03 | 
3 | SAS | 1230 | 0.09 | 40
 | PETS | 660 | 0.05 | 
Transients
Test the module under all possible combinations of various modes for the
i) thermal power, ii) water flow and iii) ambient temperature

## Slide 9
P1
F1
T1
P2
F1
T1
P3
F1
T1
P1
F2
T1
P2
F2
T1
P3
F2
T1
P1
F3
T1
P2
F3
T1
P3
F3
T1
P1
F1
T2
P2
F1
T2
P3
F1
T2
P1
F2
T2
P2
F2
T2
P3
F2
T2
P1
F3
T2
P2
F3
T2
P3
F3
T2
P1
F1
T3
P2
F1
T3
P3
F1
T3
P1
F2
T3
P2
F2
T3
P3
F2
T3
P1
F3
T3
P2
F3
T3
P3
F3
T3
Transients
Start
End

## Slide 10
Planning
What | When
Finalize HW/SW | 08.08.2014
Finalize PID | 12.08.2014
Start transients tests | 01.09.2014

## Slide 11
Questions
DT=10 oC: Which temperatures does it refer to?
What is the target DT of components? Effect on transients
Water/components temperature variation? 0.1 oC? (ref. EUROTeV-Report-2008-081)
  PID tuning depends on this condition
  Sensors’ accuracy currently 0.1 oC
  Sensors’ position?
Correlation among lab module, CLEX, CLIC…
Demineralized water