## Slide 1: IS ENGINEERING
M. Garlaschè; A. Dallocchio; D. Steyaert on behalf of L4 IS Team
Linac4 Ion Source Review - 14.11.2013

## Slide 2
Summary
Integrated mechanical design and engineering:
analytical/Finite Element analyses
experimental tests
From conceptual design to product engineering...
Courtesy J. Lettry

## Slide 3
IS01 - Front End
Goal
Structural analysis of IS Front End
Assess performance of EPGM External Insulator
Plasma Generator
1ary vacuum
2ary vacuum
O-Ring Seal
Main Loads
EPGM
Insulator
Steel Flange
Ti Insert
O-Ring Seal
Glued Steel Insert
Preloaded Screw
EPGM
Insulator
Main Insulator

## Slide 4
IS01 - Front End
Results
Worst case loading condition identified
Resistance of structure confirmed
Deformation of components negligible
Loss of primary vacuum
Max: 20MPa on generator flange
Few μm axial displacement on ceramic Main Insulator and Generator Flange
What is max stress of perp. EPGM?
Axial deformation (mm)
24 μm
22 μm
Ceramic Insulator
(Al2O3)
Courtesy M. Devoldere
Notes: Worst case loading condition:loss of primary vacuum
No real design changes following FE results

## Slide 5
IS01 - Front End
What is max stress of perp. EPGM?
Pull-out Test
Validation of resistance to screws tightening force
Choice of Insulator fiber orientation
Pull-out load VS. stroke
Rupture: 27 kN
IS Assembly: 7 kN
Global stresses OK
Peak stress in correspondance of inserts..
Eq. Stress (MPa)
EPGM Insulator Results
EPGM
Notes: Worst case loading condition:loss of primary vacuum
No real design changes following FE results

## Slide 6
IS01 - Support
Goal
Assess resistance of components
Minimize Front End displacements (beam axis)
Results
Stresses negligible
Improved Support stiffness to obtain acceptable deformations
Axial displacement (mm)

## Slide 7
IS02 – Plasma Generator
Results
Stresses: design optimized
Assembly procedure: vacuum tightness guaranteed by using special metallic seals (HNRV helicoflex)
Goal
Design towards UHV standard by implementing metallic seals
240
0
Tresca equivalent stress (MPa)
7
Helicoflex seals
Notes: Benchmark w.r.t. Stresses, elastic recovery during assembly procedure

## Slide 8
Ti Disc (H.flex seat)
Al2O3 Insulator
Steel Flange
Brazed Ti Insert
32xM8 Preloaded
H.Flex seal
IS02/03 v1– Ext. Insulator
Complex brazing of Titanium Inserts with Insulator
Goal
Improved UHV reliability with metallic seals
EPGMAl2O3
Notes: Stresses intensifications also linked to machining of holes

## Slide 9
Ti Disc (H.flex seat)
Al2O3 Insulator
Steel Flange
Brazed Ti Insert
32xM8 Preloaded
H.Flex seal
IS02/03 v1– Ext. Insulator
Outcome
High stress in ceramic
Test campaign launched for
  Checking brazing procedure
  Mastering bolts preload
  Understanding Al2O3 struct. behaviour
Principal stress (MPa)
Al2O3
Safety factor = 1.4
 CRITICAL!
Complex brazing of Titanium Inserts with Insulator
Goal
Improved UHV reliability with metallic seals
EPGMAl2O3
Notes: Stresses intensifications also linked to machining of holes

## Slide 10
IS02/03 v1 – Ext. Insulator
Influence of Ti thermal treatment on friction @ preload
Change of friction coefficient during lifetime
Tests foreseen
Rupture properties
Tightening brazed insert
Pull-out
..mastering bolts preload
..understanding Al2O3 properties
Ongoing – needed for brazing & struct. assessment
Courtesy EN/MME-ES
Friction increases after Titan thermal treatment
No measured change (NOTE: to be ideally assembled once)
Notes: Treated Titan: Coefficient of friction increases

## Slide 11
IS02/03 – Ext. Insulator
Goal
Alternative design with
No brazed inserts
Insulator (Al2O3) brazed to collars (Kovar)
Outcome
Vacuum-related load transmitted solely through collar-insulator
Eq. stress (MPa)
Principal stress (MPa)
Potential
CRACK
Solution
Abandoned
Plasticization
Ext. Insulator
Collar
Al2O3
Kovar
Steel
Notes: Bilinear isotropic hardening used for modelling Kovar yielding

## Slide 12
IS02/03 - Front End
Results
Stresses: negligible
Displacements
BASELINE
Optimization ongoing for reducing displacements
..elastic, predictable
Axial displ. (mm)
support rod
bellow
Goal
Alternative design with Insulator brazed to collars
Reduce load on collar and Ext. Insulator by bellow + support rods
New Requests:
  improve optics  no 2ary vacuum

## Slide 13
Conclusions and future outlook
June 2011  Present:
Engineering activities required ≈ 3 FTE
(2 Fellows working 50% on the L4 IS)
Present  future...
Estimate for future engineering activities ≈ 1,5 FTE
(1 Fellow working 50% on the L4 IS)
What’s Next (IS02 / IS03):
Design finalization of Front-End and Ext. Insulator: structural analysis and experimental validation
Cesium Oven – thermo-mechanical calculations
Structural analysis to integrate IS03 Plasma Generator
Cold Cs Trap: thermal analysis
Notes: Remind that eng. Supp. Comes free with design

## Slide 14
Thank you for your Attention!