## Slide 1: RF fields simulations
Alexej Grudiev, BE-RF
14/11/2013
Linac4 Ion Source Review, CERN

## Slide 2: Outline
RF field simulations setup
Plasma model as a conductor
Surface electric field enhancement
EM field distribution in plasma chamber
Ion source Impedance
Comparison with measurements
Variation of the ion source geometry
Conclusions

## Slide 3: CAD 3D model of IS-01
Didier Steyaert

## Slide 4: RF simulation setup (HFSS)
“Plasma” = conductor
10-4 < σ < 105 [S/m]
σ/ω > ε0 δ > 1mm
ε = ε0+jσ/ω; δ = (2/σωµ0)1/2
Pin
Pout
ZIS=Z:1:1
Zc=Zo
ZIS
Pin = 1W => Iin = sqrt(2Pin/Zc) = 0.11A
I=2Iin = 2*0.11A = 0.22 A
To scale the EM fields presented later, multiply by the current ratio
Coax port
Full 3D RF simulations

## Slide 5: Surface electric field enhancement
Max E-field on the surface of the Cu octupole envelop for 220 A coil current is about 3 MV/m, same as air discharge threshold. This due to sharp edge close to the coil.

## Slide 6: EM field distribution in plasma chamber region, σ=0
Magnetic field
Electric field
H-field is similar to the one of a solenoid
E-field is dominated by R,Z components.
It is mainly capacitive

## Slide 7: Field map for plasma simulations
mesh_0
mesh_2
mesh_1
mesh_3
Averaging the field over 4 meshes remove radial and azimuthal components on axis r=0 and make the distribution quasi 2D.
To be used in the plasma simulation code with 2D field representation.
Field = 1/4*[ field(mesh_0)+field(mesh_1)+ field(mesh_2)+field(mesh_3)]

## Slide 8: E-field distribution in plasma chamber. σ > 0

## Slide 9: Ion source impedance
ZPlasma = ZAnt+Plasma(σ>0) - ZAnt(σ=0)
ZAnt = RAnt +jω0LAnt
ZPlasma = RPlasma +jω0LPlasma
Model used in the RF measurements
RANT
LANT
RPlasma
LPlasma
RF Measurements IS-01:
RAnt = 0.4 Ω
LAnt = 3.2 µH
Rplasma = 4.3 Ω
Lplasma = -0.05 µH
M. Paoluzzi
Simulations IS-01:
RAnt = 0.263 Ω
LAnt = 3.02 µH
σ = 300 - 500 [S/m]
Plasma measurements (SPL-IS): H2 pressure ~ 20 mTorr, ne ~ 1018 - 1019 m-3 and Te ~ 10 eV. =>
It gives an estimate of the conductivity of 730 - 6600 S/m for the above given density range
R. Scrivens

## Slide 10: E-field distribution in plasma chamber, σ = 1000 S/m

## Slide 11: Variations: SET 1
No Cu octupole holder
Long Cu protection
Short Cu protection
W-electrode

## Slide 12: Variations SET 1: E-field distribution
Nominal
No Cu Octupole holder
Long Cu protection
Short Cu protection
W-electrode

## Slide 13: Variation of number of antenna turns
6 turns
5 turns
4 turns
3 turns
Nominal, 6 turns
5 turns
4 turns
3 turns
N.B. for 5,4,3 turns the size of epoxy and ferrites are a bit smaller. The same materials are used

## Slide 14: Variation of number of turns: impedance
~N2

## Slide 15: Variation of N turns: E-field distribution
6 turns
5 turns
4 turns
3 turns
Plasma
code

## Slide 16: Conclusions
Full 3D model with realistic material parameters is implemented and simulated using RF code HFSS
Plasma is modelled as a conductor
Surface electric field is calculated and compared to discharge limited values
Without plasma electric field distribution in the plasma chamber is dominated by R,Z components, capacitive electric field
EM field maps has been calculated for the plasma simulation code
Impedance of the ion source as a function of “plasma” conductivity is calculated and compared to the RF measurements results
Matching simulated and measured impedance values gives plasma conductivity which agrees with the one calculated from measured plasma parameters
Several variations of the IS-01 has been simulated

## Slide 17: Spare slides

## Slide 18: E-field: antenna + “plasma” (σ = 0 S/m)

## Slide 19: E-field: antenna + “plasma” (σ = 1e-4 S/m)

## Slide 20: E-field: antenna + “plasma” (σ = 1e-3 S/m)

## Slide 21: E-field: antenna + “plasma” (σ = 1e-2 S/m)

## Slide 22: E-field: antenna + “plasma” (σ = 1e-1 S/m)

## Slide 23: E-field: antenna + “plasma” (σ = 1e-0 S/m)

## Slide 24: E-field: antenna + “plasma” (σ = 1e+1 S/m)

## Slide 25: E-field: antenna + “plasma” (σ = 1e+2 S/m)

## Slide 26: E-field: antenna + “plasma” (σ = 1e+3 S/m)

## Slide 27: E-field: antenna + “plasma” (σ = 2e+3 S/m)

## Slide 28: E-field: antenna + “plasma” (σ = 3e+3 S/m)

## Slide 29: E-field: antenna + “plasma” (σ = 1e+4 S/m)