## Slide 1
Linac4 ion source
400
Ion source test stand
152
Cs-Laboratory
357
Welcome to CERN
6
9
169
72
Leak test
Production
Metrology
102
Cleaning
Assembly PG
Controls
Magnets

## Slide 2: Linac4 ISWP review, Nov. 14th 2013 Overview and status
Short introduction
  Deliverables as defined in the June 2010 Review
  Modification to the ISWP boundary conditions
Status
  Ancillary equipment, adaptability in the design
  Challenges / findings
  Ion source prototypes test results
  Simulation / Publications / reports
Outlook
  From project WP to operation
    Towards 98% reliability …
Sept. 2nd 2013 1st H- beam in linac4
Pulsed HVs + I(e-dump)
FC-LEBT
Log RF
Plasma
HV e-dump
Ferrites
Magnets

## Slide 3
Linac4 IS Collaborations | 
IPP Garching | U. Fantz
University of Jyvaskyla | O. Tarvainen, T. Kalvas
SNS | M. Stockli
KEIO University | A. Hatayama 畑山明聖
IPGP Orsay | T. Minea
ISIS | D. Faircloth
BNL | J. Alessi
J-PARC | A. Hueno
CERN
J.P. Corso, J. Coupard, M. Wilhelmsson, F. Fayet, D. Steyeart, E. Chaudet, Y. Coutron, A. Dallocchio, P. Moyret, S. Mathot, Y. Body, R. Guida, P. Carriè, A. Wasem, J. Rochez, D. Aguglia, D. Nisbet, C. Machado, N. David, S. Joffe, P. Thonet, J. Hansen, N. Thaus, P. Chigggiato, A. Michet, S. Blanchard, H. Vertergard, M. Paoluzzi, M. Haase, A. Butterworth, A. Grudiev, R. Scrivens, M. O'Neil, P. Andersson, S. Bertolo, C. Mastrostefano, E. Mahner, J. Sanchez, I. Koszar, U. Raich, F. Roncarlo, F. Zocca, D. Gerard, A. Foreste, J. Gulley, C. Rossi, G. Bellodi, J.B. Lallement, M. Vretenar, A. Lombardi
Matthias | Kronberger | SLHC-Fell. | CERN
Claus | Schmitzer | SLHC-PhD. | 
Oystein | Midttun | PhD. | 
Stefano | Mattei | Tech-Fell. | 
Hugo | Pereira | Fell | 
Jose | Sanchez | Dipl, Tech-Fell. | 
Jaime | Gil Flores | Tech-Fell. | 
Chiara | Pasquino | Tech-Fell. | 
Cristhian | Valerio | PhD. | 
Sylvia | Izquierdo | Tech-Fell. | 
Mahel | Devoldere | Tech-Fell. | 
Marco | Garlasche | Fell. | 
Serhiy | Mochalsky | Fell. | LPGP Orsay
Taneli | Kalvas | PhD. | Jyvaskyla Univ.
Masatoshi | Ohta | 太田雅俊 | Keio Univ.
Masatoshi | Yasumoto | 安元雅俊 | 
Kenjiro | Nishida | 西田健治朗 | 
Takanori | Shibata | 柴田崇統 | 
Takashi | Yamamoto | 山本尚史 | 
Thank you all 
Students & Fellows
8+19+50=77

## Slide 4: L4IS-historical Introduction
2005: Decision to copy the DESY RF volume source (reliable, no Caesium)
2008: SLHC: EU-project towards a plasma generator upgrade from Desy to 50 Hz, 100 kW 2MHz RF driven 5% duty factor.
2009: DESY-type source completed, equipped with CERN power supplies and RF generator.
May 2010: tests show that it cannot operate at 45 kV nominal voltage. The 45 keV co-extracted electron beam is focussed; it vaporizes the electron dump and induces HV-sparks.
End 2010: launched crash programme to build an improved source of CERN design operating in volume mode but upgradable to surface (Cs-based) production.
March 2011 completion of the SLHC WP.
June 2011 Linac4 IS-review https://indico.cern.ch/conferenceDisplay.py?confId=129870
The Linac4 Ion source work package (ISWP-2011) was tailored to meet:
The 3 MeV test dead line
The commissioning with beam in the tunnel
Implies: Parallelized design-simulation-purchase of raw material

## Slide 5: WPIS Time table
Date | L4-IS 3 MeV test stand | L4-IS -tunnel Bldg. 400 | L4-IS upgrades | sLHC Plasma Generator test stand | H- IS test stand | Cs Laboratory
2010 |  |  | Minimal dump, protons | RF and plasma diagnostics |  | Design
2011 | protons, mini H- pulse |  | Rev. world’s IS Rev. WPIS June | Gas Dynamics, Upgrade to HT | Design, production | 
2012 |  |  | Multistage and e- dump |  | Test and commissioning | 
2013 | Move to L4-building 400 | Commissioning in L4 building | New HT-supply & extraction |  | Operation | Surface source Proto.
2014 |  | Operation, Upgrade, control | Spare parts |  | Operation | Test of prototype
2015 |  |  |  |  | Move test stand to 152 | 
2011 Review

## Slide 6: 3MeV & L4 milestones vs. ISWP actions
 | date | L4-milestone | ISWP action
3MeV | April 2012 | 3MeV test Protons | Protons
 | May-Aug 2012 | LEBT June 2012 H- beam July 2012 | New front-end installation and commissioning Installation of proto #1 at the 3MeV test stand
 | Sept-Dec | 3MeV test H- | H- 30 mA
IS-test stand | Oct-Dec 2012 |  | Ion source test stand commissioning
Linac4 | Jan 2013 |  | Installation source in L4
 | Tbc. |  | Test IS exchange procedure (proto #1)
 | Dec 2013 | Decision to connect | 
 | Feb 2014 |  | Installation of proto #2 in linac4
 | April 2014 | L4-160 MeV commissioning completed | 20 mA required at the end of the linac4 (40 mA at the source)
 | … 2015 | LSS2 or long MD | Installation of proto #3
2011 Review

## Slide 7: WPIS H- Ion source: staged approach, 2 units each + spare
 | #1 Volume source | #2 Surface source | #3 Magnetron
Operational experience Achieved H- current | DESY 30 mA | SNS 50 mA | BNL 80 mA
Plasma Heating process | 2 MHz RF Ext. antenna | 2 MHz RF Int. & Ext. antenna | Arc discharge
Cesiation |  | Cs-chromate Single deposition: | Cs metal Constant flow
Cs-Oven test stand |  | Nov. 2011 | Nov. 2011
Electron / H- ratio | 10-100 | 10 | 0.5 - 1
357 Plasma test stand (operational) | → Sept. 2012 | 2013 | 2014-2015
3MeV test stand (until Dec-2012) (operational, Bldg. 152) | Jul. 2012- Dec-2012 |  | 
IS test stand (Bldg. 357) |  | 2013 | 2014
Linac4, building 400 | Jan 2013 | Oct 2013 | 2015
2011 Review

## Slide 8: Summary of the L4-WPIS changes
Delayed move into the tunnel, RFQ tests in 152 until June 2013.
Cancellation of the DESY source 45 kV proton commissioning of the RFQ
Decision to not build an ion source test stand in building 357.
  Should allows commissioning of the source and LEBT equipment in the tunnel before moving the RFQ
  Saves the 2015-foreseen move of the test stand from 357 to 152
  The tunnel is not the best place for IS-R&D: effectively no IS-test-stand between January and July 2013 but beam delivery to RFQ commissioning.
Decision to consider IS-03 (Magnetron) as an option “to be confirmed at a later stage”.
  To minimize delays if the option would be selected, decision to maintain a minimal task with the following deliverables:
    Insource BNL’s drawings and produce a 3D Cathia model and production drawings
    Produce a magnetron plasma generator and test it at BNL

## Slide 9: Status 14th November 2013
15 mA 45 kV H- beam available:
@ 3MeV TS since February 2013
@ Linac4 since September 2nd 2013
IS01 + DESY PG
Repaired insulator + 1 bar SF6
Mount backup option (DESY plasma generator) on IS01 Front end + extraction & e-dumping system
12 mA 45 kV H- beam available:
@ IS-TS Nov. 12th 2013
IS02 before cesiation tbc.

## Slide 10: Organization of the ISWP
Weekly
Presentation
Discussion
Decision
IS-team
Design
Production
Vacuum
Engineering
RF-HV
Specialists
Simplified
3D models
Analysis
Simulation - Measurements
Bi-Weekly meeting
Beam-optics IBSimu
Pulsed H2 injection
High voltage, B-field (Opera)
Thermal equilibrium
RF-field (ANSYS HFSS)
Photo- Spectrometry
Simulation Plasma
Bi-Weekly video meeting with KEIO university
Plasma heating
Light emission
Assembly / leak test
IS, Production, Design & Vacuum -teams
UHV-Cleaning
Collaborations
BNL, IPP, SNS, RAL, J-PARC, Uni. Orsay, Uni. Jyvaskyla
BE- ABP, CO, OP, RF
EN- MME, MEF, HE, ICE, STI
GS-SE, PH-DT
TE- EPC, VSC,

## Slide 11: IS front end
Front End
Plasma Generator
XYZ Support table
±15mm
Pumping Unit
H2 injection
Survey targets
X
Y
Z
o
o
Alignment
±3°
±3°
±3mm
Alignment table (Survey)
Beam based alignment options: Horiz. displacement & df, dw
Quick exchange in case of failure:
Pumping port
Front end

## Slide 12: “Plug & play” Plasma Generator and beam formation region
H2 Piezo Injection
Secondary Vacuum
Extraction region
Einzel lens region
Ignition chamber
Plasma chamber
Pumping port
2×700 l/min TMP
Pumping port
60 l/min TMP
Al2O3 insulator
EPGM insulator
±25kV Puller
±10kV e-dump
Ha light diffusing through
The Al2O3 Chamber
IS01
Exchangeable:
Plasma Generator
Flange + Extraction Optics
Ground electrode
Einzel lens
Insulators

## Slide 13: Al-2-diamond sealing issue
Apart from 2 units all other are non conform.
Other producer failed → Successfully achieved by CERN’s central workshop
Test with double helicoflex under way
Investigation of Front end modification
  Double knifes for Cu excluded (2×400 N/mm)
  Groove for helicoflex or O-ring + knife edge Al

## Slide 14: Epoxy-Glass fibre (EPGM) Insulator
Outgassing & limited pumping speed:
Received leaky, was sent back for removal of the SS-groove.
Very crude repair generated cracks in epoxy glued at the factory.
SS-grooved tightly glued in house.
2.1 10-2 mbar in the secondary vacuum instead of ~10-5
Paschen criteria checked before HT tests,
Outgassing rate: O(2 10-2) mbar l/s >> RGA measurement needed
Lessive NGL 17.40 spec. ALU III avec ultrasons pendant 5 h
Rinçage avec eau déminéralisée + alcool
Séchage à l’air comprimé
Etuvage à 60 °C.

## Slide 15: Secondary pumping: RGA on EPGM samples Pashen curves from representative gases
pd (sum of all gases)
! Very Close to H2O breakdown conditions
→ Successfully solved via 1 bara SF6

## Slide 16: Al2O3 main (45 kV) insulator

## Slide 17: H- source polarity
5 kV/cm

## Slide 18: Proton source polarity
5 kV/cm

## Slide 19: Active brazing Al2O3 insulator
Bellow Int.
Bellow
ext.

## Slide 20: Dry ice cleaning of Al2O3 insulator
Time evolution of the HT drain current could be related to air reactive contamination.
Cleaning with alcohol reduced drain current
CO2 dry ice (3mm beads) blasting under Nitrogen followed by drying at 60 deg.C.
The 30 kV HV tests then showed a non-measurable current drain (<0.1mA).
Surface contamination existed and is likely removed

## Slide 21: 2D Electrostatic Simulation of FE-Insulation
Screen shielding form Cs-vapour
→ Removed
1 ceramic was sent back to remove protrusions by grinding
→ Successfully passed HV tests
Protrusions induced field emission spots and
cracks lead to high fields
→ Successfully shielded

## Slide 22: FC-400
HV-racks
Vacuum
control
HV-Einzel
H2 control
H2 system
Pulsed HV
Transformers
2x Ventilation
RF-Maching
network
Access Door
Service Door
Service Door
Hoist
Access

## Slide 23: Linac4 tunnel Sept. 2013
3 MeV RFQ
45 kV LEBT
H2 distribution
2 MHz RF transformer
RF-Matching network
Installation of the LEBT, RFQ and Chopper line
Commissioning with a 45 kV 20 mA class volume source based on the DESY plasma Generator)
IS01: Volume 20 mA
a) 60-100 kW plasma Generator
b) DESY Plasma Generator
IS02: Cesiated surface 40-50 mA
IS03: BNL’s Magnetron (tbc.)

## Slide 24: RF-Insulation transformer & Matching Network
2MHz HV insulation transformer
RF-connection
Matching network
45 kV RF shield
6 turn solenoid
Beam extraction
Pumping system
Plasma Chamber
Exchangeable:
Cp, Cs, Ls measured for each Plasma Generator or solenoid antenna (3-6 turn) → fo at 1.95 MHz
Pole fixed to -45 kV potential (HV-flange) either close to extraction hole of at the middle of the plasma chamber
Capacity Cs
Capacity Cp
Inductance solenoid Ls

## Slide 25: FC-152
HV-rack
Vacuum
control
HV-Einzel
H2 control
H2 system
Pulsed HV
Transformers
Mobile roof
ventilation
RF-Maching
network
Access Door

## Slide 26: IS-test stand
Equipped identically to the first half of Linac4’s LEBT :
Solenoid
Faraday cup
H-V grids
Beam current transformer
Gas-density regulation
Plasma and beam diagnostics :
Optical photometry
Spectrometer
Emittance meter
FHR 1000, 2-Gratings 100 and 2400 lines/mm
3 Hamamatsu
10 MHz PMts

## Slide 27: Plasma light & H- beam
LEBT FC intercepting the H- beam
LEBT BCT
Courtesy: U. Raich 27/3/13
2MHz ripple observed by M. Sordet, J. Tan BPM-ToF system
4 MHz fine structure observed in the plasma light emission, O(10-15%) peak to peak .
2 MHz H- beam fine structure observed in the Volume source equipped with the DESY PG:
O(20%) peak to peak fluctuation of the H- beam intensity
(Av.: 16 mA)
0.2 ms/div
100 ms/div
Plasma ignition, stable beam region
I(RF+dt)
Ha, Hb, Hg
I(RF)
Ha
Hb
Hg

## Slide 28: Optical Emission Spectrometry
ICCD camera
Extraction
port
Optical fibre light in
Chart: 
Chart: 
Ha
Hb
Operational & eagerly awaiting plasmas
100 lines/mm
2400 lines/mm grid

## Slide 29: Linac4 IS: 357 test stand
357-R-005
357-R-011
Cs-Oven test bench
Glove Box
Cs-Washing
Cs
Cesiated water
disposal tank 200 lt
Controls’ Rack
High voltage
Cs-Ovens test stand
Piezo valves
Optics calibration
Piezo
HV
Optics
Pulsed gas injection test bench
Flammable

## Slide 30: Cs-test stand 357
Vertical actuator
Inficon Quartz sensor
Inert gas glove box
& antechamber
Industrial washing system
Cs-Oven filling
Flow and angular distribution of the Cs-atomic beam
Cleaning of cesiated components

## Slide 31: IS02 plasma Generator
Plasma view ports:
on-axis, 19° & 26°
Permanent magnet
Octupole cusp in
offset Halbach config.
Cs-transfer line
T-regulated
Cesiated
Mo-surface
Einzel lens
electron dump
25 kV puller
3 to 6 turns solenoid antenna
Filter field

## Slide 32: Plasma Generator design: IS01 vs. IS02
IS-02 Plasma Surface H- production
IS-01 Volume H- production
Cusp magnet
Filter magnet
Beam formation region (ONIX)
Cs-surface
collar
Puller
Ignition
Cs
Caesium:
Oven production
Test stand commissioning
Flow calibration
Cleaning procedure (mg range)
Cesiated surface:
Heater design
Temperature regulation
Beam optics:
Dumping of coextracted electrons
Minimize emittance

## Slide 33: Mounting the DESY PG on IS01-2 flange
SS-coupling
flange
IS01-2
Macor

## Slide 34: Permanent magnets configuration IS01-02
Piezo valve
Ignition
Viewports
Mo Plasma
electrode
Mo Collar
electrode
8×Halbach magnets
Ferrites
Filter Magnets
SLHC-3kW Av.
e-loss lines

## Slide 35: Temperature control of the Cesiated Mo-surface
Implementation of the
on-axis, 19° & 26°
Optical view ports
4 fibers (600μm core, 660μm clad, 710μm polyimide coating) inside of a SMA connector
Brazed sapphire + Quartz lens
3D-printing of the solenoid Epoxy mould

## Slide 36: Cs-Oven
Heating Jackets
Cs-Oven 1-5 g
Cs-transfer line
Co axial heating
Valves & collars
Two valves allow refilling without breaking the vacuum

## Slide 37: List of all tests at ISTS-152 and operation in L4-400
3MeV Test Stand → Ion Source Test Stand (July 2013)
DESY source in 35kV H- and protons → mid 2012
    Emittance measurements
IS01 6-turns 2 polarities 45 kV H- and protons → end 2012 and June 2013
  Variation of all parameters: RF-frequency & power, Gas pressure, collar and plasma electrode potentials, Filter field strength, Macor instead of Al2O3, short circuit of the plasma electrode
    IS01+DESY-PG 45 kV H- and protons Feb-June 2012 (OM presentation)
      One Emittance measurement
    IS02 uncesiated 4-turn 45 kV H- from Oct. 2013 (OM presentation)
L4-Tunnel
IS01+DESY-PG 45 kV H- Sept 2nd 2013 …

## Slide 38: IS-01 PG vs. Desy PG
Plasma Generator: IS01 6-turn Desy + IS-01 Optics & e-dump
RF-coupling Excellent Good
45 kV H- beam current 3 mA & stops after 40 ms 16-22 mA
Electron-dump current 1.5-3 A 0.6 A
Plasma Light Normal Normal
Electron dumping operational up to 3A !,
Higher e-current when fixing the potential of the solenoid at the middle of the plasma chamber
→ 3-5 turns solenoid & mobile antennas

## Slide 39: Response of the Pulsed HV under dynamic load: 0.6 A electrons & 16 mA H-
Pulsed HV system:
  Beam energy fluctuation meets Specification, further improvement expected with new controls electronics (end 2013)
  ± 0.5 kV stability throughout the beam pulse
  Detects over-currents and stops discharges. No traces of arcs on the electrodes
  Up to 3 A electron current successfully dumped at 10 keV on the e-dump, detailed analysis in O. Midttun’s presentation

## Slide 40: IS01+DESY PG: after 1 year integrated operation time (no maintenance) → RF-induced arcing in air
Burned wire insulator and molten magnet housing
Repaired and now operated below 20 kW RF
H2-Plasma light
RF-air arcing

## Slide 41: Mock-up pressure meas.
The pressure in the plasma chamber during ignition and H- pulse depends on 5 piezo valve operation parameters:
P0, delay, bias, pulse voltage and duration
These partial derivatives are measured.
RF-power profile ramp minimizes AVC’s overshoot
Rf-inductive plasma ignition (No spark-gap) operational
P0 piezo
RF-coupling (20,40,60 kW)
All gas pulse shapes
SEJ

## Slide 42: Simulations & benchmarking of measurement
H2-injection dynamics → 1) Neutrals at ignition ↔ P-meas.
RF-field & Plasma conductivity → 2) E and B fields
1+2 → PIC Plasma heating Keio → 3) e-density and EEDF
3 → CR-model → 4) H0 density … flux
5) Light emission ↔ OES-P observable
4 → Beam formation ONIX → 6) electron & H- beam, emittance
6 → Beam transport IBSimu → 7) emittance ↔ OES observable
7 → Beam neutralization
The Linac4 ion source team produced 24 conference papers, all published or accepted for publication from 2010 to 2013. Improving our basic understanding of H- ion source physical processes and developing measurement techniques of predictable observables is mandatory to address technical challenges and to identify the direction of development towards 98% reliability

## Slide 43: NIBS 2010 Takayama
J. Lettry, S. Bertolo, A. Castel, E. Chaudet, J.-F. Ecarnot, G. Favre, F. Fayet, J.-M. Geisser, M. Haase, A. Habert, J. Hansen, S. Joffe, M. Kronberger, D. Lombard, A. Marmillon, J. Marques Balula, S. Mathot, O. Midttun, P. Moyret, D. Nisbet, M. O’Neil, M. Paoluzzi, L. Prever-Loiri, J. Sanchez Arias, C. Schmitzer, R. Scrivens D. Steyaert, H. Vestergard, M. Wilhelmsson, Measurement of optical emission from the hydrogen plasma of the Linac4 ion source and the SPL plasma generator, AIP Conf. Proc. 1390 (2011) pp.245-254.
M. Paoluzzi, M. Haase, J. Marques Balula, D. Nisbet, CERN LINAC4 H- Source and SPL plasma generator RF systems, RF power coupling and impedance measurements, AIP Conf. Proc. 1390 (2011) pp.265-271.
M. Kronberger, E. Chaudet, G. Favre, J. Lettry, D. Küchler, P. Moyret, M. Paoluzzi, L. Prever-Loiri, C. Schmitzer, R. Scrivens, and D. Steyaert, Magnetic Cusp Configuration of the SPL Plasma Generator, AIP Conf. Proc. 1390 (2011) pp. 255-264.

## Slide 44: ICIS 2011 Giardini Naxos
J. Lettry, J. Alessi, D. Faircloth, A. Gerardin, T. Kalvas, H. Pereira, and S. Sgobba, Investigation of ISIS and BNL ion source electrodes after extended operation, Review of Scientific Instruments 83, 02A728 (2012).
Ø. Midttun, T. Kalvas, M. Kronberger, J. Lettry, H. Pereira, C. Schmitzer, and R. Scrivens, A New extraction system for the Linac4 H- ion source, Review of Scientific Instruments 83, 02B710 (2012).
C. Schmitzer, M. Kronberger, J. Lettry, J. Sanchez-Arias, and H. Störi, Plasma characterization of the SPL plasma chamber using a 2 MHz compensated Langmuir Probe, Review of Scientific Instruments 83, 02A715 (2012).
J. Lettry, U. Fantz, M. Kronberger, T. Kalvas, H. Koivisto, J. Komppula, E. Mahner, C. Schmitzer, J. Sanchez, R. Scrivens, O. Midttun, P. Myllyperkiö, M. O’Neil, H. Pereira, M. Paoluzzi, O. Tarvainen, D. Wünderlich, Optical Emission Spectroscopy of the Linac4 and SPL Plasma Generators, Review of Scientific Instruments 83, 02A729 (2012).

## Slide 45: NIBS 2012 Jyvaskyla
H. Pereira, J. Lettry, J. Alessi and T. Kalvas, Estimation of Sputtering Damages on a Magnetron H- Ion Source Induced by Cs+ and H+ Ions, AIP Conf. Proc. 1515 (2013) pp.81-88.
H. Pereira, D. Faircloth and J. Lettry, Operation and thermal modeling of the ISIS H- source from 50 to 2 Hz repetition rates, AIP Conf. Proc. 1515 (2013) pp.114-120.
S. Mochalskyy, J. Lettry, T. Minea, A. F. Lifschitz, C. Schmitzer, O. Midttun, D. Steyaert, Numerical modeling of the Linac4 negative ion source extraction region by 3D PIC-MCC code ONIX, AIP Conf. Proc. 1515 (2013) pp.31-40.
J. Lettry, D. Aguglia, Y. Coutron, A. Dallochio, H. Perreira, E. Chaudet, J. Hansen, E. Mahner, S. Mathot, S. Mattei, O. Midttun, P. Moyret, D. Nisbet, M. O’Neil, M. Paoluzzi, C. Pasquino, J. Sanchez Arias, C. Schmitzer, R. Scrivens, D. Steyaert, J. Gil Flores, H- Ion Sources For CERN’s Linac4, AIP Conf. Proc. 1515 (2013) pp.302-311.
C. Pasquino, P. Chiggiato, A. Michet, J. Hansen, J. Lettry, Vacuum simulation and characterisation for the LINAC4 H- source, AIP Conf. Proc. 1515 (2013) pp.401-408.
E. Mahner, J. Lettry, S. Mattei, M. O'Neil, C. Pasquino, C. Schmitzer, Gas injection and fast-pressure-rise measurements for the Linac 4 H− source, AIP Conf. Proc. 1515 (2013) pp.425-432.
S. Mattei, M. Ohta, A. Hatayama, J. Lettry, Y. Kawamura, M. Yasumoto, and C. Schmitzer, RF Plasma modeling of the Linac4 H- ion source, AIP Conf. Proc. 1515 (2013) pp.386-393.
Ø. Midttun, T. Kalvas, M. Kronberger, J. Lettry, R. Scrivens, A magnetized Einzel-lens electron dump for the Linac4 H- ion source, AIP Conf. Proc. 1515 (2013) pp.481-490.

## Slide 46: ICIS 2013 Chiba accepted for publication in AIP Conf. Proc.
J. Lettry, D. Aguglia, P. Andersson, S. Bertolo, A. Butterworth, Y. Coutron, A. Dallocchio, E. Chaudet, J. Gil-Flores, R. Guida, J. Hansen, A. Hatayama, I. Koszar, E. Mahner, C. Mastrostefano, S. Mathot, S. Mattei, Ø. Midttun, P. Moyret, D. Nisbet, K. Nishida, M. O’Neil, M. Otha, M. Paoluzzi, C. Pasquino, H. Pereira, J. Rochez, J. Sanchez Alvarez, J. Sanchez Arias, R. Scrivens, T. Shibata, D. Steyaert, T. Yamamoto, Status and Operation of the Linac4 Ion Source Prototypes.
Ø. Midttun, J. Lettry, and R. Scrivens, Measurements of Linac4 H- Ion Source Beam with a Magnetized Einzel Lens Electron Dump.
R. Scrivens, G. Bellodi, O. Crettiez, V. Atanasov Dimov, D. Gerard, E. Graneman Souza, R. Guida, J. Hansen, J.-B. Lallement, J. Lettry, A. Lombardi, Ø. Midttun, C. Pasquino, U. Raich, B. Riffaud, F. Roncarolo, C. A. Valerio-Lizarraga, J. Wallner, T. Zickler, Linac4 Low Energy Beam Measurements with Negative Hydrogen Ions.
C. A. Valerio-Lizarraga, J.-B. Lallement, I. Leon-Monzon, J. Lettry, Ø. Midttun, R. Scrivens, Space Charge Compensation in the Linac4 Low Energy Beam Transport Line with Negative Hydrogen Ions.
A. Grudiev, J. Lettry, S. Mattei, M. Paoluzzi, and R. Scrivens, Numerical Simulation of Electromagnetic Fields and Impedance of CERN LINAC4 H- Source taking into Account the Effect of the Plasma.
S. Mattei, M. Ohta, M. Yasumoto, A. Hatayama, J. Lettry, A. Grudiev, Plasma ignition and steady state simulations of the Linac4 H- Ion Source.
M. Ohta, S. Mattei, M. Yasumoto, A. Hatayama and J. Lettry, Numerical Study of the Inductive RF-discharge Initiation for the Linac4 H- Ion Source.
T. Yamamoto, T. Shibata, M. Ohta, M. Yasumoto, K. Nishida, A. Hatayama, S. Mattei, J. Lettry, K. Sawada and U. Fantz, Modeling of Neutrals in the Linac4 H- Ion Source Plasma; Hydrogen Atom Production Density Profile and Ha Intensity by CR Model.
K. Nishida, S. Mochizuki, M. Yasumoto, M. Ohta, J. Lettry, S. Mattei, and A. Hatayama, Equivalent Circuit of RF-Plasma with The Transformer Model.

## Slide 47: ONIX PIC-simulation of the plasma-beam formation:
IS01 & IS02 steady state H+ density
P-density: O(1018) m-3
S. Mochalskiy, Collaboration with LPGP Orsay France
13 runs @ 2weeks & 20 cpus:
IS01, (volume production), IS02, Vol. & Surface
Sensibility study: H- prod. Rate (1-7 kA/m2), filter field strength, Super particles density, plasma density (5×1017-2×1018 m-3) and electron to H- ion ratio (5:5-1:10)
positive and negative ion extraction
IS02 No-Cs
Tested Nov.12th

## Slide 48: Conclusion outlook
The ISWP could meet RFQ driven deadlines, a 15 mA, 45 kV H- commissioning beam is available in the linac4.
However, the intensity and beam emittance are not met. The IS01 optics emittance is limited by volume source e/H ratio requiring design of high current low energy e-dumping.
Two sets of prototypes were produced, more time is required to conclude on their performances and potential.
All ancillary systems are operational, all of them require improvements in reliability, controls (GUI) and monitoring.
The availability of the test stand was O(20%) over the last 4 month… many valid explanations, but 98% is very far. Numerous specialist needed, all of them very busy, all found a slot within the next few days.
Simulation of the key processes (i.e. H2-injection, RF, plasma heating) are at a level where engineering and optimization could start.
Thank to all contributors, great motivated IS-team

## Slide 49
Major contributions from IS-team students and fellows