## Slide 1: Hybrid or Monolithic ? Pixel detectors for future LHC experiments
Tomasz Hemperek
PH-ESE electronics seminar, CERN 17th December 2013

## Slide 2
The Bonn Team
Design Team:
  Hans Krueger
  Tomasz Hemperek
  Tetsuichi Kishishita
  Miroslav Havranek
  Yunan Fu
  Piotr Rymaszwski
  Xiaochao Fang
  Marcus Gronewald
Our main projects:
Thanks to our close collaborators!

## Slide 3
Overview
Current status and futere of Hybrid Pixel Sensors
Current status and futuer of Monolitic Pixle Sensors
Conclusions

## Slide 4
Moore's law in HEP
Name | D-OMEGA Ion | LHC1 | FE-I3 | FE-I4 | FE-I5
Year | 1991 | ~1996 | ~2005 | ~2011 | ???
Technology Node | 3 µm | 1µ | 0.25 µm | 0.13 µm | 65 nm??
Chip size | 8.3x6.6 mm2 | 8x6.35 mm2 | 10.8x7.6 mm2 | 10.2x19 mm2 | ???
Pixel size | 75x500 µm2 | 50x500 µm2 | 50x400 µm2 | 50x250 µm2 | 25x100 µm2 ??
Pixel array | 16x63 | 16x127 | 18x160 | 80x336 | ???
Transistor count | ??? | 800k | 3.5M | 80M | ???

## Slide 5
Price/Scaling
Technology node | 130nm | 65nm | 40nm
6T SRAM cell (um2) | 2.4 | 0.52 | 0.24
bit size in memory (um2) | ~ 3.2 | ~ 0.7 | ~ 0.32
10bit words in 100x100um | ~ 310 | ~ 1430 | ~ 3120
NRI* (um2) | $2000-$3000 | $6000-$7000 | $8000-$9000
* based on MPW prices for bigger (>25um2) designs

## Slide 6
Hybrid Pixel Detectors
-fine pitch flip-chip assembly of:
  CMOS r/o chips (CSA + DSP per pixel)
  Si (planar or 3D) or Diamond detectors
- high density electronics
- moderate - good SNR
- high material budget
- expensive assembly
Parameters
ATLAS Pixel Module (FE-I3)

## Slide 7
Current state of art implementations - FE-I4
Analog Channel
Overview

## Slide 8
Current state of art implementations - Medipix 3
Other hybrids in 130nm:
Timpix 3
VeloPix
DosePix
…

## Slide 9
Hybrid Pixels Future
125 mm
FE-X5 CMOS 130 nm 3D
?
FE-X5 CMOS 65 nm

## Slide 10
3D Integration

## Slide 11
3D Integration
FE-I4-P1
4x3mm size
IBM 0.13µm LVT 8LM
FE-C4-P1
4x3mm size
CHRT 0.13µm LP 8LM
FE-C4-P2
4x3mm size
CHRT 0.13µm LP 8LM
FE-C4-P3
2.5x2.5mm size
CHRT 0.13µm LP 8LM
61x14 array
61x14 array
30x10 array
CPPM, UniBonn, LBNL
4 years later ........

## Slide 12
65 nm prototypes designed in Bonn
Our goal:
  design Data handling Processor (DHP) chip for Bell2
  explore potential of 65 nm technology
Design of test-chips to study analog performance of 65 nm technology
Analog FE-prototypes: FE-T65-0, FE-T65-1
Other prototypes: SAR-ADC, PLL, LVDS, SEU tests
FE-T65-1
DHPT0.1 (subm.10/2011)
DHPT0.2 (subm. 03/2012)
FE-T65-0
Chip size: 1.96×1.96 mm2
SAR-ADC

## Slide 13
FE-T65-1 – single pixel
180 µm
25 µm
Analog part :
- CSA tunable input capacitance
- programmable charge injection
- FDAC – tunable feedback current
- TDAC – tunable threshold
- comparator
Digital part (custom and big std. cells):
- identical for every pixel
- configuration register 15-bits
- 8-bit shift register-counter
- mask-bit
- HitOr
Analog - 50 µm

## Slide 14
Charge sensitive amplifier with continuous reset
Version with continuous comparator
Version with dynamic comparator

## Slide 15
Charge sensitive amplifier with switched reset
LHC Mode (40 MHz)
Slow mode (6.25 MHz)
Properties of switched CSA:
- no ballistic deficit
- higher gain
- fast reset
- requires synchronous
operation
Version with continuous comparator
Version with dynamic comparator
FE – with switched CSA
2ke – 12ke; step 2ke

## Slide 16
Continuous vs dynamic comparator
Differential stage
CS Stage
Differential stage
Latch
Continuous comparator
Popular 2 stage architecture
Asynchronous operation
Consumes power even idle state
Dynamic comparator
Based on latch in metastable state
Does not consume power in idle state
Active only when CLK edge comes
Power proportional to CLK frequency

## Slide 17
Noise – continuous CSA
Continuous CSA + continuous comparator
Continuous CSA + dynamic comparator

## Slide 18
Noise – switched CSA, comparison of all versions
Switched CSA + continuous comparator
Switched CSA + dynamic comparator
CSA | Comparator | <ENC> [e-] | P [µW]
Continuous | Continuous | 144 | 10.4
Continuous | Dynamic | 183 | 10.6
Switched | Continuous | 113 | 14.6
Switched | Dynamic | 157 | 14.8
Cin = 75 mF, 40 MHz

## Slide 19
FE-I4 vs FE-T65-1 (analog part)
 | FE-I4 | FE-T65-1
Technology | 130 nm | 65 nm
Dimensions of analog part | 156 × 50 µm2 | 59 × 25 µm2
Charge sensitive amplifier | 2 stages | 1 stage
Comparator | continuous | continuous /dynamic
Analog power consumption | 12.6 + 5.4 + 3.9 = 21.9 µW / pixel | 6.8 + 3.8 = 10.6 µW (18 µW) / pixel
Analog power density | 1.75 mW / mm2 | 2.36 mW / mm2 (4 mW / mm2)
65 nm – what we have learned:
- shrinking pixel size down to 125 × 25 µm2 is possible
- dynamic comparator saves power but has larger threshold dispersion
- ENC is comparable with FE-I4
- power density has to be optimized

## Slide 20
SAR ADC IN 65nm - Layout
40 um
70um
Layout is not area optimal
Possible de-cup under DAC?
DAC
Only external sample signal needed!

## Slide 21
SAR ADC
DAC
DAC Layout
Control
Main Control Logic

## Slide 22
Asynchronous ADC Measurements @ 10MS/s
Single Ended Mode
Differential Mode
Power consumption: ~40uW @1.2V
Works up to 12.5 MS/s
Dynamic Range: 0.8V

## Slide 23
Some possibilities in 65nm (for imaging applications)
SRAM 3072x40 bits
368x231
um
ADC
ADC
ADC
ADC
200 um
200 um
100 um
100 um
SRAM 384x40 bits
100x198
um
ADC
ADC
ADC
ADC
Fast full frame storage
In pixel histograming

## Slide 24
Preemphasis
Preemphasis Off
Preemphasis On

## Slide 25
DHPT 0.1 - High Speed Link in 65nm
20m of Infiniband cable @1.6Gbps of random data

## Slide 26
65nm in Bonn
Test chips for custom IP verification
  Two mini@sic submissions in 2011 and 2012
  1.6GHz PLL
  Gigabit link driver
  LVDS transmitter & receiver
  Pixel matrices with analog front-ends (CSA + comp.)
  In pixel ADCs
DHPT 1.0, first production version
  MPW submission in Aug. 2013
  12 mm2 area, C4 bumps (SAC 305), 200µm pitch
  >300k Gates, >3MB SRAM
  PLL, 1.6Gb/s serial link, CML preamhasis
  Reference
  LVDS and HSTL IO
  DACs, ADC
  ...
DHPT 0.1 and DHPT 0.2 test chips
3 mm
4 mm
Data handling processor DHPT 1.0

## Slide 27
65nm conclusions
Possible great improvement in functionality on smaller area
Good analog performance
Good radiation tolerance*
Higher submission cost
More digital chip
Technology available on MPW with bumps/full wafers
BUT what about sensor?

## Slide 28
Traditional MAPS
- Better resolution (small pixels)
- Low(er) power
- Can be only NMOS in pixel
- Slow
Parameters

## Slide 29
State of the art MIMOSA-26

## Slide 30
Now
Future ?
  more volume → higher SNR
  collection by drift → faster charge collection → less trapping
  lower cost (no hybridization)

## Slide 31
Charge Collection in Depletion Layer
Depletion width d
  QMIP
  Cparallel plate
  High voltage on the r/o node  HV CMOS process
  High resistive substrate material  CMOS on high resistive substrate (“HR CMOS”)
  Something in-between
Chart: Depletion Width in Silicon
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120 | 125 | 130 | 135 | 140 | 145 | 150 | 155 | 160 | 165 | 170 | 175 | 180 | 185 | 190 | 195 | 200
1 | 0 | 0.30411 | 0.43008 | 0.52673 | 0.60822 | 0.68001 | 0.74491 | 0.8046 | 0.86015 | 0.91233 | 0.96168 | 1.1778 | 1.36 | 1.5205 | 1.6657 | 1.7991 | 1.9234 | 2.04 | 2.1504 | 2.2553 | 2.3556 | 2.4518 | 2.5444 | 2.6337 | 2.72 | 2.8037 | 2.885 | 2.9641 | 3.0411 | 3.1162 | 3.1895 | 3.2612 | 3.3314 | 3.4 | 3.4674 | 3.5334 | 3.5983 | 3.662 | 3.7246 | 3.7861 | 3.8467 | 3.9064 | 3.9651 | 4.023 | 4.0801 | 4.1363 | 4.1919 | 4.2467 | 4.3008
20 | 0 | 1.36 | 1.9234 | 2.3556 | 2.72 | 3.0411 | 3.3314 | 3.5983 | 3.8467 | 4.0801 | 4.3008 | 5.2673 | 6.0822 | 6.8001 | 7.4491 | 8.046 | 8.6015 | 9.1233 | 9.6168 | 10.0862 | 10.5347 | 10.9648 | 11.3787 | 11.7781 | 12.1644 | 12.5387 | 12.9023 | 13.2558 | 13.6002 | 13.936 | 14.264 | 14.5846 | 14.8983 | 15.2055 | 15.5066 | 15.802 | 16.092 | 16.3768 | 16.6568 | 16.9321 | 17.203 | 17.4698 | 17.7325 | 17.9914 | 18.2466 | 18.4982 | 18.7466 | 18.9916 | 19.2336
100 | 0 | 3.0411 | 4.3008 | 5.2673 | 6.0822 | 6.8001 | 7.4491 | 8.046 | 8.6015 | 9.1233 | 9.6168 | 11.7781 | 13.6002 | 15.2055 | 16.6568 | 17.9914 | 19.2336 | 20.4003 | 21.5038 | 22.5534 | 23.5562 | 24.5181 | 25.4436 | 26.3366 | 27.2004 | 28.0375 | 28.8503 | 29.6409 | 30.4109 | 31.1619 | 31.8953 | 32.6121 | 33.3135 | 34.0005 | 34.6738 | 35.3343 | 35.9827 | 36.6196 | 37.2456 | 37.8613 | 38.4671 | 39.0636 | 39.651 | 40.2299 | 40.8006 | 41.3633 | 41.9186 | 42.4666 | 43.0076
1000 | 0 | 9.6168 | 13.6002 | 16.6568 | 19.2336 | 21.5038 | 23.5562 | 25.4436 | 27.2004 | 28.8503 | 30.4109 | 37.2456 | 43.0076 | 48.0839 | 52.6733 | 56.8937 | 60.8219 | 64.5113 | 68.0009 | 71.32 | 74.4913 | 77.533 | 80.4598 | 83.2838 | 86.0151 | 88.6624 | 91.2328 | 93.7328 | 96.1678 | 98.5427 | 100.8617 | 103.1285 | 105.3466 | 107.5189 | 109.6482 | 111.7369 | 113.7873 | 115.8014 | 117.781 | 119.728 | 121.6437 | 123.5298 | 125.3875 | 127.2181 | 129.0227 | 130.8024 | 132.5582 | 134.2911 | 136.0018
2000 | 0 | 13.6002 | 19.2336 | 23.5562 | 27.2004 | 30.4109 | 33.3135 | 35.9827 | 38.4671 | 40.8006 | 43.0076 | 52.6733 | 60.8219 | 68.0009 | 74.4913 | 80.4598 | 86.0151 | 91.2328 | 96.1678 | 100.8617 | 105.3466 | 109.6482 | 113.7873 | 117.781 | 121.6437 | 125.3875 | 129.0227 | 132.5582 | 136.0018 | 139.3604 | 142.6399 | 145.8457 | 148.9825 | 152.0547 | 155.066 | 158.0199 | 160.9195 | 163.7679 | 166.5676 | 169.3209 | 172.0302 | 174.6975 | 177.3247 | 179.9135 | 182.4656 | 184.9825 | 187.4656 | 189.9162 | 192.3356
5000 | 0 | 21.5038 | 30.4109 | 37.2456 | 43.0076 | 48.0839 | 52.6733 | 56.8937 | 60.8219 | 64.5113 | 68.0009 | 83.2838 | 96.1678 | 107.5189 | 117.781 | 127.2181 | 136.0018 | 144.2517 | 152.0547 | 159.4763 | 166.5676 | 173.369 | 179.9135 | 186.2282 | 192.3356 | 198.255 | 204.0028 | 209.5929 | 215.0378 | 220.3482 | 225.5335 | 230.6023 | 235.5621 | 240.4196 | 245.1808 | 249.8513 | 254.4361 | 258.9398 | 263.3664 | 267.7199 | 272.0037 | 276.221 | 280.375 | 284.4683 | 288.5035 | 292.483 | 296.4091 | 300.2839 | 304.1094

## Slide 32
Options for n-on-p Read-out
p-substrate
Deep n-well
P+
p-well
Charge signal
Electronics (NMOS only)
P+
p-substrate
n+
p-well
Charge signal
Electronics (NMOS only)
n+
CCPD (HVCMOS)
DMAPS-A
“MAPS” like
CMOS with additional implants
CMOS with twin or triple wells
p-substrate
Deep n-well
P+
p-well
Charge signal
Electronics (full CMOS)
P+
nw
p-substrate
n+
p-well
Charge signal
Electronics (full CMOS)
n+
nw
deep p-well
Electronics inside charge collection well
Collection node with large fill factor  rad. hard
Large sensor capacitance (DNW/PW junction!)  x-talk, noise & speed (power) penalties
Full CMOS with isolation between NW and DNW
Electronics outside charge collection well
Very small sensor capacitance  low power
Potentially less rad. hard (longer drift lengths)
Full CMOS with additional deep-p implant

## Slide 33
Monolithic Pixel Sensors on HV-CMOS process
Parameters
Depletion (small)
Low leakage
Possible high resolution
Limited use of PMOS
I. Peric

## Slide 34
CCPD + FE-I4 (HV2FEI4)
An active sensor!

## Slide 35
3T MAPS on standard CMOS process
Parameters
A. Mekkaoui
Depletion (small)
Low leakage
Possible high resolution
Full CMOS
High capacitance
Low breakdown

## Slide 36
Monolithic technology requirements for LHC
High-resistive substrate (>1kOhm-cm)
Isolated PMOS and NMOS transistors (deep n-well/p-well)
Good breakdown performance
Thinning
Backside implantation and implant activation
Backside metallization (if needed)

## Slide 37
Simple device cross-section
High signal (full depletion possible)
Fast (collection by drift)
Small pixels
Only NMOS in active area
Input capacitnce dominated by deep-nwell tp pwell capacitance
Pros
Cons

## Slide 38
Electrostatic Potential (HV)

## Slide 39
Charge Collections
Electron Density @ 200V (no radiation)
Current on collecting electrode @200V

## Slide 40
Charge Collections Efficiency
Fluence (Neq/cm2) | Back Voltage [V] | CCE [%]
0 | 100/200 | 100
1e14 | 100 | 96
1e14 | 200 | 97
1e15 | 100 | 75
1e15 | 200 | 80

## Slide 41
ESPROS Photonic CMOS™ Process
There is more to this in this technology 

## Slide 42
EPCB01 - overview
DMAPS pixels
Deep N-well pixels
Transistor array for parameter extraction
Chip size: 1.4×1.4 mm2
First 50um, back side processed, full CMOS, “fully depleted”
(>2kOhm-cm substrate).

## Slide 43
EPCB01 - Functional Blocks
Deep N-well pixels
  3T readout
  Analog Output
DMAPS pixels
  Pixel Charge Sensitive Amplifier (CSA)
    continuous discharge
    reset
  Pixel Comparator
    asynchronous
    dynamic
  Tuning DAC
  Digital Sift Register Readout
Custom Pads
Transistors

## Slide 44
EPCB01 - Test system
MIO
GPAC
DUT
EPCB01
FPGA Multi-IO (MIO) board
General Purpose Analog Card
- universality → can be used for other DUTs
- provides bias voltages and currents for DUT
- provides power supply for the DUT
- distributes digital signals from MIO to DUT
Board carrying DUT
EPCB01

## Slide 45
EPCB01 - Pixel Array Readout
CSA- switched reset
dynamic comparator
CSA – continuous discharge asynchronous comparator

## Slide 46
EPCB01 - Pixel Array
Pixel size: 40×40 µm2
Sensing area: 20×20 µm2
PIXEL
SENSOR
RESISTOR
CSA
Q-INJ.
HIT OR
TDAC
COMP
CDS

## Slide 47
EPCB01 - Pixel Array Bias Configurations
AC coupled
resistor bias
AC coupled
self bias
DC coupled

## Slide 48
EPCB01

## Slide 49
EPCB01 – more measurements

## Slide 50
Pegasus
Parameters:
  180nm CMOS (TowerJazz)
  Different wafer materials
    18µm HR epi
    40µm HR epi
    HR bulk
  50 x 50 µm2 and 25 x 25µm2 pixels
thanks to W. Dulinski, M. Kachel (IPHC)

## Slide 51
Pegasus - Electrostatic Potential (TCAD example)

## Slide 52
PEGASUS - First signs of life
Fe55 Spectra for 18µm epi
Sr90 and Fe55 Spectra for 18µm epi
M. Kachel (IPHC)

## Slide 53
FD-SOI
Parameters
Almost perfect technology but due to back gate effect not radiation hard.

## Slide 54
HV-SOI
Layout
First signs of life
Concept

## Slide 55
More to come
150nm – submitted Q4 2012
  full CMOS
  n-type > 2kOhm-cm substrate
  thinned
  back implanted
180nm – submitted Q1 2013
  full CMOS
  p-type > 1kOhm-cm substrate
  full wafers -> thinning/back implanting possible
180nm - submitted Q1 2013
  full CMOS
  p-type - initially 100 Ohm-cm
  very HV isolation guaranteed
130nm – submission Q4 2013
  HV-CMOS(CCPD)/full CMOS
  p-type >3kOhm-cm
  full wafers -> thinning/back implanting possible
150nm - submission Q1 2014
  HV-CMOS(CCPD)/full CMOS/ possibly T3
  p-type >2kOhm-cm (~4-5k Ohm-cm)
  thinned
  back implanted
  full wafers

## Slide 56
Possible scenarios for Monolithic Sensors
Hybrid Pixels with “smart” diodes:
  HR- or HV-CMOS as a sensor (8”)
  Standard FE chip
  CCPD (HVCMOS) on FE-I4
CMOS Active Sensor + Digital R/O chip
  HR- or HV-CMOS sensor + CSA (+Discriminator)
  Dedicated “digital only” FE chip
Monolithic Active Pixel Sensor
  MAPS usually on epi substrate  diffusion signal, not suited for HL-LHC
  HR- material (charge collection by drift)  Fully depleted MAPS (DMAPS)
Diode + full analog processing
Digital only FE chip
Wafer to wafer bonding
Diode + preamp
FE chip
Diode + Amp + Digital

## Slide 57
Conclusions
Hybrid Pixel Detectors:
- minitaruzation 65nm and below
- smaller pixel
- smarter pixels
- more digital chips
- 3D, diamond or active CMOS sesors for ultra high radiation
Depleted Monolitic Detectors:
- more radiation tolerance
- will take space of hybrids/strips for less dymanding application
- as a accitve sensor layer for ultra fast enviroments

## Slide 58
Thank you!
Question, comments, suggestions:
hemperek@uni-bonn.de