## Slide 1
Development of a pixel ASIC verification environment
Elia Conti, Sara Marconi
SystemVerilog and UVM mini-workshop – 14/11/2013

## Slide 2
  Introduction
    Requirements of VE for next generation pixel chips
  Class-based SystemVerilog VE
    Device Under Test (DUT)
    Verification components
  UVM VE
    Evaluation of simulation performance
  Conclusion and future work
OUTLINE

## Slide 3
RD53 Collaboration (CMS/ATLAS)
Development of pixel readout integrated circuits for extreme rate and radiation
ATLAS and CMS phase 2 pixel upgrades (~2020)
Peak luminosity 1-2×1034 cm-2 s-1
Critical challenges on IC design
Smaller pixels to resolve tracks (size reduction)
Hit rates ~1-2 GHz/cm2 (data rate)
Radiation levels ~1 Grad (radiation hardness techniques)
Much higher output bandwidth (transmission)
Large IC format (low power)
Use of CMOS 65 nm (technology)
Goal of the verification working group:
Development of dedicated verification and simulation framework for optimization of next generation pixel chips
Introduction – RD53

## Slide 4
Simulation of alternative pixel chip architectures at increasingly refined level as design progresses
Automated verification functions
Different kinds of data sets
  realistic (extreme) pixel hits and triggers with constrained random distributions
  particle hits from external Monte Carlo simulations and sensor simulations
  mixed data
Hardware Verification and Description Language (HVDL): SystemVerilog
  module-based Device Under Test (DUT) / class-based verification components
  standardization, reusability  Universal Verification Methodology (UVM) library
[J. Christiansen, M. Garcia-Sciveres, RD53 proposal, 2013]
Introduction – Requirements of Verification Environment for next generation pixel chips (I)

## Slide 5
Simulation of alternative pixel chip architectures at increasingly refined level as design progresses
Automated verification functions
Different kinds of data sets
  realistic (extreme) pixel hits and triggers with constrained random distributions
  particle hits from external Monte Carlo simulations and sensor simulations
  mixed data
Hardware Verification and Description Language (HDVL): SystemVerilog
  module-based Device Under Test (DUT) / class-based verification components
  standardization, reusability  Universal Verification Methodology (UVM) library
Preliminary
pixel chip behavioral time-based description
Preliminary
SystemVerilog
class-based
verification
environment
Software tool: Cadence Incisive
Introduction – Requirements of Verification Environment for next generation pixel chips (II)

## Slide 6
Single pixel region with custom number of pixels
PR buffer is an array of SystemVerilog queues
Pixel Chip
Pixel Region (PR)
END OF COLUMN
(external ToA counter)
Pixel matrix
PR buffer
TRIGGER LOGIC
ToA
ToT
HIT
PACKETS
TIME TAG
HITS
TRIGGER
Digital
PUC
ToT
conv.
.....
.....
.....
PIXEL BUSY FLAGS
PR BUFFER FULL FLAG
Class-based SystemVerilog Verification Environment – DUT (I)

## Slide 7
In order to keep hit generation as general as possible a simple ToT converter module has been defined which abstracts the behavior of the analog front-end
Current ToT converter does not produce time-walked hits
Pixel Unit Cell (PUC)
Digital
PUC
ToT
converter
ANALOG HITS
DISCRIMINATOR
OUTPUTS
ToA
ToT
PIXEL BUSY FLAGS
Class-based SystemVerilog Verification Environment – DUT (II)

## Slide 8
Automated stimuli generation: randomized/external file
Conformity checks between pixel chip inputs and outputs
Monitoring and reporting on lost hits (pixel dead time/PR buffer full)
DUT
PixelChip
Flag Component
Flag Monitor
Readout Component
Readout Monitor
PixelChip Interfaces
PixelChipHarness
Clock and reset generator
PixelChipEnv
Stimuli Component
HiLevel
Generator
Hit Driver
Hit Monitor
Trigger
Driver
Conformity Checker
Trigger
Monitor
Hit
Generator
Trig_intf
Hit_intf
Flag_intf
Readout_intf
Class-based SystemVerilog Verification Environment – Block diagram

## Slide 9
Component
-instance_name : string -parent : Component #children[$] : Component
+new(_instance_name : string, _parent : Component) +body() +get_name() : string +get_parent() : Component +get_hier_name() : string +run()
Stimuli_Component
+gen : HiLevel_Generator +hit_gen : Hit_Generator +hit_drv_ar : Hit_Driver array +trig_drv : Trigger_Driver +hit_mon_ar : Hit_Monitor array +trig_mon : Trigger_Monitor +hit_ch : Channel +trig_ch : Channel Hit_drv_ch_ar : Channel array +hit_analysis_ar : Channel array +trig_analysis : Channel
+new(hit_hook : hit_intf, trig_hook : trig_intf) +body()
Readout_Component
+mon : Readout_Monitor +analysis : Channel
+new(readout_hook : readout_intf) +body()
Flag_Component
+mon : Flag_Monitor +analysis : Channel
+new(flag_hook : flag_intf) +body()
Conformity_Checker
+hit_chan : Channel array +trig_chan : Channel +readout_chan : Channel +flag_chan : Channel #expected[$] : Readout_Trans #obj : Objection
+new() +body() #service_hit() #service_readout() #service_flags()
Class-based SystemVerilog Verification Environment – Components (I)

## Slide 10
Stimuli_Component
HiLevel_Generator: generation of high level transactions (randomized or from external file)
High level transactions are fed to Trigger_Driver (translation into trigger signal) and to Hit_Generator
Hit_Generator: translation + randomization of high level transactions into a matrix of hit transactions (one Hit_Driver per pixel)
Hit_Driver: translation into “analog hit” signal (no delays modeled so far)
Hit_Monitor and Trigger_Monitor: generation of hit transactions and trigger transactions (adding time information) from pixel chip inputs
Readout_Component
Readout_Monitor: generation of readout transactions from pixel chip outputs
Flag_Component
Flag_Monitor: generation of flag transactions from pixel chip flags (pixel busy and PR buffer full)
Class-based SystemVerilog Verification Environment – Components (II)

## Slide 11
Transaction
#ID : int -next_ID : int #owner : Component
+new(owner : Component) +psprint() : string +copy() : Transaction +compare(other : Transaction) : bit
HiLevel_Trans
#BX_ID : int -next_BX_ID : int +isTrig : bit
isTrig_choice
+new(owner : Component) +psprint() : string +copy() : Transaction +compare(other : Transaction) : bit +convert(converted : Hit_Trans)
Hit_Time_Trans
+timeOfArrival : int unsigned +amplitude : int unsigned
+new(owner : Component) +psprint() : string +copy() : Transaction +compare(other : Transaction) : bit
Trigger_Time_Trans
+timePlusLatency: int unsigned
+new(owner : Component) +psprint() : string +copy() : Transaction +compare(other : Transaction) : bit
Readout_Trans
+timeOfArrival: int unsigned 2D array +amplitude : int unsigned 2D array
+new(owner : Component) +psprint() : string +copy() : Transaction +compare(other : Transaction) : bit
Generated by HiLevel_Generator
Fed to Hit_Generator and Trigger_Driver
Produced by Hit_Monitor
Fed to Conformity_Checker
Produced by Trigger_Monitor
Fed to Conformity_Checker
Produced by Readout_Monitor
Fed to Conformity_Checker
Hit_Trans
+isHit : bit +amplitude : int unsigned -next_row_ID -current_row_ID #row_ID -next_col_ID #col_ID
amplitude_value isHit_choice
+new(owner : Component, incr_ID : bit, fst_pix : bit) +psprint() : string +copy() : Transaction +compare(other : Transaction) : bit
Flag_Trans
+bufferFull: bit unsigned 2D array +pixelBusy_ToT : bit 2D array +pixelBusy_DUT : bit 2D array
+new(owner : Component) +psprint() : string +copy() : Transaction +compare(other : Transaction) : bit
Produced by Flag_Monitor
Fed to Conformity_Checker
Produced by Hit_Generator
Fed to each Hit_Driver
Class-based SystemVerilog Verification Environment – Transactions

## Slide 12
…
Input Hit Container
…
…
Predicted
DUT
Output
Actual
DUT
Output
Reference Model
Checker
Reporting on lost hits due to dead time
Reporting on conformity between DUT inputs and outputs
Reporting on pixel region
buffer full
Conformity Checker
HIT_TIME
TRANSACTION
TRIGGER_TIME
TRANSACTION
FLAG
TRANSACTION
(PR buffer full)
FLAG
TRANSACTION
(PUC busy)
READOUT
TRANSACTION
INFO
WARNING
ERROR
Class-based SystemVerilog Verification Environment – Conformity Checker

## Slide 13
Standardize into UVM for:
More solid and documented base classes
Mature standard and growing community
Highly customizable reporting features
Highly configurable and reusable verification environment
At the moment, focus on stimuli generation only
No Readout/Flag components
No Conformity Checker
Study on scalability
Motivation
UVM Verification Environment

## Slide 14
Single agent with transaction containing array of hits
Different tests can be written
PixelChipEnv
Stimuli_Component
PixelChip_test1
PixelChip_test2
DUT
PixelChip
PixelChip Interfaces
PixelChipHarness
Clock and reset generator
Trig_intf
Hit_intf
Virtual Sequencer
Virtual Sequence
Trigger Driver
Trigger Monitor
Trigger
Sequencer
Trigger Sequence
#(Trigger_Trans)
Trigger Agent
Hit Agent
Hit Monitor
Hit Driver
Analog hits
Hit Sequence
#(Hit_Trans)
Hit
Sequencer
UVM Verification Environment – Block Diagram

## Slide 15
uvm_agent
uvm_component
Trigger_Sequencer
+num_trans: int unsigned
+new(string name, uvm_component parent)
Virtual_Sequencer
+m_hit_seqr: Hit_Sequencer +m_trig_seqr: Trigger_Sequencer
+new(string name, uvm_component parent)
Hit_Sequencer
+num_trans: int unsigned
+new(string name, uvm_component parent)
uvm_driver
uvm_monitor
uvm_sequencer
Trigger_Agent
+m_trig_intf: virtual trig_intf +m_trig_seqr: Trigger_Sequencer +m_trig_driver: Trigger_Driver +m_trig_seqr: Trigger_Sequencer +ap: uvm_analysis_port
+new(string name, uvm_component parent) +build_phase(uvm_phase phase) +connect_phase(uvm_phase phase)
Hit_Driver
+hook: hitdriver_test_hook +hit_trans_count: int
+new(string name, uvm_component parent) +build_phase(uvm_phase phase) +run_phase(uvm_phase phase) +idle (N: int) +drive(Hit_Trans t) +get_hit_trans_count(): int #cycles (N: int)
Trigger_Driver
+hook: trigdriver_test_hook +trig_trans_count: int
+new(string name, uvm_component parent) +build_phase(uvm_phase phase) +run_phase(uvm_phase phase) +idle (N: int) +drive(Trigger_Trans t) +get_trig_trans_count(): int #cycles (N: int)
Hit_Monitor
+hook: hitmonitor_test_hook +hit_trans_count: int +ap: uvm_analysis_port
+new(string name, uvm_component parent) +build_phase(uvm_phase phase) +run_phase(uvm_phase phase) +get_hit_trans_count(): int
Trigger_Monitor
+hook: trigmonitor_test_hook +trig_trans_count: int +ap: uvm_analysis_port
+new(string name, uvm_component parent) +build_phase(uvm_phase phase) +run_phase(uvm_phase phase) +get_trig_trans_count(): int
Hit_Agent
+m_hit_intf: virtual hit_intf +m_hit_seqr: Hit_Sequencer +m_hit_driver: Hit_Driver +m_hit_monitor: Hit_Monitor +ap: uvm_analysis_port
+new(string name, uvm_component parent) +build_phase(uvm_phase phase) +connect_phase(uvm_phase phase)
UVM Verification Environment – Components (I)

## Slide 16
uvm_component
uvm_test
uvm_env
PixelChip_env
+m_stim_comp: Stimuli_Component
+new(string name, uvm_component parent) +build_phase(uvm_phase phase)
PixelChip_base_test
+m_env: PixelChip_env
+new(string name, uvm_component parent) +build_phase(uvm_phase phase) +end_of_elaboration_phase(uvm_phase phase)
PixelChip_test1
+new(string name, uvm_component parent) +build_phase(uvm_phase phase) +report_phase( uvm_phase phase )
PixelChip_test2
+new(string name, uvm_component parent) +build_phase(uvm_phase phase) +report_phase( uvm_phase phase )
Stimuli_Component
+m_virt_seqr: Virtual_Sequencer +m_hit_agent: Hit_Agent +m_trig_agent: Trigger_Agent +m_hit_analysis: uvm_analysis_port +m_trig_analysis: uvm_analysis_port
+new(string name, uvm_component parent) +build_phase(uvm_phase phase) +connect_phase(uvm_phase phase)
UVM Verification Environment – Components (II)

## Slide 17
Hit_Time_Trans
+timeOfArrival : int unsigned 2D array +amplitude : int unsigned 2D array
+new(string name = "") +convert2string() : string
Trigger_Time_Trans
+timePlusLatency: int unsigned
+new(string name = "") +convert2string() : string
Hit_Trans
+time_ref: int +amplitude : int unsigned 2D array -next_time_ref
amplitude_value
+new(string name = "") +convert2string(): string +increment_tref()
uvm_sequence_item
Trigger_Trans
+time_ref: int +isTrig: bit -next_time_ref
isTrig_choice
+new(string name = "") +convert2string(): string +do_copy(uvm_object rhs) +increment_tref()
Trigger_Sequence
+num_trans: int unsigned
+new(string name = "") +pre_body() +body() +post_body()
Virtual_Sequence
+m_hit_seq: Hit_Sequence +m_trig_seq: Trigger_Sequence
+new(string name = "") +pre_body() +body() +post_body()
Hit_Sequence
+num_trans: int unsigned
+new(string name = "") +pre_body() +body() +post_body()
uvm_sequence
UVM Verification Environment – Transactions

## Slide 18
Agents
One agent is used for each interface of the DUT
Sequences and sequencers
  Hit_Sequence: generates a user-defined number of Hit_Trans
  Trigger_Sequence: generates a user-defined number of Trigger_Trans
  Virtual_Sequence: higher level sequence that coordinates lower level ones
  One sequencer per each sequence
Test
  Automatically instantiated when launched by top-level module
  Specified through command line
  Configures the environment (override classes, active/passive agents, number of transactions, default sequences to be run…) before building it
   VE source code does not need to be altered, only accessing the test file one can customize the test
  Different tests are being defined
UVM Verification Environment – Sequences and components

## Slide 19
  Simulations performed with only Stimuli_Component in the PixelChip_Env
  Matrix size: 1024x256 pixels (256K)
  NO DUT actually present (further development needed)
  Debug messages NOT evaluated (they cause huge overhead)
  Performance analyzed through Incisive Advanced Profiler (Iprof):
    100 transactions sent in sequence (to each pixel):
      Memory Usage: 20.3M program + 1113.1M data + 1.0M profile = 1134.4M total
      CPU Usage: 0.8s system + 142.2s user = 143.0s total (99.9% CPU)
    10k transactions sent in sequence (to each pixel):
      Memory Usage: 20.3M program + 1113.1M data + 1.0M profile = 1134.4M total
      CPU Usage: 1.1s system + 12216.0s user = 12217.1s total (100.0% CPU)
    Resource usage mainly for randomization (of 256K values to be sent to each pixel)
    A high level strategy for generating clusters should be defined
UVM Verification Environment – Study on scalability

## Slide 20
Conclusion and future work
  Preliminary version of SystemVerilog verification environment
    Class-based SystemVerilog
    Standardized into UVM library (focus on stimuli generation only)
  Study on scalability and simulation performance
    Resource usage mainly for randomization of transactions
  Further developments on the DUT:
    Implement more complex features (i.e. PR columns)
    Event-based TLM description of pixel chip
  Further developments on the Verification environment:
    Standardization of other components into UVM
    Implementation of new components
    Definition of high level transaction generation strategy

## Slide 21
BACKUP

## Slide 22
Class-based SystemVerilog VE – HiLevel Gen.
Component
-instance_name : string -parent : Component #children[$] : Component
+new(_instance_name : string, _parent : Component) +body() +get_name() : string +get_parent() : Component +get_hier_name() : string +run()
HiLevel_Generator
+sink_hit : Channel +sink_trig : Channel +template : HiLevel_Trans +num_trans : int +objection_to_stop : Objection
+new(_name: string, _parent: Component) +body()
Transaction
#ID : int -next_ID : int #owner : Component
+new(owner : Component) +psprint() : string +copy() : Transaction +compare(other : Transaction) : bit
HiLevel_Trans
#time_ref : int -next_time : int +isTrig : bit
isTrig_choice
+new(owner : Component, incr_ID bit) +psprint() : string +copy() : Transaction +compare(other : Transaction) : bit +convert(converted : Hit_Trans)
HiLevel_Generator
abstracts high level
interaction generator
For each collision cycle it generates a HiLevel_Trans transaction: any number of transactions can be chosen
This information is sent to both Hit_Driver and Trigger_Driver on 2 separate channels
Data members of HiLevel_Trans:
time_ref associated to each transaction (data type: int)
isTrig (yes/no signal: do we want Trigger_Driver to associate a trigger to current BX?)
isTrig is randomized at each collision cycle with constraints (50% yes-no probability)

## Slide 23
Class-based SystemVerilog VE – Hit Generator
Hit_Generator takes
HiLevel_Trans transactions
from input channel and
translates them in MxN
Hit_Trans transactions to
be sent through MxN
channels to the same number
of Hit_Drivers
Hit_Trans adds
2 position indexes according to destination Hit_Driver’s
isHit (yes/no signal: do we want that pixel to be hit during the current BX)?
Hit amplitude
Hit_delay (FURTHER STUDY NEEDED) to add a delay to the hit generation (could be randomized in a configurable range)
So far, amplitude, isHit are randomized at each collision cycle for each channel with constraints (amplitude in a given range, isHit with 50% yes-no probability)
Component
-instance_name : string -parent : Component #children[$] : Component
+new(_instance_name : string, _parent : Component) +body() +get_name() : string +get_parent() : Component +get_hier_name() : string +run()
Hit_Generator
+sink_drv : Channel_ar +source : Channel +template : Hit_Trans +num_trans : int +objection_to_stop : Objection
+new(_name: string, _parent: Component) +body()
Hit_Trans
+isHit : bit +amplitude : real_rand -next_row_ID -curr_row_ID #row_ID -next_col_ID #col_ID
isHit_choice delay_value
+new(owner : Component, incr_ID : bit, fst_pix : bit) +psprint() : string +copy() : Transaction +compare(other : Transaction) : bit
HiLevel_Trans
#time_ref : int -next_time : int +isTrig : bit
isTrig_choice
+new(owner : Component, incr_ID bit) +psprint() : string +copy() : Transaction +compare(other : Transaction) : bit +convert(converted : Hit_Trans)

## Slide 24
Further study on simulation performance (I)
Simulation performance is one of the main issues of the framework
A study has been carried out in order to compare different simulators that are a reasonable option:
  Vendor A
  Vendor B
In order to obtain meaningful results, a fully developed and specific OVM-Verification Environment and Pixel Chip has been used (FEI4_B provided by ATLAS)
Both gate level and RTL model have been used for the DUT
Different philosophy between tools when dealing with optimization:
  Vendor A: Optimization options have to be indicated in the simulation command, otherwise no optimization is performed
  Vendor B: if not differently specified, optimization is automatically performed (and access to the design is restricted)

## Slide 25
Further study on simulation performance (II)
The comparison has been done on the time spent by the simulator in:
  Compilation of libraries
  Elaboration of the design hierarchy
  Actual Simulation
The two tools have shown that compilation of libraries is not a bottleneck
An important difference has instead been observed in terms of elaboration time:
  Vendor A: much faster
  Vendor B: an approach that separates the elaboration of the DUT and of the Verification Environment can be used to overcome this bottleneck (when dealing with verification)
Remarkable difference observed in terms of simulation time:
  Vendor B: simulations are 3-6X faster