## Slide 1: Upgrade and consolidation of the online computing for systems aggregated with BRIL
A.Lokhovitskiy, UC-NZ

## Slide 2: Readouts and controls
μTCA based electronics
  New developments
  Readouts and controls are network based (TCP/IP)
  Requires a “Bridge host” 1 operational and 1 spare servers
  More than 1 crate can be driven by the “Bridge host” (total network bandwidth must be lower than 1 Gbps)
VME based electronics
  Existing systems and new developments
  VME bridges based on a new PCIe controller from CAEN
  Requires a “VMEPC” 1 operataional and 1 spare servers
  3 VME crates per 1 VMEPC, daisy chains if need more

## Slide 3: Network topology with μTCA crates
Bridge PC
Bridge PC
Bridge PC
uHAL
uHAL
Experimental Network
uHAL
uHAL
Target
Target
MCH
…
ABC
component
computer
switch
IPBus target
physical link
logical link
…
Target
Target
MCH
ControlHub
Bridge PC
ControlHub
DHCP
DNS
RARP
…
IPMI
daemon

## Slide 4: Standard servers
Available options:
  Default VMEPC – 1 multicore CPU, 16 GB memory, only one empty bay for an additional HDD, optionally: CAEN A3818 4 links PCI-e controller. 1U
  Intensive online processing server – 2 multicore CPUs, 64 GB memory 1U
  Extreme edition (on demand) – 2 top multicore CPUs, 64 GB memory (???)
Redundancy
  System disk is RAID1
  M+1 (M – number of operational servers, 1 – hot spare one)
  uTCA bridge hosts will be switched by a network router.

## Slide 5: Location
Suggested to put all servers into a rack at S2.
  Pros:
    Single location of computers for all detectors.
    Better cooling
    DAQ maintenance, central power cycling/restarting
  Cons:
    Need to string 12 fibers (about 50 meter each)
  Marc has some space in a rack which is enough to install all BRIL servers and have few empty slots for an extension.

## Slide 6: Migration (1/5)
BRM
brmbcmctrl2 (CMS) - OP
brmbcmctrl3 (CMS) - OP
brmbcmctrl4 (CMS) - OP
brmbcmctrl1 (TN) - OP
BRIL (all in .cms)
VMEPC-rack-U#-01 - OP
VMEPC-rack-U#-02 – OP
VMEPC-rack-U#-03 – S
SRV-rack-U#-01 – OP (trusted)

## Slide 7: Migration (2/5)
PLT
VMEPC-S1F08-01 – OP
PLTDEV-S1F08-01 - OP
BRIL (all in .cms)
VMEPC-rack-U#-04 – OP
VMEPC-rack-U#-05 - D
VMEPC-rack-U#-06 – S
  only if VMEPC-rack-U#-03 cannot take over servicing the operational tasks for PLT. (It’s M+2 redundancy)

## Slide 8: Migration (3/5)
HF Lumi
VMEPC-2F17-18 – OP
VMEPC-2F17-19 – OP
VMEPC-2F17-20
VMEPC-2F17-21
VMEPC-2F17-22
BRIL (all in .cms)
SRV-rack-U#-02 – OP
SRV-rack-U#-03 – S

## Slide 9: Migration (4/5)
HF RADMON
Custom configuration. Not a part of the CMS online cluster.
BRIL (all in .cms)
No requirements to any additional servers. Will use resources allocated for BRM servers.

## Slide 10: Migration (5/5)
Medipix
Custom configuration. Not a part of the CMS online cluster.
BRIL (all in .cms)
SRV-rack-U#-04 – OP (2 CPUs)
SRV-rack-U#-05– S

## Slide 11: New developments with μTCA
SRV-rack-U#-06– OP
SRV-rack-U#-07– S
Total dataflow bandwidth has to be less than 1 Gbps
If exceeds, we have to install more pairs using empty slots in our rack.

## Slide 12: Proposed rack present layout