## Slide 1: Drive Beam injector front end developments
DB injector introduction
Status of Hardware design, Klystron, SHB-buncher,Pre-buncher, Gun
Gun Test Facility

## Slide 2
CLIC DB front end,
Post CDR Project
For time being only major component development:
GUN, SHB, high bandwidth 500 MHz source, 1 GHZ MBK, modulator and fully loaded accelerating structure
Gun
SHB 1-2-3
PB
Buncher
Acc. Structures
500 MHz
Modulator-klystrons, 1 GHz, 15 MW
~ 140 keV
~ 12 MeV
Diagnostics
~ 3 MeV

## Slide 3
CLIC DB injector specifications
Parameter | Nominal value | Unit
Beam Energy | 50 | MeV
Pulse Length | 140.3 / 243.7 | ms / ns
Beam current | 4.2 | A
Bunch charge | 8.4 | nC
Number of bunches | 70128 | 
Total charge per pulse | 590 | mC
Bunch spacing | 1.992 | ns
Emittance at 50 MeV | 100 | mm mrad
Repetition rate | 100 | Hz
Energy spread at 50 MeV | 1 | % FWHM
Bunch length at 50 MeV | 3 | mm rms
Charge variation shot to shot | 0.1 | %
Charge flatness on flat top | 0.1 | %
Allowed satellite charge | < 7 | %
Allowed switching time | 5 | ns

## Slide 4: CLIC drive beam injector layout
Thermionic gun
Prebuncher
Buncher
Slit
Quadrupole
Bend
Accelerating cavity
53 MeV
140 KeV
6 MeV
26 MeV
SHB
Solenoids

## Slide 5
Parameter | Value
 | 2.64
 | 0.480
 | 50.0
Satellite(%) | 2.2
Parameter | Value
 | 2.64
 | 0.480
 | 50.0
Satellite(%) | 2.2
DB injector optimization
Final phase space at 50 MeV
phase space after TW buncher
Shahin Sanaye Hajari, IPM
Satellites and total losses significantly reduced !

## Slide 6
Tentative klystron
parameters
PARAMETER | VALUE | UNITS
RF Frequency Bandwidth at -1dB RF Power: Peak Power Average Power RF Pulse width (at -3dB) HV pulse width (at full width half height) Repetition Rate High Voltage applied to the cathode Tolerable peak reverse voltage Efficiency at peak power RF gain at peak power Perveance Stability of RF output signal at nominal working point RF phase ripple [*] RF amplitude ripple Pulse failures (arcs etc.) during 14 hour continuous test period Matching load, fundamental and 2nd harmonic Average radiation at 0.1m distance from klystron Output waveguide type, | 999.516 ≥ 1 ≥ 20 150 150 165 50 tbd, ≤ 180 tbd 67 ≤ 70 tbd, > 48 tbd ±1 (max) ±1 (max) < 1-2 tbd < 1 WR975 pressurised | MHz MHz MW kW μs μs Hz kV kV % dB μA/V1.5 RF deg % VSWR μSv/h 2-3 bar
Status: First Contract under negotiation with Thales

## Slide 7
Tentative klystron
parameters
Efficiency for 20 MW for different voltages (Thales study)

## Slide 8
ETH: Topology defined-matrix transformer based
Pulse transformer design almost finished
Expected prototype beginning 2014
Active bouncer theoretical design almost finished – construction in 2014
Modulator design advancing well
Davide Aguglia

## Slide 9
Sub-harmonic bunching system
Status:
RF design existing, mechanical design advanced,
Discussion with CERN work shop on realization
Power source:
500 MHz, 15-115 kW, wide band (60 MHz) sources needed for fast phase switching.
Solid state favored Started to discuss with industry and collaborations.
Hamed Shaker, IPM
 | SHB 1 | SHB 2 | SHB 3
Beam velocity | 0.62 c | 0.62 c | 0.62 c
Current | 5 A | 5 A | 5 A
Voltage | 15 kV | 30 kV | 45 kV
Bunch form factor | 0.058 | 0.57 | 0.73
Detuning | 1.6 MHz | 12.1 MHz | 12.7 MHz

## Slide 10
Sub-harmonic buncher design
Raphael Leuxe

## Slide 11
Pre-buncher design
Mohsen Dayyani Kelisani, IPM
About 100 kW of power needed for the pre-buncher with beam loading

## Slide 12
Typical MAGIC snapshot: particle positions in r-z
Contour plots of field components at t=35ns
Jacques Gardelle, CEA-CESTA
DB gun simulations

## Slide 13
a1 = 62,5 °
a2 = 35°
a1 = 67,5 °
a2 = 65°
rrms = 8 mm
ex,rms = 14 mm.mrad
rrms = 10,5 mm
ex,rms = 10 mm.mrad
Small cathode
new geometry dak 50mm
DB gun simulations
Jacques Gardelle, CEA-CESTA

## Slide 14
« Front-end Drive beam injector » CTF3
CTF 3 benchmark simulations
using MAGIC
Jacques Gardelle, CEA-CESTA

## Slide 15
CTF 3 benchmark simulations
Jacques Gardelle, CEA-CESTA

## Slide 16
Drive Beam gun simulations
Large cathode: 140 kV, 10 mm cathode, 5 A, 50 mm
Comparism with MAGIC (blue)
Emittance: Magic: 14.5; EGUN : 20-27 (depending on number of rays)
Same result after changing the anode aperture to 15 mm

## Slide 17
Thermionic Gun design

## Slide 18
Thermionic Gun design
B. Cadilhon,
CEA-CESTA

## Slide 19
Modulator based on a Marx structure with two 1700V IGBTs/cell
First prototype performances objective (for summer 2014)
    Output voltage range : 0 to -30kV
    Output current range : 0 to 10A
    Pulse width (on top) : 150µs
    Flatness of the top : ~ 1-2%
    Rep. rate : 10Hz
One of the key points of the modulator is the IGBTs driving circuit :
 first we decided not to use fiber optics to trigger the IGBTs
 technical solution with ferrite cores seems to be robust (under tests)
Schematic of a Marx cell
Photography of a 1.5kV Marx cell prototype
First experimental tests
on a 4 cells Marx prototype
HV Modulator status
CEA/CESTA
Bruno Cassany, CEA-CESTA

## Slide 20
Material | Max. Energy to stay solid
Aluminium | 836 J.g-1
Cuivre | 522 J.g-1
Titane | 1023 J.g-1
Graphite | 2715 J.g-1
Energy deposition in a beam dump by the 140 keV beam
Kevin Pepitone, CEA-CESTA

## Slide 21
Gun Test Facility

## Slide 22
Gun test facility

## Slide 23: Conclusion and Outlook
Challenging Drive beam frond project
Key elements under design or manufacturing , nice progress
Large collaborative effort
Hope to get some ‘real’ CLIC drive beam hardware to test in 2014

## Slide 24: End

## Slide 25
DB-accelerator structure
Input and output coupler design finished
Correct match, input reflection < 30 dB.
(red and green: two different geometries; red is final)
RF-design existing,
next steps: mechanical design and prototype
Rolf Wegener

## Slide 26
Calculs du canon proptotype CLIC0/ADELE
géométrie SLAC

## Slide 27
a1 = 52, 5°
a1 = 67,5 °
a1 = 90 °
black squares a2 = 30°; red circles a2 = 50°; blue up-triangles a2 = 70°;
Large cathode
new geometry dak 50mm