## Slide 1: Beam instrumentation developments at CTF3
E. Bravin, A. Goldblatt, T. Lefevre, S. Mazzoni, A. B. Morell, E. Nebot del Busto, R. Pan, J. R. Towler, M. Wendt,

## Slide 2: Introduction
BPM: cavity and stripline
BLM status
Longitudinal profile: Electro Optical and streak upgrade
Spectrometry: recent and future installations
OTR/ODR tests

## Slide 3: Main Beam Cavity BPM: Setup and Sensitivity
Reference cavity charge sensitivity: 130 V nC-1. Predicted 117 V nC-1.
Dipole cavity position sensitivity: 16.5 V nC-1mm-1. Predicted 17.1 V nC-1mm-1.
BPM required to measure orbit with 50 nm and 50 ns resolutions.
15 GHz stainless steel prototype cavity BPM installed in CALIFES.
Two cavities: Position (dipole) and reference (monopole).
Beam tests last spring.
No motor control to vary beam position, used corrector magnets.

## Slide 4: Main Beam Cavity BPM: Calibration and Plans
Calibration using corrector magnets.
13 μm horizontal beam jitter measured with focused beam.
Measurements will be repeated during next run using translation stages.
Redesigned
Prototype design has been adapted based on beam tests.
  Copper to give higher internal Q: reducing time resolution, improving spatial resolution
  New feedthrough coupler design to remove tuners on opposite waveguide wall.
  Monopole cavity dimensions altered to restore frequency and Q after changing feedthroughs
New redesigned prototype should be manufactured from copper and ready for bench testing in March.
A three BPM system is foreseen later in the year to demonstrate the combined spatial and temporal resolution.
Reference
Cavity
Position Cavity

## Slide 5: Stripline BPM development for CLIC drive beam
Stripline prototype with short-circuited electrodes installed in TBL at CTF3 and successfully tested with beam (2013)
FESA class developed for synchronous data acquisition with the rest of TBL BPMs (Fall 2013)
Resolution tests to be performed using MIA-SVD analysis (First run of 2014)
BEAM
STRIPLINE BPM
TBL Beam sweep in horizontal and vertical planes

## Slide 6: Stripline BPM development for CLIC drive beam
2 Stripline prototypes with 50Ω-terminated electrodes developed for CLIC Module, currently under fabrication (to be received in spring 2014).
8-port design for increased notch tunability and loop-through calibration.
Enhanced PETS interference suppression at 12 GHz (*).
Cold tests planned for summer 2014.
Beam tests planned for autumn 2014.
D. Gudkov BE-RF
(*)

## Slide 7: BLM investigations at TBL
Ionization Chambers
Diamond pCVD
ACEM
PEP-II
Fibre based BLM (200 um pure silica core + MPPC readout)
    RIA~200-300dB/km for 10kGy@0.22Gy/s (with Co60 and 445nm)
Ionization Chambers: They fulfill CLIC requirements
    Test response against low energy (< 150 MeV) particles
ACEM (Al Cathode +PMT)
    Simulations estimate sensitivity to beam losses of ~10mA. Consistent with observation
PEP-II (Cherenkov crystal + PMT) and diamond (pCVD)
    Fast time response. They disentangle losses within 150 ns pulse

## Slide 8: BLM investigations: work plan
RF structures as source of BLM background
    Cherenkov fibre + MPPC and pCVD detectors at Xbox 1
    Observation of X-rays and electrons escaping the structure
    Limit to sensitivity of BLM system?
Fiber based system improvements
    Signal deconvolution and position resolution with long pulses
    Extra fiber for H/V disentangling
    Choice of photodetector (optimization for CLIC-like conditions)
    Background subtraction (minimize contributions from fibre section not covering the beam line)
Measurement of beam losses at nominal TBM
    X-talk of beam losses from drive and main beam (and extrapolations at high energy)

## Slide 9: Electro-Optic bunch length monitor
Hardware and software: ready to use.
New 4mm thickness crystal installed instead of 1mm. Signal expected 11 times stronger
New stretcher: laser pulse can be chirped to 8 ps from 110 fs.
Added two detachable mirrors in the laser lab. Switching between single-shot and step scanning is possible now.
Principle of the monitor is tested by real e-beam.

## Slide 10: Electro-Optic bunch length monitor
Beam measurements: synchronisation between e-bunch and laser pulse
First E-O signal measured by a photomultiplier
Next steps: bunch length measurements, resolution improvement
100 ps
A laser pulse (top trace) is visible 420ns after the trigger signal (RF), bottom trace. Evidence for a depolarisation induced by the E-O crystal

## Slide 11: Bunch Length monitor: streak cameras
Delay Loop OTR line upgrade (Jan 2014): from 6 achromats down to 1 (f = 5000 mm).
Synch light
OTR
CLEX line upgrade (planned): installation of elliptical mirror (less chromatic dispersion and aberrations)
New software interface (allows remote operation)

## Slide 12: Spectrometers: segmented dump
Segmented beam dump installed in CTS line (Aug. 2013)
Based on 2011 design installed in TBL (M. Olvegaard).
Performance:
SW: D. Gamba
(zero-length approximation)

## Slide 13: Spectrometers: Cherenkov crystals
Planned installation in Califes line towards future high charge beams:
32 silica crystals
each coupled to a GRIN collimator (dia 1.8 mm, acc, angle 0.15 deg)
Requirement | Min | Typ | Max
Temporal resolution [ps] |  | 100 | 600
Measurement duration [ns] |  | 100 | 150
Repetition rate [Hz] | 0.8 |  | 5
Energy resolution [%] |  | 0.5 | 
Energy range [%] |  | 10 | 
Central beam energy [MeV] | 200 |  | 250
Number of bunches | 1 |  | 200
GEANT simulations by A. Apyan
To sensor
Requirements tuned for CALIFES. BI test of light transmission (light yield, dispersion, coupling etc.)

## Slide 14: Spectrometers: Cherenkov crystals
Light yield (@ 400 nm):
From GEANT simulations: 2.5 x 10-4 ph/e- collected
-5 dB attenuation (insertion and transmission)
-> 7.5 x 10-5 photons/e- at the sensor -> 102-104 ph/bunch
@ 850 nm: 10-103 ph/bunch
Energy 200 MeV
sx = 1 cm, sy =2 mm
sθx = 0 rad, sθy =0 μrad
Dispersion (80 m of SiO2 fibre, 10 nm BW)
DT (@ 600 nm) = 233 ps
DT (@ 850 nm) < 80 ps
Microstructured fibres: -7 dB for “zero” dispersion.

## Slide 15: Coherence length test
Interference: stable phase relation between two sources.
For OTR(ODR), key parameter is the coherence length:
ODR experiment: two screens at distance d -> Interference when d <= Lc
Test of model with (simpler) OTR in Califes: Lc ≅ 2.5 cm @ 200 MeV, l = 500 nm:
Ideal to study the coherent regime
Warstki 1975
SR mask
optics
target

## Slide 16: Summary
Continued involvement of BI team for CLIC studies
Maintenance (screen replacement, alignment, etc. )
Post-2016: possible utilisation of Califes line for BI tests (see presentation of W. Farabolini Wed, 9:00)