## Slide 1: detector R&D challenges for energy frontier physics
Lucie Linssen, CERN

## Slide 2: Outline
Detector requirements at hadron and lepton colliders
Challenges/technologies in vertex/tracking detectors
Challenges/technologies in calorimetry
Possible common development areas
Outlook
In ~20 minutes:
Impossible to pay justice to the broad spectrum of detector R&D;
Impossible, also, to cover pp en e+e- options in a balanced way;
My apologies

## Slide 3: Sources
Material used for this talk was taken from:
ECFA High Luminosity LHC experiments workshop, Aix-les-Bains, 2013
http://indico.cern.ch/conferenceDisplay.py?confId=252045
FHC Hadron Collider physics and experiments, indico
https://indico.cern.ch/categoryDisplay.py?categId=5258
In particular detector talks by D. Fournier and W. Riegler
LCWS13, linear collider workshop, Tokyo, 2013
http://www.icepp.s.u-tokyo.ac.jp/lcws13/
CLIC CDR (vol 2), Physics and Detectors at CLIC,
CERN-2012-003, arXiv:1202.5940
CLIC CDR (vol 3), The CLIC Programme: towards a staged e+e- Linear Collider exploring the Terascale, CERN-2012-005, http://arxiv.org/abs/1209.2543
With apologies for not having asked individual permissions

## Slide 4: hadron vs. lepton colliders
p-p collisions | e+e- collisions
Proton is compound object Initial state not known event-by-event Limits achievable precision | e+/e- are point-like Initial state well defined (√s / polarization) High-precision measurements
Circular colliders feasible | Linear Colliders (avoid synchrotron rad.)
High rates of QCD backgrounds Complex triggering schemes High levels of radiation | Cleaner experimental environment trigger-less readout Low radiation levels
High cross-sections for colored-states | Superior sensitivity for electro-weak states

## Slide 5: CLIC physics aims => detector needs
impact parameter resolution:
e.g. c/b-tagging, Higgs BR
jet energy resolution:
e.g. W/Z/h di-jet mass separation
angular coverage, very forward electron tagging
momentum resolution:
e.g. Smuon endpoint
Higgs recoil mass, Higgs coupling to muons
W-Z
jet reco
smuon
end point
(for high-E jets)
+ requirements from CLIC beam structure and beam-induced background

## Slide 6: CLIC machine environment CLIC machine environment
Drives timing
requirements
for CLIC detector
 | CLIC at 3 TeV
L (cm-2s-1) | 5.9×1034
BX separation | 0.5 ns
#BX / train | 312
Train duration (ns) | 156
Rep. rate | 50 Hz
σx / σy (nm) | ≈ 45 / 1
σz (μm) | 44
Beam related background:
Small beam profile at IP leads very high E-field
  Beamstrahlung
    Pair-background
      High occupancies
    γγ to hadrons
      Energy deposits
very small beam size

## Slide 7: CLIC conditions => impact on detector
CLIC conditions => impact on detector technologies:
High tracker occupancies => need small cell sizes
(beyond what is needed for resolution)
    Small vertex pixels
    Large pixels in intermediate regions
    Limited strip length in tracker
Bkg energy => need high-granularity calorimetry
Bkg suppression => overall need for precise hit timing
    ~10 ns hit time-stamping in tracking
    1 ns accuracy for calorimeter hits
Low duty cycle
    Triggerless readout
    Allows for power pulsing
      => less mass and high precision in tracking
      => high density for calorimetry

## Slide 8: Challenges in LC detector R&D
Combined requirements lead to the following challenges:
Vertex and tracker
Very high granularity
Dense integration of functionalities
Including ~10 ns time-stamping
Super-light materials
Low-power design + power pulsing
Air cooling
Calorimetry
Fine segmentation in R, phi, Z
Time resolution ~1 ns
Ultra – compact active layers
Pushing integration to limits
Power pulsing
ultra – light
ultra – heavy
and compact

## Slide 9: detector requirements HL-LHC
Maintain performance at full sensitivity for discovery and
precision measurements at low pT, under severe pile-up conditions
Pileup
  <PU> ≈ 50 events per crossing by LS2
  <PU> ≈ 60 by LS3
  <PU> up to 140 for lumi-leveling at 5x1034cm-2s-1 at HL-LHC
  (accounting for uncertainty and bunch-to-bunch variations)
Radiation damage
  Performance longevity after 300 fb-1
  Replace elements with limited lifetime
Extend performance to larger η
Profit from detector technology advances
Enhance trigger + DAQ

## Slide 10: comparison CLIC  LHC detector
In a nutshell:
CLIC detector:
High precision:
  Jet energy resolution
    => fine-grained calorimetry
  Momentum resolution
  Impact parameter resolution
Overlapping beam-induced background:
  High background rates, medium energies
  High occupancies
  Cannot use vertex separation
  Need very precise timing (1ns, 10ns)
“No” issue of radiation damage (10-4 LHC)
  Except small forward calorimeters
Beam crossings “sporadic”
No trigger, read-out of full 156 ns train
LHC detector:
Medium-high precision:
  Very precise ECAL (CMS)
  Very precise muon tracking (ATLAS)
Overlapping minimum-bias events:
  High background rates, high energies
  High occupancies
  Can use vertex separation in z
  Need precise time-stamping (25 ns)
Severe challenge of radiation damage
Continuous beam crossings
Trigger has to achieve huge data reduction

## Slide 11: from HL-LHC to FHC
Some very (!) first assessments about extrapolation from LHC to FHC
What are the changes the detectors have to cope with ?
Collisions with larger boost => need more forward coverage
Longer barrel ?
Increased forward η-coverage (jet coverage up to η=6?)
Cope with higher particle/jet energies for interesting physics
Larger tracker (muon system) radius and/or higher B-field
Deeper calorimetry for less leakage (~2 Λi extra)
(Muon energy loss)
Issues of background suppression and radiation levels 14 TeV => 100 TeV:
25% increase of pp cross section
Charged multiplicity will go up by ~50%
Average pt will go up by ~1/3 (from 0.6 GeV to 0.8 GeV)
One can expect factor 2 increase in fluence and dose levels at first pixel layer

## Slide 12: first thoughts on FHC detectors
 a first iteration on dimensions:
To achieve physics performance for high-E objects
Increased forward coverage up to ~η=6
without extrapolation on detector technology/precision capabilities
Room for smart ideas and use of new technologies !
D. Fournier et al.

## Slide 13: CLIC detector concept
ultra low-mass
vertex detector
with 25 μm pixels
all-silicon tracker
fine grained (PFA) calorimetry, 1 + 7.5 Λi,
strong solenoid
4 T - 5 T
return yoke with
Instrumentation
for muon ID
complex forward region with final beam focusing
6.5 m
… in a few words …

## Slide 14: Vertex/tracker technologies
Overall challenges:
More accuracy:
  Small cell sizes
  Low-mass
    => Low power
    => Interconnects: high-density + vertical
Integrated designs, including:
  Low-mass supports
  Cooling
  Power delivery
  Signal transmission
Manufacturability in large areas at low cost
Move away from most expensive elements (e.g. silicon sensors, bump-bonding)
Radiation hardness (for pp case)
A few technology examples on the next slides

## Slide 15: Vertex detector: monolithic CMOS (ILC)
Monolithic sensor, CMOS process
high-resistivity in thin epitaxial layer
Fast signal component (drift)
Electronics integrated in pixel
Rolling shutter read-out (coarse timing)
Analog or digital readout possible
2 types of sensors for inner and outer layers MIMOSA-30 : Dual sided readout out
1 side for spatial resolution (16x16 μm pixel),
1 side for timing (~10μs, 16x64 μm pixel)
MIMOSA-31 : Larger pixel for reduced power consumption (35x35 μm)
Functional ILC prototype 0.6% X0

## Slide 16: Monolithic pixels => ALICE ITS
From ILC designs + RHIC detector to ALICE upgrade for 2018
20 μm pixels
For CLIC and FHC would need increased rate and increased radiation hardness

## Slide 17: Through Silicon Vias (TSV)
Through Silicon Via (TSV)
Vertical electrical connection passing through Si wafer
  eliminates need for wirebonds
  4-side buttable chip/sensor assemblies
  large active surfaces => less material
E.g. Medipix TSV project (ALICE / CLIC / ACEOLE / AIDA) with CEA-Leti
130 nm IBM Medipix(RX) wafers, via-last process
successful completion of first phase: demonstrate feasibility
on-going second phase: demonstrate good yield
Next phase: with Timepix3 and thin sensors
• 240 μm TSV diameter
• wafers thinned to 120 μm
• 5 μm copper layer for TSV
First Medipix3 Image
taken with TSV assembly

## Slide 18: CLIC vertex detector
Vertex + forward tracking
CLIC_ILD
~25×25 μm pixel size => ~2 Giga-pixels
0.2% X0 material per layer <= very thin !
  Very thin materials/sensors
  Low-power design, power pulsing, air cooling
  Aim: 50 mW/cm2
Time stamping 10 ns
Radiation level <1011 neqcm-2year-1 <= 104 lower than LHC

## Slide 19: CLIC vertex detector R&D (1)
CLICpix demonstrator
64×64 pixels, fully functional
65 nm technology
25×25 μm2 pixels
4-bit ToA and ToT info
Data compression
Pulsed power: 50 mW/cm2
Hybrid approach pursued: (<= other options possible)
Thin (~50 μm) silicon sensors
Thinned high-density ASIC
  R&D within Medipix/Timepix effort
Low-mass interconnect
  Micro-bump-bonding (Cu-pillar option)
  Through-Silicon-Vias (R&D with CEA-Leti)
Power pulsing
Air cooling
1.6 mm
64×64 pixels
65 nm ASIC development
ATLAS, CMS, CLICdp => RD53
RMS 4.2% gain variations

## Slide 20: CLIC vertex detector R&D (2)
thin sensors, down to 50 μm
power pulsing, air cooling, light supports
further ongoing R&D activities
Watching other R&D, e.g. micro-channel cooling

## Slide 21: Hybrid detector with HV-CMOS
HV-CMOS MAPS:
180 nm High Voltage process
Vbias ~100 V, 10-20 μm depletion layer
Integrated sensors, fast signal collection
Hybrid option:
Capacitive Coupled Pixel Detector (CCPD)
HV CMOs chip as integrated sensor+ amplifier
Capacitive coupling to readout chip
through layer of glue => no bump bonding
Ongoing R&D with FEI4, Timepix, CLICpix

## Slide 22: HL-LHC tracker upgrades
Macro-pixel / Strip module
“large tracker pixels” also needed for CLIC
With smaller granularity and less mass

## Slide 23: Calorimeter technologies
Overall challenges:
More accuracy:
  Shower reconstruction of particles within the jet
  Need hit-time accuracy
    => ~1 ns for CLIC
    => ~25 ns for LHC (ideally <200 ps for HL-LHC and FHC)
Integrated designs, involving:
  High density => little space for active layers
    => ~2 mm in linear collider ECAL
    => <7 mm in linear collider HCAL
  High channel count
  Low-power design
  Minimal space for cooling
Manufacturability in large areas at low cost
Radiation hardness (for pp case)
A few technology examples in the next slides

## Slide 24: PFA calorimetry at CLIC
ECAL
Si or Scint. (active) + Tungsten (absorber)
cell sizes 13 mm2 or 25 mm2
30 layers in depth
HCAL
Several technology options: scint. + gas
Tungsten (barrel), steel (endcap)
cell sizes 9 cm2 (analog) or 1 cm2 (digital)
60-75 layers in depth (HCAL depth ~7 Λi)
many technologies pursued

## Slide 25: ECAL: Si-W (CALICE)
30 layers in depth
cell size 5.5x5.5mm2
~100 M ECAL channels at ILC (ILD)
~2000 m2 silicon
Successful beam tests
Currently: technological Si-ECAL prototype
Real-scale detector integration model
Full-scale mechanical structure

## Slide 26: ECAL: Scint-ECAL (CALICE)
Row of MPPC (SiPM)
1 cm
absorber
scintillator strips x,y
integrated electronics (SKIROC)
Fully integrated modules,
successful beam tests at DESY
Strips of 45*5*2 mm3, 144 channels/ plane
5 mm wide strips
MPPC
1600 pixels
1×1 mm2
currently exploring
SiPM with more pixels

## Slide 27: A-HCAL (CALICE)
AHCAL 2nd generation fully integrated prototype
undergoing beam tests
3 cm
3x3 cm2 scintillator tiles with SiPMs
Integrated electronics (SPIROC chip)
LED SiPM calibration
Power-pulsing
220 cm long modules
Active layer thickness of 5.4 mm

## Slide 28: digital DHCAL glass RPC’s (CALICE)
W-DHCAL π- at 210 GeV (SPS)
Steel DHCAL
Tungsten DHCAL
500’000 readout channels
54 glass RPC chambers, ~1m2 each
PAD size 1×1 cm2
Digital readout (1 threshold)
Fully integrated electronics
Total 500’000 readout channels
Other large-scale protoypes:
1m3 semi-digital HCAL with glass RPC’s
4 large (~1m2) micromegas readout planes
Ongoing R&D with lower-resistivity glass
for better rate dependence

## Slide 29: CLIC forward calorimetry
2 forward calorimeters: Lumical + Beamcal
Tungsten thickness 1 X0, 40 layers
BeamCal sensors GaAs, 500 mm thick
LumiCal sensors silicon, 320 mm thick
Readout at the outer radius
BeamCal angular coverage 10 - 40 mrad
LumiCal coverage 38 – 110 mrad
doses up to 1 Mgy
neutron fluxes of up to 1014 per year
Very compact !
Active layer gap is 0.8 mm
Moliere radius 11 mm
high-radiation performance
=> collaboration with LHC beam monitors

## Slide 30: HL-LHC CMS end cap calorimetry
Potential replacement of the CMS end-cap calorimetry (EE+HE)
Main motivation:
Radiation resistance
Extension of the η-coverage (for jets from VBF)
Several detector options
They represent a nice illustration of recent technology advances
Shashlik design
  Radiation-hard scintillators (e.g. crystal scintillator for EE)
Dual fiber read-out: scintillation & Cerenkov – following work of DREAM/RD52
  using doped/crystal fibers => allows e/h correction
Fine-grained Particle Flow Calorimeter – following work of CALICE
  active layers GEM/Micromegas or Silicon => detailed jet reconstruction

## Slide 31: Possible common pp/e+e- development areas
Vertex+tracking detector technology
  R&D in integrated hybrid detectors (including developments with HV-CMOS)
  Advanced radiation-hard microelectronics
  Interconnect technologies
  Low-mass engineering
  Low-mass detector cooling (e.g. microcooling options)
  Detector powering
  New low-mass solutions with small strips / large pixels
Fine-grained calorimetry
  Optimisation of jet energy resolution + bkg suppression with PFA
  Compact, large area detectors
Overall detector engineering aspects and large+strong detector magnets
Simulation tools and methods
  Flexible detector geometry descriptions for simulations in detector optimisation phase
  PFA-like event reconstruction tools
  Jet clustering
Non-exhaustive, to be completed

## Slide 32: Summary/outlook
Many exciting detector R&D projects for high-energy e+e- and pp !
Collaborative efforts, creativity, perseverance and new technologies
help to overcome challenges
When comparing e+e- with pp: many challenges are common, others diverge
In most cases, basic technology advances can be carried out in common
Implementations are nearly always application-specific
thank you

## Slide 33
SPARE
SLIDES

## Slide 34: CLIC detector and physics study
Light-weight cooperation structure
No engagements, on best-effort basis
With strong collaborative links to ILC
http://lcd.web.cern.ch/LCD/Home/MoC.html
CLICdp: 21 institutes

## Slide 35: pp table of comparison

## Slide 36: CLIC_ILD and CLIC_SiD
CLIC_ILD
CLIC_SiD
7 m
Two general-purpose CLIC detector concepts
Based on initial ILC concepts (ILD and SiD)
Optimised and adapted to CLIC conditions

## Slide 37: Vertex detectors
Categories of candidate technologies
 | Monolytic CMOS | (3D) integrated | Hybrid pixel
Examples | DEPFET, FPCCD, MAPS, HV-CMOS | SOI MIT-LL, Tezzaron, Ziptronix | CLICpix (TimePix3, Smallpix)
Technology | Specialised HEP processes, r/o and sensors integrated | Customized niche industry Processes with focus on Interconnectivity | Industry standard ASIC processes; HEP-specific high-resistivity sensors
Depletion layer | Partial | Partial or full | Full => large fast signals
Granularity | Down to 5 μm pixel size | Down to 5 μm pixel size | 25 μm pixel size
Thickness | ~50 μm total thickness achievable | ~50 μm total thickness achievable | ~50 μm sensor + ~50 μm r/o
CLIC
ILC

## Slide 38: Vertex detectors
Categories of candidate technologies
 | Monolytic CMOS | (3D) integrated | Hybrid pixel
Examples | DEPFET, FPCCD, MAPS, HV-CMOS | SOI MIT-LL, Tezzaron, Ziptronix | CLICpix (TimePix3, Smallpix)
Technology | Specialised HEP processes, r/o and sensors integrated | Customized niche industry Processes with focus on Interconnectivity | Industry standard ASIC processes; HEP-specific high-resistivity sensors
Depletion layer | Partial | Partial or full | Full => large fast signals
Granularity | Down to 5 μm pixel size | Down to 5 μm pixel size | 25 μm pixel size
Thickness | ~50 μm total thickness achievable | ~50 μm total thickness achievable | ~50 μm sensor + ~50 μm r/o
CLIC
ILC
Smaller pixels
Thinner detectors
High level of pixel functionality
Fast time-stamping

## Slide 39: CLIC vertex R&D: power pulsing

## Slide 40: Linear collider, Si-tracker R&D
1024-channel KPIX chip
Sensor with double metal-layer routing
Connectivity via Kapton pig-tail cable
SiD tracker module
“chip on sensor”
Silicon tracker for the Linear Collider
=> Aim for ~1% X0 per layer
Only limited R&D ongoing
1.3 m

## Slide 41: calorimetry and PFA
Jet energy resolution and background rejection drive the overall detector design
=> => fine-grained calorimetry + Particle Flow Analysis (PFA)
Typical jet composition:
60% charged particles
30% photons
10% neutrons
Always use the best info you have:
60% => tracker
30% => ECAL
10% => HCAL

What is PFA?
Hardware + software !

## Slide 42: calorimetry and PFA
Simulated image
(gives good feeling of the granularity)
FPA-based simulation
(to determine depth of tungsten HCAL)

## Slide 43: time development in hadronic showers
(depends on active material)

## Slide 44: Analog HCAL: scintillator/tungsten
HCAL tests with 10 mm thick Tungsten absorber plates,
Tests in 2010+2011 with scintillator active layers, 3×3 cm2 cells => analog readout
CERN SPS 2011
visible Energy
protons
longitudinal shower profile, pions
good agreement with Geant4

## Slide 45: HCAL: SDHCAL (CALICE)
Steel SDHCAL
500’000 readout channels
~50 glass RPC chambers, 1m2 each
PAD size 1×1 cm2
Semi-digital readout (3 thresholds)
200 ns time-slicing
Fully integrated electronics
Full SDHCAL stack successfully tested:
2012 (2011) CERN - ongoing
  Steel absorber
With power-pulsing !
Separate power-pulsing tests in 3T magnet
=> Stable signal response
Colour for threshold 1, 2, 3

## Slide 46: Calorimetry: Micromegas / GEM
After successful tests with 30×30 cm GEM chambers, development towards of 1m2 plane has started.
50 cm
Micromegas
Two 1 m2 chambers, multi-threshold readout
Successfully tested within SDHCAL stack, 2012
GEM foil
1 m

## Slide 47: background suppression at CLIC
Full event reconstruction + PFA analysis with background overlaid
  => physics objects with precise pT and cluster time information
  Time corrected for shower development and TOF
Then apply cluster-based timing cuts
  Cuts depend on particle-type, pT and detector region
  Allows to protect high-pT physics objects
Use well-adapted jet clustering algorithms
  Making use of LHC experience (FastJet)
+
tCluster
Triggerless readout of full train
 t0 physics event (offline)

## Slide 48: time window / time resolution
Translates in precise timing requirements of the sub-detectors
The event reconstruction software uses:
 t0 physics event (offline)

## Slide 49: PFO-based timing cuts

## Slide 50: Software compensation
High granularity of the calorimeter can be used to distinguish between electromagnetic (dense) and hadronic (less dense) shower components
CALICE
Steel-AHCAL data
 Improved resolution (20% better) and linearity

## Slide 51: details of forward detector region
IP at ~2 m
forward calorimeters
“FCAL”

## Slide 52: CLIC strategy and objectives
2013-18 Development Phase
Develop a Project Plan for a staged implementation in agreement with LHC findings; further technical developments with industry, performance studies for accelerator parts and systems, as well as for detectors.
2018-19 Decisions
On the basis of LHC data and Project Plans (for CLIC and other potential projects), take decisions about next project(s) at the Energy Frontier.
4-5 year Preparation Phase
Finalise implementation parameters, Drive Beam Facility and other system verifications, site authorisation and preparation for industrial procurement.
Prepare detailed Technical Proposals for the detector-systems.
2024-25 Construction Start Ready for full construction and main tunnel excavation.
Construction Phase
Stage 1 construction of CLIC, in parallel with detector construction.
Preparation for implementation of further stages.
Commissioning
Becoming ready for data-taking as the LHC programme reaches completion.