## Slide 1: Review of Master plan: PIC – US1 – US2 list
Meeting for RLIUP preparation - Lucio Rossi

## Slide 2: PIC – 1st Magnets and Cryolink
IR (Interaction Region)
  IT , 150 mm aperture in P1 and P5
  TAS, 60 mm (with Absorbers): fine tuning apert.
  D1, 150 mm
  Correctors for IR (MCBX and HO): 150 mm
  (Arc sextupole at 600 A ??)
  New powering of IR magnets with EPC and DFBs on surface + SC links
  New powering with SC links at P7 (RR) Even more necessary also in view of new access to P7 (in Ext. WS or LS2)

## Slide 3: PIC – 2nd : cryogenics
  New Cryoplant P4 for SCRF (LS2)
  New cryoplants for IRs sized for new MSs including CCCs cryoseparation/connection from Arc This is needed already in PIC to avoid to decrease the margin that we have at nominal and avoiding to degrade the availability.
  How well we know e-cloud today at 25 ns ?

## Slide 4: PIC – 3rd
Collimators reduced impedance
  4 new Mo-GR (2ndary for betatron) in LS2 for test
  18 new Mo-GR (2ndary for betatron)
New collimators in IR (change of aperture)
  12 (MoGR / W)
New collimators for INJ (2, i.e. 6/beam)
New TCLA for Q4/Q5 (4)
DS Suppressor cryocol (11T) inn P2: 2? In LS2
Beam diagnostics
  Cryo BLMs (link to triplet)
  BLM - Rad Hard Electronics (IR3 / IR7 / LSS) ~300 BLMs
  Fast Vacuum Wire Scanners (Initial R&D paid by LIU)
  New BPMs Q1 to Q5 (4 directional couplers & 6 BPMs = 40 total + 10 spares)
  Upgrade Synchrotron Light Monitor + NEW Beam gas vertex detector
TDI and kickers (probably not)

## Slide 5: US1 –
LRBB Compensating Wires
Beam Diagnostics
  Lumi monitor
  Second undulator/beam ??
No change in MS.
SC links for EPC and DFBL of MS on surface (and also 6 kA leads of DFBA). (move in PIC for R2E T.B.V.)
SC RF 800 MHz probably not
Collimators:
  TCAP for warm magnets (4)
  TCP diffusion rate control in P4 (2) (need Halo monitor)
  DS suppressor cryocol (11T) in P7 (4)
Remote handling in part…

## Slide 6: US2 – 1st
MS full remodelling
  New TAN, D2, Q4 , Q5,
  New QRL in MS from new IR plant with full redundancy (also for ATLAS and CMS plant?)
  EPC and DFB removed on surface with Sc links (DFBL and correctors of DFBA)
  New MS in Q6 (4 magnets)
SC RF
  CCC 2 + 2 (In the // plane and in  plane )
  800 MHz (if not US1)
  Collimation
    TCL and TCLD in P1 and P5 (cryocol): 8+8
  Crystal Coll?

## Slide 7: US2 – 2nd
New QPS logics and displaced on surface
New Interlocks
Diagnostics
  Halo monitor and control: e-lens (TBC) or other…
High band feedback system
TDI & dilution Kickers ?
Remote Handling