## Slide 1
Introduction
Radon is a radioactive gas present in virtually every where man is located though at a varying concentration. It is a primordial radionuclide formed naturally by the radioactive decay of radium in uranium decay-series. It is found in soil, rock, water, air and in the finished products of parent materials. The health concern associated with exposure to radon through inhalation is an increased risk of developing lung cancer. When inhaled, it attach itself to the surface of the respiratory tract and create a pathway for radiation exposure in the lung. These accumulate over time where they gradually cause damage to the cell that lines the lung and subsequently lung cancer. Radon have been classified along with asbestos and tobacco smoke as a Group 1 carcinogen (Nsiah-Akoto et al., 2011), due to the correlation that exist between exposure to this radioactive gas and lung cancer. This necessitates this research.
Materials and methods
This study was conducted using solid state nuclear track detector (SSNTD) CR-39. The dosimeters were distributed randomly and hung on the walls of the laboratories at a height of 1.5m above the floor as representative of breath height inside the rooms. After the exposure, the detectors were etched in 6 N NaOH at 80 0C for 4 h.
Alpha-tracks caused by radon were counted under an optical microscope connected to a micro-camera which was connected to a personal computer. The observed track densities (TD) were converted into radon concentrations (Rn) in Bq m-3 using the calibration factor (CF) supplied by the manufacturer divided by the exposure time ( ) according to the relation,
1
Fig 1: (a) Alpha track detector dosimeter CR-3 (b) Water bath used for etching
Results
Measurement of Radon Concentration
The concentration of radon measured ranged between 461.05 and 633.95 Bq m-3 with a mean value of 473.86 Bq m-3. The mean value is within the recommended ICRP level of 200 - 600 Bq m-3 (ICRP, 1993) but higher than WHO recommendation value of 200 Bq m-3.
Estimation of Annual Effective Dose
The annual effective dose (E) to the occupants of these laboratories due to radon exposure was estimated using the relation
E = ARn x F x O x T x DCF 2 (UNSCEAR 2000)
Where ARn is the radon concentration (Bq m-3), F is the equilibrum equivalent concentration (EEC) factor for indoor exposure (0.4), O is the occupancy factor (0.2), T is the number of hours in a year (8760 h).
The annual effective dose was estimated to vary between 2.06 to 3.99 mSv y-1 with a mean value of 2.99 mSv y-1. These values are within the ICRP recommendation limit of 3-10 mSv y-1 (ICRP, 1993). However, this value is still high compared to that observed in several other countries as shown in Table 1.
Table 1: Comparison of radon concentration in different countries
Some Factors Affecting Variation Of Radon Concentration
  Effects of ventilation
  Effects of floor height
  Age of a building
  Location of a building
  Life style of residential dwellers
  Building materials
  Seasonal variation
  http://www.epa.gov/radiation/radionuclides/radon.html http://www.physics.isu.edu/radinf/radon.html
Conclusions
A survey to determine the indoor radon concentration in selected laboratories of Covenant university Ota was performed. The mean radon concentration was 473.86 Bq m-3 which translated to annual effective mean dose of 2.99 mSv y-1. This value is within the ICRP recommendation limit but greater than that recommended by WHO.
References
Obed, R.I., Lateef, H.T., Ademola, A.K., 2010. Indoor radon survey in a University campus of Nigeria. J.Med. Phys. 35, 242-246.
Obed, R.I., Ademola, A.K., Ogundare, F.O., 2011. Radon measurements by nuclear track detectors in dwellings in Oke-Ogun area, South-western, Nigeria. Radiat. Prot. Dosim. doi:10.1093/rpd/ncr196.
Nsiah-Akoto I., Fletcher J.J., Oppon O.C., Andam A.B., 2011. Indoor Radon Levels and the Associated Effective Dose Rate Determination at Dome in the Greater Accra Region of Ghana. Research Journal of Environmental and Earth Sciences. 3(2): 124-130, 2011.
Pinel J., Fearn T., Darby S.C., Miles J.C.H.,(2011). Seasonal Correction Factors for Indoor Radon Measurements in the United Kingdom. Radiation Protection Dosimetry vol. 58, Issue 2, pp. 127-132.
United Nations Scientific Committee on the Effects of Atomic Radiation, 2006. Effects of Ionizing Radiation: UNSCEAR 2006 Report. In: Report to the General Assembly Scientific Annexes A and B: Report to the General Assembly Scientific Annexes A and B V. 1, vol. 1. United Nations, NewYork.
Acknowledgments
ICTP, Italy.
Covenant University Ota
ACHUKA J.A. AND USIKALU M.R.
DEPARTMENT OF PHYSICS COVENANT UNIVERSITY OTA, OGUN STATE, NIGERIA
PRESENTED @
3RD BIENNIEL AFRICAN SCHOOL OF FUNDAMENTAL PHYSICS AND ITS APPLICATION (ASP) 2014, DAKAR, SENEGAL
RADON MEASUREMENT IN SELECTED LABORATORIES OF COVENANT UNIVERSITY OTA, SOUTHWESTERN NIGERIA
Table 1: Comparison of radon concentration in different countries |  | 
Countries | Radon concentration (Bq m-3) | References
USA | 46 | EC, 1995
Sweden | 108 | EC, 1995
Finland | 123 | EC, 1995
Japan | 29 | EC, 1995
Spain | 86 | EC, 1995
Portugal | 81 | EC, 1995
Greece | 92 | EC, 1995
Australia | 11 | EC, 1995
Czechoslovakia | 140 | EC, 1995
Ghana (Dome) | 467 | Nsiah-Akoto et al., 2011
Nigeria (Ota) | 474 | This study
Table 2: Contributions from sources of radon in houses | 
Source | Estimated contribution (Bq)
Soil gas transport (b) | 0 – 6.0
Release from potable H20 | 0 – 2.0
Soil gas diffusion | 0.1 - 0.2
Diffusion from building materials | 0.01 – 1.0