## Slide 1
Apollonio
andrea.apollonio@cern.ch
Acknowledgements: L. Ponce, B. Todd,
J. Wenninger, D. Wollmann, P. Zeiler, M. Zerlauth
Availability predictions for post LS1 operation and HL-LHC

## Slide 2: Motivation: Faults and Lost Physics
B. Todd
Need for a more effective way of assessing the impact of different ‘fault types’

## Slide 3: Outline
Monte Carlo model for Availability predictions
Predictions for Post-LS1 Operation
Predictions for HL-LHC
Potential of Petri-Nets for Availability predictions
Conclusions

## Slide 4: Outline
Monte Carlo model for Availability predictions
Predictions for Post-LS1 Operation
Predictions for HL-LHC
Potential of Petri-Nets for Availability predictions
Conclusions

## Slide 5: Baseline for Performance Evaluation
Sequence of LHC Operational states:
Turnaround
Stable Beams
Machine Fault
2012 Observations (average values):
  Turnaround: 5.5 h
  Fault time per fill: 4.8 h
  Stable Beams: 6.1 h
The model reproduces a realistic timeline of 1 year of LHC OP:
  Assumes 2012 parameters as reference
  Includes intensity Ramp-up
  Allows for sensitivity analyses to relevant parameters
Monte Carlo model for performance evaluation (MATLAB):
  Generation of random numbers based on 2012 distributions

## Slide 6: Availability Model: Timeline
L(t)
t
~ 5.5 h
Fault Time
Turn
around Time
Stable
Beams Time
Peak Lumi
Lumi
Lifetime
End
of p-p
Operation
FAULT

## Slide 7: Availability Model: Input Parameters
Fault Time distributions  from eLogbook
Turnaround Time  only average value can be deduced from eLogbook and PM
Stable Beams Time distributions  from PM
Peak Luminosity distributions  from TIMBER (exponential fit)
Luminosity Lifetime distributions  from TIMBER
Machine Failure Rate: # fills with failures/ total # physics fills  deduced from PM

## Slide 8: Fault time distributions in 2012
4 lognormal distributions were adopted to model the failures in 2012:
“Shaping” these distributions allows making predictions for possible future operational scenarios

## Slide 9: Model Validation: 2012 Operation
AVG SIMULATED:
  23.00 [fb-1]
2012 MEASURED:
  23.27 [fb-1]
REL ERROR:
1.14%
Simulated years of operation: 1000, ~1.5 min Simulation Time
The model was validated for 2012 operation (verifying Integrated Lumi, SB time, Fault Time, Turnaround time, number of fills,…):

## Slide 10: Model Extension: Levelling
L(t)
t
The model was then extended to include levelling:
Assumption: exponential decay of instantaneous luminosity
Example for Full HL parameters
Lumi Lifetime depends on many factors, extrapolation from cross-section at 7 TeV (85 mb)
~6.5 h

## Slide 11: Model Extension: Levelling
L(t)
t
~ 6.2 h
Peak Lumi
Lumi
Lifetime
End
of p-p
Operation

## Slide 12: Outline
Monte Carlo model for Availability predictions
Predictions for Post-LS1 Operation
Predictions for HL-LHC
Potential of Petri-Nets for Availability predictions
Conclusions

## Slide 13: Assumptions for post-LS1 LHC Operation
160 days of operation
25 ns operation with and without Linac4
(BCMS and Standard + Linac4)
4.5 h average luminosity lifetime (~10 h in 2012)
6.2 h average turnaround time (5.5 h in 2012)
4 logn distributions for the fault time + future scenarios
2 stable beams time distributions:
  END OF FILL: gauss(mean 9.6 h)
  EMERGENCY DUMPS: exp(mean 4.6 h)

## Slide 14: Post-LS1 Availability: Possible Scenarios
Possible future scenarios:
Extension of 2012 fault distributions to Post-LS1 operation
Impact of UFOs at 6.5/7 TeV
Impact of increased BLM thresholds and Beam-Induced Quenches (BIQ)
Impact of LS1 mitigations wrt SEUs
Possible impact of increased energy on SEUs
Combination of 3 and 4: Impact of increased BLM thresholds and Beam-Induced Quenches (BIQ)+ SEUs mitigations

## Slide 15: Post LS1 LHC Operation
Courtesy J. Wenninger

## Slide 16: Post-LS1 LHC: some results…
As 2012,
turnaround time 5.5  6.2h
  Avg: 42.5 [fb-1] (reference)
SEU mitigation* (50  20)
  Avg: 43.3 [fb-1] (+1.8%)
* Only SEU not requiring an intervention
100 UFO dumps due to 7TeV
  Avg: 38.6 [fb-1] (-10%)

## Slide 17: Post LS1 LHC Operation and Availability
Failure Scenario/ Mitigation | Assumption | Simulated impact on Integrated Luminosity (BCMS) | Simulated impact on Integrated Luminosity (LINAC4)
1. 2012 Fault distributions | - | 42.5 [fb-1] (reference) | 42.7 [fb-1] (reference)
2. UFOs (6.5/7TeV) | 100 UFO dumps | 38.6 [fb-1] (-10 %) | 39.0 [fb-1] (-10 %)
3. UFOs + BIQ | Factor 3 higher BLM thresholds, 33 UFOs, 3 BIQ | 41.4 [fb-1] (-2.6 %) | 41.5 [fb-1] (-2.8 %)
4. SEU mitigations | 20 SEU dumps | 43.3 [fb-1] (+1.8 %) | 43.6 [fb-1] (+2.1 %)
5. SEU increase due to higher energy | 60 SEU dumps (+50% wrt 2012) | 41.7 [fb-1] (-1.8 %) | 41.9 [fb-1] (-1.8 %)
6. Combined impact of scenarios 3 and 4 | - | 41.8 [fb-1] (-1.6 %) | 42.1 [fb-1] (-1.4 %)
Summary of fault scenarios and impacts:

## Slide 18: BCMS Predictions: Sensitivity Analysis
Impact of Average Fault Time:
-75%
-50%
-25%
+25%
2012
+75%
+50%
+100%

## Slide 19: Outline
Monte Carlo model for Availability predictions
Predictions for Post-LS1 Operation
Predictions for HL-LHC
Potential of Petri-Nets for Availability predictions
Conclusions

## Slide 20: Assumptions for HL-LHC Operation
160 days of operation
2.19*10^35 [cm-2s-1] virtual peak luminosity (Full HL)
Levelling at 5*10^34 [cm-2s-1]
4.5 h average luminosity lifetime
6.2 h average turnaround time
4 logn distributions for the fault time + scenarios
2 stable beams time distributions
  END OF FILL: gauss(mean 9.6 h)
  EMERGENCY DUMPS: exp(mean 4.6 h)
Intensity ramp-up not included

## Slide 21: HL-LHC: some results…
As 2012,
turnaround time 5.5  6.2h
  Avg: 213 [fb-1] (reference)
100 UFO dumps due to 7TeV
  Avg: 179 [fb-1] (-15%)
SEU mitigation (50  20)
  Avg: 220.5 [fb-1] (+3%)
* Only SEU not requiring an intervention

## Slide 22: High-Luminosity LHC and Availability
Summary of fault scenarios and impacts:
Failure Scenario/ Mitigation | Assumption | Simulated impact on Integrated Luminosity
1. 2012 Fault distributions | - | 213 [fb-1] (reference)
2. UFOs (6.5/7TeV) | 100 UFO dumps | 179.5 [fb-1] (-15%)
3. UFOs + BIQ | Factor 3 higher BLM thresholds, 33 UFOs, 3 BIQ | 203 [fb-1] (-5%)
4. SEU mitigations | 20 SEU dumps | 220.5 [fb-1] (+3%)
5. SEU increase due to higher energy | 60 SEU dumps (+50% wrt 2012) | 206 [fb-1] (-3%)
6. Combined impact of scenarios 3 and 4 | - | 208.5 [fb-1] (-2%)
HL-LHC results are more sensitive to the selected fault scenarios given the longer levelling time
Optimization of SB time can play a significant role for luminosity production

## Slide 23: HL-LHC Predictions: Sensitivity Analysis
Impact of Average Fault Time:
-75%
-50%
-25%
+25%
2012
+75%
+50%
+100%

## Slide 24: Outline
Monte Carlo model for Availability predictions
Predictions for Post-LS1 Operation
Predictions for HL-LHC
Potential of Petri-Nets for Availability predictions
Conclusions

## Slide 25: Preliminary Petri Net Model of LHC Operation*
Beam from SPS
Random Peak Lumi + Lumi Lifetime
Random Failures
Integrated Lumi Counter
Radom Time for Fault Diagnostics
Radom Fault Time
* Using CPN Tools

## Slide 26: Preliminary Petri Nets Model of LHC Operation*
Random Peak Lumi
+ Lumi Lifetime
Beam from SPS
* Using CPN Tools

## Slide 27: Outline
Monte Carlo model for Availability predictions
Predictions for Post-LS1 Operation
Predictions for HL-LHC
Potential of Petri-Nets for Availability predictions
Conclusions

## Slide 28: Conclusions and Outlook
Increasing machine availability towards better LHC performance will be one of the big challenges of the Post-LS1 era
A model to quantify the potential gain/loss of integrated luminosity in different operational scenarios was developed in MATLAB
Predictions could be improved with more reliable data sources, allowing for more accurate data correlation
UFOs have the potential to be one of the main limitations for future LHC operation
Petri-Nets could be exploited for Availability predictions and further modelling

## Slide 29
THANKS A LOT FOR YOUR ATTENTION!

## Slide 30: Peak Lumi distributions in 2012

## Slide 31: High-Luminosity LHC and Availability
Impact of Turnaround Time, assuming 2012 fault distributions:

## Slide 32: 2012 Peak Luminosity
Unif Distribution:
a = 3000 [Hz/cm2]
b = 5000 [Hz/cm2]
Norm Distribution:
μ = 6285 [Hz/cm2]
σ = 569
“Low” Peak Lumi
“High” Peak Lumi

## Slide 33: 2012 Luminosity Lifetime (Low)
Norm Distribution:
μ = 10.5 [h]
σ = 2.5
“Low” Peak Lumi
“High” Peak Lumi

## Slide 34: 2012 Luminosity Lifetime (High)
Norm Distribution:
μ = 10.05 [h]
σ = 3.2
“Low” Peak Lumi
“High” Peak Lumi

## Slide 35: 2012 SB Distribution
Exp Distribution:
μ = 6.0809 [h]