## Slide 2: Outline
1. LHC Physics in Context of Availability
Key Performance Indicators
Availability vs Operation
2. Tracking Availability: 2010-2012
2012 experience, limitations
System survey results
3. Tracking Availability: post LS1
LHC System Availability Tracker (LSAT) Requirements
Implementation
4. The Cardiogram: August 2012
Reverse engineering
5. The future
Milestones and Timeline
Integration with Maintenance Management

## Slide 3
Context of Availability

## Slide 4: Context of Availability
integrated luminosity is a function of…
time colliding physics beams
turnaround between successive physics beams
time to clear faults
physics performance during colliding beams
machine understanding
& operator skill
availability!
These are not independent variables

## Slide 5: Context of Availability
time colliding physics beams
turnaround between successive physics beams
time to clear faults
physics performance during colliding beams
availability!
the Availability Working Group has been concentrating on understanding these relationships
Studied 2010-2012 availability
Studied protection system dependability
Analysed methods currently employed
Proposes a future direction

## Slide 6
Fault Tracking: 2010 - 2012

## Slide 7: The Survey
Q1: How systems find out that something is faulty?
Q2: How do systems keep track of what is faulty and needs repairing?
Q3: root cause / failure mode of every fault / event identified?
Three key questions:

## Slide 8: The Survey – Typical Results
… there are more rows

## Slide 9: Fault / Event Information Flow
for each
equipment group

## Slide 10: Dump Cause – 2012
[5]
11
26
74
228
246
585 dumps

## Slide 11
Fault Tracking: post LS1

## Slide 12: Fault / Event Information Flow

## Slide 13: Fault / Event Information Flow

## Slide 14: Fault / Event Information Flow

## Slide 15: Fault / Event Information Flow
2. Information Interpretation
1. Common Data Format
3. Viewing and Reporting

## Slide 16
1. Common Data Format
a common set of fields to describe faults / events:

## Slide 17
2. Information Interpretation
Interpreters to convert information from equipment logs to the common format
see how we go…
eLogbook – change is minimal
Small – moved by hand
Logged Variables– use them as a starting point
JIRA, Power Converter Logs
to be investigated…

## Slide 18
3. Viewing and Reporting
Outstanding Faults List
All faults which are active at a requested moment in time
Availability Tracking
system / sub-system availability shown across a defined time frame
Availability Matrices
For systems completing “failure-mode” the availability matrices drawn on the fly
Cardiogram
The most interesting view…

## Slide 19
Cardiogram

## Slide 20: Cardiogram – August 2012
energy
beam-1 intensity
beam-2 intensity
stable beams = producing physics
post-mortem = beam dump
faults recorded

## Slide 21: Cardiogram – August 2012
energy
beam-1 intensity
beam-2 intensity
stable beams = producing physics
post-mortem = beam dump
faults recorded

## Slide 22: Cardiogram – August 2012
The whole raw cardiogram for August 2012 is in the indico folder with this presentation
A modified cardiogram showing some consolidated information is also found there

## Slide 23
Information to be Displayed in the Fault Area:

## Slide 24
Milestones and Timeline

## Slide 25: Q. What will a “Maintenance Tracker” cover?
585 dumps
A. machine events that need maintenance / repair to continue operation…
≈50%

## Slide 26: Q. What will a “Maintenance Tracker” miss?
A. machine events that do not need maintenance / repair to continue operation…
Operator = End of Fill
Feedback events
Beam Loss / UFO events
Pre-cycles
Transfer Line Steering
Waiting for handshakes
The maintenance / asset management tool alone will not provide the information needed.

## Slide 27: Milestones and Timeline
2014:
eLogbook – additional fields
Interpreter feasibility and first implementation
Viewer – first implementation
Reverse engineering more data from 2012…
v1 Prototype ready for LHC restart
interaction with MMP to identify common areas

## Slide 28: Milestones and Timeline
2015:
Every week – manual corroboration of data = operators + experts
Every Technical Stop – production of availability snapshot
…Evian 2015 – review of whole year’s data
Online tweaking of v1 prototype = v2… v3…
Determine “usefulness”

## Slide 29: Milestones and Timeline
Longer term:
Regular interaction with MMP whilst we learn
LHC System Availability Tracker

## Slide 30: Conclusions
to optimise time in physics and faults we must track faults coherently
inverse femtobarn is a performance metric of LHC…
… a function of time in physics, faults, beam performance and turnaround time
& machine understanding
LHC System Availability Tracker based on the eLogbook… developed in 2014
prototype with manual interaction… used in 2015
If LSAT worthwhile integrate into other asset / maintenance tracker tools… 2015+
AWG aims at providing a tool, gathering and generating required information for availability tracking. Information gathered will be used to generate reports and views to assess LHC availability in the post LS1 era.
AWG will collaborate with MMP on defining and exploiting tools and needs required for effective tracking of availability and measuring effects on physics performance of the LHC.