## Slide 1: The past and future RF performance in LHC
Pierre Maesen BE/RF
On behalf of the LHC RF team

## Slide 2: Content
- LHC RF System
- RF performance up to 2012
  Tools used for faults tracking
LS1 ACS upgrades at PT4
LS1 ADT upgrades at PT4
- Prospects for RUN 2
  Tools that could help

## Slide 3
16 SC Cavities in 4 Modules
16 Klystrons
300 kW @ 400 MHz
1000 Interlocks
All connected to the beam dump
8 Transverse Dampers
32 Tetrodes
- LHC RF System

## Slide 4
UX45 RA43-47
Notes: Talk about modules = RF unit

## Slide 5
Wattcher LO
Wattcher HI (fast)
[SIS] (slow)
Load
Circulator
Klystron
Cavity
Main Power Coupler
(ceramic window)
Arc
detector
HOM coupler
MC Vacuum
Beam
HOM Power [SIS]
HOM Temperature [SIS]
RF Switch
Veto
Helium pressure (cavity quench)
Helium level (Cryo OK)
RF power path & critical interlocks
Generates RF Veto and
Beam Interlock since 2011
[SIS]: Software interlock
Also connected to BIS:
RF frequency
Cavity vector sum (total voltage)
Faraday Cage UPS fail
A. Butterworth

## Slide 6
HV interlocks
Brings down complete module (4 Klystrons)
RF interlocks (Trips 1 Klystron)
ACS RF & HV interlock chains
L. Arnaudon

## Slide 7: - RF performance up to 2012
Chart: Week number
| 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48
 | 1 | 1 | 0 | 8 | 1 | 0 | 2 | 0 | 0 | 0 | 1 | 3 | 1 | 2 | 1 | 0 | 0 | 0 | 3 | 3 | 2 | 1 | 1 | 1 | 1 | 0 | 2 | 2 | 4 | 1 | 0 | 1
2011:
78 faults in total
11% of all beam dumps
2 Faults per week during physics
2012: (Fault analysis: D. Glenat)
43 faults in total
x% of all beam dumps
1.3 Faults per week during physics
Some difficult weeks/periods:
  2 x Crowbars
  Defective HV cable
  RF driver
Fault statistics 2012
crowbar
crowbar
RF driver
RF driver
HV cable

## Slide 8
Most critical equipment : the current Thyratron crowbar suffers from spurious trips
Solid-state replacement developed using Thyristor-Stack: very promising and showing comparable performance (See: Paper at IPAC12 by G. Ravida)
1 unit installed since September 2012
  No spurious trip observed
  Few trips due to klystron arcs
Thyratron replacement
Notes: Thyratron are sensitive to heater and reservoir current

## Slide 9
Second wondering
faulty : Filament
current interlocks
2 culprits identified:
  Several klystron HV connectors
    Spring contacts degraded (black deposit)
    Contacts needed to be cleaned repeatedly
    New connector design without springs,
    with special Multi-Contact installed
  Cable head defective welding…LS1
Klystron filament “I fil too low” faults

## Slide 10: - Tools used for faults tracking
Equipment’s build with manual written logbook … scanned -> EDMS id 879141, 879146, 879150, 879151, 1082985
LHC commissioning with MS OneNote logbook
HMI Labview from FESA classes
LHC RUN 1 followed with OP and RF logbooks
  Rapid overview & general cmd on Delphine’s RF page
Faults tracking with LASER, post mortem TIMBER and RF specialist buffers in VME boards
PVSS for Cryo and Vacuum in monitor mode
Manual extraction and corrections for statistics

## Slide 11
C3.B2 quench on HOM

## Slide 12
ACS modules Vacuum during 2008 incident

## Slide 13
He liquid levels during C3.B2 quenches

## Slide 14: - LS1 ACS upgrades at PT4
New induction welding campaign on HV connectors
      Before After
8 last new klystrons/16 for nominal performance
  58 kV/9.5 A => 300 kW CW RF
4/4 new HV solid state crowbars
Maintenance campaign of ageing tetrode in modulator
New Air cooling of HV Bunkers
O. Brunner

## Slide 15: - LS1 ACS upgrades at PT4 cont.
LHC ACS module M1.B2 to be replaced
  To overcome C3.B2 limitation at 1.3 MV acc. field
New version of PLC software UNITY V8
New version of FESA ?
Replacement of all Windows XP consoles
R2E
  ACS module Cryo control racks will be displaced
  UX451 PAD moved further away from tunnel
    Access with LHC-TNL, no LHC-RF list anymore

## Slide 16
ADT vertical and horizontal kickers
Tetrode amplifiers
Old Flow meters

## Slide 17: - LS1 ADT upgrades at PT4
New amplifier-kicker clamp
Improvement of the HVPS by adding HV switches allowing a remote off line of a faulty amplifier
New HVPS cables to avoid cable burning
Replacement of power attenuator with power load
New flow-meters in replacement to the old Eletta from LEP time
Adding redundancy to the problematic kicker vacuum interlock
E. Montesinos

## Slide 18: - LS1 ADT Feedback upgrade
Large coax recabling campaign
Major upgrade of electronics to house all new features accumulated since 2009
Double the number of pickups, new upgraded beam position modules
Multiple output DACs:
  Independent treatment of different bunch groups (high/low gain, high/low bandwidth)
  Independent cleaning performance
D. Valuch

## Slide 19: - Prospects for RUN 2
Restarting injectors & LHC … Delicate
  Safety for people and equipment
Scrubbing 25ns… No problem
  Scrubbing 5ns TBC see LBOC meetings
25 ns operation with nominal current…
  Promising, see presentations in Evian and Chamonix by P. Baudrenghien et al.
Klystrons at 58kV/9A instead of 50kV/8A
More flexibility in pickups and ADT functionality
Plenty of hope 

## Slide 20: - Prospects for RUN 2
Equipment ageing ?
  Inspection during technical stops…
  ACS tuning cables inside insulation vacuum etc.
  New development to replace klystron modulator tetrode
  Dispersion of klystron age
Component obsolescence FPGA, DSP !
  So far enough VME spare boards…
Manpower for piquet’s ?
  Young students are friendly but CERN needs continuity and experienced staff !

## Slide 21: - Tools that could help
FESA V? & TIMBER mandatory ready in time !
Remote monitoring from home very useful
  Remote control with piquet role ( gains time and avoids displacements )
  Down to expert PLC tools on TN via UNITY
More user friendly configuration of LASER ?
  Better “hierarchisation” of alarms, faults...
Automatic event logging in the RF logbook
  But editable for correction or addition of signals charts & comments => easier statistics
Replacement of Labview by Inspector BE/OP ?
  Parallel development during RUN 2

## Slide 22
New Inspector display
Example for Linac 4

## Slide 23
Thank you for your attention
Questions ?

## Slide 24: RF interlocks
Higher order mode power
Main coupler vacuum
Cryo + Vacuum
Access system
Radiation
Reflected power
Arc detectors

## Slide 25: HV interlocks
Klystron faults
HV bunker faults
External faults

## Slide 26: Interlocks connected to BIS (UX45)
RF Veto Module 1
RF Veto Module 2
Arc detector on Main Coupler
Fast Reflected Power (Wattcher HI)
Sum of RF Veto interlocks
He pressure (cavity quench)
Faraday cage power status
RF frequency interlock

## Slide 27: Solid state crowbars (“fast protection system”)
Very simple circuit
No cooling (±10W)
90 litters oil volume
Sophisticate circuit
Water/oil Cooling
350 litters oil volume
Limited lifetime
Gianfranco Ravida/S. Menoni
Solid State device has better performances than the thyratron
Validated during 2012 running period
In series production

## Slide 28: Repair of the high voltage connectors
Zone with welding defect
P. Martinez-Yanez/G. Ravida
Klystron filament glitches responsible for frequent RF trips during operation
Procedure validated to re-weld the connectors without damaging the insulation material
Campaign in LHC will soon be launched

## Slide 29: Digital measurement system for the klystron modulators
Zone with welding defect
DCCT’s and tetrodes used in LHC are no longer produced by industry
Development of a FPGA based electronic located in HV modulator
  -> the crowbar survival challenge!
Prototype built: looks very promising
Evaluation tests for tetrode replacement
Anders Mikkelsen/D. Valuch/G. Ravida/S. Menoni