## Slide 1: Collinear resonant ionization laser spectroscopy of rare francium isotopes
IPN Orsay, IKS Leuven, University of Manchester, New York University and University of Birmingham

## Slide 2: The first dedicated ISCOOL experiment
This proposal aims at pushing the limits of laser spectroscopy sensitivity.
To measure for the first time cases with yields of only 1 atom per second.
ISCOOL is essential to realize this project, by providing bunched ions beams.

## Slide 3: Outline of proposal
New innovation in laser spectroscopy.
Ultra-high sensitivity and efficiency combined with high resolution.
New semi permanent beam-line.
New pulsed laser laboratory.
New versatile method of producing clean beams for decay spectroscopy.
Capability to study single atom yields even with large isobaric contamination

## Slide 4: Physics Motivation:Francium
Initial case which forms part of larger study of this region of the nuclear chart.
Deformed (oblate) intruder π(s1/2) state believed to be ground state of 199Fr, and isomeric state in 201,203Fr.
218,219Fr border of region of reflection asymmetry, yielding important information on the transition from spherical to octupole-quadrupole deformed nuclear structure.

## Slide 5: Intruder levels and large deformation in neutron deficient francium
1/2+
7/2-
9/2-
1/2+
7/2-
9/2-
201Fr
203Fr
π(1/2+) proton intruder state becomes the ground state in 195At and 185Bi
Systematic reduction in energy of the
Deformed π(1/2+) in isotopes in
This region of the chart
Suggests that 199Fr has
I=1/2+ ground state spin
with an associated large
oblate deformation.
The isomer shifts of 201,203Fr
And their magnetic moments
will provide important
information to better
understand the evolution of
nuclear structure in this region.

## Slide 6: Border of the region of reflection asymmetry
Region characterised by reversal in odd-even staggering, which is attributed to presence of octupole-quadrupole deformation.
Also characterised in the interleaving alternating band structure connected by enhance E1 transitions

## Slide 7: Previous and proposed isotopes
201
202
203
204
205
206
207
208
209
210
211
212
213
214
intruder 1/2+
isomer
218
219
220
221
222
223
224
225
226
227
228
229
230
Region of reflection asymmetry
Previous measurements
106
107
105
106
102
1
103
104
103
103
104

## Slide 8: Beyond francium
Surrounding isotones Ra and Rn to complete the description of the π(1/2)+ level and border of region of reflection asymmetry.
Bi isotope chain out to 218Bi (yield of 103) and possibly even further from N=126.
Quadrupole moments and spin assignment in neutron deficient Po, Bi and Pb isotopes. Providing a full description of the shape evolution in this region.
Shape transitions beyond N=126

## Slide 9: Nuclear Information from laser spectroscopy
Coupling of nuclear and atomic total angular momentum vectors giving rise to a hyperfine splitting of the atomic transitions.
It is possible to extract nuclear observables from these measurements without introducing nuclear model dependence.
Unambiguous assignment of the nuclear spin, nuclear moments and changes in charge radius across an isotope chain.
High resolution laser spectroscopy techniques are required to resolve the full structure.

## Slide 10: CRIS beam line and method
Combining high resolution
nature of collinear beams
method with high sensitivity
of in-source spectroscopy.
Allowing extraction of
B factors and quadrupole
moments.
Relative Frequency (MHz)
68Cu

## Slide 11: Collinear resonant ionization laser spectroscopy (CRIS)
RIS performed on a fast atomic bunched beam.
Pulsed Amplified CW laser has a resolution which is Fourier limited to π/t (dye).
Background events are due to non-resonant collisonal ionization, which is directly related to the vacuum
Very high total experimental efficiency
  Neutralization 50-90%
  Ionization efficiency 50-100% (no HFS)
  Detection efficiency almost 100%
  Transport through ISCOOL 70-80%
  Transport to experiment 80-90%
Up to 50% efficiency possible
1:30 From Jyvaskyla off-line tests
( K. Flanagan, PhD)

## Slide 12: Previous CRIS of Yb at ISOLDE
Charge exchange efficiency into meta stable states
Below saturation on second step
CW beam and duty cycle losses due to lasers
Total efficiency
1:100 000
Previous work limited to yields
greater than 107 ions/μC
Ch. Schulz et al., J. Phys. B, 24 (1991) 4831

## Slide 13: Limiting factors:Efficiency and isobaric contamination
From the ISCOOL tests in November a limit of 108pps were trapped and measured on an MCP.
Conservative efficiency of 1:30 (number from Jyvaskyla work) and a pressure of 10-9 mbar and a high isobaric contamination of 107 (expect much lower).
Background suppression:
Pressure 10-9 mbar = 1:200 000
Detection of secondary electrons by MCP
Alpha decay detection allows removal of all isobaric contamination (50-100cts/s)
Limited to > 100pps
Limited >5pps
With 50% efficiency and signal limited noise regime = 0.3pps
This underlines the importance of improving
beam purity for future HIE-ISOLDE and ISCOOL work

## Slide 14: Logistical planning 2008-2009
Finalize technical design and commence construction of beam line components March/April 2008
Purchasing and shipping of equipment to CERN Summer 2008
Installation of equipment winter shutdown 2008
Initial off-line optimization March/April 2009

## Slide 15: Break down of beam time request
Year | Run | Isotopes | Number of shifts | Preparation requirements
2009 | 1 | 206-203 | 11 | 1 shift for Tl/Fr optimization
2010 | 2 | 218,219 | 9 | 
2010 | 3 | 202,201 | 12 | 
Total of 33 shifts requested over 2
year period.
Run 1. will work with ground state
yields between 107-105pps
Thank you for your attention

## Slide 16: Available resources
Manchester: 2 Academics, 1 postdoc, 2 PhD students, 2 Technical staff.
Leuven: 1 Academic, 2 postdocs, 2 PhD students.
Orsay:2 Academic, 1 postdoc, 1 PhD student.
Birmingham: 1 Academic, 1 postdoc, 2 PhD students.
Total of 20 people

## Slide 17: Technical Drawings
Preliminary

## Slide 20: Signal to noise: Limits of detection
Signal Noise Ratio (SNR) > 5 for total confidence in laser spectroscopy.
SNR =(S/√(S+B))*√t where S is the signal rate, B is the background rate and t is the time in seconds
By eliminating the background the SNR reduces to √(S*t) which presents the ultimate limit on the time it takes to collect data.