## Slide 1: JLab ERL, 802 MHZ cavity design, and Polarized Source
Andrew Hutton
Jefferson Lab

## Slide 2: Jefferson Lab IR Demo Free-electron Laser
FEL Specifications
2 – 8 microns at > 1 kW average power
sub-picosecond pulse length
up to 75 MHz rep rate
3-40 keV sub picosecond x-rays

## Slide 3
Injector
Cryomodule
Wiggler
Beam Stop
Gun
Periodic Magnetic Field
Electron Beam
Total Reflector
Niobium SRF Cavity with
Oscillating Electromagnetic Field
Free Electron Laser Operation in ERL
Light Output
Electron Beam
Drive Laser
Output Mirror

## Slide 4: ENERGY RECOVERY WORKS
Required RF rises from 14.8 kW with beam off to 15.2 kW with energy recovery at 3.5 mA but rises to 35.7 kW with no recovery at 1.1 mA

## Slide 5: Benefits of Energy Recovery

## Slide 6: Existing JLab 4th Generation IR/UV Light Source
E = 120 MeV
135 pC pulses @ 75 MHz
(20 μJ/pulse in 250–700 nm UV-VIS
in commissioning)
120 μJ/pulse in 1-10 μm IR
1 μJ/pulse in THz
The first high current ERL
14 kW average power
Ultra-fast (150 fs)
Ultra-bright
(1023 ph/sec/mm2/mrad2/0.1%BW)
UV harmonics exceed FLASH average brightness (1021 average, 1027 peak ph/sec/mm2/mrad2/0.1%BW)

## Slide 7
Jefferson Lab FEL Superconducting Linac

## Slide 8: Longitudinal Matching Scenario
DC Gun
SRF Linac
Dump
IR Wiggler
Bunching Chicane
Requirements on phase space:
high peak current (short bunch) at FEL
  bunch length compression at wiggler
  using quads and sextupoles to adjust compactions
“small” energy spread at dump
  energy compress while energy recovering
  “short” RF wavelength/long bunch,
  large exhaust dp/p (~10%)
  get slope, curvature, and torsion right
  (quads, sextupoles, octupoles)
E
f
E
f
E
f
E
f
E
f
E
f

## Slide 9: Higher Order Corrections
Without nonlinear corrections, phase space becomes distorted during deceleration
Curvature, torsion,… can be compensated by nonlinear adjustments
  differentially move phase space regions to match gradient required for energy compression
E
t
Required phase bite is cos-1(1-DEFEL/E); this is >25o at the RF fundamental for 10% exhaust energy spread, >30o for 15%
  typically need 3rd order corrections (octupoles)
  also need a few extra degrees for tails, phase errors & drifts, irreproducible & varying path lengths, etc, so that system operates reliably
In this context, harmonic RF very hard to use…

## Slide 10: The M55 cavity system can map out phase response of any of the elements in the injector

## Slide 11: Major R&D Efforts Around the World
Injector, injector, injector! No existing injector delivers required CW brightness. Many groups are working on this: LBNL, Cornell, Wisconsin, JLab, KEK, Daresbury, BNL, PKU…
Brightness preservation: Solutions to coherent synchrotron radiation (CSR) emittance degradation, longitudinal space charge (LSC) in pulse compression
Halo control essential for CW – non-Gaussian tails!!!
High order mode & beam breakup control in cavities
Wakefield and propagating mode damping
Handling sizeable (~ 20 kW! @ 100 mA) THz radiation in bends
Resistive wall heating in undulators
Reducing srf dynamic load to lower refrigerator costs; probably more important than increasing gradient
< 1mA local loss allowed
High HOM power lost at
srf temps?
100W/m at 4mA on JLab IR FEL

## Slide 12: JLab FEL Accelerator Capabilities
 | Near Term Capability | Full Capability | Internal Target (Near Term)
 | external target | external target | internal target
E (MeV) | 80-320 | 80-610 | 80-165
Pmax (kW) | 100 | 300 | 1650
I (mA) | 0.31-1.25 | 0.5/3.75 | 10
fbunch (MHz) | 750/75 | 750/75 | 750/75
Qbunch (pC) | 1.67-0.4/16.7-4 | 5-0.67/50-6.7 | 13.5/135
etransverse (mm-mrad) | ~1/~3 | ~2/~5 | ~3/~10
elongitudinal (keV-psec) | ~5/~15 | ~10/~25 | ~15/~50
Polarization | No | Up to 600 mA | No
 | 750 MHz drive laser; single F100 | 12 GeV RF drive; three F100s | 12 GeV RF drive; three F100s

## Slide 13
Four sorts of the unwanted beam (beam halo)
Fraction of the phase space distribution that is far away from the core (due to the beam dynamics)
Low charge due to not well attenuated Cathode Laser (ERLs) – but real bunches that have proper timing for acceleration
Due to the Cathode Laser but not properly timed (scattered and reflected light)
Field emission: Gun (can be DC or RF), Accelerator itself (can be accelerated in both directions)
High Dynamic Range Diagnostic Development is Essential
Evtushenko

## Slide 14
DarkLight Feasibility Test
Goal
Simulate high-power ERL operation with an internal gas-jet target controlling power deposition from beam loss and impedance/wake effects from both beam core and halo components through a 10 cm long small aperture (6, 4, or 2 mm diameter)
i.e., put > 400 kW through a coffee stirrer!
Target
Chamber
Tube block
Stepper motor
Designed and constructed by MIT-Bates R&E Center in collaboration with JLab FEL staff
DarkLight Collaboration
Notes: 14

## Slide 15
600 MeV, 2 pass acceleration
200 pC, 1 mm mrad injector
Up to 4.68 MHz CW repetition rate
Recirculation and energy recovery
10 nm fundamental output, 10 nm/H harmonic
50 fs-1000 fs near-Fourier-limited pulses
JLAMP FEL designed for unparalleled average brightness of 10-100 eV photons
Baseline: seeded amplifier operation using HHG
HGHG amplifier + oscillator capability
THz Wiggler for synchronized pump/probe

## Slide 16
CW operation gives high average brightness in both fundamental and harmonics
4th Gen
3rd Gen
2nd Gen
JLAB-UV FEL
JLAB-THz
UV harm
NLS
Infrared FELs
FLASH
LCLS
XFEL
JLAMP harm
JLAMP

## Slide 17: F100 Cryomodule
108 MV, 20 MV/m, 7-cell cavities
20 MV, 5 MV/m, 5-cell cavities
HOM Damping increased for FEL application
Meets all CERN ERL requirements except frequency
Upgrade made possible by advances in SRF

## Slide 18: F100 Cavity String December 2013

## Slide 19: SRF Cryomodules for LHeC: SNS-Style Conceptual Design
E. Daly, J. Henry, A. Hutton, J. Preble and R. Rimmer
JLab Accelerator Division
20-JAN-2014
4 cavity SNS Style

## Slide 20: Proposal : SNS-Style Cryomodule 4 cavities per CM, 802.5 MHz
Supply End Can
Return End Can
Based on SNS CM
  5-cell Low Loss Shape
  Coaxial Fundamental Power Coupler
  Single RF Window
  DESY-style HOM Couplers
  Cold Tuner Drive
Overall Length – 7.524 m
Beamline Length – 6.705 m
End Cans include integral heat exchanger for improved efficiency at 2K operations
4X RF Power Coupler
Scaled for β = 1

## Slide 21: SNS High Beta Cryomodule

## Slide 22: Example of Low-Loss Cavity Parameters (805 MHz) to be modified for 802.5 MHz
0 degree wall angle
Same shape for mid & end cell
Could use SNS cryomodule
N2/k~3000, better than JLab-LL
Assuming Ea=15MV/m, then Ep=36MV/m, Bp=50mT.
Assume Rres~10nΩ at 2K, so Q0~2.0e10, Ploss~12.6W at 15MV/m
MP and HOM NOT investigated yet
Frequency [MHz] | 805
Cavity inner diameter [mm] | 316.7
Beam pipe diameter [mm] | 75.74
Cavity total length [mm] | 1165
Cavity active length [mm] | 925.2
Ep/Ea | 2.40
Bp/Ea [mT/(MV/m)] | 3.34
Geometry factor [Ω] | 288
Ra/Q [Ω] | 764
Ra*Rs (=G*Ra/Q) [Ω2] | 2.20 x 105
Cell-to-cell coupling k | 0.84%

## Slide 23: Measured Results for Production SNS High Beta Cavity
Average Qo at 10 MV/m = 2.0E10
Dissipated Power = 8.4 Watts
Average Qo at 15 MV/m = 1.64E10
Dissipated Power = 23.2 W
T = 2.0 K
Sample size = 7 Cavities
Fundamental Power Coupler
HOM Coupler
HOM Coupler
Field Probe
SNS-style CM : 4 cavities at 15 MV/m, 56 MV total
  Qo = 1.64x1010 ~110 W per Cryomodule
  Qo = 3.0x1010 ~ 60 W per Cryomodule

## Slide 24: Performance/Design Maturity and Cost Considerations
Design maturity
  Cryostat design is complete, SNS cryostat and cryogenic connection is a “drop in” design
  Jefferson Lab has existing 750 MHz and 800 MHz cavity designs
    Needs HOM coupling design, detail SNS style coupler for this application
    Can use SNS coupler with minimal changes for CW operations (lower average power in this case, makes the design simpler)
Production
  Cryostat and power coupler costs from SNS production (2002) available
    Costs need to be corrected for small quantity production and escalation
  Jefferson Lab in-house cavity assembly to control schedule

## Slide 25: Engineering and Design Effort
Table illustrates estimated labor effort for engineering design activities including analysis, design drawings, assembly drawing and technical specifications for a complete engineering design – “Ready for Production”
Design activities are split into three groups – cavity, helium vessel & tuner and cryostat
Assumes only incremental changes (scaling) from SNS Designs
PRELIMINARY costs to be confirmed upon scope agreement
Documentation generated is sufficient to support procurement and production for JLAB scope of work.
Option 2b represents one possible split of work
  JLAB collaborates with CERN on their scope while designing the cryostat components (vacuum vessel, thermal shield, magnetic shield, cryogenic piping, end cans, etc.)
  CERN designs cavity, helium vessel and tuner
Option | Design Team | Cavity Type | Cavity (weeks) | Helium Vessel & Tuner (weeks) | Cryostat (weeks) | Total (weeks) | 
2a | JLAB | SNS-Style | 43.5 | 13 | 71 | 127.5 | 
2b | JLAB | SNS-Style | 4.35 | 1.3 | 71 | 76.65 | 
 | CERN |  | 43.5 | 13 | 0 | 56.5 | 

## Slide 26: Conclusion
SNS-Style Cryomodule
  Design work is primarily the cavities
    Leverage CERN engineering resources
CERN participation in engineering and design welcome
MESA cryomodule could be prototype

## Slide 27: JLab 750 MHz FEL Cryomodule Concept
Cavity / Helium Vessel / FPC / Warm Window
Top Hat Bellows
Returm Header
Spaceframe
Thermal Shield
~10 m
HOM Waveguides
Tank diameter increased to accommodate HOM loads

## Slide 28: Polarized Electron Gun

## Slide 29: Source Parameter Comparison
Parameter | CEBAF | JLab/FEL | Nuclear Physics at Jlab FEL | Cornell ERL | LHeC | eRHIC | CLIC | ILC
Polarization | Yes | No | Yes | No | Yes | Yes | Yes | Yes
Number electrons/microbunch | 2.5 x 106 | 8.3 x 108 | 4.4 x 106 | 4.8 x 108 | 1 x 109 | 2.2 x 1010 | 6 x 109 | 3 x 1010
Number of microbunches | CW | CW | CW | CW | CW | CW | 312 | 3000
Width of microbunch | 50 ps | 35 ps | 35 ps | 2 ps | ~ 100 ps | ~ 100 ps | ~ 100 ps | ~ 1 ns
Time between microbunches | 2 ns | 13 ns | 0.67 ns | 0.77 ns | 25 ns | 71.4 ns | 0.5002 ns | 337 ns
Microbunch rep rate | 499 MHz | 75 MHz | 1497 MHz | 1300MHz | 40MHz | 14MHz | 1999 MHz | 3 MHz
Width of macropulse | - | - | - | - | - | - | 156 ns | 1 ms
Macropulse repetition rate | - | - | - | - | - | - | 50 Hz | 5 Hz
Charge per micropulse | 0.4 pC | 133 pC | 0.7 pC | 77 pC | 160 pC | 3.6 nC | 0.96 nC | 4.8 nC
Charge per macropulse | - | - | - | - | - | - | 300 nC | 14420 nC
Average current from gun | 200 uA | 10 mA | 1 mA | 100 mA | 6.5 mA | 50 mA | 15 uA | 72 uA
Average current in macropulse | - | - | - | - | - | - | 1.9 A | 0.0144 A
Duty Factor | 2.5 x 10-2 | 2.6 x 10-3 | 5.2 x 10-2 | 2.6 x 10-3 | 4 x 10-3 | 1.4 x 10-3 | 0.2 | 3x10-3
Peak current of micropulse | 8 mA | 3.8 A | 19 mA | 38.5 A | 1.6 A | 35.7 A | 9.6 A | 4.8 A
Current density* | 4 A/cm2 | 19 A/cm2 | 2 A/cm2 | 500 A/cm2 | 8 A/cm2 | 182 A/cm2 | 12 A/cm2 | 6 A/cm2
Laser Spot Size* | 0.05 cm | 0.5 cm | 0.1 cm | 0.3 cm | 0.5 cm | 0.5 cm | 1 cm | 1 cm
Existing
Proposed
* Loose estimates
Challenges depend on specific beam requirements

## Slide 30: Key Features of a Polarized Photogun
Vacuum
  Static Vacuum
  Dynamic Vacuum
High Voltage
  Eliminating field emission
Drive Laser
  Reliable, phase locked to machine
  Adequate Power, Wavelength Tunable?
Photocathode
  High Polarization, QE
  Long Lifetime

## Slide 31
Jlab - ILC High Current Polarized Electron Source
Parameter | Value
Laser Rep Rate | 1500 MHz
Laser Pulselength | 50 ps
Laser Wavelength | 780 nm
Laser Spot Size | 350 µm FWHM
High-Pol Photocathode | SSL GaAs/GaAsP
Gun Voltage | 200 kV DC
CW Beam Current | 4 mA
Run Duration | 1.4 hr
Extracted Charge | 20 C
1/e Charge Lifetime | 85 C
Bunch charge | 2.7 pC
Peak current | 53 mA
Current density | 55 A/cm2
R. Suleiman et al., PAC’11, New York (NJ, USA), March 28 – April 1, 2011

## Slide 32: How Long Can Gun Operate at 6.5 mA?
6.5 mA operation, 23 C/hr, 560 C/day.
Photocathode with 1% initial QE, 2W at 780nm and gun with 80 C charge lifetime
  Achieved at JLab during 4mA test
Need initial laser power ~ 1 W to produce 6.5mA
Should be able to operate at 6.5mA for 2 hours before running out of laser power.
Imagine a 10W laser and 1000 C charge lifetime. This provides 4 days of operation.
Message: high current polarized beam applications need photoguns with kilo-Coulomb charge lifetime

## Slide 33: Summary
JLab has over 15 years experience in designing, constructing and operating high-power CW ERLs
  Facility under-utilized, available for ERL studies
JLab designed JLamp, a 600 MeV ERL-based light source
  Many similarities with CERN ERL Test Facility
JLab has over 25 years of experience with high-power SRF design, production and operation
  Built over 90 cryomodules, including 805 MHz SNS modules
  SNS Cryostat can be modified for CERN 802 MHz cavities
JLab has active polarized source development
We are ready to collaborate