## Slide 1: Injection and extraction
Wolfgang Bartmann
CERN
(based on lectures by Brennan Goddard)

## Slide 2: Injection, extraction and transfer
Beam transfer (into, out of, and between machines) is necessary.
An accelerator has limited dynamic range.
Chain of stages needed to reach high energy
Periodic re-filling of storage rings, like LHC

## Slide 3
Injection, extraction and transfer

## Slide 4: Injection, extraction and transfer
Kickers and septa
Normalised phase space
Injection methods
  Single-turn hadron injection
  Injection errors, filamentation and blow-up
  Multi-turn hadron injection
  Charge-exchange H- injection
  Lepton injection
Extraction methods
  Single-turn (fast) extraction
  Non-resonant multi-turn extraction
  Resonant multi-turn (slow) extraction

## Slide 5: Kicker magnet
I
Ferrite
B
g
B = m0I / g
L = m0wl / g (magnet length l)
dI/dt = V/L
Typically 3 kA in 1 ms rise time
w
Pulsed magnet with very fast rise time
(100ns – few μs)

## Slide 6: Magnetic septum
Yoke
Septum coil
I
Bo = m0I / g
Typically I 5-25 kA
Pulsed or DC magnet with thin (2-20mm)
septum between zero field and high field region

## Slide 7: Electrostatic septum
E0
E=0
High voltage
electrode
Hollow earth
electrode
Thin wire or
foil (~0.1 mm)
High Voltage
Electrode
Hollow earth
electrode
Septum wires
E = V / g
Typically V = 200 kV
E = 100 kV/cm
g
DC electrostatic device with very thin (~0.1mm)
septum between zero field and high field region

## Slide 8: Normalised phase space
x
x’
Area = pe
Area = pe

Real phase space
Normalised phase space

## Slide 9: Normalised phase space
Transform real transverse coordinates x, x’ by

## Slide 10: Single-turn injection – same plane
Septum magnet
Kicker magnet
Septum deflects the beam onto the closed orbit at the centre of the kicker
Kicker compensates for the remaining angle
Septum and kicker either side of D quad to minimise kicker strength
F-quad
t
kicker field
intensity
injected
beam
‘boxcar’ stacking
Injected beam
Circulating beam
D-quad

## Slide 11: Single-turn injection
Large deflection by septum
 septum
Normalised phase space at centre of idealised septum

## Slide 12: Single-turn injection
p/2 phase advance to kicker location

## Slide 13: Single-turn injection
Kicker deflection places beam on central orbit
 kicker
Normalised phase space at centre of idealised kicker

## Slide 14: Injection oscillations
For imperfect injection the beam oscillates around the central orbit. 1
kicker  error

## Slide 15: Injection oscillations
For imperfect injection the beam oscillates around the central orbit. 2

## Slide 16: Injection oscillations
For imperfect injection the beam oscillates around the central orbit. 3

## Slide 17: Injection oscillations
For imperfect injection the beam oscillates around the central orbit. 4

## Slide 18: Injection oscillations
Betatron oscillations with respect to the Closed Orbit
Transfer line
LHC (first turn)
Horizontal
Vertical

## Slide 19: Injection errors
kicker
bpm1
bpm2
phase m
~p/2
~p/2
~p/2
septum
Angle errors
Dqs,k
Measured
Displacements
d1,2
d1 = Dqs (bsb1) sin (m1 – ms) + Dqk (bkb1) sin (m1 – mk)
≈ Dqk (bkb1)
d2 = Dqs (bsb2) sin (m2 – ms) + Dqk (bkb2) sin (m2 – mk)
≈ -Dqs (bsb2)
Dqs,
Dqk,
d1
d2

## Slide 20: Filamentation
Non-linear effects (e.g. magnetic field multipoles ) present which introduce amplitude dependent effects into particle motion.
Over many turns, a phase-space oscillation is transformed into an emittance increase.
So any residual transverse oscillation will lead to an emittance blow-up through filamentation
  “Transverse damper” systems used to damp injection oscillations - bunch position measured by a pick-up, which is linked to a kicker

## Slide 21: Filamentation

## Slide 22: Filamentation

## Slide 23: Filamentation

## Slide 24: Filamentation

## Slide 25: Filamentation

## Slide 26: Filamentation

## Slide 27: Filamentation

## Slide 28: Filamentation

## Slide 29: Filamentation

## Slide 30: Filamentation

## Slide 31: Damping of injection oscillations
Residual transverse oscillations lead to an emittance blow-up through filamentation
“Transverse damper” systems used to damp injection oscillations - bunch position measured by a pick-up, which is linked to a kicker
Damper measures offset of bunch on one turn, then kicks the bunch on a subsequent turn to reduce the oscillation amplitude
Injection oscillation

## Slide 32: Optical Mismatch at Injection
x
x’
Matched phase-space ellipse
Mismatched injected beam
Can also have an emittance blow-up through optical mismatch
Individual particles oscillate with conserved CS invariant:
ax = g x2 + 2a xx’ + b x’2

## Slide 33: Optical Mismatch at Injection
Filamentation fills larger ellipse with same shape as matched ellipse
x
x’
Turn 0
Turn N
Time

## Slide 34: Multi-turn injection
For hadrons the beam density at injection can be limited either by space charge effects or by the injector capacity
If we cannot increase charge density, we can sometimes fill the horizontal phase space to increase overall injected intensity.
  Condition that the acceptance of receiving machine is larger than the delivered beam emittance

## Slide 35: Multi-turn injection for hadrons
Septum magnet
No kicker
Bump amplitude decreases and inject a new bunch at each turn
Phase-space “painting”
Closed orbit bumpers
Varying amplitude bump

## Slide 36: Multi-turn injection for hadrons
Turn 1
Septum
Example: CERN PSB injection, fractional tune Qh = 0.25
  Beam rotates π/2 per turn in phase space
On each turn inject a new batch and reduce the bump amplitude

## Slide 37: Multi-turn injection for hadrons
Turn 2

## Slide 38: Multi-turn injection for hadrons
Turn 3

## Slide 39: Multi-turn injection for hadrons
Turn 4

## Slide 40: Multi-turn injection for hadrons
Turn 5

## Slide 41: Multi-turn injection for hadrons
Turn 6

## Slide 42: Multi-turn injection for hadrons
Turn 7

## Slide 43: Multi-turn injection for hadrons
Turn 8

## Slide 44: Multi-turn injection for hadrons
Turn 9

## Slide 45: Multi-turn injection for hadrons
Turn 10

## Slide 46: Multi-turn injection for hadrons
Turn 11

## Slide 47: Multi-turn injection for hadrons
Turn 12

## Slide 48: Multi-turn injection for hadrons
Turn 13

## Slide 49: Multi-turn injection for hadrons
Turn 14

## Slide 50: Multi-turn injection for hadrons
Turn 15
In reality filamentation occurs to produce a quasi-uniform beam
Phase space has been “painted”

## Slide 51: Injection mismatch
For multiturn injection over n turns, injected beam ellipse is deliberately mismatched to circulating beam ellipse to reduce losses
er

## Slide 52: Charge exchange H- injection
Multiturn injection is essential to accumulate high intensity
Disadvantages inherent in using an injection septum
  Width of several mm reduces aperture
  Beam losses from circulating beam hitting septum
  Limits number of injected turns to 10-20
Charge-exchange injection provides elegant alternative
  Possible to “cheat” Liouville’s theorem, which says that emittance is conserved….
  Convert H- to p+ using a thin stripping foil, allowing injection into the same phase space area

## Slide 53: Charge exchange H- injection
H- beam
Injection chicane dipoles
Circulating p+
p+
Stripping foil
H0
H-
Displace orbit
Start of injection process

## Slide 54: Charge exchange H- injection
H- beam
Injection chicane
Circulating p+
p+
Stripping foil
H0
H-
End of injection process

## Slide 55: Charge exchange H- injection
Paint uniform transverse phase space density by modifying closed orbit bump and steering injected beam
Foil thickness calculated to double-strip most ions (>99%)
  50 MeV - 50 mg.cm-2
  800 MeV - 200 mg.cm-2 (~1mm of C!)
Carbon foils generally used – very fragile
Injection chicane reduced or switched off after injection, to avoid excessive foil heating and beam blow up

## Slide 56: “Overinjection”
Multiturn injection of hadrons
Charge exchange injection
NO Septum needed  overinject on already occupied phase space area
Septum  cannot inject on already occupied phase space area

## Slide 57: H- injection - painting
Time
x’ vs x
y’ vs y
y vs x
Note injection into same phase space area as circulating beam
~100 turns

## Slide 58: Problems with foils
Foil damage
Present machines on the high beam power frontier are approaching the limits of foils
Sarah Cousineau, Laser stripping WS, Fermilab, 26-27 Sept-2013

## Slide 59: Problems with foils
Beam loss and radiation
  Beam loss due to foil scattering (foil is highest loss point in SNS accelerator complex)
Emittance growth due to foil scattering
  Relevant for multi-purpose machines
Laser stripping avoids a mechanical interaction with the beam
Neutralisation (H-  H0)
Stripping (H0 p+)

## Slide 60: H- injection with laser stripping
H- beam
Injection chicane
Circulating p+
p+
H0
H-
Wiggler or laser for neutralisation
Laser for excitation
Dedicated design of stripping chicane magnet

## Slide 61: Laser stripping concept: H- to H0
Either Lorentz-stripping in a wiggler magnet…
or Photo-dissociation

## Slide 62: Lorentz stripping
H- ion moving in magnetic field  Lorentz force tends to break it up
Binding energy of extra electron 0.76 eV
In ion rest-frame electric field E is the Lorentz-transform of the magnetic field B in the lab-frame
The ion’s lifetime can be parametrized as
,

## Slide 63: H0 --> p+ stripping divergent laser beam
Scheme developed and tested at SNS (Danilov et al.):
Resonant excitation of ground-state H0 in field free region
Stripping of excited electron in magnetic field
Large spread of effective resonance frequencies divergent beam
H-
Divergent laser light

## Slide 64: Lepton injection
Single-turn injection can be used as for hadrons; however, lepton motion is strongly damped (different with respect to proton or ion injection).
  Synchrotron radiation
Can use transverse or longitudinal damping:
  Transverse - Betatron accumulation
  Longitudinal - Synchrotron accumulation

## Slide 65: Betatron lepton injection
Beam is injected with an angle with respect to the closed orbit
Injected beam performs damped betatron oscillations about the closed orbit
Septum magnet
Closed orbit bumpers or kickers

## Slide 66: Betatron lepton injection
Injected bunch performs damped betatron oscillations
In LEP at 20 GeV, the damping time was about 6’000 turns (0.6 seconds)

## Slide 67: Synchrotron lepton injection
Septum magnet
Beam injected parallel to circulating beam, onto dispersion orbit of a particle having the same momentum offset Δp/p
Injected beam makes damped synchrotron oscillations at Qs but does not perform betatron oscillations
Closed orbit bumpers or kickers
Bumped circulating beam
Injected beam
xs = Dx · Δp/p0
xs
p = p0
p = p0 + Δp
Inject an off-momentum beam

## Slide 68: Synchrotron lepton injection
F
E
Double batch injection possible….
Longitudinal damping time in LEP was ~ 3’000 turns (2 x faster than transverse)
Injection 1 (turn N)
Injection 2 (turn N + Qs/2)
Stored beam
RF bucket

## Slide 69: Synchrotron lepton injection in LEP
Synchrotron Injection in LEP gave improved background for LEP experiments due to
small orbit offsets in zero dispersion straight sections

## Slide 70: Injection - summary
Several different techniques
  Single-turn injection for hadrons
    Boxcar stacking: transfer between machines in accelerator chain
    Angle / position errors  injection oscillations
    Optics errors  betatron mismatch oscillations
    Oscillations  filamentation  emittance increase
  Multi-turn injection for hadrons
    Phase space painting to increase intensity
    H- injection allows injection into same phase space area
  Lepton injection: take advantage of damping
    Less concerned about injection precision and matching

## Slide 71: Extraction
Different extraction techniques exist, depending on requirements
  Fast extraction: ≤1 turn
  Non-resonant multi-turn extraction: few turns
  Resonant multi-turn extraction: many thousands of turns
  Resonant low-loss multi-turn extraction: few turns
Usually higher energy than injection  stronger elements (∫B.dl)
  At high energies many kicker and septum modules may be required
  To reduce kicker and septum strength, beam can be moved near to septum by closed orbit bump

## Slide 72: Fast single turn extraction
Septum magnet
Kicker magnet
Kicker deflects the entire beam into the septum in a single turn
Septum deflects the beam entire into the transfer line
Most efficient (lowest deflection angles required) for p/2 phase advance between kicker and septum
Closed orbit bumpers
    Whole beam kicked into septum gap and extracted.

## Slide 73: Fast single turn extraction
For transfer of beams between accelerators in an injector chain.
For secondary particle production (e.g. neutrinos)
Septum deflection may be in the other plane to the kicker deflection.
Losses from transverse scraping or from particles in extraction gap
Particles in SPS extraction kicker rise- and fall-time gaps

## Slide 74: Synchronisation I
Beam from PS has to be injected into right SPS bucket wrt to SPS revolution frequency
Set frequency
  Before beam is transferred, e.g. from SPS to LHC, the two machines must be synchronised on a common frequency fc
  Now the LHC can choose the bucket in which the first bunch will be injected  SPS must shift the beam to adapt to this position
fc

## Slide 75: Synchronisation II
“Coarse” rephasing
  Shift the beam in the SPS to reach wanted LHC bucket
  To do so the particles will run for a short period on an average radius which is different from the central orbit (“radial steering”)
  Matching of common frequency fc with SPS revolution frequency (TDC)
“Fine” rephasing – phase matching
  Correct the position within the bucket
  Matching of and (phase lock loop)
Set frequency
Constant frequency offset
Coarse rephasing
Fine rephasing
Extraction
ΔΦ(, ) vs turn

## Slide 76: Synchronisation III
Triggering the SPS extraction and LHC injection kickers
  Timing event: has only 1ms resolution; serves as prepulse;
  With fc calculate exact timing of kicker pulse for SPS and LHC
Arm counter
Generate warning pulse which goes to SPS and LHC
Calculate RF periods for SPS extraction and LHC injection kicker pulse

## Slide 77: Multi-turn extraction
Some filling schemes require a beam to be injected in several turns to a larger machine…
And very commonly Fixed Target physics experiments and medical accelerators often need a quasi-continuous flux of particles…
Multi-turn extraction…
  Non-Resonant multi-turn ejection (few turns) for filling e.g. PS to SPS at CERN for high intensity proton beams (>2.5 1013 protons)
  Resonant extraction (ms to hours) for experiments

## Slide 78: Non-resonant multi-turn extraction
Extracted beam
Bumped circulating beam
Septum
Fast bumper deflects the whole beam onto the septum
Beam extracted in a few turns, with the machine tune rotating the beam
Intrinsically a high-loss process – thin septum essential
Fast closed orbit bumpers
    Beam bumped to septum; part of beam ‘shaved’ off each turn.

## Slide 79: Non-resonant multi-turn extraction
Example system: CERN PS to SPS Fixed-Target ‘continuous transfer’.
  Accelerate beam in PS to 14 GeV/c
  Empty PS machine (2.1 ms long) in 5 turns into SPS
  Do it again
  Fill SPS machine (23 ms long)
  Quasi-continuous beam in SPS (2 x 1 ms gaps)
  Total intensity per PS extraction ≈ 3  1013 p+
  Total intensity in SPS ≈ 5  1013 p+

## Slide 80: Non-resonant multi-turn extraction
CERN PS to SPS: 5-turn continuous transfer
Qh = 0.25
1 2 3 4 5
Bump vs. turn
1
2
3
4
5
septum

## Slide 81: Non-resonant multi-turn extraction
CERN PS to SPS: 5-turn continuous transfer – 5th turn
Qh = 0.25
1 2 3 4 5
Bump vs. turn
5

## Slide 82: Non-resonant multi-turn extraction
CERN PS to SPS: 5-turn continuous transfer
  Losses impose thin (ES) septum… second septum needed
  Still about 15 % of beam lost in PS-SPS CT
  Difficult to get equal intensities per turn
  Different trajectories for each turn
  Different emittances for each turn
1
2
3
4
5
I
1
2
3
4
5

## Slide 83: Resonant multi-turn extraction
Extracted beam
Bumped circulating beam -
particles moved across
Septum by resonance
Septum
Slow bumpers move the beam near the septum
Tune adjusted close to nth order betatron resonance
Multipole magnets excited to define stable area in phase space, size depends on ΔQ = Q - Qr
Closed orbit bumpers
    Non-linear fields excite resonances which
    drive the beam slowly across the septum

## Slide 84: Resonant multi-turn extraction
3rd order resonances
  Sextupole fields distort the circular normalised phase space particle trajectories.
  Stable area defined, delimited by unstable Fixed Points.
  Sextupoles families arranged to produce suitable phase space orientation of the stable triangle at thin electrostatic septum
  Stable area can be reduced by increasing the sextupole strength, or (easier) by approaching machine tune Qh to resonant 1/3 integer tune
  Reducing DQ with main machine quadrupoles can be augmented with a ‘servo’ quadrupole, which can modulate DQ in a servo loop, acting on a measurement of the spill intensity
Rfp

## Slide 85: Third-order resonant extraction
Particles distributed on emittance contours
ΔQ large – no phase space distortion
Septum wire

## Slide 86: Third-order resonant extraction
Dedicated sextupole magnets produce a triangular stable area in phase space
ΔQ decreasing – phase space distortion for largest amplitudes
Septum wire

## Slide 87: Third-order resonant extraction
Septum wire

## Slide 88: Third-order resonant extraction
Septum wire

## Slide 89: Third-order resonant extraction
Septum wire

## Slide 90: Third-order resonant extraction
DQ small enough that largest amplitude particles are close to the separatrices
Fixed points locations discernable at extremities of phase space triangle
Septum wire

## Slide 91: Third-order resonant extraction
ΔQ now small enough that largest amplitude particles are unstable
Unstable particles follow separatrix branches as they increase in amplitude
Septum wire

## Slide 92: Third-order resonant extraction
Stable phase area shrinks as ΔQ gets smaller
Septum wire

## Slide 93: Third-order resonant extraction
Separatrix position in phase space shifts as the stable area shrinks
Septum wire

## Slide 94: Third-order resonant extraction
As the stable area shrinks, the beam intensity drops since particles are being continuously extracted
Septum wire

## Slide 95: Third-order resonant extraction
Septum wire

## Slide 96: Third-order resonant extraction
Septum wire

## Slide 97: Third-order resonant extraction
Septum wire

## Slide 98: Third-order resonant extraction
As ΔQ approaches zero, the particles with very small amplitude are extracted
Septum wire

## Slide 99: Third-order resonant extraction
Example – SPS slow extraction at 450 GeV/c.
~3 x 1013 p+ extracted in a 2-4 second long spill (~200,000 turns)
Intensity vs time:
~108 p+ extracted per turn

## Slide 100: Second-order resonant extraction
An extraction can also be made over a few hundred turns
2nd and 4th order resonances
  Octupole fields distort the regular phase space particle trajectories
  Stable area defined, delimited by two unstable Fixed Points
  Beam tune brought across a 2nd order resonance (Q→0.5)
  Particle amplitudes quickly grow and beam is extracted in a few hundred turns

## Slide 101: Resonant extraction separatrices
Amplitude growth for 2nd order resonance much faster than 3rd – shorter spill
Used where intense pulses are required on target – e.g. neutrino production
3rd order resonant extraction
2nd order resonant extraction

## Slide 102: Resonant low-loss multi-turn extraction
Adiabatic capture of beam in stable “islands”
  Use non-linear fields (sextupoles and octupoles) to create islands of stability in phase space
  A slow (adiabatic) tune variation to cross a resonance and to drive particles into the islands (capture)
  Variation of field strengths to separate the islands in phase space
Several big advantages
  Losses reduced virtually to zero (no particles at the septum)
  Phase space matching improved with respect to existing non-resonant multi-turn extraction - all ‘beamlets’ have same emittance and optical parameters

## Slide 103: Resonant low-loss multi-turn extraction
Septum wire
Unperturbed beam
Increasing non-linear fields
Beam captured in stable islands
Islands separated and beam bumped across septum – extracted in 5 turns
1 2 3 4 5
Bump vs. turn
Qh = 0.25
Courtesy M. Giovannozzi

## Slide 104: Extraction - summary
Several different techniques:
  Single-turn fast extraction:
    for Boxcar stacking (transfer between machines in accelerator chain), beam abort
  Non-resonant multi-turn extraction
    slice beam into equal parts for transfer between machine over a few turns.
  Resonant multi-turn extraction
    create stable area in phase space  slowly drive particles into resonance  long spill over many thousand turns.
  Resonant low-loss multi-turn extraction
    create stable islands in phase space: slice off over a few turns.
Thank you for your attention