## Slide 1: Energy Deposition Results in: Decay Tube Window & Shutter
1st AWAKE Performance Meeting 28.10.2013 Athanasios.Manousos@cern.ch, Vasilis.vlachoudis@cern.ch

## Slide 2: Introduction

## Slide 3: Simulation Setup Beam & Materials
Beam Parameters
  Energy : 400 GeV
  Intensity : 3.5*1011 p+ (Ultimate: 3.5 1011)
  1 sigma : 6mm at the window
  Frequency: 0.14Hz
  Center of beam is at center of window
  Divergence → 30urad
Materials
  Tube Window: Titanium Grade 2
  Shutter: Iron

## Slide 4: Simulation Setup Geometry Layouts
Shutter
Tube Window

## Slide 5: FLUKA: Energy Deposition Calculations Decay Tube Window
Max Energy Deposited: ~ 0.2 Joules/cm3/Pulse

## Slide 6: FLUKA: Energy Deposition Calculations Shutter
Max Energy Deposited: ~ 2.5 Joules/cm3/Pulse

## Slide 7: Summary
Maximum Energy Deposited:
  ~ 0.2 Joules/cm3/Pulse on Window
  ~ 2.5 Joules/cm3/Pulse on Shutter
Both presented simulations are accepted.
Questions ??

## Slide 8: Backup Slides
Material Definition:
  TG2:
Material | Mass Fraction %
Carbon | 0.1
Iron | 0.3
Hydrogen | 0.015
Nitrogen | 0.03
Oxygen | 0.25
Titanium | 99.2