Feasibility of (semi-) automated Tune Control in the PS
LTC - Extended Meeting, 2008-03-06
Session 5 - Beam Plans for Accelerator Physics Systems
LHC Tune and Chromaticity Diagnostic
and
Feedback Control Systems
Ralph J. Steinhagen, AB-BI
for the 'invincible Gauls'
A. Boccardi, F. Follin, M. Gasior, R. Jones, P. Karlsson,
G. Sivatskiy, R.J. Steinhagen, J. Wenninger

---
Outline
Base-line LHC Q, Q' and C- diagnostics overview
  - System overview and hardware status
Application overview
Commissioning of Q, Q' and C- beam parameter control
  - Instrumentation, diagnostics and related corrector circuits
  - Feedback options and setup

---
Reminder: LHC Tune and Chromaticity Requirements
The measurement and control of
  - -- orbit, tune, chromaticity, energy and coupling --
  - will be an integral part of the LHC operation
Stability requirements summary (Chamonix'06):
... “FBs are most beneficial and (likely) required before the very first ramp!”
after two years, experience from RHIC/Tevatron and many MDs in the SPS
  - ... we are ready and believe to be prepared to meet the LHC challenge!

---
Reminder: Tune and Chromaticity Drifts during LHC ramp
Exp. perturbations are about 200 times than required stability!
however: maximum drift rates are expected to be slow in the LHC
    - Tune:	ΔQ/Δt|max < 10-3 s-1
    - Chromaticity:	ΔQ'/Δt|max < 2 s-1
Requires active control relying on beam-based measurements
← the critical/difficult parameter

---
LHC Q Base-Line Q Instrumentation
Back-bone: Base-Band-Q Principle on a Slide
BBQ detector
BBQ front-end
Basic principle: AC-coupled peak detector
  - no saturation, self-triggered, no gain changes between pilot and nominal
  - intrinsically down samples spectra: ... 6 GHz → 1kHz ... frev
    - Base-band operation: very high sensitivity/resolution ADC available
    - Measured resolution estimate: < 10 nm → ε blow-up is a non-issue
One of the few turn-key systems in the LHC
  - easy/very fast commissioning – done in parallel with RF capture

---
LHC Q Base-Line Q Instrumentation
BBQ System Overview
Back-bone: Base-Band-Q Meter1 (BBQ)
  - well tested and proven solution:	SPS, LEIR, PSB, RHIC, Tevatron, ...
Pick-ups: 40 cm strip-lines
Shakers: 1 m strip-lines
  - magnetic deflectors driven ± 3 A max.
  - working bandwidth: 1 - 6 kHz
  - maximum kick angle: 0.1nrad@7TeV	→ 23 nm@β = 180m per turn
3 x 2 (nearly) identical installation (tunnel	(2 development/hot-spare systems on the surface)
... some redundancy:	8 systems available vs. 2 needed
1M. Gasior: LHC-Project-Report-853
LHC Tunnel
UA47/UA43 Cavern

---
LHC Q Base-Line Q Instrumentation
Hardware Status
UA47-BY12 & BY13
BBQ based systems: (~ 1 more week)
  - all acquisition systems are in place
  - remaining: front-end installation, final cabling and HW acceptance test
  - N.B. transverse damper available as exciter
Head-Tail/Fast-Intra-Bunch-Position Monitor
  - acquisition system (scopes) in place
  - final cabling pending (~ 2 days, April)
Schottky: US-LARP responsibility (soonish)
  - cabling, detectors in place
  - HW, SW acquisition and control system pending
we are in good shape and ready for first beams... whenever we get the 'go-ahead'
Head-Tail
Schottky
BBQ-FFT1/2
'on-demand'
2008-01-16

---
LHC Base-Line Q/Q' Diagnostics Overview – Q/C-
BPM and BBQ exploitation
Commissioning Phase A.3 (choices first circulating beam):
FFT based acquisition using LHC BPMs - Phase A.2 → J. Wenninger, V. Kain (excite and/or analyse injection oscillation spectra)
  - initial tune adjustments (first 100 turns, integer Q, local C- correction, etc.)
  - CON: slow, no fast periodic acquisition possible, problematic with large Q'
FFT based acquisition using LHC BBQ with either
  - simply no excitation! - yields sufficient data in most cases...
  - ...for the others: fall-back to one of the following excitation based methods:
  - 'RF transverse damper' or 'BQK' (aka. 'tune shaker'),
    - preferred choice: no timing required, fast and easy amplitude tuning
  - 'MKQA' (aka. 'tune' or 'aperture kicker') triggered by the MTG
    - mainly for cross-calibration and measurements involving BPMs or HT
  - CON: slower tune (→ chromaticity) tracking, problematic with large Q'
Phase-Locked-Loop (PLL) based acquisition
  - requires excitation using either the 'BQK' or 'RF transverse damper'
  - can cope with wide range of Q', SPS experience: robust measurement

---
LHC Base-Line Q/Q' Diagnostics Overview – Q/C-
BBQ Use-Cases Abstraction
Three independent BBQ Tune/Coupling diagnostic chains available per beam:
  - PPL based acquisition of Q, Q'...
    - one measurement at high/reduced acquisition frequency, targets:
      - 100 Hz for feedbacks (driven by need to reduce feedback latencies)
      - 1 Hz for general purpose logging
    - expert: high frequency data that is event synchronised and buffered (post-mortem, PLL setup), typical length: 5 min ↔ < 1 MB of data
    - main use: monitoring/logging, feedbacks, fill-to-fill studies, ...
  - FFT based acquisition of Q,Q'... – 'periodic'
    - one measurement every 1 second starting from first-injection
    - intended use: monitoring/logging, (feedbacks), fill-to-fill studies, ...
  - FFT based acquisition of Q,Q'... – 'on demand'
    - n-measurements synchronised to an external event (BPM, BQ, ...)
    - intended use: expert diagnostics, detailed studies, ...

---
LHC Base-Line Q/Q' Diagnostics Overview – Q/C-
Operational & BI-Expert Interface: TuneViewer
Tested and/or used at SPS, PSB, PS, LEIR for about a year now (~debugged)
Main responsibility: R. Steinhagen (AB-BI),	co-maintained and input from F. Follin, J. Wenninger (AB-OP)

---
LHC Base-Line Q/Q' Diagnostics Overview – Q/C-
TuneViewer – Functional Overview I/II
Same interface/can acquire from any CERN BBQ-FFT/PLL based system
  - same diagnostics look-and-feel across accelerators
  - several different FFT analysis tools available
  - Standard displays: Q/Q' traces, FFT-vs-time, FFT spectra, S/N ratios, raw oscillation data, BTF, ... → modular, can be used as a fixed-display
  - standard CO interfaces: SDDS, LSA, JAPC, timing where applicable
  - developed having commissioning and expert diagnostics in mind
    - however: provides reduced level of detail for day-to-day operation
  - off-line diagnostics, re-tuning, comparison and expert analysis of multiple	Q/Q' parameters and data sets possible
additional LHC specific 'plugins':
  - Q/Q' 'slow' steering ('one point trim'), kick/BPM timing synchronisation,
  - Q/Q' real-time feedback control:
    - implements the same algorithms as the Q/Q' feedback controller
    - any tested settings are easily applied to the Q/C-/Q' FB controller
Some features in the testing/development pipeline...

---
LHC Base-Line Q/Q' Diagnostics Overview – Q/C-
TuneViewer – Functional Overview II/II

---
LHC Base-Line Q/Q' Diagnostics Overview – Q/C-
Betatron-Coupling Measurement
No orbit, Q, Q' feedback without control of betatron-coupling
FFT/PLL measures eigenmodes that in the presence of	coupling are rotated w.r.t. “true” horizontal/vertical tune
  - A1,x: “horizontal” eigenmode in vertical plane
  - A1,y: “horizontal” eigenmode in horizontal plane
Decoupled feedback control:
  - qx, qy	→	quadrupole circuits strength
  - |C-|, χ	→	skew-quadrupole circuits strength
χ
first implemented and tested at RHIC/
tested/operational at CERN
R. Jones et.al., “Towards a Robust Phase Locked Loop Tune Feedback System”, DIPAC'05, Lyon, France, 2005

---
LHC Base-Line Q/Q' Diagnostics Overview – Q/C-
Betatron-Coupling Measurement (Real-Beam Data)

---
LHC Base-Line Q/Q' Diagnostics Overview – Q/C-
Simplified LHC Phase-Locked-Loop Scheme
beam response
reference signal
BBQ
Trans. Damper/
Tune Tickler
R(fe)∙cos(2πfe-φ)
A∙sin(2πfe)
X
fLP
X
fLP
Rect.
2
Pol.
NCO
phase loop
ampl. loop
R(ω)
φ
φ
ILP
QLP
QLP
ILP
rect2polar
sin(2πfe)
cos(2πfe)
R(ω)
Gpre(s)
zinput(t)
Gex(s)
zexciter(t)
Δf
Δa
beam response signal
90°

---
LHC Base-Line Q/Q' Diagnostics Overview – Q/C-
Since 2006: SPS PLL Operation
either: ΔQ/Δt|max ≈ 0.3 within 300 ms, (o. of magnitude faster than LHC requirement)
or: tune resolution: ΔQres≈ 10-6...10-7 but reduced bandwidth (~1..2 Hz)
tune trace
phase response
amplitude response
frev ≈ 43 kHzﾧ

---
LHC Base-Line Q/Q' Diagnostics Overview – Q'
RF momentum modulation – LHC Commissioning Phase A.3
  - class: Q' is proportional to momentum induced tune changes
Kicked Head-Tail Phase-Shift – LHC Phase A.3 (~ copy++ of SPS installation)
  - multiple dependences on beam parameter other than Q'
  - limited by emittance growth/orbit budget → it's an MD tool
    - still provides good cross-reference and general beam diagnostics!
Side-exciter/BTF based method – end 2008/beginning of 2009
  - needs broader acceptance (human component) and assessment with LHC beam (parameters)
Continuous Head-Tail Phase-Shift – 2009++
  - Tested various schemes in 2007 at the SPS but need further assessment
the measured tune change
the RF induced momentum change (known)

---
Q' through RF momentum modulation based method
There are multiple but similar detection techniques:
  - modulation below Qs → classic schoolbook example
  - modulation above Qs → Brüning's and/or McGinnis' method
LHC RF power permits only slow modulation (J. Tückmantel et al.)
slow modulation
fast modulation
Q' diagnostic &
FB operation

---
Q' through RF momentum modulation based method
Controllability of Q' depends on ability to track the tune both accurately & fast
  - intrinsic to this problem:
  - LHC expectations:
    - Tune:	ΔQ/Δt|max < 10-3 s-1
    - Chromaticity:	ΔQ'/Δt|max < 2 s-1
→ Chose to tackle the LHC Q' measurement in the high accuracy limit:
  - very small but slow Δp/p modulation while tracking Q with a PLL
    - fmod:	0.5 Hz	(setup)	→ 5 Hz	(nominal)
    - Δp/p:	~10-4	(setup)	→ ~10-5	(nominal)
  - Feasibility supported by LHC Q' tracker prototype tests in the SPS
    - fmod = 0.5 Hz, Δp/p = 2·10-5: ΔQres ~ 10-5, ΔQ'res<1
    - limited by the fmod DAC quantization
“slow” compared to Q/Q' drifts
e.g. in the SPS/RHIC/CPS/PSB

---
FFT Based Q Acquisition
Δp/p ~ 2·10-5 driven Q modulation (Q'v ~ 36 units)

---
Dedicated PLL based Q/Q' tracking study at the SPS
Modulation Amplitude: Δp/p ≈ 1.85∙10-5
tune
induced Q' changes
PLL phase
PLL amplitude [a.u.]

---
Dedicated PLL based Q/Q' tracking study at the SPS
Modulation Amplitude: Δp/p ≈ 1.85∙10-5
tune
Q'/Q
real-time Q' detection algorithm (agrees with SPS cross-calibration):
  - Q' resolution better than 1 unit (nominal performance) → reproducible
N.B. tracking transients: ΔQ' feed-down on ΔQ (non-centred orbit)
    - ΔQ/Δt >> ΔQ'/Δt → SPS specific, LHC: ΔQ/Δt|max < 10-4/s

---
Dedicated PLL based Q/Q' tracking study at the SPS
Modulation Amplitude: Δp/p ≈ 1.85∙10-5
Q'/Q
tune
Scans to assess the maximum useful range yield showed that this method can cope with values of Q' up to at least 34 units
  - larger than (any other) Fourier based method ... (usually damping limited)
Q = 26.18

---
LHC Base-Line Q/Q' Diagnostics Overview – Q'
Q' Through Kicked Head-Tail Phase Shift
First order: copy of SPS system
  - increased sampling:	5000 (LHC) vs. 2000 (SPS)
  - increased bandwidth:	> 3 GHz vs. 2 GHz
  - switch on & use system
Some intrinsic limitations:
  - requires large kicks; issues:
    - sig. emittance blow-up
    - machine protection → measurement remains a MD/pilot beam tool!
uncertainties due to multiple dependences on beam parameter other than Q':
  - Impedance, non-linear damping (Q'/Q'', RF damper), non-lin. Qs,
  - Very low LHC Qs = 30 Hz issue	→ oscillations need to prevail > 350++ turns for useful Q' analysis

---
LHC Base-Line Q/Q' Diagnostics Overview – Q'
HeadTail Viewer – Functionality
BI-expert tool known and used by many in ABP, BI, OP & RF
Misnomer: 'Head-Tail' is actually a 'Fast-Intra-Bunch-Position-Monitor'
  - many long. and trans. beam diagnostics cross-calibrations possible
  - Implements standard analysis/displays for:
    - Raw and phase compensated Sum/Difference signal oscillation data
    - Tune, betatron-coupling, closed orbit, bunch length-vs-time
    - Phase-evolution-vs-turn → Q'-vs-turn, HT-Q' estimate
    - Amplitude-envelope (damping/instability growth times),
    - 1D-trace & 2D longitudinal and transverse bunch spectra
      - in-bunch & coupled bunch mode instabilities, chromatic frequencies
    - ...
    - in the pipeline: fast relative bunch intensity changes, BPM type acquisitions, processing speed performance
  - off-line diagnostics, re-tuning, comparison and expert analysis of multiple	longitudinal, Q, Q' data sets possible
If you have questions, feel that something is missing or is too much (= bugs) → please let me know

---
Commissioning of the
Q, C- & Q'
Feedback Loops

---
Total Number of (FB) Corrector Circuits
Powering Layout of the SSS Correction Scheme IP4↔IP5

---
Summary: Total Number of (FB) Corrector Circuits
Orbit: 530 correction dipole magnets/plane (71% are of type MCBH/V, ±60A)
  - total 1060 individually powered magnets (60-120 A)
  - ~30 shared between B1 & B2
Tune:
  - 16x ±600A circuits powered from even IPs (2, 4, 6, 8), 2 families
  - independent for Beam 1&2, but coupling between planes
  - can use them independently, optional use of DS quadrupoles
Chromaticity:
  - 32x ±600A circuits powered from even IPs,4 families (ΔQ'~1→1A@7TeV)
Coupling: four skew quadrupoles per arc, 1/2 families
    - Beam 1: 12x ±600A
    - Beam 2: 10x ±600A
Total: 1130 of 1720 circuits/power converter → more than half the LHC is controlled by beam based feedback systems!

---
LHC: Divide-and-Conquer Feedback Architecture
Divide:
  - FB zoo: Orbit, Tune, Chromaticity, β-Coupling,	Energy, ..., Luminosity, (Beta-Beating)
    - develop/commission on a one-by-one basis
  - Feedback controller into:
    - Space Domain: ΔQx/y → quadrupole circuits currents, etc.
      - classic parameter control – pre-requisite for any beam steering
    - Time Domain: compensate for dynamic behaviour
      - relaxed controller for commissioning (low-bandwidth PI controller)
Conquer:
  - Once feedback operation on a per-parameter basis is established, reintegrate and test/commission inter-loop coupling and other constraints.
LHC Feedback hierarchy:
  - Orbit (Energy) → Tune/Coupling PLL → Q' Tracker → Q/C-/Q' feedback

---
Future Integration of Q/Q' Measurements for Q/Q' Control
Full LHC Beam-Based Control Scheme
(Skew-) Quadrupole settings
ΔQ,ΔC-
Σ
Tune/Coupling
Controller
Qref,C-ref
Qavg
Q'ref
ΔQmod
Sextupole Settings
Q'
Chromaticity
Reconstr.
Σ
Chromaticity
Controller
f0+Δf, Δp/p
A∙sin(2πfe)
reference signal
φ
Δf
Phase
Detector
Low-pass
Filter
PLL-Control Law
e.g. PID
NCO
orbit ref.
δ, Δp/p, Δf
Δp/p RF
modulation
Orbit Feedback
Controller
Σ
(12x/10x)
16x2
32x
1075x2
530x2
x2
2x2
BBQ
BPMs
CODs
RF
mini-
AC
dipole/
damper
2 (+2) x 2
Orbit/Energy Feedback
Tune/Coupling PLL
Chromaticity Tracker/Feedback
further: fBW(PLL) » fBW(Q') ≥ fBW(Q, C-)
Tune/Coupling Feedback
LHC FBs: 2158 input devices, 1136 output devices → total: ~3300 devices!
R(fe)∙sin(2πfe+φ)
beam response
A∙sin(2πfe)
LHC
beam response
Δf

---
Orbit Feedback II/III
Common Feedback/Feed-Forward Control Layout
Each LHC feedback controller implementation split into two sub-systems:
  - Service Unit: Interface to users/software control system
  - Feedback Controller: actual parameter/feedback control logic
    - Simple streaming task for all feed-forwards/feedbacks:	(Monitor → Network )FB→ Data-processing → Network → PC-Gateways
    - Can run auto-triggered (first beams)
    - Hardware and functional specifications already available
CMW
Database settings,
operation,other user
Service Unit
Ethernet UDP/IP
Ethernet UDP/IP
m x
n x
Monitor-Frontend
PC-Gateways
Monitor-Frontend
PC-Gateways
Monitor-Frontend
FB/FF Controller
PC-Gateways
...
...
beam instrument
corrector magnets
beam response
Surface
Tunnel

---
TestBed
Commissioning the Orbit Feedback Controller – Test Bed
Test-bed complementary to Feedback Controllers:
  - Simulates the open loop and orbit response of COD→BEAM→BPM
    - Decay/Snap-back, ramp, squeeze, ground motion simulations, ...
    - Keeps/can test real-time constraints up to 1 kHz
  - Same data delivery mechanism and timing as the front-ends
    - transparent for the FB controller
Central Timing
generator
... t=20/40 ms Dt<1 ms
FC Test Bed
covers whole ring (27 km)
  BI-Frontend
  PC-Gateways
Feedback Controller
CTR
CTR
CTR
CTR
buffer etc.
buffer etc.
PPC
c-alg.
PC-CO
DAB
DAB
18 BPM/crate
16 COD/gateway
70x
network
   50 x
   network
beam response

---
Commissioning of Feedbacks I/IV
Most feedbacks checks can be and are done during hardware commissioning:
  - Interfaces and communication from BI and to PO front-ends (done)
  - Interfaces to databases, tune kicker, PLL FESA integration (soon)
Using the 'test-bed' we will do the further tests without beam: (in progress)
  - analysis routines, time-domain and circuit failure interception routines
Things that have to and can only be checked with beam:
  - PO-Circuits/BI-Instrument polarities, planes, mapping
    - reduced number of corrector circuits → ~ 1-2 shifts/FB
  - PLL: beam transfer function and rough test of calibrations
It is possible to run feedbacks already after above procedures:
  - auto-triggered at 0.1 – 1 Hz & lower closed loop bandwidth – “day 1..N”
  - In case of Q, Q' we will have the following options:
  - a) Input: 'FFT + peak detector' or PLL
  - b) Control level: TuneViewer GUI (slow) or Tune Feedback Controller (fast)
    - both implement the same algorithms!
is done
while threading
the first beam!

---
Commissioning of Feedbacks with Beam II/IV
Example: PLL Setup – Step I (HW lag compensation)
Essentially BTF and compensation consists of the adjustment of four parameters, preferably during injection plateau (stable tune and chromaticity)
  - 1st step: verify necessary excitation amplitude and plane mapping
  - 2nd step: verify long sample delay (once per installation, constant)
    - full range BTF (will be partially done also without beam)
    - count ±π wrap-around → number of delayed samples

---
Commissioning of Feedbacks with Beam III/IV
Example: PLL Setup – Step II (beam phase compensation)
Measure dφ/df slope ( ~ front-end non-lin. phase and kicker cable length)
Adjustments of the locking phase (tune-peak – phase matching)
dφ/df
Δφ

---
Commissioning of Feedbacks with Beam IV/IV
Example: PLL Setup – Step III → Ready for Q/C-/Q' Tracking
Based on commissioning experience at the SPS and RHIC:
  - provided stable circulating beam and absence of “surprises”, the initial PLL setup with beam can be quite fast: < 30 minutes net!
  - verification of proper loop operation in less than a minute (= one BTF)
Including verification of circuit mapping and polarities:
  - ~2-4 half-shifts with per beam per feedback loop

---
Conclusions
Baseline Q/Q' diagnostics and controls is in good shape
  - compatible with large values of chromaticity and nominal LHC operation
  - Feedback architecture, strategies and algorithms are well established
    - same feedback architecture for orbit, tune/coupling, chromaticity...
  - LHC priorities: Orbit/Energy FB → Q/C- PLL → Q' Tracker → Q/Q'/C- FB
Commissioning of feedbacks:
  - Most of the requirements for a minimum workable feedback systems are already fulfilled after threading and establishing circulating beam
    - about two to four half shifts/beam/feed-back for PLL/FB specific procedures
  - Feedbacks are most useful when used at an early stage
    - feedback signals provide feed-forward information for next cycles
'Egg of Columbus' principle: LHC is not the first machine with a BBQ, Q/Q' PLL system or beam-based feedback system, however: there is no guarantee for 'no surprises' or perfect commissioning prior to real LHC operation!
  - We are well prepared but some things need to be tested with real beam!

---
... after the Q/Q' commissioning
Thank you for your attention
the Q(')auls

---
additional supporting slides

---
PLL based Q/Q' tracking study at the SPS
PLL Side Exciter (SEX) based Tune Width/Q' Measurement
Resonant phase change ↔ tune width change
  - → “free” real-time tune footprint measurement
  - → measurable dependence of ΔQ ~ Q'
driven 2nd order resonance:
Q
Q-ΔQ
Q+ΔQ
2ΔQ ≈ 0.002 « 2Qs

---
PLL based Q/Q' tracking study at the SPS
PLL Side Exciter (SEX) based Tune Width/Q' Measurement
tan[φ(Q-ΔQ)]
tan[φ(Q+ΔQ)
(ΔQ = 0.001)
ΔQ' ~ 2.6
Inverse amplitude response R-1(Q)
Side-exciter phase appears to changes linearly with Q' (2007 MDs)
  - No additional momentum modulation
  - Absolute scale requires calibration w.r.t. to classic Q' measurement
  - Non-linear effects require further assessment → 2007 MD Target #2/3

---
OFC Scheme
Orbit Feedback/Feed-Forward Control Scheme
The feedback controller consists of three stages:
  - Compute steady-state corrector settings	based on measured parameter shift Dx=(x1,..., xn) that will move	the beam to its reference position for t→∞.
  - Compute a that will enhance the transition
  - Feed-forward: anticipate and add deflections to compensate	changes of well known sources
space
domain
time
domain
external input
(trigger, control parameter, Lumi-Feedback etc.)
Feedback Controller
ff estimate1
Σ
+
actual beam parameter
+
+
Dx → dss
d(t=0) → dss
Σ
G(s)
reference
“classic” parameter
correction
“classic”
feedback controller
machine
response
-
feedback-path = measured beam parameter

---
Reminder: Solution in Time-Domain
LHC PC (LR circuit) model G(s): rate-limited first order system with delays:
  - Linear optimal PI controller:
  - including non-linearities (delay & rate-limit):
: being the circuit time constant
K0:I-to-δ transfer func.
1/α: “effective” FB freq.
DPID(s) gains are independent on non-linearities and delays!!

---
Some Results: Smith-Predictor and Anti-Windup
reference
current response
ramping rate
integral signal
without anti-windup
without Smith Predictor
with full delay and windup
compensator scheme:

---
Nominal Feedback Response T0
Full LHC orbit simulation @1KHz sampling, (BPM sampling: 25Hz)
reference amplitude @7TeV:
  0.2 μm
   16 μm (working point)
 160 μm
800 μm

---
Nominal Feedback Disturbance Rejection Sd0
Full LHC orbit simulation @1KHz sampling, (BPM sampling: 25Hz)
reference amplitude @7TeV:
  0.2 μm
   16 μm (working point)
 160 μm
800 μm

---
Loop Interdependences and Cross-Talk II/III
Multiple FBs and measurements acting on the same RF cavity frequency	(N.B. radial position limited by collimator gap)
  - Q' tracker, energy FB (≈'radial loop'), Q'' and other optics measurements
  - strategy: orbit feedback acts as a slave system controlling the RF
    - dispersion orbit is subtracted/not corrected by 'regular OFB'
    - energy FB corrects w.r.t. to the by the Q' tracker set reference
      - ΔfRF = (ΔfQ' - Δfmeas )
classic
SVD based
classic
SVD based

---
Reminder: Solution in Space-Domain
Response Matrix and Calibration Uncertainties
Matrices are direct observables and can thus be measured with beam!
  - Imperfect optics and calibration errors may deteriorate convergence speed but not the convergence accuracy
  - Example: 2-dim error surface projection
perfect optic	→ 1 iteration
20% beta-beat	→ ~2 iterations
20% calibration error	→ ~7 iterations

---
Example: LHC Orbit Feedback Test at the SPS I/II
Real-Beam Data
BPM
Reading
(μm)
feedback off
450 GeV
Time (ms)
feedback on
injection at 26 GeV
feedback on (zoom)
~ measurement noise !!
ramp

---
BBQ-PLL based Q/Q' tracking
Since 2006: Vertical Tune Shifts due to SPS Impedance
See APC 2006-11-10 for details
Vertical tune shift are a result of:
  - SPS transverse impedance and changing bunch length/intensity

---
BBQ-PLL based Q/Q' tracking
Since 2006: Collimator Imp. Qx versus Full Gap Opening
See APC 2006-11-10 for details
Tune resolution: ΔQres≈ 10-6...10-7

---
LHC Q/Q' System Overview
LHC Q/Q' system: 5 racks, 9 VME crates, 10 DAB front-ends:
UA43-BY10 - support cavern left of IP4 [CFV-UA43-BQB2]
  - PLL-B2 (operation): Q/C- Phase-Locked-Loop System Beam 2
    - connected to BQK.6R4 (aka. 'Q shaker')
  - FFT-B2 (operation): periodic acq., logging, fill-to-fill studies, Beam 2
UA47-BY07 - support cavern right of IP4 [CFV-UA47-BQB1]
  - PLL-B1 (operation): as above but Beam 1
    - connected to BQK.6L4
  - FFT-B1 (operation) as above but Beam 1
UA47-BY12 [CFV-UA47-BQ → CFV-UA47-BQFFT?]
  - FFT-B1, FFT-B2: on demand FFT spectra acquisition
    - connected to RF damper system
    - software + hardware (TTL) link to MKQA
    - N.B. can be also used for periodic acquisition
  - (BQSHT-B1/B2: 'Head-Tail' acquisition system)
SX4-BY11 – surface building [CFV-SX4-BQDEVB1, CFV-SX4-BQDEVB2]
  - DEV-B1: LHC FFT/PLL/HT development system
  - DEV-B2: (Q: move to SPS? - “easier”/more available test-bed)

---
BBQ-PLL and -FFT Installation Overview
FFT2.B1
FFT2.B2
PLL.B1
FFT1.B1
PLL.B2
FFT1.B2
DEV.B1
DEV.B2

---
Head-Tail and Schottky Installation Overview
HT.B1
HT.B2
BQS.B1
BQS.B2

---
Technical Network and Data Communication I/II
CERN's Technical Network as backbone
  - Switched network
    - no data collisions
    - no data loss
  - double (triple) redundancy
Core: “Enterasys X-Pedition 8600 Routers”
  - 32 Gbits/s non-blocking, 3·107 packets/s
  - 400 000 h MTBF
  - hardware QoS
    - One queue dedicated to real-time feedback
    - ~ private network for the orbit feedback
Routing delay	~ 13 μs
longest transmission delay (exp. verified)	~ 320 μs	(500 bytes, IP5 -> Control room ~5 km)
  - 20% due to infrastructure (router/switches)
  - 80% due to traveling speed of light inside the optic fibre
worst case max network jitter « targeted feedback frequency!

---
Technical Network and Data Communication II/II
The maximum latency between CCC and IR5
  - tail of distribution is given by front-end computer and its operating system