## Slide 1
TLEP ... Lattice Design & Beam Optics
B. Holzer / B. Haerer
latest (good) news
Parameter-List on TLEP-WEB Page is hopelessly out of date
and out of reality
Quo usque tandem abutere, Catilina, patientia nostra?

## Slide 2
Present study case:
E=175 GeV,
ε = 2nm / 0.002nm

## Slide 3
Lcell=50m
Dipole: Ndipole = 2932
Ldipole = 21.3 m
due to techn. reasons: 2 * 11 m
bending angle = 2.14 mrad
B0 = 580 Γ
Quadrupole (arc):
Lquadrupole = 1.5 m
k=3.55*10-2 m-2
g=20.7 T/m
aperture: r0=30σ =11mm
Btip= 0.23 T
β ≈ 100m, Dx= 15.3 cm
FoDo Cell
At present the dipole length is “symbolic”. Due to technical reasons we think of putting
2 dipoles of 11m length each between the quads
TLEP ... Lattice Design (175 GeV)
V9e -> V10

## Slide 4
TLEP ... Lattice Design
24 Arcs : built out of 56 standard FoDo cells & 2 half bend cells at beginning and end
length of arc: ≈ 3.0km
each arc is embedded in dispersion free regions ...
arcs are connected by straight. sections ... 12 long (mini β and RF)
... 12 ultra shorties tbc
to be optimised

## Slide 5
TLEP Octant
Straight – Arc – Arc – Straight
arcs are connected in pairs via a disp-free-empty cell
-> only reason: in case of additional insertions we get the boundary conditions for free.

## Slide 6
TLEP Arc-Straights
8 Straights : 9 empty (i.e. dispersion free) FoDo cells including matching sections
arc-straight, l = 450m
arc cells
empty cells
arc cells
empty cells
to be optimised: βy at matching section,
needs an additional quadrupole lens  already built in but not used yet.
and / or optimisation of the lens positions

## Slide 7
TLEP The Ring
rf-sections
Lring = 79.9km
4 min- betas,
24 disp free straights, 12 long straights
8 for rf equipment, 4 for mini-betas & rf
*
*
*
*
*
*
*
*
*
*
*
*

## Slide 8
TLEP Lattice ... converging to a realistic approach
Questions to answer:
* hardware of the lattice
e.g. LHeC type dipoles
* feasibility of the cell design
flanges / pumps / BPMs etc
* what about synchrotron radiation ... do we need absorbers and where ?
Fluka / Helmut / Manuela
* vacuum design
Mark, Roberto, Cedric
* tolerance considerations
do we get the hor & vert. emittance ????
BH & BH
* what kind of correctors & BPMs do we need and where to install them
Alexander (Petra 3), Francis, Montse (ALBA)
* do we need a weak bend at the end of the arc (YES) and how weak should it be ?
Helmut & family
* how does the lattice scale with cell length / phase advance
BH &BH

## Slide 9
TLEP V9e
... first FLUKA results
FLUKA status and plan Sixth TLEP workshop CERN, 16 -18 October 2013
F. Cerutti#, A. Ferrari#, L. Lari*, A. Mereghetti#
power density in the dipole chambers has to be reduced
by installation of lead shield
power density along the dipoles
-> shorter dipole design

## Slide 10: Peak Dose on the coils
TLEP V9e
... first FLUKA results
the ideal FLUKA world ;-))

## Slide 11
TLEP V9e
... first Vacuum Considerations (court. C. Garion, R. Kersevan)
schematic cell layout:
assuming “reasonable” drifts
realistic BB interconnects
Sy-Li Absorber
realistic BQ interconnects

## Slide 12
TLEP V10
..Lattice Modifications: court. B. Haerer
V9e cell
V10 cell
“old” Cell Layout
? ... do we keep the cell length ?
? ... do we cut the dipole length ?
? ... do we enlarge the FoDO length ?

## Slide 13
Next steps:
1) Optics fine tuning: including vacuum design & Fluka
2) Tolerances & Emittances for a realistic machine
can we keep the small vertical ε
3) Include orbit corrections & BPMs (cell length ??)
PETRA3, ALBA ... nested correctors ?
4) Include a weak bend at the end of the arc
... how weak -> sy-li fan geometry, Ecrit
5) Lattice for lower energies
scaling of ε -> re-shuffle FoDo structure
6) goto 1),
goto 2)

## Slide 14
TLEP V.xxx ...Lattice Modifications for smaller energies
equilibrium emittance
scaling of dispersion in a FoDo
scaling of D with phase advance
90o
Lcell = 50m
Lcell = 100m
Lcell = 150m
coarse tuning via cell length, fine tuning via phase advance & wigglers