## Slide 1: Preliminary Data Quality Checking
Bethany Broekhoven
LSU
CALET TIM Nov. 2013

## Slide 2: Note
This presentation is being presented in hopes to start a discussion on the Data Quality Checking plots and displays. In this presentation, we are trying to determine which plots are key plots as well as which key plots are beneficial to all collaborators and should be run on a recurring routine to produce them.
DQC, CALET TIM - Nov 2013
2
11/19/2013

## Slide 3
Main Purpose:
The main purpose of the Data Quality Checking is to monitor the overall status of CALET using Level 1 data.
Displaying Data Quality Checks:
Data Quality Checks will be displayed on a website for all CALET collaborators to observe. CALET collaborators will be able to choose which Data Quality Checks they wish to view.
DQC, CALET TIM - Nov 2013
3
11/19/2013

## Slide 4: Types of Data Quality Checking
Housekeeping and Normal Operation
  To monitor housekeeping data of CALET
Positional
  To track CALET and the ISS in their orbit
Electronics Health Status
  To assess the instrument electronics status and performance over the long term
Detector Health Status
  To assess the instrument detectors status and performance over the long term
Rates
  To monitor the trigger rates of CALET
DQC, CALET TIM - Nov 2013
4
11/19/2013

## Slide 5: Housekeeping and Normal Operation
Temperature/Voltage vs. Time
  To monitor temperature/voltage as a function of time
  Required Input: Temperature/Voltage data and Timestamp
Events vs. Time
  To monitor the number of events as a function of time
  Required Input: Number of Events and Timestamp
Error Counts vs. Time
  To monitor the number of record errors as a function of time
    Make sure the number of record errors is consistent
  Required Input: Number of Errors and Timestamp
DQC, CALET TIM - Nov 2013
5
11/19/2013

## Slide 6: Housekeeping and Normal Operation
Instrument mode (e.g. normal, calibration, SAA, etc.) vs. Time
  To track the operational configuration of CALET as a function of time
  Required Input: Instrument Mode data and Timestamp
Trigger Configuration vs. Time
  To monitor the trigger configuration as a function of time
  Required Input: Trigger Configuration data and Timestamp
DQC, CALET TIM - Nov 2013
6
11/19/2013

## Slide 7: Positional
CALET Orientation/ Position vs. Time
  To track detector orientation/position as a function of time
  Required Input: CALET Orientation/ Position data and Timestamp
ISS Altitude, Geographic Lat./Lon., Geomagnetic Lat./Lon., L-shell (Re) vs. Time
  To track ISS’s position as a function of time
  Required Input: ISS Altitude, Geographic Lat./Lon., and Geomagnetic Lat./Lon. data and Timestamp
ISS Obstacle (solar arrays) Orientation/ Position vs. Time
  To track ISS obstacle orientation/position as a function of time
  Required Input: ISS obstacle Orientation/ Position data and Timestamp
DQC, CALET TIM - Nov 2013
7
11/19/2013

## Slide 8: Positional Effects
Temperature vs. Geomagnetic Lat. and L-shell
  To monitor temperature as a function of CALET’s position in the geomagnetic field
  Possibly only temperatures at the end points of the detector
  Required Input: Temperature and Geomagnetic Lat./L-shell position data
Geomagnetic Latitude vs. Longitude
  Possible plot showing the event rate as a function of geomagnetic position
    Can look for anomalies such as the SAA
DQC, CALET TIM - Nov 2013
8
11/19/2013

## Slide 9: Electronics Health Status
Pedestal vs. Time
  Plot pedestal and mean pedestal values vs. time
  To monitor pedestal values as a function of time
  Required Input: Pedestal data and Timestamp
Pedestal Width vs. Time
  To look for anomalies and changes in the pedestal width and shifts
  To look for intermittent/dead channels
  Used to determine Front-End Components (FEC) behavior over time
  Required Input: Pedestal data and Timestamp
DQC, CALET TIM - Nov 2013
9
11/19/2013

## Slide 10: Electronics Health Status
Pedestal vs. Temperature
  To monitor the pedestal data as a function of temperature
  Required Input: Pedestal and Temperature data
Pedestal vs. Voltage
  To monitor the pedestal data as a function of voltage
  Required Input: Pedestal and Voltage data
The same plots in the Electronics Health Status section can be produced for the charge injections calibrations.
DQC, CALET TIM - Nov 2013
10
11/19/2013

## Slide 11: Detector Health Status
Pseudo Energy vs. Time
  To monitor pseudo dE as a function of time
  Required Input: pseudo dE data and Timestamp
Pseudo Energy vs. Temperature
  To monitor pseudo dE data as a function of temperature
  Required Input: pseudo dE and Temperature data
Pseudo Energy vs. Voltage
  To monitor the pseudo dE data as a function of voltage
  Required Input: pseudo dE and Voltage data
DQC, CALET TIM - Nov 2013
11
11/19/2013

## Slide 12: Detector Health Status
Pseudo Energy vs. Event Size
  To monitor pseudo dE as a function of event size
  Helps look for a noisy channel
  Required Input: pseudo dE and Event Size data
Pseudo Energy Distribution
  To look for anomalies as well as changes in energy width and shifts
  To look for intermittent/dead channels
  Used to determine FEC behavior over time
  Required Input: pseudo dE data
DQC, CALET TIM - Nov 2013
12
11/19/2013

## Slide 13: Detector Health Status
Orbit averaged CHD, IMC and TASC pseudo energy deposit spectrum selected on like trigger settings.
  To monitor changes in the detector performance over long term
  Required Input: pseudo dE data on selected trigger settings
Orbit averaged CHD, IMC and TASC pseudo energy deposit histograms for events that do not generate a shower selected on like trigger settings.
  To monitor changes in the detector performance over long term
  Required Input: pseudo dE data for particular events on selected trigger settings
Can also do an L-shell cut and a South Atlantic Anomaly (SAA) cut on the above two Data Quality Checks.
DQC, CALET TIM - Nov 2013
13
11/19/2013

## Slide 14: Rates
Rates vs. Time
  Trigger Rates and Detector Count Rates
  To monitor the rates as a function of time
  Required Input: Trigger Rates and Timestamp
Rates vs. Geomagnetic Lat. and L-shell
  To monitor trigger rates as a function of CALET’s position in the geomagnetic field
  Required Input: Trigger Rates and Geomagnetic Lat./L-shell position data
DQC, CALET TIM - Nov 2013
14
11/19/2013

## Slide 15: Rates
Dead Time vs. Time
  To monitor detector dead time and make sure it is within dead time range
  Required Input: Rates data, Online Clock Counter, Offline Clock Counter and Timestamp
Pedestal vs. Rates
  To monitor the pedestal data as a function of trigger rates
  Required Input: Pedestal and Trigger Rate data
Pseudo Energy vs. Rates
  To monitor the pseudo dE data as a function of trigger/detector count rates
  Required Input: pseudo dE and Trigger/Detector Count Rate data
DQC, CALET TIM - Nov 2013
15
11/19/2013

## Slide 16: Questions/Comments?
DQC, CALET TIM - Nov 2013
16
11/19/2013